## Slide 1
PSD13, September 2023
Martin Sharratt – Director, AP Technologies
Broadcom’s NUV-MT SiPM technology

## Slide 2: Broadcom at a Glance
FY22 net revenue of $33.2B
22 Category-Leading Semiconductor and Infrastructure Software Divisions
$4.9B investment in R&D in FY22
One of the industry’s broadest IP portfolios with >17,000 patents in FY22

## Slide 3: From photodiode to SPAD
Photodiode
1 photon
 1 electron
APD
1 photon
 100 electrons
SPAD / SiPM
Geiger mode:
1 photon  millions of electrons
p-n junctions in semiconductors are the basis of
  Photodiodes
  APDs
  SPADs
Can be differentiated by gain
Gain can be driven by reverse bias
APD: Avalanche Photodiode internal gain 10 to 100
SPAD: Single Photon Avalanche Diode Geiger mode internal gain up to 10M
-
+
Broadcom
AFBR-S5
Broadcom
AFBR-S4
Breakdown voltage

## Slide 4: From SPAD to SiPM
t
current
t
current
SPAD working in Geiger mode
…
Sum of individual SPAD dischargesignals
Silicon Photomultiplier (SiPM)
Single SPAD discharge signal regardless of number of incident photons

## Slide 5
3.89 mm
SiPM Images
…
30 µm
Quenching resistor
Metal readout line
SPAD

## Slide 6
AFBR-S4N: NUV-MT SiPM

## Slide 7: NUV-MT – Performance Overview
/mm2)
12 V OV, 25°C
 | NUV-MT
Sensitivity range (nm) | 250 to 900
Peak sensitivity (nm) | 420
PDE at 420nm (%) | 63
Gain (M) | 7.3
DCR (kcps/mm2) | 120
SPAD pitch (µm) | 40
CT (%) | 23
AP (%) | 1
𝛕recharge (ns) | 55
Typ. OV | 12
Temp. coefficient (mV/°C) | 30
Vbreak (V) | 32.5
PDE (%)
PDE @ 420nm (%)
Wavelength (nm)
25°C,12VOV
420nm PDE is >55% at 7VOV
Overvoltage
25°C,12VOV

## Slide 8: NUV-MT – Performance Overview
25°C,12VOV
Dark count-rate (kcps/mm2)
 | NUV-MT
Sensitivity range (nm) | 250 to 900
Peak sensitivity (nm) | 420
PDE at 420nm (%) | 63
Gain (M) | 7.3
DCR (kcps/mm2) | 120
SPAD pitch (µm) | 40
CT (%) | 23
AP (%) | 1
𝛕recharge (ns) | 55
Typ. OV | 12
Temp. coefficient (mV/°C) | 30
Vbreak (V) | 32.5
Overvoltage
~65kcps @ 7VOV
Dark Current
-0V to >50V
-20°C to +60°C

## Slide 9: NUV-MT – Performance Overview
AP < 1%
Total correlated noise (%)
 | NUV-MT
Sensitivity range (nm) | 250 to 900
Peak sensitivity (nm) | 420
PDE at 420nm (%) | 63
Gain (M) | 7.3
DCR (kcps/mm2) | 120
SPAD pitch (µm) | 40
CT (%) | 23
AP (%) | 1
𝛕recharge (ns) | 55
Typ. OV | 12
Temp. coefficient (mV/°C) | 30
Vbreak (V) | 32.5
Overvoltage
~17% @ 7VOV
25°C,12VOV

## Slide 10: NUV-MT – Performance Overview
dVBD/dT = 30mV/°C
 | NUV-MT
Sensitivity range (nm) | 250 to 900
Peak sensitivity (nm) | 420
PDE at 420nm (%) | 63
Gain (M) | 7.3
DCR (kcps/mm2) | 120
SPAD pitch (µm) | 40
CT (%) | 23
AP (%) | 1
𝛕recharge (ns) | 55
Typ. OV | 12
Temp. coefficient (mV/°C) | 30
Vbreak (V) | 32.5
Temperature (°C)
Vbreak (V)
31
33.5
-20°C
60°C

## Slide 11: NUV-MT: New Package Design
Overmolded PCB with bond wire
Focus:
  Highest transmittance of mold compound in UV-blue
  Long term stability (no yellowing)
  High reliability & ruggedness
  Cost efficiency & Simple + Flexible supply-chain
  High Package Fill Factor
175µm
0.1mm
Typical Backside (LGA)

## Slide 12: NUV-MT: Overmold Material
Candidates selected for best optical peformance over lifetime
  3000hrs at 120°C correspond to lifetime of about 20 years at 25°C
420nm
97% transmittance
90% transm.
PDE vs. Time
200 hrs
680 hrs
3000 hrs
at 420 nm
63.8%
62.8%
PDE vs time Production package

## Slide 13: NUV-SiPM Product Summary & Outlook
Part no | Technology | Size (mm2) | Channels | Package | Status
AFBR-S4N22P014M | NUV-MT | 2 x 2 | 1 | Overmolded PCB | E-Samples
AFBR-S4N44P014M | NUV-MT | 4 x 4 | 1 | Overmolded PCB | in production
AFBR-S4N66P014M | NUV-MT | 6 x 6 | 1 | Overmolded PCB | in production
AFBR-S4N66P024M | NUV-MT | 13 x 6 | 2 x 1 | Overmolded PCB | in production
AFBR-S4N44P044M | NUV-MT | 8 x 8 | 2 x 2 | Overmolded PCB | in production
AFBR-S4N44P164M | NUV-MT | 16 x 16 | 4 x 4 | Overmolded PCB | in production
AFBR-S4KTIA3315B | NUV-B* | 3 x 3 | 1 | TIA-module | in production
*TIA module to be upgraded to NUV-MT

## Slide 14
Thank you!
Please come and talk to me in the industrial exhibit
mjs@aptechnologies.co.uk