## Slide 1: Beam-beam and optics studies in FCC-ee
T. Prebibaj
In collaboration with:
K. Andre, X. Buffat, H. Barotsik, M. Jebramcik, J. Keintzel, S. Kostoglou, E. H. Maclean, T. Pieloni, P. Raimondi, L. Sievert, K. Skoufaris, R. Tomas, W. Van Goethem, L. Van Riesen-Haupt, Y. Wu
EPFL-LPAP Activity Meeting
16/04/2026
Work supported by the Swiss Accelerator Research and Technology (CHART)

## Slide 2: FCC-ee
The Future Circular electron-positron Collider (FCC-ee) is a proposed 90.7 km circumference collider designed to operate at four energies: 45.6 GeV (Z), 80 GeV (WW), 120 GeV (ZH), and 182.5 GeV (ttbar)
Conceptual Design Report published in 2019 Feasibility Study Report in 2025 Decision point expected in 2028.
fcc.web.cern.ch

## Slide 3: A very brief overview of relevant beam dynamics concepts

## Slide 4: Beam dynamics in FCC-ee
Performance
Beam-beam
Radiation
Imperfections
Corrections
Optics

## Slide 5: The collider lattice
Performance
Beam-beam
Radiation
Imperfections
Corrections
Optics
Collider lattice is fundamental for all systems (e.g. magnets, insertions, …) & performance.
  Two main variants: GHC (“Global Hybrid Correction”) by K. Oide and LCC (Local Chromaticity Correction) by P. Raimondi.
  A review panel recommended adopting the LCC optics as the new baseline (read advantages).
LCC v106.2.1 at Z

## Slide 6: The collider lattice
Performance
Beam-beam
Radiation
Imperfections
Corrections
Optics
LCC v106.2.1 at Z
cm
mm
Collider lattice is fundamental for all systems (e.g. magnets, insertions, …) & performance.
  Two main variants: GHC (“Global Hybrid Correction”) by K. Oide and LCC (Local Chromaticity Correction) by P. Raimondi.
  A review panel recommended to adopt the LCC optics as the new baseline (read advantages).

## Slide 7: Synchrotron Radiation
Performance
Beam-beam
Radiation
Imperfections
Corrections
Optics
Image source
Synchrotron Radiation (SR) power (<50 MW per beam) is the main constraint on beam intensity (or total current ).
  SR causes exponential damping of transverse & longitudinal emittances.
  Quantum excitation leads to an equilibrium emittance in the horizontal and longitudinal planes and to a very small (but non-zero) vertical emittance.
  In practice, the vertical emittance is dominated by machine imperfections that lead to vertical dispersion and betatron coupling.

## Slide 8: Lattice imperfections
Performance
Beam-beam
Radiation
Imperfections
Corrections
Optics
Courtesy of L. Sievert
J. Wenninger, “Linear Imperfections”, CAS 2018.
Lattice imperfections give rise to numerous undesired effects!
  Orbit & optics distortions (e.g. coupling, beta-beating, …)  emittance increase and/or losses  loss of performance.
  Developing correction schemes to keep these effects under control is a major challenge.
  Lara is working on modelling these imperfections and understanding their impact on performance in presence of beam-beam.

## Slide 9: Beam-beam effects
Performance
Beam-beam
Radiation
Imperfections
Corrections
Optics
Beam-beam interactions modify key lattice properties (e.g. tunes, beta-beating, …) and can degrade beam quality (e.g. emittance blow-up, instabilities, …).
  Minimizing these effects is essential for maximizing luminosity.
Typical for FCC-ee at Z:

## Slide 10: FCC-ee parameters & performance
Performance
Beam-beam
Radiation
Imperfections
Corrections
Optics
Luminosity is given by:
Parameters from optics comparison report, values may have been updated since then.

## Slide 11: Beam dynamics in FCC-ee
Performance
Beam-beam
Radiation
Imperfections
Corrections
Optics

## Slide 12: Beam dynamics in FCC-ee
Performance
Beam-beam
Radiation
Imperfections
Corrections
Optics

## Slide 13: Focus of my studies
Performance
Beam-beam
Radiation
Imperfections
Corrections
Optics
Analyze current FCC-ee lattices to identify sensitivities to beam-beam forces & machine imperfections.
Develop correction schemes / tuning knobs for improving beam stability and performance in beam-beam dominated regimes.

## Slide 14: Sensitivity of vertical emittance on a lattice with beam-beam

## Slide 15: A tracking example without radiation
(i.e. like a proton accelerator)

## Slide 16: A tracking example without radiation
Without beam-beam

## Slide 17: A tracking example without radiation
Without beam-beam
With beam-beam (only linear): phase space mismatch
Beta-beat from beam-beam

## Slide 18: A tracking example without radiation
Without beam-beam
With beam-beam (only linear): phase space mismatch
After rematching linear optics (we will see later how…)

## Slide 19: A tracking example without radiation
Without beam-beam
With beam-beam (only linear): phase space mismatch
After rematching linear optics (we will see later how…)
Removing off-momentum dependence (by forcing a monochromatic beam…)

## Slide 20: A tracking example without radiation
Without beam-beam
With beam-beam (only linear): phase space mismatch
After rematching linear optics (we will see later how…)
Removing off-momentum dependence (by forcing a monochromatic beam…)
Removing strong non-linear elements (crab sextupoles)
Strong linear optics distortions from beam-beam would lead to a phase space mismatch.
Non-linear properties of the lattice are not negligible on the beam emittance.
Beam-beam
Optics

## Slide 21: A tracking example with radiation
Beam emittance ↔ equilibrium emittance
Emittance source in ideal lattice: four vertical wigglers distributed around the lattice

## Slide 22: A tracking example with radiation
Equilibrium w/o beam-beam
Tracking with beam-beam (only linear)
Tracking w/o beam-beam
Equilibrium with beam-beam (only linear)
Strong linear optics distortions from beam-beam lead to different equilibrium emittance.
Non-linear properties of the lattice are not negligible to equilibrium emittance.

## Slide 23: A tracking example with radiation
Equilibrium w/o beam-beam
Tracking with beam-beam
Tracking w/o beam-beam
Equilibrium with beam-beam
Strong linear optics distortions from beam-beam lead to different equilibrium emittance.
Non-linear properties of the lattice are not negligible to equilibrium emittance.
Non-linear contribution of beam-beam and beamstrahlung (BS) are also not negligible.
Beam-beam
Optics
Radiation

## Slide 24: An example of a tuning knob with beam-beam

## Slide 25: Rematching linear optics
Rematching quadrupoles

## Slide 26: Rematching linear optics
Rematched lattice:
  Optics distortions compensated in arcs and technical insertions.
  Maintained additional focusing induced by beam-beam at IPs (“dynamic β*”)

## Slide 27: Reducing vertical emittance blow-up
Equilibrium w/o beam-beam
Tracking with beam-beam
Tracking w/o beam-beam
Equilibrium with beam-beam
Rematching linear optics

## Slide 28: Tuning-knob and luminosity

## Slide 29: Reducing vertical emittance blow-up
Equilibrium w/o beam-beam
Tracking with beam-beam
Tracking w/o beam-beam
Equilibrium with beam-beam
Rematching linear optics
Some considerations:
  Beam-beam forces are very non-linear → optics distortions are amplitude dependent → correcting the zero-amplitude optics leads to overcorrection of higher amplitudes → some intermediate correction?
  Rematching the non-linear properties?
  So far: ideal lattice with “fake” emittance sources (vertical wigglers). What will matter in a lattice with lattice imperfections?

## Slide 30: Lattices with imperfections and beam-beam

## Slide 31: Tracking in lattices with imperfections (in progress…)
Beam-beam
Optics
Radiation
Performance
Imperfections
Corrections
w/o beam-beam
with beam-beam
with beam-beam
with beam-beam and partial optics rematching

## Slide 32: Summary & Outlook

## Slide 33: Summary & Outlook
Vertical emittance blow-up in the ideal lattice with beam-beam
  Multiple effects contribute to emittance growth in tracking with beam–beam, even in an ideal lattice.
  How much we want to control these effects in practice?
Tracking tuned lattices with beam-beam
  Initial exploratory tracking simulations with “quasi-strong” beam-beam.
  Plan to study/understand source of losses and emittance increase (as in the ideal lattice) and propose potential mitigations.
RDT sensitivity scans with beam-beam (in backup slides)
  Ongoing work towards understanding which RDTs drive performance with beam-beam and how to compensate them.
Thank you for your attention!

## Slide 34: Backup

## Slide 35: Beam-beam and RDT scans
3Qy
Qx-2Qy
2Qx-Qy
Qx+2Qy
2Qx+Qy
Qx-Qy
2Qy
2Qx
Qx
Qy
Qx-3Qy
3Qx-Qy
2Qx-2Qy
4Qy
4Qx
3Qx
2Qx+2Qy
1st order resonances
2nd order resonances
3rd order resonances
4th order resonances
RDTs:
  3rd order normal: f1020, f1011, f1002, f3000, f2100
  3rd order skew: f0030, f0012, f2010, f2001, f1110
  4th order normal: f4000, f3100, f2020, f2011, f2002, f1120, f0040, f0031
  4th order skew: f3010, f3001, f2110, f2101, f1021, f1012, f1030, f1003
  …

## Slide 36: RDTs of ideal lattice
RDTs:
  3rd order normal: f1020, f1011, f1002, f3000, f2100
  3rd order skew: f0030, f0012, f2010, f2001, f1110
  4th order normal: f4000, f3100, f2020, f2011, f2002, f1120, f0040, f0031
  4th order skew: f3010, f3001, f2110, f2101, f1021, f1012, f1030, f1003
  …
“Agnostic” approach:
  Change individual RDTs either locally (e.g. at IPs) or globally
  Track with beam-beam and see impact on performance (lifetime, emittance, lumi, …)
(m-1/2)
(m-1)
Notes: fjklm units of [m]^(1-n/2), n = j+k+l+m
e.g.: sextupole m ^ -1/2. octupole is m^-1

## Slide 37: Changing a single RDT
RDTs:
  3rd order normal: f1020, f1011, f1002, f3000, f2100
  3rd order skew: f0030, f0012, f2010, f2001, f1110
  4th order normal: f4000, f3100, f2020, f2011, f2002, f1120, f0040, f0031
  4th order skew: f3010, f3001, f2110, f2101, f1021, f1012, f1030, f1003
  …
“Agnostic” approach:
  Change individual RDTs either locally (e.g. at IPs) or globally
  Track with beam-beam and see impact on performance (lifetime, emittance, lumi, …)

## Slide 38: Changing a single RDT
RDTs:
  3rd order normal: f1020, f1011, f1002, f3000, f2100
  3rd order skew: f0030, f0012, f2010, f2001, f1110
  4th order normal: f4000, f3100, f2020, f2011, f2002, f1120, f0040, f0031
  4th order skew: f3010, f3001, f2110, f2101, f1021, f1012, f1030, f1003
  …
“Agnostic” approach:
  Change individual RDTs either locally (e.g. at IPs) or globally
  Track with beam-beam and see impact on performance (lifetime, emittance, lumi, …)
Standard (truncated) SVD:
  Build linear response matrix R with large number of individually powered correctors:
  Define a target RDT change:
  Invert using truncated SVD:
  While it minimizes , it leads to cross-talk between RDTs.

## Slide 39: Changing a single RDT
Standard (truncated) SVD:
  Build linear response matrix R with large number of individually powered correctors:
  Define a target RDT change:
  Invert using truncated SVD:
  While it minimizes , it leads to cross-talk between RDTs.
Standard (truncated) SVD
Target

## Slide 40: Changing a single RDT
RDTs:
  3rd order normal: f1020, f1011, f1002, f3000, f2100
  3rd order skew: f0030, f0012, f2010, f2001, f1110
  4th order normal: f4000, f3100, f2020, f2011, f2002, f1120, f0040, f0031
  4th order skew: f3010, f3001, f2110, f2101, f1021, f1012, f1030, f1003
  …
“Agnostic” approach:
  Change individual RDTs either locally (e.g. at IPs) or globally
  Track with beam-beam and see impact on performance (lifetime, emittance, lumi, …)
Standard (truncated) SVD:
  Build linear response matrix R with large number of individually powered correctors:
  Define a target RDT change:
  Invert using truncated SVD:
  While it minimizes , it leads to cross-talk between RDTs.

## Slide 41: Changing a single RDT
RDTs:
  3rd order normal: f1020, f1011, f1002, f3000, f2100
  3rd order skew: f0030, f0012, f2010, f2001, f1110
  4th order normal: f4000, f3100, f2020, f2011, f2002, f1120, f0040, f0031
  4th order skew: f3010, f3001, f2110, f2101, f1021, f1012, f1030, f1003
  …
“Agnostic” approach:
  Change individual RDTs either locally (e.g. at IPs) or globally
  Track with beam-beam and see impact on performance (lifetime, emittance, lumi, …)
Standard (truncated) SVD:
  Build linear response matrix R with large number of individually powered correctors:
  Define a target RDT change:
  Invert using truncated SVD:
  While it minimizes , it leads to cross-talk between RDTs.
A more “weighted SVD” :
  Split R into target & non-target RDT parts:
  Solve a weighted least squares:
  A suppresses cross-talk of non-target RDTs
  B limits corrector strengths
  Reduces to standard SVD solution when A=B=0

## Slide 42: Example: changing f3000 by +25%
“Weighted” SVD
Standard (truncated) SVD
Target
Target

## Slide 43: Changing a single RDT
RDTs:
  3rd order normal: f1020, f1011, f1002, f3000, f2100
  3rd order skew: f0030, f0012, f2010, f2001, f1110
  4th order normal: f4000, f3100, f2020, f2011, f2002, f1120, f0040, f0031
  4th order skew: f3010, f3001, f2110, f2101, f1021, f1012, f1030, f1003
  …
“Agnostic” approach:
  Change individual RDTs either locally (e.g. at IPs) or globally
  Track with beam-beam and see impact on performance (lifetime, emittance, lumi, …)
Standard (truncated) SVD:
  Build linear response matrix R with large number of individually powered correctors:
  Define a target RDT change:
  Invert using truncated SVD:
  While it minimizes , it leads to cross-talk between RDTs.
A more “weighted SVD” *:
  Split R into target & non-target RDT parts:
  Solve a weighted least squares:
  A suppresses cross-talk of non-target RDTs
  B limits corrector strengths
  Reduces to standard SVD solution when A=B=0
*Need to make sure tunes, chroma, second order dispersions, higher order RDTs, … remain unperturbed.

## Slide 44: Tracking
RDTs:
  3rd order normal: f1020, f1011, f1002, f3000, f2100
  3rd order skew: f0030, f0012, f2010, f2001, f1110
  4th order normal: f4000, f3100, f2020, f2011, f2002, f1120, f0040, f0031
  4th order skew: f3010, f3001, f2110, f2101, f1021, f1012, f1030, f1003
  …
“Agnostic” approach:
  Change individual RDTs either locally (e.g. at IPs) or globally
  Track with beam-beam and see impact on performance (lifetime, emittance, lumi, …)
  Xsuite
  LCC 106.1.0 at Z
  Tapered lattice, no imperfections
  Quantum radiation + beamstrahlung, no Bhabha scattering
  Weak-strong beam-beam: strong beam initialized with equilibrium lattice emittances and 251 slices.
  8000 particles tracked for 8000 turns
  Monitoring in RF sections (dispersion-free)
  Artificial aperture at 20σ in both transverse plane (LimitRect) and at the bucket length (LongitudinalLimitRect).

## Slide 45: RDT scans with beam-beam
3rd order normal

## Slide 46: RDT scans with beam-beam
Even with an agnostic/numerical approach, one can:
  Rank relative importance of individual RDTs with beam-beam (e.g. f1011<f3000<f1002)
  Quantify their impact on observables (e.g. f3000 causes mainly losses).
Caveats:
  Difficult to disentangle local RDT effects (e.g. IP geometric aberrations) from global effects (e.g. losses)
  Single-RDT scans are not fully isolated due to coupling to higher-order RDTs
Outlook / potential directions:
  Understand why specific RDTs drive performance with beam-beam
    Resonance excitation?
    coupling to higher-order terms (e.g. 2nd-order dispersion)
  Can the numerical scans guide us to specific corrector configurations?
3rd order normal
Also work in progress!