## Slide 1
LPAP Activity Meeting 07 May 2026
Parametrization of Electron Cloud Buildup Models
Adam Furman Lotta Mether, Luca Sabato, Tatiana Pieloni, Mike Seidel

## Slide 2
Overview
A brief overview of electron clouds.
Electron cloud buildup simulations, using PyECLOUD.
Modelling electron cloud buildup.
Predicting model parameter values a priori.
Observations, limitations, and strategies.
Tools you can use.

## Slide 3
A brief overview of electron clouds
Electron clouds occur when the conditions inside a particle accelerator facilitate the buildup of electrons over time.
Beam Chamber
Synchrotron Radiation

## Slide 4
A brief overview of electron clouds
Some amount of initial electrons (from synchrotron radiation or residual gas collisions) is present in the beam chamber.
Beam Chamber
Synchrotron Radiation

## Slide 5
A brief overview of electron clouds
The electrons are kicked by the electromagnetic force of a passing bunch and hit the beam chamber wall.
Beam Chamber
Synchrotron Radiation

## Slide 6
Image: Giovanni Iadarola
A brief overview of electron clouds
The secondary electron yield (SEY) curve, a material property, defines secondary electron emission based on incident energy.

## Slide 7
Image: Giovanni Iadarola
A brief overview of electron clouds
Some (low energy) electrons are reflected off the wall. Higher energy electrons trigger the emission of true secondaries.

## Slide 8
Image: Giovanni Iadarola
A brief overview of electron clouds

## Slide 9
A brief overview of electron clouds
Magnetic fields influence the shape of the electron cloud.
Images: Giovanni Iadarola

## Slide 10
A brief overview of electron clouds
The cloud saturates when its field is strong enough to prevent the extraction of new electrons at the surface.
When? Depending on…
The bunch intensity.
The secondary electron yield curve (material properties).
Photoemission from synchrotron radiation.
Magnetic field type and strength.

## Slide 11
Electron cloud buildup simulations
Bunch Intensity
Filling Scheme
Secondary Electron Yield
Magnets
PyECLOUD

## Slide 12
Electron cloud buildup simulations
PyECLOUD
One of the simulation outputs is the electron cloud linear density over time – this is what we will focus on modelling.

## Slide 13
Electron cloud buildup simulations
There is one oscillation per bunch passage.

## Slide 14
Electron cloud buildup simulations
We often perform parameter sweeps to study e-cloud buildup in a new machine configuration.
SEY
Intensity

## Slide 15
Sensitivity to parameters: SEY
A low SEY value can lead to the electron cloud decaying. Note, here SEY > 1.0

## Slide 16
Sensitivity to parameters: SEY
The buildup can be quite slow.

## Slide 17
Sensitivity to parameters: SEY
The characteristic shape of a buildup curve looks a lot like a “logistic” or “sigmoid” curve.

## Slide 18
Sensitivity to parameters: SEY
Note that both the saturation density and the time to reach it change as a function of SEY.

## Slide 19
Sensitivity to parameters: Intensity
Let’s start with one of the curves we already saw.

## Slide 20
Sensitivity to parameters: Intensity
Stepping down in intensity, we again fail to build up.

## Slide 21
Sensitivity to parameters: Intensity
Stepping up, the saturation density increases.

## Slide 22
Sensitivity to parameters: Intensity
We increase the intensity again – and the saturation density decreases! There must exist some critical intensity…

## Slide 23
Sensitivity to parameters: Magnets
So far, we have only shown plots in drift sections.

## Slide 24
Sensitivity to parameters: Magnets
In a dipole, the saturation density increases.

## Slide 25
Sensitivity to parameters: Magnets
… as in a quadrupole.

## Slide 26
Sensitivity to parameters: Magnets
In a sextupole, there is a noticeable effect on the time to reach saturation as well as the saturation density.

## Slide 27
Modelling buildup curves
Can we reduce the buildup curve data to a (simple) model? Will such a model capture the trends seen in parameter sweeps?
Desired Features
Saturation.
Independent of initial N.
Increase with SEY.
Critical (worst) intensity.
Response to magnets.

## Slide 28
Modelling buildup curves
Total change in N. of e-
Rate of primary e- (photoemission)
Rate of secondary e- (SEY)
Rate of collisions with walls.

## Slide 29
Modelling buildup curves
Beam density.
Flux over whole perimeter

## Slide 30
Modelling buildup curves
This automatically limits the model to describing average density within each bunch passage.

## Slide 31
Modelling buildup curves

## Slide 32
Modelling buildup curves

## Slide 33
Modelling buildup curves
No dependance on initial density!

## Slide 34
Modelling buildup curves
The model captures the average density well.

## Slide 35
Modelling buildup curves
… and it works even when we don’t build up.

## Slide 36
Modelling buildup curves
… and it works even when we don’t build up.

## Slide 37
Modelling buildup curves
For magnets, the curve fit does not work as well (expected).

## Slide 38
Modelling buildup curves
To understand dependance on SEY and intensity, we need to turn a parameter sweep into predictive models.
Desired Features
✅Saturation
✅Independent of initial N.
❓Increase with SEY.
❓Critical (worst) intensity.
🚫Response to magnets.

## Slide 39
Predictive models

## Slide 40
Predictive models: Critical Intensity
The slope of the correlation is highest for low intensities.

## Slide 41
Predictive models: Critical Intensity

## Slide 42
Predictive models: Critical Intensity
At some critical intensity, buildup occurs for the lowest SEY.
As intensity increases, its effect on the saturation density diminishes.

## Slide 43
Predictive models: Beta
These shapes look familiar(?)

## Slide 44
Aside: the SEY function

## Slide 45
Predictive models: Beta
For low intensities, there are not many points in the “steep” region.

## Slide 46
Predictive models: Beta
The scale factor B of the function increases with intensity.
The other parameters have less clear, possibly linear trends.

## Slide 47
Summary of predictive models

## Slide 48
Predictive models: Beta
Visually, the quality of some fits appears to degrade.

## Slide 49
Predictive models: Beta
We largely still see the same behavior of the parameters.
However, now we only really have three new parameters.

## Slide 50
Counting parameters

## Slide 51
Including photoemission

## Slide 52
Including photoemission

## Slide 53
Including photoemission

## Slide 54
Including photoemission

## Slide 55
Prediction correct.

## Slide 56
Simulations that build up slowly are more sensitive to photoelectrons.
Photoemitted electrons are a tiny fraction of total.
May be another instance of “critical intensity” behavior.
Increases the complexity of predicting simulations with photoemission.

## Slide 57
Photoemission distributions
Absorber structures in the FCC-ee lattice.

## Slide 58
Photoemission distributions
LCC lattice synchrotron radiation flux distributions.

## Slide 59
Evaluating Filling Schemes
The model easily compares different design options.

## Slide 60
In summary
We understand how different parameters can change electron cloud behavior.
We adopt and expand an existing model for average electron cloud density over time.
We fit this model successfully to simulations.

## Slide 61
In summary
We can predict our model parameters from simulation inputs…
… as a function of both SEY and bunch intensity, finding clear trends.
And we understand how photoemission can be added and when it has a strong effect.

## Slide 62
But there are some limitations.
We don’t capture any information about the spatial distribution of electrons.
We know the model cannot fully account for magnetic fields (but a fix is coming soon!).

## Slide 63
Outlook

## Slide 64
Tools developed
Developed the Electron Cloud Analysis package.
https://github.com/furmada/Electron-Cloud-Analysis
Generating, running, curve fitting, and working with PyECLOUD simulations made much easier through a common API.
Transforms hundreds of individual output files into a single database which can easily be queried.

## Slide 65
LPAP Activity Meeting 07 May 2026
Thank you.