## Slide 1: Development of the Rapid Cycling Synchrotron 1 (RCS1) for the Muon Collider
John Adams Institute for Accelerator Science
12th March 2026
T. Fernandes de Nobrega
T. Hirt Madden
M. Savage
F. Straniero
G. Weis
A. Yousif

## Slide 2
Overview
2
Introduction
Lattice
Magnets
RF Cavities
Environmental
and Societal Considerations
Conclusions
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026

## Slide 3
Introduction
3
Why a Muon Collider?
10TeV CM energy collider with broad physics potential (Higgs coupling, electroweak studies, BSM).
Muon collider ‘best of both worlds’ combining benefits of lepton and hadron colliders.
Higher energy reach and less synchrotron radiation than electron-positron collider.
Point-like collisions at the full centre-of-mass energy with clean initial states.
Source: R. Taylor, MuCOL consolidated parameters report (Oct 2025)
RCS1
Key Challenges
Muon beam production is a tertiary process (protons->pions->muons) so need high intensity proton beam
Muon beams require cooling to reduce emittance
Short muon lifetime (2.2μs) means high accelerating gradients are required
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026

## Slide 4
Introduction
4
Rapid Cycling Synchrotrons
Due to short muon lifetime, muons must be produced, cooled, and accelerated extremely quickly to higher energies where lifetimes are longer due to time dilation.
The current design uses a chain of four ‘Rapid Cycling Synchrotron’ (RCS) rings to rapidly accelerate the muons in early stage of the chain before injection into main collider ring.
This design study focuses on the RCS1 ring, considering lattice, magnet and RF cavity design.
RCS1 Parameters specified by MuCOL consolidated parameters report (Oct 2025)
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026

## Slide 5: Lattice Design
T. Fernandes de
Nobrega
M. Savage
5
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026

## Slide 6
Lattice
6
Overview
Started with lattice file from a previous RCS1 design study and analysed using Xsuite.
Ring consists of 34 repeating cells.
2 RF cavities per cell.
Analysed beam aperture and optics to inform magnet and RF cavity design.
Performed particle tracking on single muon and example muon bunch to assess lattice performance.
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026

## Slide 7
Lattice
7
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
The Single Arc Cell
The single arc cell consists of 16 dipole magnets, 10 quadrupole magnets and 7 sextupole magnets.
Plot (left) of the RCS1 arc created using Xsuite.
Visualisation (right) of the RCS1 single arc cell were created using
Beam Delivery Simulation (BDSIM) software.
Quadrupole
Dipole
Sextupole
Location of RF cavities

## Slide 8
Lattice
8
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
Lattice Parameters (from MuCol):
Here are some of the notable parameters of the lattice that we are expecting to achieve in our Xsuite model.
Ensuring Reachable Accelerating Gradient:
RF voltage of a cavity, (10 cavities per linear section):
[MV]
Total number of linear sections:
Acceleration per turn:
    [MV] [GV]
RCS1 Parameters specified by MuCOL consolidated parameters report (Oct 2025)

## Slide 9
Lattice
9
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
Beam Aperture and Optics
Beam size in the horizontal (blue) and vertical (red) transverse components for , , and .
beam size chosen to ensure reasonable aperture size for magnets and RF cavities.
Ideally would an aperture size to contain of the beam.

## Slide 10
Lattice
10
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
Twiss Parameters for the Single Arc Cell
Alpha is as expected focusing in one direction and defocusing in the other.
Beta is as expected comparing with lattice results produced by L. Soubirou.
Gamma larger in x-direction than in the y-direction, suggesting larger angular spread in horizontal plane, as expected.
Short arc length requires dispersion suppression, hence explaining the fluctuations.

## Slide 11
Lattice
11
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
Twiss Parameters for the Single Arc Cell
Beta is as expected comparing with lattice results produced by L. Soubirou.
Zooming in on the section for which we have the lattice optics from L. Soubirou.
Can see very similar , and a with a similar shape but a slightly higher expected amplitude.
Soubirou L, et al. Optics design status for the muon collider rapid cycling synchrotrons (2025) doi:10.1088/1742-6596/3094/1/012004.

## Slide 12
Lattice
12
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
Twiss Parameters for the Full Ring
Twiss parameters , and plotted in - and -directions for the full 6km ring.
Twiss parameters are periodic and stable closed orbit is produced.
Start and end points of the plots match.

## Slide 13
Lattice
13
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
Investigating the Introduction of Straight Sections
Other variations of ring structure were considered to have dedicated locations for the RF cavities.
The cavities under consideration have lengths that allow them to fit within the zero-dispersion region of the lattice.
Therefore, straight sections no longer needed to be considered.

## Slide 14
Lattice
14
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
Single Particle Tracking
Particle energy evolution over a single turn.
Energy gained only at locations of the cavities, as expected.
For first turn, energy starts at 63 GeV and reaches 78 GeV.
Particle energy evolution over multiple turns.
Require 17 turns to reach energy of 314 GeV.
Both plot show the expected energy gains required per turn.
Suggests that the lattice can reach its expected performance.

## Slide 15
Lattice
15
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
Multiple Particle Tracking
The horizontal and vertical phase spaces of the muon beam before tracking through the RCS1.
Momentum spread modelled (specified from MuCOL parameters report).

## Slide 16
Lattice
16
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
Multiple Particle Tracking
The horizontal and vertical phase spaces of the beam after tracking through the RCS1 (17 turns).
Beam is diverging at the end of tracking (not ideal for closed loop).
No significant emittance growth visible.

## Slide 17
Lattice
17
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
Conclusions
Single particle tracking successfully performed showing expected optics.
Transverse beam size determined to provide aperture sizes for magnet and RF teams.
Expected energy gains over a single turn and over all turns needed to reach ejection energy.
Beam is seen to be diverging after tracking through the RCS1 but showing no significant emittance growth.
Future work
Optimisation of the lattice to produce more realistic beam size to minimise the aperture size.
Further investigation with multiple particle beam tracking.
Considering other lattice designs such as the hybrid-FODO and combined-function cells*.
*Soubirou L, et al. Optics design status for the muon collider rapid cycling synchrotrons (2025) doi:10.1088/1742-6596/3094/1/012004.

## Slide 18: Magnet Design
T. Hirt Madden
G. Weis
18
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026

## Slide 19
Dipole Magnet – Specification
19
Requirements for RCS1
Initial requirements from the muon collider annual meeting (Breschi et. al):
Magnetic field in aperture 1.8T
Good Field Region (GFR) 30x100mm
1ms ramp from -1.8T to 1.8T
This work focusses on a dipole with H-topology.
GFR was updated to 43.4x43.4mm towards the end of the project
after updates from the lattice team.
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
Breschi, M. 2025 et.al (2025) , NC magnet configuration (dipoles and quadrupoles) [PowerPoint]. IMCC and MuCol Annual Meeting. May 13th

## Slide 20
Only one quadrant of magnet required
Coordinates generated using 12 input parameters (eg. pole height, aperture height, pole chamfer width)
Magnet simulation created in FEMM using the pyFEMM interface
Visualisation produced using FEMM (Finite Element Method Magnetics) software.
Dipole Magnet – Geometry
20
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
conductor
pole chamfer
shim
Good Field Region
yoke
external chamfer
pole

## Slide 21
1
2
3
4
5
Dipole Magnet - Analysis
21
Post process analysis
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
Contour traced in red
1
2
3
4
5
Similar approach used to measure:
Field parallelism
Yoke saturation
Block integrals used to measure:
Magnet/coil area
Magnetic field energy
Method to extract central field strength and field quality.

## Slide 22
Dipole Magnet – Optimisation process
22
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
T. Head et al., scikit-optimize: Sequential model-based optimization in Python, 2018. https://scikit-optimize.github.io/
Cost function designed, with minimum at desired outcomes.
Bayesian optimisation (gp_minimize from skopt) used to vary parameters and optimise cost function.
Example cost function
Field quality
Field direction
Field strength
Yoke saturation
Magnetic energy
Current density

## Slide 23
Dipole Magnet - Results
23
Failed optimisations
Weights and forms of the penalties had to be constantly adjusted
Input parameters and search ranges had to be altered
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
Yoke oversaturation penalty too low
No penalty for current density

## Slide 24
Dipole Magnet – Results
24
Optimisation outcomes with new GFR specification with various Pole Widths
130mm
100mm
160mm
100mm
130mm
160mm
100mm
130mm
160mm
100mm
130mm
160mm
(With 6 turns)
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026

## Slide 25
Dipole Magnet
25
Ramping considerations
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
Field quality worsens at lower B-Fields
Using optimal 130mm design
At B = 1.800T
≥1.801T
=1.800T
≤1.799T
At B = 0.500T
≥0.501T
=0.500T
≤0.499T

## Slide 26
Dipole Magnet
26
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
Conclusions
Optimisation process developed for dipole magnet
Optimal parameters found at various pole widths for H-shaped dipole with tapered pole
Best parameters found for 130mm pole width with:
  Field strength of 1.8T
  Field quality over the good field region.
  Minimised Magnetic field energy
Future work
Add penalty for non-constant field quality at lower B-fields
Explore different yoke and pole geometries (Hourglass topology)
Dynamic analysis with power requirements

## Slide 27
Quadrupole
27
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
*Breschi, M., A. Macchiagodena, P. L. Ribani, et al. NC Magnet Configuration (Dipoles and Quadrupoles). IMCC and MuCol Annual Meeting, 13 May 2025. https://indico.desy.de/event/45968/contributions/186232/
Design Parameters
Muon Collider annual meeting*
Field Gradient of approx. 30[T/m]
Field homogeneity of at least
Ramp times of about 1[ms]
Aperture size 40[mm]
Lattice team beam size – 45[mm]

## Slide 28
Conductor
- Copper
Iron Yoke
Magnetic Pole
Air Boundary
Quadrupole
28
Configuration
MAP Configuration
  Based on a design at MuCol annual meeting*
Built in Python
7 Varying parameters define whole geometry (e.g. pole width, nose width, yoke width)
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
Hyperbolic Profile
Shims
*Breschi, M., A. Macchiagodena, P. L. Ribani, et al. NC Magnet Configuration (Dipoles and Quadrupoles). IMCC and MuCol Annual Meeting, 13 May 2025. https://indico.desy.de/event/45968/contributions/186232/
Designs from femm
Alternative triangular coil geometry

## Slide 29
Quadrupole
29
Design Considerations
Good field region
  ()
Gradient = [T/m]
Pole tip field
  [T]
    [mm][T]
Use Supermendur for magnetic poles
  49% cobalt
  49% iron
  2% vanadium
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
Possible pole saturation
Saturation!
*‘DC Magnetization Curves of Soft Magnetic Materials: Finite Element Method Magnetics’. Accessed 8 March 2026. https://www.femm.info/wiki/SoftMagneticMaterials.
Supermendur*
Pure Iron
  Choose a higher saturation material for Poles

## Slide 30
Quadrupole
30
5 Objectives
Maximise field gradient [T/m]
  Maximise Quadrupole Coefficient from multipole expansion over radius of measurement -
Maximise field homogeneity
  Minimise the largest higher multipole harmonic coefficient relative to the quadrupole coefficient -
Minimise total magnetic energy[J/m]
  Calculated by Femm
Minimise average yoke density [T] to 1.4[T]
  Average over shown region of yoke
Minimise Current Density [A/] to 8[A/]
  Measured with area of coil 0.6 to account for cooling etc
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
*Ferran Pousa, A., S. Jalas, M. Kirchen, et al. ‘Bayesian Optimization of Laser-Plasma Accelerators Assisted by Reduced Physical Models’. Physical Review Accelerators and Beams 26, no. 8 (2023): 084601. https://doi.org/10.1103/PhysRevAccelBeams.26.084601.
**Hudson, Stephen, Jeffrey Larson, John-Luke Navarro, and Stefan M. Wild. ‘libEnsemble: A Library to Coordinate the Concurrent Evaluation of Dynamic Ensembles of Calculations’. IEEE Transactions on Parallel and Distributed Systems 33, no. 4 (2022): 977–88. https://doi.org/10.1109/TPDS.2021.3082815.
Multi Objective Bayesian Optimisation with Optimas[*, **]

## Slide 31
Quadrupole 40mm Aperture Design
31
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
Supermendur poles max gradient
Objective | Value
Field Gradient [T/m] | 30.9
Field Homogeneity[10^x] | -3.33
Total Magnetic Energy [J/m] | 1703
Yoke Density [T] | 1.33
Current Density [A/mm^2] | 7.6
Iron Poles 30 [T/m]
Objective | Value
Field Gradient [T/m] | 30.1
Field Homogeneity[10^x] | -3.67
Total Magnetic Energy [J/m] | 2496
Yoke Density [T] | 1.27
Current Density [A/mm^2] | 4.16
Parameter | Value | Parameter | Value
yw [mm] | 132 | ss | 0.1498
nw [mm] | 72.49 | sg | 10
pw [mm] | 180.2 | mpf [T] | 1.241
cw [mm] | 60 | NI [A] | 20786
x [mm] | 750 |  | 
Parameter | Value | Parameter | Value
yw [mm] | 171.5 | ss | 0.142
nw [mm] | 76.3 | sg | 1
pw [mm] | 297.2 | mpf [T] | 1.57
cw [mm] | 145 | NI [A] | 26135
x [mm] | 965.5 |  | 
Supermendur poles 30 [T/m]
Objective | Value
Field Gradient [T/m] | 35.1
Field Homogeneity[10^x] | -3.37
Total Magnetic Energy [J/m] | 2324
Yoke Density [T] | 1.42
Current Density [A/mm^2] | 3.41
Parameter | Value | Parameter | Value
yw [mm] | 144.7 | ss | 0.125
nw [mm] | 57.2 | sg | 5.58
pw [mm] | 249.1 | mpf [T] | 1.49
cw [mm] | 156 | NI [A] | 24989
x [mm] | 886.8 |  | 
Cheap Material
Higher running cost
Expensive material
Cheaper running cost
Expensive Material
Higher running cost
Maximises higher material saturation

## Slide 32
Quadrupole 67.5 mm Aperture Design
32
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
Objective | Value
Field Gradient [T/m] | 19.5
Field Homogeneity[10^x] | -3.73
Total Magnetic Energy [J/m] | 4800
Yoke Density [T] | 1.46
Current Density [A/mm^2] | 8.27
Parameter | Value
yw [mm] | 191
nw [mm] | 123
pw [mm] | 250
cw [mm] | 126
x [mm] | 920.6
ss | 0.0951
sg | 5.516
mpf [T] | 1.4
NI [A] | 39579
Larger aperture size not able to reach target gradient
Approx. twice magnetic energy
Almost twice the current turns compared to 40mm
This is the trade off for a larger aperture

## Slide 33
Quadrupole
33
Post Analysis – Fitting Magnets into Lattice
Peak Beam Rigidity[Tm]
Lattice design magnet lengths 1.89[m]
Lattice peak specified
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
Lattice Specifying [T/m] gradients!
3.38T pole tip field at 67.5mm aperture
[]
Best parameters for apertures:
40mm
  G=30.9[T/m]
67.5mm
  G=19.5[T/m]
Magnet Length

## Slide 34
Quadrupole
34
Conclusion
Developed a Python generated quadrupole geometry
Optimised quadrupole parameters
  Achieved 30[T/m] at 40[mm] Aperture
  Achieved 19.5[T/m] at 67.5[mm] Aperture
  Achieved field homogeneity to
Next Steps
Full parameter and objective space to be further explored
  More iterations required for convergence
Consideration of the ramping effect – AC magnet problem
Consider alternative geometries
  minimising airgap inside magnet – alternate coil geometry
  Chamfer corner of Yoke – reduce B field density bunching at corners
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026

## Slide 35: RF Cavity Design
F. Straniero
A. Yousif
35
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026

## Slide 36
Why Superconducting Elliptical Cavities?
36
Advantages
High gradient is necessary to quickly accelerate muons.
Well established technology, so no need for much R&D.
Lower breakdown rate, compared to normal-conducting.
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
Disadvantages
Much higher energetic cost, due to higher currents and refrigeration.
Require extra-space for cryomodule.
Experimental Investigations on Superconducting Niobium Cavities at Highest Radiofrequency Fields, L. Lilje et al, https://www.researchgate.net/publication/48409802_Experimental_Investigations_on_Superconducting_Niobium_Cavities_at_Highest_Radiofrequency_Fields

## Slide 37
Why Superconducting Elliptical Cavities?
37
Advantages
High gradient is necessary to quickly accelerate muons.
Well established technology, so no need for much R&D.
Lower breakdown rate, compared to normal-conducting.
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
Disadvantages
Much higher energetic cost, due to higher currents and refrigeration.
Require extra-space for cryomodule.
Frequency (MHz) | Bore radius (cm) | Length cell(cm) | Previous designs: | Notes
352 | 8.52 | 37.474 | LEP* | The cavities would be quite long and large, requiring much refrigeration and space in linear sections
1300 | 3.5 | 11.530 | TESLA, ILC** | The aperture radius is smaller than 352, hence need a very narrow beam.
*A superconducting 352MHz Prototype cavity for LEP, G. Arnold-Mayer et al., https://cds.cern.ch/record/878555/files/cer-002551711.pdf
**The superconducting TESLA cavity, B. Aune et al., https://cds.cern.ch/record/429906/files/0003011.pdf

## Slide 38
How Much Accelerating Field Do We Need?
38
From lattice group: RF cavities distributed along the ring (683 cavities in 6km).
Need to go from 63GeV to 313.6GeV in17 turns.
Each cavity is 1.038m (in the accelerating part)  708.95m of accelerating sections.
= (this is considerable).
Transit time factor and
In Superfish
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026

## Slide 39
Superfish vs CST Solvers
39
Superfish
2D solver*
Finite differences method.
Optimizes geometry.
Iteratively directly solves the linearized matrix problem.
Uses hexagonal 2D meshing.
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
CST
3D solver**
Finite elements method.
Does not optimize geometry.
Solves the eigenvalue problem through Advanced Krylov subspace method.
Tetrahedral mesh.
*SUPERFISH-A COMPUTER PROGRAM FOR EVALUATION OF RF CAVITIES WITH CYLINDRICAL SYMMETRY, K.Halbach, R.F. Holsinger, Particle Accelerators 1976, Vol. 6, pp 213-222
** https://www.3ds.com/products/simulia/cst-studio-suite/electromagnetic-simulation-solvers (last accessed 10/03/2026)

## Slide 40
Why 1.3 GHz?
40
Upsides:
1.3GHz cavities are a mature, well-established technology, which has been already modelled and tested for the TESLA cavities and for ILC*.
Superconducting 1.3GHz cavities allow us to reach some of the highest gradients attainable, which is a strong-requirement in the muon collider, given the muons short lifetime.
1.3 GHz cavities require smaller cryomodules, as a rule of thumb the cavity resonant frequency scales with the inverse of the cavity diameter.
Downside:
Their compactness results in a smaller bore radius, currently set at 35mm. From lattice group the beam size is 45mm at 2σ, hence a good proportions of particles will be lost per cavity.
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
*The superconducting TESLA cavity, B. Aune et al., https://cds.cern.ch/record/429906/files/0003011.pdf

## Slide 41
Cavity Geometry – 9 Identical Cells (Except Endcups)
41
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
End-cup
D/2= 109.250mm
B_dome = 15.480mm
A_dome = 18.576mm
R_bore = 35.000mm
B_iris = 77.657mm
A_iris = 38.829mm
L/2 = 57.652 mm
Middle-cup
D/2= 109.250mm
B_dome= 16.000mm
A_dome= 19.200mm
R_bore = 35.000mm
B_iris = 76.017cm
A_iris = 38.009mm
L/2 = 57.652 mm
A Design for a 3 TeV Rapid Cycling Synchrotron for Muon Acceleration in the SPS Tunnel. T. Dascalu et al. https://cds.cern.ch/record/2723310/files/JAI%20Muon_RCS.pdf

## Slide 42
Superfish Design
42
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
Figures of merit:
r/Q = 433.455 Ohm F = 1300.0015MHz
Q = 0.728042E+10. Shunt Impedance = 1.055e7 Ohm
Maximum H (at Z,R = 0.0,8.92828) = 94926.5 A/m,
Maximum E (at Z,R = 0.0,0.565685) = 39.0705 MV/m
Ratio of peak fields Bmax/Emax = 3.0531 mT/(MV/m)
Peak-to-average ratio Emax/E0 = 1.5077
Transit-time factor = 0.7592616

## Slide 43
Superfish Design
43
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
Figures of merit:
r/Q = 433.455 Ohm
F = 1300.0015MHz
Q = 0.728042E+10
Shunt Impedance = 1.055e7 Ohm
Maximum H (at Z,R = 0.0,8.92828) = 94926.5 A/m,
Maximum E (at Z,R = 0.0,0.565685) = 39.0705 MV/m
Ratio of peak fields Bmax/Emax = 3.0531 mT/(MV/m)
Peak-to-average ratio Emax/E0 = 1.5077
Transit-time factor = 0.7592616
Field properties
Transit time = 0.7593
E0 = 27.38MV/m
E_peak = 40.44 MV/m

## Slide 44
HOM were also observed, far enough from TM01
44
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
TM010 mode and on axis field
TE11 – 2.042GHz
TM11 – 1.778GHz
TM – 2.325 GHz
TM – 2.5234 GHz
CST Designs
Single cell designs

## Slide 45
9 Cell 3D Design – 1299.4 MHz
45
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026

## Slide 46
Simulating Right Endcup and Beampipe is Important
46
Field with beampipe and optimized endcup:
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
Field without beampipe and no endcup:

## Slide 47
Simulating Right Endcup and Beampipe is Important
47
Field with beampipe and optimized endcup:
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
Field without beampipe and no endcup:
Lossy mode,
While the frequency is right, the amplitude decreases, showing field leakage.

## Slide 48
Some Discrepancies Between Field Properties:
48
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
Figure | Superfish | CST
Frequency (GHz) | 1.3000 | 1.2994
Shunt Impedance (MΩ) | 1.055e7 | 1.756e7
R/Q (Ω) | 433.455 | 865.101
Peak field/E0 | 1.5077 | 2.3994

## Slide 49
352 MHz Superfish
49
We started by existing designs that are relatively close in resonant frequency values to our required values of: 352 MHZ.
List of tuneable parameters:
By employing the general relation:
Tuned the bore radius and cavity diameter.
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
  Frequency
  Diameter
  DOME_B
  LEFT_DOME_B
  RIGHT_DOME_B
  DOME_A/B
  LEFT_DOME_A/B
  RIGHT_DOME_A/B
  WALL_Angle
  LEFT_Wall_angle
  RIGHT_Wall_angle
  RIGHT_BEAM_tube
  BORE_radius
Single Cell Cavity shape 352 MHZ
E-field within Cavity 352 MHZ

## Slide 50
352 MHz CST Design
50
Single Cell Design
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
Multicell Design

## Slide 51
RF Cavities
51
Conclusions
Both 352MHz and 1300MHz cavities were investigated, with 2D optimization and 3D design to confirm the results. More realistic models with extra beampipe were studied as well.
Cavities would reach the required gradient to rapidly accelerate muons over 17 turns.
The ideal cavity, given spatial constraints and previous work, would be the 1300MHz one.
Further Work
Cryomodule design and study of packing factor for multicell cavities.
Feasibility study to reuse SPS tunnel, given cryomodule size.
Study of parasitic higher order modes, which could damage the beam.
Design of klystron and waveguides complex.
Further studies on how to reduce environmental impact of RF.
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026

## Slide 52: ESG Considerations
52
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026

## Slide 53
Environmental and Social Considerations
53
Like any other large experimental project, we must consider the environmental and social impact of a project like the muon collider.
Capex costs: building new infrastructure, new tunnels, new beamlines, new magnets and RF cavities. Advantages: could reuse already built tunnels (eg SPS)*.
Opex costs: running continuously superconducting refrigeration, for both magnets and RF, Klystron powering for RF, plus human needed costs (heating, computing etc). Advantages, could reuse heat from to heat homes in winter like at CERN**.
Radiation safety problems: the decay of muons in the accelerator would produce a significant emission of neutrinos, which would travel to the surface of the earth. Hence the accelerator rings would need to be positioned so that no major human settlement is impacted.
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
*C. Accettura et al., Interim report for the International Muon Collider Collaboration (IMCC), arXiv:2407.12450 [physics], Jan. 2025. doi: 10.48550 arXiv.2407.12450. Accessed: Jan. 12, 2026. [Online]. Available: http:arxiv.org/abs/2407.12450
**https://home.web.cern.ch/news/news/cern/heating-homes-worlds-largest-particle-accelerator (last accessed 10/03/2026)

## Slide 54
Environmental and Social Considerations – Construction and Capital Expenditure
Building new infrastructure, new tunnels, new beamlines, new magnets and RF cavities.
Materials needed to build the components have an associated Global Warming Impact (GWI) index which is the carbon footprint associated with the production of material.
For example, we estimate that the project requires 16 dipole magnets per arc cell and there are 34 repeating single arc cells, amounting to a total of 344 dipole magnets.
Hence, calculating the total mass of the dipole magnets to be 12,040 metric tons of steel and steel has a GWI of 2.05kg, which amounts to roughly 25,000 metric tons of carbon dioxide.
Mitigation: Could reuse already built tunnels (eg SPS)*.
      Using steel sourced using renewable power
54
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
*C. Accettura et al., Interim report for the International Muon Collider Collaboration (IMCC), arXiv:2407.12450 [physics], Jan. 2025. doi: 10.48550 arXiv.2407.12450. Accessed: Jan. 12, 2026. [Online]. Available: http:arxiv.org/abs/2407.12450

## Slide 55
Environmental and Social Considerations – Operational Expenditure
Running continuously superconducting refrigeration, for both magnets and RF, Klystron powering for RF.
It is estimated that LHC consumes 10,000 tonnes of liquid nitrogen to cool its 36,000 tonnes of cold mass magnets to 80 K, which is double the cold mass magnets of this project of 14,325 tonnes.
Human needed costs such as heating and computing.
Radiation safety problems: the decay of muons in the accelerator would produce a significant emission of neutrinos, which would travel to the surface of the earth. Hence the accelerator rings would need to be positioned so that no major human settlement is impacted.
Mitigation: a. Could reuse heat from to heat homes in winter like at CERN**.
      b. Using energy recovering linacs where the kinetic energy of beam particles is used to increase the RF intensity of the linac and hence accelerates newly injected particles.
55
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
**https://home.web.cern.ch/news/news/cern/heating-homes-worlds-largest-particle-accelerator (last accessed 10/03/2026)

## Slide 56: Conclusions
56
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026

## Slide 57
Conclusions
57
Lattice
Single particle tracking successful with expected optics.
Determined transverse beam size for aperture constraints for magnet and RF teams.
Expected energy gains per turn and over 17 turns met.
Multiple particle tracking achieved showing minimal emittance growth but diverging.
Magnets
Optimised both dipole and quadrupole magnets.
For dipole, best configuration with 130mm pole width with field strength of 1.8T, field quality over good field region.
John Adams Institute | RCS1 Design for Muon Collider | 12/03/2026
For quadrupole:
  achieved 30 T/m at 40mm aperture,
  achieved 19.5 T/m at 67.5mm Aperture
  achieved field homogeneity to
RF Cavities
Investigated 352MHz and 1.3GHz, optimised in 2D and confirmed with 3D designs.
Cavities capable of producing required accelerating gradients achieved.
Ideal cavity determined to be the 1300 MHz.
Environmental and Social Considerations
Need to consider effective policies to protect the environment and minimise negative social effects.

## Slide 58
Conclusions
58
Design Study Report
The report covering the design study of the RCS1 has been completed.
Not yet available.
Will be published on the CERN document servers.
John Adams Institute | RCS1 Design for Muon Collider | 12/03/2026

## Slide 59: Acknowledgements
59
A big thank you to all the following people for time, help and support:
J. Bauche
C. Plostinar
R. Taylor
L. Soubirou
H. Wakeling
Also, cannot miss to mention
Emmanuel Tsesmelis for his dedication,
help and support throughout the project.
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026

## Slide 60
Any Questions?
60
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026

## Slide 61
Backup Slides
61
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026

## Slide 62
Quadrupole
62
Design Generation in Python
Hyperbolic nose profile*
Geometry Reduced to 9 parameters
and fixed
  7 Varying geometry variables
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
*Bauche, Jérémie. ‘An Introduction to Magnets for Accelerators’. https://indico.cern.ch/event/1621143/contributions/6831399/

## Slide 63
Quadrupole
63
5 Objectives
  Maximise Field Gradient [T/m] =
  Minimise Field Homogeneity =
  Minimise Total Magnetic Energy[J/m] – Calculated by Femm
  Minimise Yoke Density [T] to 1.4[T] -
  Minimise Current Density [A/] to 8[A/] -
John Adams Institute | RCS1 Design for Muon Collider | 16/04/2026
Multipole Expansion[***,****]:
Geometry designed skew
Skew Pole
Normal Pole
Block integral over entire geometry
defined as rectangle of half yoke width and between the pole base and top part of yoke
Allow 40% of area for cooling etc
*Ferran Pousa, A., S. Jalas, M. Kirchen, et al. ‘Bayesian Optimization of Laser-Plasma Accelerators Assisted by Reduced Physical Models’. Physical Review Accelerators and Beams 26, no. 8 (2023): 084601. https://doi.org/10.1103/PhysRevAccelBeams.26.084601.
**Hudson, Stephen, Jeffrey Larson, John-Luke Navarro, and Stefan M. Wild. ‘libEnsemble: A Library to Coordinate the Concurrent Evaluation of Dynamic Ensembles of Calculations’. IEEE Transactions on Parallel and Distributed Systems 33, no. 4 (2022): 977–88. https://doi.org/10.1109/TPDS.2021.3082815.
***Bauche, Jérémie. ‘An Introduction to Magnets for Accelerators’. https://indico.cern.ch/event/1621143/contributions/6831399/
****Breschi, M., A. Macchiagodena, P. L. Ribani, et al. NC Magnet Configuration (Dipoles and Quadrupoles). IMCC and MuCol Annual Meeting, 13 May 2025. https://indico.desy.de/event/45968/contributions/186232/
Multi Objective Bayesian Optimisation
with Optimas[*, **]