## Slide 1
FCC-ee Muon Detector R&D (FY2026)
Scintillator + Drift tube tracker (report today)
µRWELL
Bing Zhou
April 3, 2026
FCC-ee L2L3 meeting

## Slide 2
Scintillator Strip Prototype Module Construction at Michigan
Received 20 triangular strips (4cm base, 2cm height) from Alan Bross
and Jim Freeman (arXiv:2202.08184)
Received samples of YS-2M and YS-4M 1.5mm diameter fibers from Kuraray
Purchased 35 Hamamatsu S13360-3075PE SiPMs
Constructed five quad-counters, including the fiber holder, SiMP holder, and FE boards, assembled into two modules with two quad-counters each, + a spare, following the Fermilab procedure closely
Readout from both ends of the modules for a total 32 readout channels
Quad-counter assembly
Module assembly (two quad-counters)
SiPM holder attachment
Front-end Electronics Board
Module assembly into the external Al box

## Slide 3
Cosmic Ray Studies at Michigan
CAEN module with 32-channel Citiroc ASIC, with both high and low gain readouts
Calibrate using single PE peaks in the high gain readout
Channel with cosmic hit
Channel without cosmic hit
Low gain readout
High gain readout
Cross calibrate the low-gain readout

## Slide 4: Tests with beams at CERN (11/12 – 20/2025), (3/18 – 4/6/2026)
Scintillator modules, readout in both ends
4 sMDT chambers
UM postdoc and students to carry out the test beam tests
Top
Bottom
18 cm
~100 cm
~3 cm
0 2 4 6 8 10 12 14
15 13 11 9 7 5 3 1
Center
4 cm
4 cm
15-18 cm
15-18 cm
15-18 cm
15-18 cm
A0
A2
A1
B3
C3
B4
C4
B2
C2
B1
C1
B0
6 cm
E0
E2
E1
E3
6 cm
D1
D2
D3
D4
D0
C0
A3
A5
A4
A6
conjunction of the straw tracker test

## Slide 5
Raw ADC Spectra from Low Gain Readouts
Blue module
Yellow module
Strips illuminated
by the beam
From all 32 channels

## Slide 6
A First Look at the Time Information
Blue module
Yellow module
beam
t1
t2
L
t1
t2
z
Time difference between the two modules
Time difference between the two ends
of the same strip
Should be able to measure the z-position along
the strip from the time information to a few cm.

## Slide 7
Q1
Q2
A First Look at the Position Measurement
Four sMDT chambers provide accurate tracking information,
Improve the position measurement from charge sharing
Very preliminary, without calibrations and corrections
Expected ~2 mm or better
position resolution!