## Slide 1: US FCCee Tracking/PID L2
Carl Haber

## Slide 2: Topics
Semiconductor Tracking – MAPS, considering a US MAPS discussion
Fast Timing
Gaseous Tracking
  Drift Chambers
  Straw Tubes
  dN/dx
Low mass mechanics
Plan for BNL Tracking Workshop May 5-8 BNL has been postponed to a proposed CERN Oct 2026 alternative

## Slide 3: Genesis
I do not have any unified handle on how FCCee efforts in tracking and timing connect to Genesis
I am aware of proposals (not inclusive) in these areas
  SEU mitigation in ASICs
  Simulation of semiconductor devices for fast timing – Si and wide-band-gap materials
I do have a concern that folks will attempt to squeeze their ideas to meet the requirements of Genesis to the detriment of a more focused effort targeting FCCee specifically

## Slide 4: Reports from Straw Tube effort at U Mich
We have designed a new frontend electronics board that results in ~10-20 mV signal for a single electron after an amplification factor of 10^5 and the noise RMS is about 2.7 mV on chamber. We have performed cosmic ray dN/dX studies in the lab and the results are what we expected. We are also taking 1 GeV, 2 GeV, 5 GeV, and 10 GeV mixed hadron test beam studies this week at CERN. The test beam will finish next Wednesday.
We mainly used the funding to support a mechanical engineer to design a straw chamber and also for the new frontend board fabrication. We have used up all the $30k funding from the last year.

## Slide 5: New Effort at LBNL proposed to LDRD
Approval/funding not known at this time
Targets inner pixels and wrappers
Acquire technical/engineering experience with thin semiconductors – thinning, bending, simulation
Design considerations for an inner wrapper layer ~35 cm
Wide band gap electronics to measure fast timing signals – aims at an eventual “hot” wrapper (no cooling), very conceptual
Carbon based transmission lines integrated with low mass CF support structures
Currently also using AI methods to enhance position resolution from AC SiC-LGADs with promising results

## Slide 6: Connections to DRD
Generally the semiconductor group is well integrated into DRD3
For fast timing, non-silicon (WG6), a US member is co-convenor
MAPS
Drift
Straws
Low Mass – note Elba workshop this Spring

## Slide 7: Other reports from attendees
MAPs
Drift chamber
Low mass