## Slide 1: An Introduction to Field Programmable Gate Arrays
UK Advanced Instrumentation Course 2026
Andrew W. Rose, Imperial College London
awr01@imperial.ac.uk

## Slide 2: What this lecture is (and what it is not)
This lecture is a somewhat light-hearted introduction to what FPGAs are, and why they are both brilliant and horrible
Unfortunately, 1 hour does not give time to go into any depth – several weeks or months of hands-on work would be more realistic

## Slide 3: Recall From Trigger & DAQ lectures
CPU
FPGA

## Slide 4: Recall From Trigger & DAQ lectures
CPU
FPGA
So… I should probably justify those statements…

## Slide 5: A Note on timescales
At 40MHz BX rate, a 4GHz CPU could perform 100 CPU operations (not enough to be useful) before having to pass to the next core
Compare that to the O(10M) detector channels
What technology can we use?

## Slide 6: Programmable devices
Application-specific integrated circuits (ASICs): optimised for fast processing, design encoded into silicon
“Programmable ASICS”: Field-programmable gate arrays (FPGAs)

## Slide 7: An aside: The history of electronics
Digital electronics really started with the advent of the thermionic valve (colloquially, the “vacuum tube”)

## Slide 8: The history of electronics
Valve transistors

## Slide 9: The history of electronics
Valve transistors
First
solid-state transistors
Notes: Bardeen and Brattain, later much advanced by Shockley

## Slide 10: The history of electronics
Valve transistors
Solid-state transistors
First
solid-state transistors

## Slide 11: The history of electronics
First
multi-transistor
silicon
Notes: Jack Kilby

## Slide 12: The history of electronics
First
multi-transistor
silicon
Packaged
Logic

## Slide 13: The history of electronics
First
multi-transistor
silicon
Packaged
Logic
“Mini” processor
board

## Slide 14: ASICs
Application Specific Integrated Circuit (ASIC)
APV25 - Imperial College, London

## Slide 15: ASICs
Application Specific Integrated Circuit (ASIC)
$
Qty
ASIC
APV25 - Imperial College, London

## Slide 16: ASICs
Application Specific Integrated Circuit (ASIC)
$
Qty
ASIC
Off-the-shelf device
APV25 - Imperial College, London

## Slide 17: Two philosophies: Space vs. Time
Have each operation performed by dedicated logic and let signal propagate as a wave through the logic
Combinatorial

## Slide 18: Two philosophies: Space vs. Time
Have each operation performed by dedicated logic and let signal propagate as a wave through the logic
Combinatorial
Fast! but messy, hard to understand, not scalable and low throughput

## Slide 19: Two philosophies: Space vs. Time
Have each operation performed by dedicated logic and let signal propagate as a wave through the logic
Combinatorial
Fast, but messy, hard to understand, not scalable and, as a result, low throughput

## Slide 20: Two philosophies: Space vs. Time
Have each operation performed by dedicated logic and do that same operation on every clock cycle
Pipelined/Parallel
Slightly slower, but clean, easy to understand, scalable and high throughput

## Slide 21: Up against the speed of light…
Wait for the signal to propagate
“Sea-of-logic” approach
Limits clock speed
Do less each clock-cycle
Reuse logic for different data on each clock-cycle
Many steps needed for final result compensated for by much higher clock speeds
Combinatorial
Pipelined/Parallel

## Slide 22: Two philosophies: Space vs. Time
Have each operation performed by dedicated logic and do that same operation on every clock cycle
Have each operation performed by the same logic performing a different operation on every clock cycle
Sequential
Pipelined/Parallel

## Slide 23: Two philosophies: Space vs. Time
Have each operation performed by dedicated logic and do that same operation on every clock cycle
Have each operation performed by the same logic performing a different operation on every clock cycle
Sequential
Pipelined/Parallel
A debate as old as electronic computing itself

## Slide 24: Two philosophies: Space vs. Time
Have each operation performed by dedicated logic and do that same operation on every clock cycle
Have each operation performed by the same logic performing a different operation on every clock cycle
“The parallel approach to computing does require that some original thinking be done about numerical analysis and data management in order to secure efficient use.
In an environment which has represented the absence of the need to think as the highest virtue, this is a decided disadvantage”
Daniel Slotnick, 1967
Sequential
Pipelined/Parallel

## Slide 25: And the story diverges…
Programmable Array Logic
Microprocessor
Pack entire logic circuits in a chip
Perform all logical operations in one location, but sequentially
Sequential
Pipelined/Parallel

## Slide 26: And the story diverges…
Programmable Array Logic
Microprocessor
Pack entire logic circuits in a chip
Perform all logical operations in one location, but sequentially
No further discussion of microprocessors
Sequential
Pipelined/Parallel

## Slide 27: Sum-of-products theorem
Any Boolean operation may be expressed as
the OR of AND operations (Sum of products form)
Or
the AND of OR operations (Product of sums form)
Notes: ‘outline’ of coverage
time-plan
- What is an FPGA
- And why are they important for HEP
questions
- any time

## Slide 28: Programmable Logic Devices (PLDs)
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
?
Unprogrammed
Notes: ‘outline’ of coverage
time-plan
- What is an FPGA
- And why are they important for HEP
questions
- any time

## Slide 29: Programmable Logic Devices (PLDs)
Programmed
Notes: ‘outline’ of coverage
time-plan
- What is an FPGA
- And why are they important for HEP
questions
- any time

## Slide 30: Programmable Logic Devices (PLDs)
Originally one-time programmable
Later field reprogrammable
What did people do? Build boards with many PLDs…
Notes: ‘outline’ of coverage
time-plan
- What is an FPGA
- And why are they important for HEP
questions
- any time

## Slide 31: Complex PLDs (CPLDs)
Feedback
Feedback
Notes: ‘outline’ of coverage
time-plan
- What is an FPGA
- And why are they important for HEP
questions
- any time

## Slide 32: Programmable Interconnect matrix

## Slide 33: An alternative approach
Why bother with the complexity of the PLD cell?
Replace the PLD cell with a simple SRAM:
  Data-in becomes the “address”
  Outputs the preloaded value for a given input

## Slide 34: An alternative approach
Why bother with the complexity of the PLD cell?
Replace the PLD cell with a simple SRAM:
  Data-in becomes the “address”
  Outputs the preloaded value for a given input
The Field Programmable Gate Array
(FPGA)

## Slide 35: Field Programmable Gate Arrays (FPGAs)
‘Simple’ Programmable Logic Blocks
Massive Fabric of Programmable Interconnects
Notes: A field-programmable gate array (FPGA) is a large-scale integrated circuit that can be programmed after it is manufactured rather than being limited to a predetermined, unchangeable hardware function. The term "field-programmable" refers to the ability to change the operation of the device "in the field," while "gate array" is a somewhat dated reference to the basic internal architecture that makes this after-the-fact reprogramming possible.

## Slide 36: Evolution of features in FPGAs

## Slide 37: Evolution of features in FPGAs
Who wants to waste all the LUTs as RAM?

## Slide 38: Evolution of features in FPGAs
Who wants to waste all the LUTs for multiplication?
Big chips need dedicated clocking!

## Slide 39: Evolution of features in FPGAs

## Slide 40: Evolution of features in FPGAs
Who wants to waste LUTs AND re-invent industry-standard blocks?

## Slide 41: Evolution of features in FPGAs
Who wants to waste LUTs AND re-invent industry-standard blocks?

## Slide 42: A note on I/O
Traditionally, many hundreds of general-purpose pins (Gen I/O) up to a few hundred MHz
Latest generation Gen I/O up to 1.8Gbps
Programmable logic standards
Since 2002, FPGAs have been adding dedicated Multi-gigabit transceivers
Arms race - Ever more and ever faster

## Slide 43: Combinatorial Logic Block

## Slide 44: Combinatorial Logic Block
Registers on the output of every cell
Perfect for pipelined logic

## Slide 45: Integrated Digital Signal Processing

## Slide 46: Integrated Digital Signal Processing
So many registers
Perfect for pipelined logic

## Slide 47: Biggest Xilinx “Ultrascale+” Devices
Upwards of 8.9 million logic cells
  All clocked at up to 500MHz
  Over O(1015) operations/second
    1 PetaBOp
Upwards of 12,000 DSPs
All pipelined
Fully programmable

## Slide 48: Biggest Xilinx “Ultrascale+” Devices
Upwards of 8.9 million logic cells
  All clocked at up to 500MHz
  Over O(1015) operations/second
    1 PetaBOp
Upwards of 12,000 DSPs
All pipelined
Fully programmable
4.2 Tb/s!!!!

## Slide 49: Biggest Xilinx “Ultrascale+” Devices
Upwards of 8.9 million logic cells
  All clocked at up to 500MHz
  Over O(1015) operations/second
    1 PetaBOp
Upwards of 12,000 DSPs
All pipelined
Fully programmable
So what is the catch?
4.2 Tb/s!!!!

## Slide 50: FPGAs: What’s the Catch?
Incredibly hard to program efficiently
  Thinking in a parallel, pipelined-fashion is exceptionally difficult
  A handful of real experts in CMS
Efficient use depends on efficiently structured data

## Slide 51: FPGAs: What’s the Catch?
Incredibly hard to program efficiently
  Thinking in a parallel, pipelined-fashion is exceptionally difficult
  A handful of real experts in CMS
Efficient use depends on efficiently structured data
“The parallel approach to computing does require that some original thinking be done about numerical analysis and data management in order to secure efficient use.
In an environment which has represented the absence of the need to think as the highest virtue, this is a decided disadvantage”
Daniel Slotnick, 1967
Recall:

## Slide 52: FPGAs: What’s the Catch?
Incredibly hard to program efficiently
  Thinking in a parallel, pipelined-fashion is exceptionally difficult
  A handful of real experts in CMS
Efficient use depends on efficiently structured data
The chip is just the start – needs to be attached to something
You are also responsible for the infrastructure

## Slide 53: How to preserve your sanity using FPGAs
Keep your data-flow fully flow-forwards
  No iterations
  or at least
  Flatten your loops

## Slide 54: Prototype CMS Tracking Trigger: Kalman Filter

## Slide 55: Prototype CMS Tracking Trigger: Kalman Filter

## Slide 56: Prototype CMS Tracking Trigger: Kalman Filter
The maths is a relatively simple part of a more complex whole

## Slide 57: Prototype CMS Tracking Trigger: Kalman Filter
Kalman Filter is iterative

## Slide 58: Prototype CMS Tracking Trigger: Kalman Filter
Kalman Filter must handle combinatorics

## Slide 59: Prototype CMS Tracking Trigger: Kalman Filter
Kalman Filter data-flow is data-dependent

## Slide 60: An aside on High-Level Synthesis
Due to an arbitrary decision by DoE/DARPA/U.S. Govt, FPGA vendors moved C->FPGA compilers from a curiosity to a top-priority
Reinforced by push for heterogeneous, energy-efficient computing
Flattens loops, deals with pipelining for you
  Very simple to get started
  “Hurrah, we can get our software people writing firmware”
From practical experience
  We see very inefficient usage of resources
  Hard to understand “what the compiler has done”
  Requires many pre-processor directives to instruct code to do “what you want”
So, how do you program massively parallelized devices efficiently?

## Slide 61: Hardware Description Languages
Need a language to describe hardware
Novelly – called a “Hardware Description Language” (HDL)
Also called FIRMWARE
Two popular languages are VHDL , VERILOG
Easy to start learning… Hard to master!
Notes: ‘outline’ of coverage
time-plan
- What is an FPGA
- And why are they important for HEP
questions
- any time

## Slide 62: Hardware Description Languages
Describe Logic as collection of Processes operating in Parallel
Language Constructs for Synchronous Logic
Compiler (Synthesis) Tools recognise certain code constructs and generates appropriate logic
Not all constructs can be implemented in FPGA!
Notes: ‘outline’ of coverage
time-plan
- What is an FPGA
- And why are they important for HEP
questions
- any time

## Slide 63: Example
architecture behavioural of test is
begin
process(x, y)
begin
-- compare to truth table
if ((x='1') and (y='1')) then
F <= '1’;
else
F <= '0’;
end if;
end process;
G <= x or y;
end behavioural;
library ieee;
use ieee.std_logic_1164.all;
entity test is
port(
x: in std_logic;
y: in std_logic;
F: out std_logic;
G: out std_logic);
end test;
Must write code with
understanding of how
it will be implemented.
Can also enter code via schematic entry:
  Easier to navigate, but not vendor independent
  Will there ever be a standard graphical programming language?

## Slide 64: How to you know it works?
Simulate design extensively!
  Much quicker than debugging inside the FPGA

## Slide 66: Testbench Suite
“Event display”

## Slide 67: Testbench Suite
Clock-by-clock summary
End-of-event summary

## Slide 68: Designing Logic with FPGAs
High level Description of Logic Design (HDL)
Synthesise into a Netlist
  Boolean Logic Representation
Target FPGA Device
  Translate
  Mapping
  Routing
Bit File for FPGA
Notes: ‘outline’ of coverage
time-plan
- What is an FPGA
- And why are they important for HEP
questions
- any time

## Slide 69: Configuring an FPGA
Millions of SRAM cells holding LUTs and Interconnect Routing
Volatile Memory: Lose configuration when board power is turned off.
Keep bit patterns describing the SRAM cells in non-Volatile Memory e.g. PROM or memory card
Configuration takes ~ secs
Notes: ‘outline’ of coverage
time-plan
- What is an FPGA
- And why are they important for HEP
questions
- any time

## Slide 70: It doesn’t work: How to debug
Simulate, simulate & simulate again!
  Much quicker than debugging inside the FPGA
Route out signal to periphery
  Few debug pins always handy
  Can connect UART for uC debug (StdIn/StdOut)
Use chipscope
  Rebuild design with embedded logic analyser
    Can be a bit like quantum mechanics
    If you look (i.e. make a measurement) your code can behave differently
    Chipscope presence can affect the original design

## Slide 71: Floorplan of firmware in MP7

## Slide 72: Floorplan of firmware in MP7
Communication
DAQ
MGTs and DAQ buffers
MGTs and DAQ buffers
Algorithms

## Slide 73: When & why should I (not) use an FPGA?
FPGAs are expensive (high-end £10k-100k cf. £100)
FPGAs are power-hungry (Although also very efficient if used correctly!)
Programming FPGAs is like designing logic circuits not like programming sequential microcontrollers
Large firmware build-times are tens of hours or days
Floating-point ops and iterative algorithms awkward in FPGAs (That said, you “control” the silicon, so, of course, it can be done)
FPGAs best for high through-put, low- and/or fixed-latency operations

## Slide 74: The Future of the FPGA?
Heterogenous computing on chip
But is it suitable for our typical applications in particle physics?
  Hardware Triggers? Probably not – better suited as co-processor
  Accelerated HLTs? Maybe – but GPUs more likely…

## Slide 75: Conclusion
FPGAs are intrinsically parallel
Modern FPGAs are exceptionally powerful
FPGAs are a monumental PAIN IN THE BACKSIDE to program
  Partly due to the clunky, verbose HDLs
  Mainly due to the difficulty of conceptualizing massively parallel logic and pipelined logic
Get them wrong and you unleashed a world of pain on yourself
Get them right and you can do magic and have a lot of fun in the process

## Slide 76: Thank you
Any questions?