## Slide 1: CFD Simulation of Target Cell and Gas Supply System
Siddharth Thakker
April 8th, 2026 Institute of Nuclear Physics Johannes Gutenberg University Mainz

## Slide 2: Experimental setup
Vacuum chamber
Superconducting solenoid
Tracking detectors (forward scattering)
Integrating Cherenkov detector ring
Luminosity detector
Liquid hydrogen target loop
Lead Shielding
Tracking detector (forward scattering)
Beam

## Slide 3: The liquid hydrogen target loop
Fig: Loop flow diagram

## Slide 4: Design requirements
accommodate full azimuthal angle
polar angle range between 25º to 45º
3135W of heat deposited in target cell by the beam
Systematic effects affecting APV uncertainty –
  Density reduction, ∆/ – A static decrease in target density caused by beam-induced heating within the illuminated volume.
  Density fluctuation, δ/ – Time-dependent variations in density occurring over the beam’s helicity periods.

## Slide 5: Target cell specifications
Pressure/temperature | 2.4bar / 20K
Cell length | 60cm
Mass flow rate | < 2kg/s
lH2 pump head | < 0.1bar
Beam area on target | 25mm2
Heat deposited | 3.1kW
Target thickness | 4.3g/cm2
lH2 ∆ρ/ρ | <2%
lH2 δρ/ρ at 1 kHz | <10ppm
Table: All design parameters for target cell

## Slide 6: Target cell
beam
Manifold
Hydrogen target shell
Inner cone
Exit window
Entrance window
Fig: Target cell
with manifold
H2
H2

## Slide 7
Fig: Target cell During operation
Fig: Target cell Animation of the liquid hydrogen flow

## Slide 8: Hydrogen target shell
Hemispherical window
Beam exit
(in mm)
Thickness:

## Slide 9: Inner Cone/ Conical Flow Diverter
Flow in
(in mm)
Holes
Flow out
Thickness:

## Slide 10: CFD simulation of target cell
Target cell with its manifold
Steady state simulation
20K liquid H2
Mass flow 1.9 kg/s
Turbulence using K-epsilon viscous model
5x5mm rastered beam depositing 3.1kW

## Slide 11
Velocity contour
Avg total velocity 4.9 m/s
Flow in
Flow out
---------------- beam
Inside the inner cone: velocity > 0.025m/s, turbulent

## Slide 12
Low velocity regions with < 1m/s
Problematic regions close to windows
Flow in
Flow out
---------------- beam

## Slide 13
Temperature contour
lq H2 is expected
to boil at 23.2K
Flow in
Flow out
---------------- beam

## Slide 14: Temperature variation at the beam
Entrance window
Exit window

## Slide 15: Gas supply and safety
Fig: P2 P&ID diagram
Parts
Active gas cabinet
Gas Panel
Supply lines
Exhaust lines
Operation
Commencing – Vacuum in supply lines, inerting the exhaust lines, hydrogen supplied to the loop and cooled
During the experiment – lq H2 in the loop, exhaust lines in place
After the experiment – lq H2 slowly boils and returns to tank via check valve

## Slide 16
Active Gas Cabinet: Bottle connections of
Hydrogen
Helium – to test leaks
Nitrogen – to provide an inert environment in the exhaust line
Argon isobutane
Gas Panel
Gas Panel
The gas panel is the main control station
Connections to/from AGC, hydrogen tank, Target loop and exhaust lines
Vacuum pump venting out to exhaust lines through LN2 trap
Active Gas Cabinet

## Slide 17: Exhaust and emergency relief
A primary exhaust line, where all other lines connect
Exhaust for vacuum chamber
Emergency case 1 – high pressure in the gas lines
Emergency case 2 – Explosion of the target cell
Case 1
Case 2

## Slide 18: Summary and next steps
Lq H2 target cell design
CFD simulation of the target cell
Problem identification in the geometry
Gas supply and safety
Next steps
  Advancing simulation with added multiphase and transient state
  Extraction of required values of density fluctuation and reduction
  Modification in the geometry to satisfy all requirements
Thank you

## Slide 19: Extra slides

## Slide 20
Pathlines
Flow in
Flow out
Flow from holes
in inner cone
Flow turns around, goes upstream

## Slide 23: Heat exchanger
Used to remove the heat load from the target loop using He gas coolant
Will be modeled after the Qweak Counter flow heat exchanger with copper finned tube
The mass flow needed can be calculated:
For ex, He inlet – 10 atm and 14K, Outlet – 3 atm 20K, then 101g/s He flow is required
The HX design will be assessed with CFD
P is the total cooling power
∆H is the He enthalpy bw He inlet and outlet

## Slide 24: High power heater (HPH)
Used to mitigate lH2 density variations and relaxation time when the beam trips
HPH works in a feedback loop with the read-back of a temperature sensor in the Lq H2
Ensures that the target is operated at constant heat load and regulate the temperature
The qweak like heater is designed to have eight layers of Nichrome wire wrapped around crossed G10 boards.

## Slide 25: Beam guide
(in mm)
Entrance window
Thickness at entrance window: