## Slide 1: QSHS Analysis Early Pipeline and Injection Tests
Claude Mostyn

## Slide 2
The Overall Procedure
QSHS First Analysis Tests
Claude
Mostyn

## Slide 3
The Overall Procedure
QSHS First Analysis Tests
Claude
Mostyn

## Slide 4
The Overall Procedure
QSHS First Analysis Tests
Claude
Mostyn

## Slide 5
The Data Set
The data is a series of power spectral densities after double heterodyne and Welch average
Local oscillator tracks cavity resonance (hardware heterodyne), then digital uses LO - at
Tuning range between 75 and 130o, TM010 4.25 to 5.4 GHz, step 0.3 the cavity FWHM
No antenna coupling/reflection measurements this run – both antenna undercoupled
100 sec integration times, long cable before first amplification at 4K plate
Signal line gain 130 dB
0
QSHS First Analysis Tests
Claude
Mostyn
Single Raw PSD
PSDs throughout run

## Slide 6
The Data Set
0
QSHS First Analysis Tests
Claude
Mostyn
Hardware injections are
No 1st-stage amp · 100 s integration · undercoupled antenna
Testing early hardware and software injection retrieval
CW hardware injections (single frequency) at -10/-20 dBm through 120 attenuation, signal at cavity
Hardware injection frequency tracked tuning rod, so we tune through multiple signals
Software “axion like” signals can be injected at random frequency into the raw PSDs before analysis - Maxwell–Boltzmann lineshape (∆f ≈ 3 kHz at 4.5 GHz)
100 random software injections per tested power used as first test
Receiver chain, Not fully implemented

## Slide 7
The Data Set
0
QSHS First Analysis Tests
Claude
Mostyn
Software injected signal examples,
a) peak amplitude =, b) 0.8,
Testing early hardware and software injection retrieval
CW hardware injections (single frequency) at -10/-20 dBm through 120 attenuation, signal At cavity
Hardware injection frequency tracked tuning rod, so we tune through multiple signals
Software “axion like” signals can be injected at random frequency into the raw PSDs before analysis - Maxwell–Boltzmann lineshape (∆f ≈ 3 kHz at 4.5 GHz)
100 random software injections per tested power used as first test

## Slide 8
Predominant data loss was digitiser failure for first run, fixed by second run
IF band cropped to −0.3 to +2.3 MHz (centered on 1 MHz resonance bin)
DC zero gets averaged out
Mode crossings retained: too frequent at QSHS high range frequencies to cut; effects handled during analysis and candidate recovery instead
Gain-profile flatness cuts and frequency drift cuts not implemented for this short test run — both standard in ADMX/HAYSTAC
Data Cuts + Cropping
1
QSHS First Analysis Tests
Claude
Mostyn
Cut | No. Spectra Lost
Digitiser Failure | 532
 | 0
 | 17
Mode tracking failure | 1
Cut | No. Spectra Lost
Digitiser Failure | 532
 | 0
 | 17
Mode tracking failure | 1
Mode map
coloured by reason
for data cut,
-10dBm RUn
Good Data
Digitiser Failure
Mode Tracking Failure
Switching Failure
Data Lost over full CW injection test run

## Slide 9
Mode crossings retained: too frequent at QSHS high range frequencies to cut; effects handled during analysis and candidate recovery instead
QSHS cavity from simulations:
Approximately 60% is clear tuning state (well-separated from other mode)
40% sees some amount of form factor degradation, with 22% seeing a >10% relative form factor drop
Data Cuts + Cropping
1
QSHS First Analysis Tests
Claude
Mostyn
Full experimental QSHS mode maps at RT (top) and LT (bottom)
Zoomed of high angle on right
Clear tuning, high form factor
Mode crossing, reduced form factor
Post mode crossing, recovering form factor

## Slide 10
Predominant data loss was digitiser failure for first run, fixed by second run
IF band cropped to −0.3 to +2.3 MHz (centered on 1 MHz resonance bin)
DC zero gets averaged out
Mode crossings retained: too frequent at QSHS high range frequencies to cut; effects handled during analysis and candidate recovery instead
Gain-profile flatness cuts and frequency drift cuts not implemented for this short test run
Data Cuts + Cropping
1
QSHS First Analysis Tests
Claude
Mostyn
Simulated (ANSYS HFSS) mode map, coloured by mode crossings
Simulated form factor by frequency,
Coloured by mode crossings

## Slide 11
Data Cuts + Cropping
1
QSHS First Analysis Tests
Claude
Mostyn
Predominant data loss was digitiser failure for first run, fixed by second run
IF band cropped to −0.3 to +2.3 MHz (centered on 1 MHz resonance bin)
DC zero gets averaged out
Mode crossings retained: too frequent at QSHS high range frequencies to cut; effects handled during analysis and candidate recovery instead
Gain-profile flatness cuts and frequency drift cuts not implemented for this short test run
Cropped PSDs, across -10dBm tests
Full PSDs, across -10dBm tests

## Slide 12
Gain Drift
1
QSHS First Analysis Tests
Claude
Mostyn
Temporal drift: <0.2% of mean PSD. Slight negative correlation with room temperature (RT amplifier)
Frequency-dependent drift dominates — primarily receiver electronics; consistent with hotload across different cools → calibration feasible
Q-dependent component: near mode crossings, falling cavity Q causes additional PSD amplitude decrease
Current correction: global median shift per PSD. Final model: data-driven hotload calibration (deferred to when full receiver chain installed)
Time dependence (~ frequency dependence) of PSD amplitude by IF frequency bin

## Slide 13
Baseline Removal
Goal: remove receiver electronics baseline per PSD without reducing axion-scale SNR; produce Gaussian residuals. Target: Gaussian to ~4.5σ
Warm baseline: first pass fits a single baseline to multiple PSDs to handle small scale structure without fitting out candidates
Cold baseline: second per-spectra fit pass to remove fast-moving with tuning angle broader frequency scale structure
2
QSHS First Analysis Tests
Claude
Mostyn
Cropped PSDs, across -10dBm tests

## Slide 14
Warm Baseline
HAYSTAC-like method
Group PSDs by time intervals (30 minutes here) and produce a single averaged spectra
Perform a Savitsky Golay (window 251, order 2 vs. PSD length 3408) fit
Mask IF bins in individual PSDs >4.5σ from fit, repeat with new average PSD over 3 iterations
2
QSHS First Analysis Tests
Claude
Mostyn
Example PSD group, before and after first pass baseline removal

## Slide 15
Warm Baseline
2
QSHS First Analysis Tests
Claude
Mostyn
HAYSTAC-like method
Group PSDs by time intervals (30 minutes here) and produce a single averaged spectra
Perform a Savitsky Golay (window 251, order 2 vs. PSD length 3408) fit
Mask IF bins in individual PSDs >4.5σ from fit, repeat with new average PSD over 3 iterations
PSDs post first pass/cold baseline removal, across -10dBm tests

## Slide 16
Warm Baseline
Alternative hotload measurement or direct calibration
FIR1 (default ×8 decimation filter) introduces passband ripple that is baked into the power spectra once produced
FIR4 planned for next run
Overall shape of gain passband tracks hotload spectra
Could either implement a full hotload baseline spectra across tuning range, or develop a specific calibration model
2
QSHS First Analysis Tests
Claude
Mostyn
FIR filter transfer function (top) and example PSD, peak structures align

## Slide 17
Baseline Removal
2
QSHS First Analysis Tests
Claude
Mostyn
Alternative hotload measurement or direct calibration
FIR1 (default ×8 decimation filter) introduces passband ripple that is baked into the power spectra once produced
FIR4 planned for next run
Overall shape of gain passband tracks hotload spectra
Could either implement a full hotload baseline spectra across tuning range, or develop a specific calibration model
All group averages from cold baseline pass
Hotload spectra from previous cool, peaks match the “tilt” seen in PSD groups

## Slide 18
Baseline Removal - Cold
Four post-warm categories: slow curves (a)/ cavity peaks (b) / cavity troughs (c) / S-shaped (d)
Using per-spectra fit of form
With
Converges for all spectra, slightly underfits some sharp frequency structure (for 3% of spectra)
Structure likely from standing waves in 0.8 m superconducting cable
2
QSHS First Analysis Tests
Claude
Mostyn
Example individual PSD spectra and fits

## Slide 19
Baseline Removal - Cold
2
QSHS First Analysis Tests
Claude
Mostyn
PSDs reasonably flat post-baseline removal
SNR retention: 0.92 ± 0.06 (for high power CW injections)
Signal bins kept as single high counts
Gaussian to 3
No systematic IF interference bins identified (outside cavity resonance region) — noise predominantly stochastic
All PSDs from -10 dBm run post baseline removal

## Slide 20
Baseline Removal - Cold
PSDs reasonably flat post-baseline removal
SNR retention: 0.92 ± 0.06 (for high power CW injections)
Signal bins kept as single high counts
Gaussian to 3
No systematic IF interference bins identified (outside cavity resonance region) — noise predominantly stochastic
2
QSHS First Analysis Tests
Claude
Mostyn
Histogram for a single PSD post baseline removal, CW injection maximally detuned from cavity resonance
CW injection maximally on cavity resonance

## Slide 21
Baseline Removal - Cold
2
QSHS First Analysis Tests
Claude
Mostyn
SNR retention: 0.92 ± 0.06 (for high power CW injections)
Signal bins kept as single high counts
Gaussian to 3
No systematic IF interference bins identified (outside cavity resonance region) — noise predominantly stochastic
-10 dBm CW injection signal heights before and after baseline removal, dashed line shows ideal no reduction
Coloured by minimum detuning of signal from resonance
Comparison of different baseline methods and resulting signal SNR reduction
Single pass causes excess candidate

## Slide 22
RF mapping assumes constant conversion based on fixed 20.5 MHz offset of local oscillator
Lorentzian weights used as
For the normalised Lorentzian transfer function, evaluated at each bin , and the per-spectrum () overall stan. dev.
Total integration time per frequency bin =100 secs contributing spectra (between 5 and 25 across range, dependent on cavity FWHM)
IF drift not monitored, no weighting based on system noise temperature, form factor, Q etc.
Spectra Combination
3
QSHS First Analysis Tests
Claude
Mostyn
Combined Spectrum, for clear tuning region of -10dBm injection tests

## Slide 23
Grand Spectrum Rebins
4
QSHS First Analysis Tests
Claude
Mostyn
Combined spectrum bin width 763 Hz – to grand axion linewidth 2390 Hz
0.5 overlap fraction to reduce misalignment suppression of signals
Lineshape weighting found to have no notable effect on recovery of signals (either CW or software) at these power levels
Final conversion to not yet done. Requires corrections for bin-bin correlations from baseline removal, any SNR suppression factors, bin-overlap DOF reduction, calibration per grand bin etc.
Grand spectrum with inverse variance weighting only (top, blue), and with inverse variance and lineshape weighting (bottom, orange)

## Slide 24
Candidates - Hardware
5
QSHS First Analysis Tests
Claude
Mostyn
Rolling σ cut: flag highest- bin, mask neighbours, lower threshold, flag all beating threshold, repeat.
12/14 Candidates returned in first 25, 85% recovery at 0.35 candidates/MHz for -10 dBm tests, 108 candidates needed to return all CW injections
Frequency detuning: 0.03 ± 0.04 MHz, zero within error; positive bias in higher detuning cases consistent with a systematic in IF→RF conversion (LO or cavity drift)
Candidate clustering: residual baseline non-Gaussianity from standing waves in SC
Combined spectrum and top 25 candidates for -10 dBm clear region
Combined spectrum and top 25 candidates for -20 dBm higher frequency clear region

## Slide 25
Candidates - Hardware
5
QSHS First Analysis Tests
Claude
Mostyn
Rolling σ cut: flag highest- bin, mask neighbours, lower threshold, flag all beating threshold, repeat.
12/14 Candidates returned in first 25, 85% recovery at 0.35 candidates/MHz for -10 dBm tests, 108 candidates needed to return all CW injections
Frequency detuning: 0.03 ± 0.04 MHz, zero within error; positive bias in higher detuning cases consistent with a systematic in IF→RF conversion (LO or cavity drift)
Candidate clustering: residual baseline non-Gaussianity from standing waves in SC

## Slide 26
5
QSHS First Analysis Tests
Claude
Mostyn
Candidates, Software
90% recovery threshold: peak injected power → at cavity accounting for 130 dB gain and bin width 763 Hz. *.
Using only 100 MC injections here, propagated needs calibrating with hardware injection tests
*- estimate based on uncertain gain
90% recovery point (current config)
Software injection recovered vs injected peak amplitude
Software injection recovery fraction vs injected peak amplitude

## Slide 27
Full Runs and Range
CW signal bins visible across most of accessible range; amplitude decreases toward higher frequencies (undercoupled static antenna + mode crossings)
Large frequency discontinuities in tuning range obvious and cause regions of low spectra coverage
Thermal settling after large rod movements: 30 min to 1 hr cooldown required (relevant for rescan jumps)
QSHS First Analysis Tests
Claude
Mostyn
Full combined spectrum, -20dBm run
CW injected signals recovered in top 50 using different search methods
Out of 35 total for -10 dBm run and out of 55 total for -20 dBm run

## Slide 28
5
QSHS First Analysis Tests
Claude
Mostyn
Candidate Recovery
Regular mode crossings create localised noise elevations — global σ cut clusters in these regions, need to either cut mode crossings (loses a lot of range for QSHS cavity) or use a local score
Rolling z-score (window ≈5 cavity linewidths ≈3.5 MHz) ranking each bin by deviation from local mean rather than global spectrum gives significantly improved results
108 → 28 candidates needed to recover all -10 dBm injections in the no-mode-crossing region
Top 25 candidates for -20dBm combined spectrum, using rolling cut
Top 25 candidates for -20dBm combined spectrum, using rolling local z-score cut

## Slide 29
Data Cuts & Drift
Final data cut metrics need deciding.
Baseline Removal
1st-stage amp + adjustable antenna should reduce fast varying small-scale structure/standing waves
Potentially develop direct calibration (FIR filter + hotload), or full hotload measurement for cold pass
Spectra Combination
May want to use more sophisticated weighting (considering form factor, system noise temperature measurements, etc.)
Grand Spectrum
Statistics corrections (bin-bin correlations, SNR suppression factor, bin-overlap DOF, etc.)
Candidate Recovery
Final re-binning/search metric method needs to be decided
Target sensitivity or candidate number needs to be set
Exclusion Limits
Conversion to - will require full noise temperature measurements and potentially full hardware injection campaign, improved lineshape hardware injection methods underway
Overall exclusion limit setting logic/final injection test suite needs deciding
Rescan Analysis
Altered analysis if combining original and rescan data sets
QSHS First Analysis Tests

## Slide 30
Thank You!
Contact Details:
Claude Mostyn cfmostyn1@sheffield.ac.uk
Supervisor Ed Daw
e.daw@sheffield.ac.uk

## Slide 31
Gain Drift
1
QSHS First Analysis Tests
Claude
Mostyn
Temporal drift: <0.2% of mean PSD. Slight negative correlation with room temperature (RT amplifier)
Frequency-dependent drift dominates — primarily receiver electronics; consistent with hotload across different cools → calibration feasible
Q-dependent component: near mode crossings, falling cavity Q causes additional PSD amplitude decrease
Current correction: global median shift per PSD. Final model: data-driven hotload calibration (deferred to when full receiver chain installed)
Temperature dependence of PSD mean

## Slide 32
Gain Drift
1
QSHS First Analysis Tests
Claude
Mostyn
Hotload spectrum (brown, noise in light brown) tracks PSD mean amplitude (blue), using hotload scaling factor (extra amplifier added)
Temporal drift: <0.2% of mean PSD. Slight negative correlation with room temperature (RT amplifier)
Frequency-dependent drift dominates — primarily receiver electronics; consistent with hotload across different cools → calibration feasible
Q-dependent component: near mode crossings, falling cavity Q causes additional PSD amplitude decrease
Current correction: global median shift per PSD. Final model: data-driven hotload calibration (deferred to when full receiver chain installed)

## Slide 33
Gain Drift
1
QSHS First Analysis Tests
Claude
Mostyn
Temporal drift: <0.2% of mean PSD. Slight negative correlation with room temperature (RT amplifier)
Frequency-dependent drift dominates — primarily receiver electronics; consistent with hotload across different cools → calibration feasible
Q-dependent component: near mode crossings, falling cavity Q causes additional PSD amplitude decrease
Current correction: global median shift per PSD. Final model: data-driven hotload calibration (deferred to when full receiver chain installed)
Hotload spectrum tracks PSD mean amplitude
PSD mean amplitude becomes approximately linear in where