## Slide 1: Electron spin polarization preservation in the Electron-Ion Collider
EIC Accelerator Collaboration Meeting on Polarized Beams and Polarimetry
September 8th, 2026
Matt Signorelli
Postdoctoral Research Associate
Brookhaven National Laboratory

## Slide 2: Overview
Background
Electron Storage Ring (ESR) of the Electron-Ion Collider (EIC)
Best Adjustment Groups for ELectron Spin (BAGELS)
Conclusions
New Software Plug: SciBmad
Relevant papers cited at bottom of slides
Also see my PhD thesis “Electron spin polarization preservation in the Electron-Ion Collider”
Notes: 1 min

## Slide 3: Background: What is the EIC?
Electron-Ion Collider (EIC)
  Collides spin-polarized hadrons (e.g. protons) with spin-polarized electrons for a wide range of energies
  Study origin of proton spin, among other outstanding Standard Model questions
Hadron Storage Ring (HSR)
  41, 100, and 275 GeV
Electron Storage Ring (ESR)
  5, 9, and 18 GeV
HSR
ESR
IP8
IP6
Notes: Talk about how they go really fast and then smash with spins like that
Hadrons not
Red / pink think is PART of EIC

## Slide 4: Background: Electron Spin Polarization
Ring with only dipoles bends beam
Periodic spin direction on closed orbit
Dipole
Notes: Dipoles bend the beam

## Slide 5: Background: Electron Spin Polarization
Ring with only dipoles & quadrupoles (focusing)
Periodic spin direction on closed orbit
Dipole
Quadrupole
Notes: Make quad arrows bigger

## Slide 6: Background: Electron Spin Polarization
What if we want longitudinal spin at the interaction point?
Use solenoids:

## Slide 7: Background: Electron Spin Polarization
Is that it?
For hadrons, mostly. But…
Electrons emit a lot of synchrotron radiation!
Effects on polarization:
  Sokolov-Ternov (spin flip) effect
  Radiative Depolarization
  Kinetic effects (usually small)

## Slide 8: Background: Electron Spin Polarization
Sokolov-Ternov Effect
Photons emitted when bending in a magnetic field
Sometimes, spin will flip when a photon is emitted
  Relativistic quantum mechanical effect
More likely to flip anti-parallel than parallel!
In a perfectly homogenous field, builds up polarization to !

## Slide 9: Background: Electron Spin Polarization
Radiative Depolarization (a simplistic picture)
Ring with only dipoles and quadrupoles
No depolarizing effects in a perfectly planar ring
Dipole
Quadrupole

## Slide 10: Background: Electron Spin Polarization
Radiative Depolarization (a simplistic picture)
Electron stochastically sees different magnetic fields
Depolarizes an electron bunch!
How to remedy this? Traditionally, “spin matching” is used…

## Slide 11: Background: Electron Spin Polarization
“Spin Matching”

## Slide 12: Background: Electron Spin Polarization
“Spin Matching”
Magnet
Horizontal
Vertical
Longitudinal
Closed orbit precession

## Slide 13: Background: Electron Spin Polarization
“Spin Matching”

## Slide 14: Background: Electron Spin Polarization
Sokolov-Ternov effect
  Builds up polarization at a rate
Radiative depolarization
  Depolarizes at a rate , where
Both effects balance out!
  Builds up to at a rate

## Slide 15: Background: Resonances
We want to avoid resonances!
  Beam would “blow up”!
“Tune”: # of oscillations/turn in a ring
  Horizontal
  Vertical
  Longitudinal
  Spin
Resonance:
where
This guy pushes his arms out every seconds
If the kid’s swinging is commensurate, resonance!
If not, then the kid won’t go very high
Notes: Beam will blow up
Integer multiples of the tunes -> blow up
Go one by one, oscillate in each plane

## Slide 16: Electron Storage Ring of the EIC

## Slide 17: Electron Storage Ring of the EIC
Rotates to longitudinal at interaction point(s) for ~5, ~9, and ~18 GeV beams
Exact energies chosen to avoid spin resonances, specifically integer
At 5 and 18 GeV, spin tune precession across rotator is equal to that if rotator is turned off
For 9 GeV, this is NOT the case, so and 1-IP different from 2-IP1
1. M. G. Signorelli et al, “Polarization preservation methods for the Electron Storage Ring of the EIC”, MOPC83 IPAC ‘24
Notes: Show with arms/hands how it rotates
Calculation not too fun so won’t detail

## Slide 18: Electron Storage Ring of the EIC
Polarized bunches injected and swapped out when sufficiently depolarized
Simultaneously store bunches with both positive and negative helicity at the IP
Half of bunches polarized parallel to arc field, half anti-parallel
  Sokolov-Ternov works FOR anti-parallel
  Sokolov-Ternov works AGAINST parallel
Figure credit: Christoph Montag
Notes: Show with arms/hands how it rotates
Calculation not too fun so won’t detail

## Slide 19: Electron Storage Ring of the EIC
Spin match?
Horizontal
Vertical
Longitudinal
achievable by choosing magnet strengths
Yes, when the vertical beam size is small…
It’s complicated…
Notes: Now that we avoid resonances, what about the radiative depolarization?

## Slide 20: Electron Storage Ring of the EIC
5 and 10 GeV cases do not require a “longitudinal spin match” (LSM)
At 18 GeV, the effect on polarization is significant
For an LSM, we need solenoids that produce 11 T fields!
  Not feasible to engineer
A solution is needed…
Min

## Slide 21: Electron Storage Ring of the EIC
ESR has two interaction points two spin rotators
Can we use the second rotator to achieve some partial LSM?
In-depth study performed, but improvement only marginal3:
Is there any other way to restore high polarization?
No LSM
(Partial) LSM??
3. M. G. Signorelli et al, “Electron Polarization Preservation in the EIC”, MOPA052, IPAC ‘23

## Slide 22: Best Adjustment Groups for ELectron Spin (BAGELS)
All work published in M. G. Signorelli and G. H. Hoffstaetter, “BAGELS for simultaneous polarization, orbit, and optics control in electron storage rings”, Phys. Rev. Accel. Beams 28, 031002 , Editor’s Suggestion

## Slide 23: Best Adjustment Groups for ELectron Spin
To best solve this, we need a deeper understanding of spin dynamics
At every position around ring, attach a special spin 3-vector to each
“Invariant spin field” : Projection of spin along is invariant!
spin action (adiabatic invariant)
The invariant spin field (ISF) defines polarization properties of a ring

## Slide 24: Best Adjustment Groups for ELectron Spin
Radiative depolarization (not simplistic)
Consider what happens to the spin action with photon emission
To leading order, this is the bad thing!

## Slide 25: Best Adjustment Groups for ELectron Spin
the bad thing!
Without a longitudinal spin match,
Vertical closed orbit bumps tilt , causing small impacts on around the ring:
On a computer, we can optimize many (~50+) vertical bumps to reduce globally !
Vertical bumps + optimizer
Turn on bump magnets
Notes: Theta I is bump strength

## Slide 26: Best Adjustment Groups for ELectron Spin
“We solved the problem! We just have to optimize ~50+ bumps in the control room!”
Polarization measurements are costly, ~50+ variables will take way too long
How can we reduce the number of knobs to turn in the control room?
Consider how at m positions around ring depends on all n bumps (expand in ):
“Linear response matrix”
Seek orthogonal, linear combinations of bumps that maximize
Each linear combination is a knob that maximally impacts polarization
Which make this term really big?

## Slide 27: Best Adjustment Groups for ELectron Spin
Instead of ~50+ knobs, only k most effective, orthogonal groups of bumps!
Also want minimal impacts on other things, e.g. the orbit y small
These bump groups have maximal impacts on spin, minimal on the orbit
They are the Best Adjustment Groups for ELectron Spin!
Lagrange multipliers
First k eigenvectors with largest eigenvalues
Lagrange multipliers
First k generalized eigenvectors with largest eigenvalues
Notes: More formally
pca

## Slide 28: BAGELS: 1-IP 18 GeV ESR
Turning only 4 BAGELS knobs in the 1-IP 18 GeV ESR:
  “Analytical” = first-order, Map Tracking = Monte Carlo simulation (nonlinear)
Max orbit < 1mm everywhere, nearly doubled!
Notes: Monte carlo tracking result
Go slow here, talk about right plot

## Slide 29: BAGELS: 2-IP 18 GeV ESR
Turning only 4 BAGELS knobs in the 2-IP 18 GeV ESR:
Max orbit < 1mm everywhere, more than tripled!
BAGELS saves the polarization without a longitudinal spin match!
Notes: Monte carlo tracking result
Go slow here, talk about right plot

## Slide 30: BAGELS: Polarization-Safe Error Correction
E.g., magnet errors will couple horizontal & vertical motion requires correction
4 BAGELS coupling correction knobs
  Minimal impacts to polarization + orbit
Tested on 10 random 1-IP ESR lattices
All exceed polarization requirements!
  Excellent linear coupling control
  2 green seeds show nonlinear coupling outside of BAGELS’s current scope
We can also use BAGELS to do something else and NOT affect polarization
= coupling matrix
= orbit y AND
Measure of coupling
Notes: GO SLOWLY HERE. NOW d goes on BOTTOM
THIS SLIDE WILL TAKE 2-3 minutes
DESCRIBE PLOT IN DETAIL AND WHAT COLORS MEAN

## Slide 31: BAGELS: Polarization-Safe Beam Size Match
What else can BAGELS do?
Remember the vertical spin match in the ESR?
Electron vertical beam size is naturally ~zero, so we ignored this
To maximize collisions with the ions, we must increase to match the ion beam
One way is to create vertical dispersion
Vertical orbit excited with photon emission
Can be made using vertical orbit bumps
Will damage polarization if not careful
Must have at the IP
Slide 21
Notes: Just know that the amount of photons emitted in the vertical correlated to vertical dispersion

## Slide 32: BAGELS: Polarization-Safe Beam Size Match
Let’s apply BAGELS here:
Obtain 1 BAGELS polarization-safe beam-size matching knob, turn to achieve :
= vertical dispersion around the ring
= orbit y, spin-orbit coupling , at the IP
Requirements exceeded with beam size match!
Notes: Just know that the amount of photons emitted in the vertical correlated to vertical dispersion

## Slide 33: Conclusions
EIC-ESR will provide 5, 9, 18 GeV spin-polarized electrons
Without longitudinal spin match, 18 GeV polarization is marginal, but…
Novel Best Adjustment Groups for ELectron Spin (BAGELS) method:
  Nearly doubles in the 1-IP
  More than triples in the 2-IP
  Provides knobs for correcting polarization in real life
  Provides polarization-safe knobs to correct coupling due to errors
  Provides polarization-safe knobs for beam-size matching
Notes: 1 min

## Slide 34: New Software: SciBmad
New, CPU/GPU-accelerated, forwards-/ backwards-/ Taylor-differentiable accelerator physics code
Full suite of nonlinear analysis tools for design, e.g:
18 GeV EIC-Electron Storage Ring DA
6,271 lattice elements
20,746 particles (64-bit precision)
2,000 turns including radiation damping
8.2 minutes on one GPU
nth order resonance driving terms / detune coefficients
And super fast symplectic tracking:
One resonance normal form
Invariant spin field expansions
Amplitude-dependent tunes

## Slide 35: New Software: SciBmad
Parallelized over particles AND parameters (“batch” parameters):
  E.g. set a sextupole strength to be 100,000 different strengths:
  Currently being used for dynamic aperture optimization in the EIC-ESR
Arbitrary time-dependent parameters
  E.g., an AC-kicker (perhaps for RDP)
18 GeV EIC-ESR Radiative Depolarization
  6,271 lattice elements
  25,000 particles (64-bit precision)
  5,000 turns including radiation
36.8 minutes on one GPU
100,000 different lattices on one GPU!
Also GPU-parallelized!

## Slide 36: New Software: SciBmad
SciBmad is fully documented and in a production-ready state
  https://bmad-sim.github.io/SciBmad.jl/
Project status is kept up-to-date
Currently being used in EIC design

## Slide 37: Acknowledgements
Excited to have contributed significantly to the EIC during my PhD
Work would not have been possible without the help of many
Georg H. Hoffstaetter de Torquat
David Sagan
Christoph Montag
Vadim Ptitsyn
J. Scott Berg
Desmond P. Barber
Mike Blaskiewicz
Jorg Kewisch
Daniel Marx
Etienne Forest
Oleksii Beznozov
Laurent Deniau
Joe Devlin
Cornell ERL/EIC Group
All SciBmad contributors
And the rest of the EIC team
Notes: 1 min

## Slide 38: Thank you!
Questions?

## Slide 39: Backup Slides
N
S
Magnet will rotate
= magnetic moment
Notes: South repels south
North repels north

## Slide 40: Backup Slides
N
S
For single particles,
Spin precesses around magnetic fields
Notes: 30s

## Slide 41: Backup Slides
Intentionally tilt to cancel left-over spin-orbit coupling from rotator and random errors
Use least-invasive vertical orbit bump: “Opposing pair”
  Delocalized tilt, but localized and localized coupling
Can we just solve for least squares?
  NO! Values for some with little impact will exceed linear response regime
at all bends
All opposing pair strengths
Linear response matrix

## Slide 42: Backup Slides
PCA works well (as shown in all “old” BAGELS method results), but what if we also want to find knobs that minimize the orbit excursions at all elements while maximizing spin-orbit coupling in the bends? E.g., if is the response matrix of the orbit at all elements, we seek:
The quotient is called a generalized Rayleigh quotient. This problem can be equivalently expressed as maximizing subject to . Letting and
Best Adjustment Groups for ELectron Spin are those generalized eigenvectors of and with largest eigenvalues! Use these to solve

## Slide 43: Backup Slides
One way to correct global delocalized coupling caused by random errors is with vertical orbits through the sextupoles, to create delocalized coupling which cancels out that leftover
Using the BAGELS method, we can calculate bumps which maximally impact the coupling matrix components at all elements, while minimally impacting the spin-orbit coupling function at the bends and orbit excursion at all elements!
Basis bump which generates delocalized coupling only
“Equal pair”. Now seek:
where
Equal pair
These knobs are the Best Adjustment Groups for ELectron Spin for global coupling correction using vertical orbit bumps!

## Slide 44: Backup Slides
Another way to generate vertical emittance is with delocalized vertical dispersion so that a vertical amplitude is excited when a photon is emitted
Specifically we seek to maximize in the bends
Using the BAGELS method, we can calculate bumps which maximally create in the bends while minimally impacting the spin-orbit coupling function at the bends and the orbit excursion at all elements, and generating no delocalized coupling
where
bump
Basis bump which generates delocalized only
“2 pair”. Now seek: