## Slide 1: Atom Interferometry in the UK
Jon Coleman

## Slide 2: Outline – Atom Interferometry in the UK
UK efforts
  Experimental Efforts
    Birmingham
    RAL Space
    M Squared
    Imperial
    Liverpool
    NPL
  Sr
    Clocks - NPL
    Source - Oxford
  MAGIS-UK
  AION

## Slide 3: University of Birmingham

## Slide 4: UoB Atom Interferometry
UoB Gravity Gradiometer in “Beast from the East” storm, March 2018
m.holynski@bham.ac.uk
Developing gravity gradiometers for field applications1
Demonstrate application feasibility and improve sensor readiness
Outdoor application demonstrations
Challenging environmental conditions (0 °C, wind)
Detection of 100s kg
masses in laboratory
Currently ~ 1000 E/Hz½ in field, optimising to achieve ~200 E/Hz½ in next year
Building MKII system in launch configuration, aiming to detect tunnels in <60 s per point
1. for example: A. Hinton et al, Phil. Trans. R. Soc. A, 375, 20160238 2017

## Slide 5: UoB Atom Interferometry
Transportable gravimeters and compact gradiometry for UAVs
UAV GG prototype and MOT creation in flight
UoB Gravimeter with FG5s at NERC SLR facility measuring tides (2017)
Investigating applications in satellite laser ranging, geophysics, metrology
Current performance 5 ng in 30 min, now focusing on long term stability and accuracy
Compact and flexible OSSB laser system for reduced systematics1
Compact cold atoms systems
Building low size, weight, power gravity gradiometer
12 kg, 50 litres, initial target ~2000 E/Hz½
m.holynski@bham.ac.uk
1. L. Zhu et al, Opt. Express 26, 6542-6553, 2018

## Slide 6: UoB Atom Interferometry
and partners
Collaboration with multiple industry partners
  Testbed systems for atom interferometry: techniques and new hardware
  16 Innovate UK projects in atom interferometry, e.g.:
REVEAL: Industrial prototype gravity gradiometer with
CASPA: 6U CubeSat payload for atomic sensing in space with
RTF: Rapid test of new hardware or techniques
GP: testing of atom interferometers on moving platforms
and partners
m.holynski@bham.ac.uk

## Slide 7: Quantum Sensors at RAL Space
Dr. Tristan Valenzuela
UKRI/STFC – RAL Space

## Slide 8: RAL Space Objectives
Identify current technology needs Space Electronics for Cold Atoms, Lasers, Vacuum, …
Liaise with agencies UKSA, ESA
Build partnership relations with academia and industry Uni of Birmingham, Uni of Strathclyde, UK QT Hubs e2v, SSTL
“Space-ify” subsystems
Integrate space ready quantum sensors

## Slide 9: Gravity Gradiometer
70cm tall fountain
2 layers m-metal shield
(not yet present)
3D MOT
2D MOT
Status:
Vacuum chamber assembled
Optics assembled
3D MOT being optimised and characterised
m-shield being procured
Next Steps:
Atomic fountain implementation and optimization
Rabi oscillations and Ramsey Spectroscopy
Gravity measurement (Atom Interferometry in atomic fountain, single cloud)
Atom Cloud “Juggling”
Gravity Gradient measurement (Atom Interferometry in atomic fountain, two clouds)
Notes: We are currently finishing the setup of our Gravity Gradiometer. We have a 2D-3D MOT working and are optimising and characterising the 3D MOT. We expect to get the atoms to temperatures below . After what, we will be launching the cold atom cloud in a 70cm tall atomic fountain to perform interferometry in one cloud for gravity measurements or two clouds simultaneously for gravity gradient measurements.
We are currently finishing the setup of our Gravity Gradiometer. We have a 2D-3D MOT working and are optimising and characterising the 3D MOT. We expect to get the atoms to temperatures below 5𝜇K. After what, we will be launching the cold atom cloud in a 70cm tall atomic fountain to perform interferometry in one cloud for gravity measurements or two clouds simultaneously for gravity gradient measurements.

## Slide 10: M Squared

## Slide 14: Imperial College London

## Slide 15: Waiting on Slides

## Slide 18: University of Liverpool
Particle Physics

## Slide 19
Looking for a new way to do fundamental Physics…
Part of our strategy for the future

## Slide 20: Liverpool
Add work with Perl
Work in Collaboration with late Martin Perl (Nobel Laureate, visiting professor @ U. Of Liverpool)

## Slide 21: Initial results

## Slide 23: NPL

## Slide 24: NPL Rb Fountain
Conversion of Rb frequency standard
‘fountain clock’ into an interferometer.
Joint project with Liverpool and NPL

## Slide 25: Rb Fountain
Ramsey Fringes on two clouds taken simultaneously
Low phase noise
Long coherence times

## Slide 26: Strontium
NPL
  have an extremely good system working
  with the fermionic isotope
Oxford
  developing a new type of cold-atom source for Sr
  simple to construct and operate
other work at Birmingham and Durham
  also using cold Sr
  different objectives

## Slide 27: NPL

## Slide 30: University of Oxford

## Slide 31
Use M Squared Laser systems
2D MOT cold-atom source
A compact high-flux source of laser-cooled strontium atoms
Oxford Physics:
Chris Foot, Dongyang Xu (aka Leo), Elliot Bentine &Peter Zhou
Loading a 3D MOT
  Stainless steel oven welded to CF40 flange

## Slide 32: MAGIS-UK

## Slide 33: UK Plans for MAGIS
Option for building a 10m test-stand
  AION-10 as a test-stand for MAGIS and AION
Fast and flexible turnaround
  Produce multiple physics results whilst MAGIS/AION is in preparation
Provide UK hardware & Physics contribution to MAGIS-100
8.7 m at Stanford supporting the present 10 m-scale experiment

## Slide 34: UK Contributions
  AION-10 as a test-stand for atomic concepts to be used in MAGIS-100
    As well as a prototype for AION-100
  UK contributions in Hardware and Manpower
  Interferometry Lasers (MSquared as a potential vendor)
  Camera’s. e.g. EMCCD as low noise high-contrast device
    Working with Fermilab to improve technology
  Contributions in hardware for Control and readout
    Requirements are to integrate with existing sequencing and schemes that have been developed
    Link with Fermilab infrastructure
    Ideally linked to do time synchronization
  Work with Stanford for AION atom source – and prototyping ruggedization
  Work on integration, commissioning and running,
    A substantial fraction of time is foreseen to be spent at Fermilab to contribute towards the construction, commissioning, as well as operations and data-taking.

## Slide 35: AION - Proposal
Networking atom interferometers for
  Fundamental physics
Build another detector networked with MAGIS
  LIGO/Virgo style collaboration
Non-common background mode rejection
Provide unequivocal proof of any observation
AION and UK involvement in MAGIS presented to the Gordon and Betty Moore Foundation – 22/3/91

## Slide 36: Summary
Science Driven
  Linking UK expertise with world leading US program for fundamental physics
Involvement in International Experiment
  Atomic, Particle physicists, astronomers, cosmologists etc, working in collaboration
  next generation design
  Probe for new physics
Bringing together fundamental science and existing UK technology companies
Huge Scientific and Innovation Imperative

## Slide 37: Questions or Comments?

## Slide 38: MAGIS-100 Present Status
New experiment at Fermilab
  potential to for larger scale at SURF
Using Atom Interferometry to:
  Explore the dark sector
  Test quantum mechanics at Large Distance Scales
  Prototype for a mid-band gravity wave detector
MAGIS-100 endorsed by Fermilab management
  Stage 1 approval via PAC
Strong interest and encouragement from funding agencies
Looking to start construction in FY19