## Slide 1
Jason Hogan
Stanford University
March 25, 2019
First AION Workshop
Imperial College London
The MAGIS-100 Project in the US
Notes: 25 min +5 min questions

## Slide 2: MAGIS Collaboration
Part of the proposed Fermilab Quantum Initiative:
http://www.fnal.gov/pub/science/particle-detectors-computing/quantum.html#magis
Notes: Collaboration between atomic physicists and particle physicists
scientists and engineers

## Slide 3: Physics motivation
Dark matter and new forces
Time-dependent signals caused by ultra-light dark matter candidates (dilaton, ALP, relaxion …)
Dark matter that affects fundamental constants: electron mass, fine structure constant
Time-dependent EP violations from B-L coupled dark matter
New forces
Advancing quantum science
Atom de Broglie wavepackets in superposition separated by up to 10 meters
Durations of many seconds, up to 9 seconds (full height launch)
Quantum entanglement to reduce sensor noise below the standard quantum limit
Gravitational wave detector development
Probe for studying cosmology
Explores range of frequencies not covered by other detectors
LIGO sources before they reach LIGO band
Optimal for sky localization: predict when and where events will occur (for multi-messenger astronomy)

## Slide 4: Atomic sensors for gravitational wave detection
MIGA: Terrestrial detector using atom interferometer + optical cavity (Bouyer, France)
Atomic clocks and atom interferometry offer the potential for gravitational wave detection in an unexplored frequency range (“mid-band”)
Mid-band
0.03 Hz to 3 Hz
Satellite proposal using optical lattice clocks + drag free inertial reference (Kolkowitz et al., PRD 2016)
Mid-band science
LIGO sources before they reach LIGO band
Optimal for sky localization: predict when and where inspiral events will occur (for multi-messenger astronomy)
Probe for studying cosmology
Search for dark matter (dilaton, ALP, …)
MAGIS: Atom interferometry with clock atoms serving as both inertial reference + phase reference (Hogan, Kasevich)
Potential for single baseline detector (use atoms as phase reference/local clock)
Notes: Basic concept: atoms are good clocks (phase ref.) and good inertial references. Use clock to measure light-flight time between two inertial references traveling on their geodesics.
The mid-band is not covered by other GW detectors, would be complementary. Mid-band is very promising for sky localization and parameter estimation.
There are several large baseline proposals for GW detectors using clocks and atom interferometers (on ground and in space), each with a different approach and technical pros/cons, but based on similar basic concepts. It makes sense to study many ideas.

## Slide 5: Sky position determination
λ
Sky localization precision:
Mid-band advantages
- Small wavelength λ
- Long source lifetime (~months) maximizes effective R
Images: R. Hurt/Caltech-JPL; 2007 Thomson Higher Education
R

## Slide 6: Projected sensitivity to dark matter
Sensitivity to ultralight scalar dark matter
Sensitivity to B-L coupled new force
~ 1 year data taking
Assuming shot-noise limited phase resolution
Arvanitaki et al., PRD 97, 075020 (2018).
Graham et al. PRD 93, 075029 (2016).

## Slide 7: Quantum science
Realizing macroscopic quantum mechanical superposition states
Distance: Wave packets are expected to be separated by distances of up to 10 meters (current state-of-art 0.5 meters)
Time: Support record breaking matter wave interferometer durations, up to 9 seconds (current state-of-art 2 seconds)
Entanglement: 20 dB spin squeezed Sr atom sources takes advantage of quantum correlations to reduce sensor noise below the standard quantum limit (shot noise)

## Slide 8: Light Pulse Atom Interferometry
Long duration
Large wavepacket separation

## Slide 9: Current generation: Stanford 10-meter fountain
10-meter tall Rb atomic fountain
54 cm
Record wavepacket separation due to multiple laser pulses
Milestones
Record matter wave interferometer duration (>2 s)
Record wavepacket separation (>0.5 meter)
Record effective temperature (< 50 pK)
First observation of phase shift due to space-time curvature across a single particle’s wavefunction
Large momentum transfer 90 ћk
Record accelerometer scale factor
Dual species (85Rb / 87Rb) gradiometer
First demonstration of phase shear readout and point source interferometry techniques

## Slide 10: Gradiometer detector concept
Atoms
Atoms
Laser
Compare two (or more) atom ensembles separated by a large baseline
Science signal is differential phase between interferometers
Differential measurement suppresses many sources of common noise and systematic errors
Science signal strength is proportional to baseline length (DM, GWs).
GW source (e.g., black hole binary inspiral)
Baseline
Gradiometer

## Slide 11: MAGIS-100: GW detector prototype at Fermilab
Matter wave Atomic Gradiometer Interferometric Sensor
100-meter baseline atom interferometry in existing shaft at Fermilab
Intermediate step to full-scale (km) detector for gravitational waves
Clock atom sources (Sr) at three positions to realize a gradiometer
Probes for ultralight scalar dark matter beyond current limits (Hz range)
Extreme quantum superposition states: >meter wavepacket separation, up to 9 seconds duration
100 meters
Notes: MAGIS = Matter wave Atomic Gradiometer Interferometric Sensor

## Slide 12: Gordon and Betty Moore Foundation grant
MAGIS-100 at Fermilab
Atom interferometry sensor development at Stanford
New funding received from GBMF
$9.8M, 5 years, start date Jan 2019
100 meter vacuum tube (Fermilab design contribution)
Three atomic sources (Stanford design contribution)
Atom interferometry laser system (Northwestern design contribution)
Hogan
Kasevich
Hogan

## Slide 13: GW Sensitivity development plan (part of GBMF grant)
Phase noise improvements:
10x from higher flux
10x from squeezing
Atom source scaling: ~
MAGIS-km additional factor of 3x improvement in phase noise from flux + quantum entanglement (spin squeezing)

## Slide 14: MAGIS-100 timeline: Design phase
Dec 2019
Summer 2019
Fall 2019
Dec 2019
Target Completion
Summer 2020
Fall 2020
Dec 2020
Fall 2020
Dec 2021
Summer 2021
Northwestern
Northwestern
Years 4 and 5 for science data taking and analysis

## Slide 15: MAGIS-100 Location: MINOS building
Ground level of MINOS building
From: L. Valerio (Fermilab), MAGIS Project Engineer

## Slide 16: MAGIS-100 Location: Shaft in MINOS building
Top and bottom of ~100m shaft.
From: L. Valerio (Fermilab), MAGIS Project Engineer

## Slide 17: Preliminary designs – 3D model
ATOM
SOURCE
LASER
PLATFORM
ATOM
SOURCE
ATOM
SOURCE
Atom sources mounted to 2m sections with in-vacuum optics for atom launch.
Top, middle, and bottom atom source details
From: L. Valerio (Fermilab), MAGIS Project Engineer

## Slide 18: Preliminary designs – 3D model
Civil engineering drawing of shaft and proposed location of mounting brackets.
Cutaway view of laser platform and top of shaft.
From: L. Valerio (Fermilab), MAGIS Project Engineer

## Slide 19: Stanford Sr 10-meter prototype
Sr gradiometer CAD
(atom source detail)
Trapped Sr atom cloud
(Blue MOT)
Two assembled Sr atom sources

## Slide 20: 10-meter Sr prototype design
Assembly to occur in summer/fall 2019
Layer thickness 0.02 inch
Conservative
100 μm gaps
staggered layer design
Example multi-layer design
2D FEM shielding results
2D transverse octagonal shield simulation, with coils for transverse bias field
Vacuum system CAD
Magnetic shield design and simulations
Bias magnetic field simulation
Ripple ~ 21%
Gradient ~ 40 mG/m

## Slide 21: 10-m prototype: Atom source connection
Atom source
Connection node
CAD model of lower atom source in Sr 10-m prototype.

## Slide 22: Atom source connection node
Atom detection: imaging from two directions
Lattice shuttle, lattice launch
Vacuum pumping
Functions
10-m prototype CAD

## Slide 23: MAGIS-100 atom sources sub-systems
3x Sr atom sources targeting 1e6 atoms/s, nK temperature
Commercial Sr beam (oven, Zeeman slower, 2D MOT) Fall 2019
3D cooling vacuum chamber, pumps Spring 2020
Magnetic coils (quadrupole for MOT, bias coil set) Spring 2020
Laser frequency locks: 461 nm, 689 nm (narrow), 679 nm, 707 nm Summer 2020
Laser frequency control (AOMs, fiber EOMs) Summer 2020
RF electronics for laser frequency control Summer 2020
Power electronics (magnetic coils, DC power rails) Summer 2020
Timing control electronics Summer 2020
Laser delivery optics frame Fall 2020
1064 nm dipole trap (matter wave lensing, evaporation, shuttle) Fall 2020
Detection/diagnostics imaging system Fall 2020
Remote monitoring and tweak-up system Winter 2020
Environmental isolation and control (temperature, water infiltration, laser safety) Winter 2020
System level component list (sub-systems)
Design based on existing Sr atom sources

## Slide 24: Atom optics
Two detection modes:
Single photon transitions on clock transition
  Long-baseline gradiometer configuration
  Gravitational wave detection
  Scalar dark matter search
Two-photon Bragg transitions
  Compare two co-located isotopes
  Time-varying Equivalence Principle violating new forces
  B-L vector coupled dark matter search

## Slide 25: Clock gradiometer using single photon transitions
Two ways for phase to vary:
Gravitational wave
Dark matter
Each interferometer measures the change over time T
Laser noise is common-mode suppressed in the gradiometer
Excited state phase evolution:
Graham et al., PRL 110, 171102 (2013).
Arvanitaki et al., PRD 97, 075020 (2018).

## Slide 26: LMT and Resonant Pulse Sequences
Graham, et al., PRD (2016)
LMT beamsplitter (N = 3)
Resonant sequence (Q = 4)
Graham, et al., PRL (2013)
Sequential single-photon transitions remain laser noise immune

## Slide 27: Extreme LMT with clock atoms
Clock atoms (e.g. strontium)
Alkali atoms (e.g. rubidium)
Two photon Raman/Bragg transitions for atom optics
Requires large detuning, high power to suppress spontaneous emission
Current state of the art: ~100 pulses
Single photon transition for atom optics
Spontaneous emission naturally highly suppressed (150 s lifetime clock state, other levels far detuned)
Possibility to support > 106 pulses

## Slide 28: Clock atom interferometry demonstration
5S2 1S0
5P 1P1
5P 3Pj
461 nm
30.5 MHz
689 nm
7.4 kHz
698 nm
1 mHz (87Sr)
Blue MOT
Red MOT
Pushed
red MOT
AI Ports
Goal: 698 nm clock transition in 87Sr
Use 689 nm transition in 88Sr for initial demonstration of LMT clock AI
689 nm transition features:
1-photon AI possible
22 μs lifetime
High Rabi frequency possible
Right AI Beam
Left AI Beam
Push Beam
Fluorescence Beams
Imaging
Experimental sequence and detection protocol
Ground state
(pushed)
Excited state

## Slide 29: Rabi oscillations
Measured inhomogeneous loss could support 1000 ћk atom optics (>95% efficiency)
High Q, high Rabi frequency (MHz), 150 ns π-time, good contrast
Residual decay explained by finite beam sizes
Trade-off between Rabi frequency and Q
Rabi oscillations on the 689 nm transition
Q = 87.7
Q = 82.5

## Slide 30: LMT beam splitter demonstration
Sequential π-pulses show similar efficiency
41ħk Beam Splitter
(after TOF)
Beam splitter (π/2)
+ 20 alternating π pulses

## Slide 31: Mach-Zehnder Interferometer (Preliminary!)
Contrast = 0.9
Visibility = 0.83
Right Beam
Left Beam
M = 0 (1ħk)
π
π/2
π/2
Right AI Beam
Left AI Beam
This sequence first demonstrated (on 698 nm transition) in:
L. Hu, N. Poli, L. Salvi, and G. M. Tino, PRL 119, 263601 (2017).

## Slide 32: Mach-Zehnder & LMT (Preliminary!)
Contrast = 0.83
Visibility = 0.67
Right Beam
Left Beam
M = 1 (3ħk)
π
π/2
π/2
π
π
π
π
Right AI Beam
Left AI Beam

## Slide 33: Mach-Zehnder & LMT (Preliminary!)
Contrast = 0.79
Visibility = 0.47
Right Beam
M = 2 (5ħk)
Left Beam
π
π/2
π
π
π
π
π
π/2
π
π
π
Right AI Beam
Left AI Beam

## Slide 34: Mach-Zehnder & LMT (Preliminary!)
M | N π | ħk | Visibility | Contrast
0 | 1 | 1 | 0.83 | 0.90
1 | 5 | 3 | 0.67 | 0.83
2 | 9 | 5 | 0.47 | 0.79
Next steps: Extend to higher LMT and implement gradiometer sequences.
Consistent high contrast; reduction of visibility as expected due to phase noise.

## Slide 35: Collaborators
Rb Atom Interferometry
Mark Kasevich
Tim Kovachy
Chris Overstreet
Peter Asenbaum
Remy Notermans
Theory
Peter Graham
Roger Romani
Savas Dimopoulos
Surjeet Rajendran
Asimina Arvanitaki
Ken Van Tilburg
MAGIS-100:
Joseph Lykken (Fermilab)
Robert Plunkett (Fermilab)
Swapan Chattopadhyay (Fermilab/NIU)
Jeremiah Mitchell (Fermilab)
Roni Harnik (Fermilab)
Phil Adamson (Fermilab)
Steve Geer (Fermilab)
Jonathon Coleman (Liverpool)
Tim Kovachy (Northwestern)
Sr Atom Interferometry
Jan Rudolph
TJ Wilkason
Hunter Swan
Yijun Jiang
Ben Garber
Connor Holland
DE-SC0019174
N00014-17-1-2247
GBMF7945

## Slide 36: Backup

## Slide 37: Technical noise suppression
LMT
Composite pulse sequences
Practical limitation of extreme LMT is fidelity of the atomic transitions
Technical noise (e.g., laser intensity, frequency) reduces transfer efficiency
Well-known techniques can be used to avoid this, at the cost of pulse area
Detuning
Time
Detuning
Time
Intensity
Adiabatic rapid passage (ARP)
π/2 π90 π/2
π/2 π90
π/2
ARP figures from: Kovachy et al., PRA 86, 011606 (2012).

## Slide 38: Two-photon laser frequency noise in a gradiometer
Consider a laser frequency error dw that varies at the GW frequency
Phase error:
GW Signal:

## Slide 39: Large space-time area atom interferometry
54 cm
Long duration (2 seconds), large separation (>0.5 meter) matter wave interferometer
Kovachy et al., Nature 2015
90 photons worth of momentum
max wavepacket separation
World record wavepacket separation due to multiple laser pulses of momentum

## Slide 40: Ultralight scalar dark matter
Ultralight dilaton DM acts as a background field (e.g., mass ~10-15 eV)
Electron
coupling
Photon
coupling
DM scalar field
+ …
e.g., QCD
DM coupling causes time-varying atomic energy levels:
DM induced oscillation
Time
Dark matter coupling
DM mass density

## Slide 41: GW Sensitivity for a Satellite Detector
L = 4 × 107 meters
Dots indicate remaining lifetimes of 10 years, 1 year and 0.1 years
Satellite detector concept
Two spacecraft, MEO orbit
Atom source in each
Heterodyne laser link
Resonant/LMT sequences

## Slide 42: Compare to LISA
Atom test mass
- Records laser noise
- Acts as phase reference
LISA:
Atom interferometer:
Second baseline needed for phase reference:
Atoms
(Figures adapted from LISA yellow book.)