## Slide 1: AION meeting March 8th 2019
Prepared by Chris Foot from discussions w. Oliver, Jon, Mike@Bham and Richard@NPL
Suggestions for breaking down the large WP containing construction of AI10:
A) tasks on critical path to a working device (minimal requirements)
B) R&D for improved interferometer and next generation (or put into AI100 WP?)
Next stages (at the workshop?): division of tasks amongst people/institutions and detailed costing for proposal.

## Slide 2: Tasks for construction of AI10
Support structure, enclosure, temperature control and clean air (responsibility of host site)
Vacuum: manufacture and bake-out of tubes, vacuum pumps. Viewports (antireflection coated for multiple wavelengths)
Strontium oven (heaters and T-control)
Lasers: cooling, transport and launching – see separate list.
A) Laser mode cleaning: propagation in vacuum and steering mirror(s) at top of interferometer tube B) Coriolis compensation system/steering mirror fixed to ground at base.
Magnetic shielding and bias magnetic field (four straight wires?)
Control system: light pulse timing and shaping (also laser cooling and transport sequence).

## Slide 3: Laser system including optics and electronics
blue cooling - M Squared (MSL)?
red cooling - diode or MSL?, frequency stabilisation scheme?
clock – power critical for one-photon interferometry
repumping - diode lasers (from AO Sense as in Stanford/MAGIS)?
Transport by optical tweezers from sidearm into vertical tube (transport rail for moving the focusing lens, or could be on the other list)
optical lattice for launching without heating
Optics: mirrors, polarisers, AOMs, EOMs, shutters, optical fibres Build a modular system (as planned at Stanford)
Laser safety: interlocks and access
Electronics: servo-control for multiple systems
Laser frequency stabilisation – NPL reference cavity (or frequency comb)?

## Slide 4: R&D – focus on areas complementary to MAGIS
Composite pulses – compensation for intensity inhomogeneity etc.
Efficient cooling of > 109 cold atoms to < 100nK. This beyond the regime of state-of-the-art experiments (currently around 106 atoms)
Spin-squeezing - investigation of sensitivity enhancement
Cooling and launching atoms a temperature sufficiently low for AI100, e.g. 30m fountain height
Networking of interferometer with Stanford device/MAGIS to eliminate localised noise/interference.
(Detection sufficient to achieve quantum projection noise limited detection with 109 atoms with ~ 20 dB squeezing.)
Active stabilisation schemes for tall structures (as at large telescopes?)
gravitational gradient noise and its mitigation (or in AI100 WP ?)