## Slide 1: WP R&D Tasks 2 & 3
R&D design goals to support 5e-19 /rt(Hz) strain sensitivity in AI-100:
Task 1: Atom Preparation
  Prepare 109 atoms at < 100 nK within 10 s; transport from sidearm to AI tube
Task 2: Spin Squeezing
  Realise 20 dB of metrologically useful squeezing on the clock transition

## Slide 2: R&D task 2: Atom preparation - challenges
High-flux 87Sr source: 1011 slow atoms/second
  State of the art: 109 atoms/second
Big 87Sr “blue” MOT: 1011 atoms
  State of the art: 5 x 108 atoms
Narrow-line cooling of 1010 atoms to 1 uK in dipole trap (+ optical pumping)
  State of the art: 107 atoms
Evaporative cooling of 109 atoms to < 100nK
  State of the art: 106 atoms
Horizontal transport over 50 cm with heating < 100 nK
  State of the art: few uK heating

## Slide 3: R&D task 3: Spin squeezing - challenges
Still need cold 87Sr for the spin squeezing R&D system
Apply 20 dB spin squeezing on “clock” transition
  Option 1: Cavity – either weak measurement or one axis twisting (“cavity feedback”)
  Option 2: Interactions – e.g. through Rydberg dressing
Squeezing must be metrologically useful
  Low dephasing and decoherence
Squeezing must not induce too much heating (< 100 nK)
  Cavity: Challenging due to dipole forces from cavity spatial mode; Rydberg: untested
Squeezing must be compatible with 109 atoms
  Cavity: large cavity mode volume; Rydberg: must avoid inelastic collisions
Squeezing must be compatible with transport, lattice launch and delta-kick lens
  Preserve squeezing in magnetic sublevels, then transfer to clock states in AI tube?
Detection noise low enough to measure squeezed population distribution

## Slide 4: R&D tasks 2&3: Cost
Rough cost estimates for new R&D systems
  Assume no in-kind contribution but access to specialised test & measurement
Do we need to settle on a budget and present this at the workshop?
Laser systems for cooling | £605,000
Laser stabilisation ("clock" laser plus stability transfer) | £580,000
Experimental control and electronics | £125,000
Vacuum system and camera | £110,000
Test and measurement | £100,000
Total | £1,520,000
Laser systems for cooling | £435,000
Laser stabilisation ("clock" laser plus stability transfer) | £580,000
Experimental control and electronics | £125,000
Vacuum system, camera and squeezing cavity | £140,000
Test and measurement | £100,000
Total | £1,380,000
Task 2: cooling
2 PDRA + 2 students + capital as below
Task 3: squeezing
2 PDRA + 2 students + capital as below