## Slide 1: WP AION-Upgrade Task 2
Design goals for 5e-19 /rt(Hz) strain sensitivity in AI-100:
Task 2a: Atom Preparation
  Prepare 109 atoms at < 100 nK within 10 s; transport from sidearm to AI tube
Task 2b: Spin Squeezing
  Realise 20 dB of metrologically useful squeezing on the clock transition
Need to shrink θ
Note added by RH 26/03/19: Actual requirement is 108 atoms/s, so fewer atoms can be used if the cooling sequence can be made shorter.
Jason Hogan hopes to achieve a very short 1 s sequence  he’s aiming for 108 atoms. Either approach is hard, in slightly different ways.
Note added by RH 26/03/19:
The goals above are long-term ambitions to support AI-km performance. In the shorter term, “realistic deliverables” for years 1-3 could be:
2a: Prepare 107 atoms at < 500 nK within 10 s (matching MAGIS-100 goal of 106 atoms/second)
2b: Achieve 20 dB of squeezing on the clock transition, but with no guarantee of metrological usefulness (e.g. not yet controlling anti-squeezing)

## Slide 2: Upgrade task 2a: Atom preparation
High-flux 87Sr source: 1011 slow atoms/second
  State of the art: 109 atoms/second
Big 87Sr “blue” MOT: 1011 atoms
  State of the art: 5 x 108 atoms
Narrow-line cooling of 1010 atoms to 1 uK in dipole trap (+ optical pumping)
  State of the art: 107 atoms
Evaporative cooling of 109 atoms to < 100nK
  State of the art: 2 x 105 atoms
Horizontal transport over 50 cm with heating < 100 nK
  State of the art: few uK heating
  10.1103/PhysRevLett.119.223202 quotes up to 1010/s flux of slow 88Sr at hottest oven setting; I have scaled by natural abundance ratio 87Sr/88Sr.
  10.1140/epjd/e2015-60288-y and 10.1103/PhysRevA.96.053415 report comparable flux. AOSense claims better (1011/s of 88Sr) in a datasheet but no data is presented and no peer reviewed publication is available.
  5e8 atoms is estimated from experience and talking to other Sr groups. Blue MOT size is not usually quoted in publications - Sr BEC experiments with high atom number usually load a magnetic trap reservoir so don’t need a big blue MOT. We can’t use a magnetic trap reservoir in AION because there are too many untrapped hyperfine states in 87Sr  lots of atoms would be wasted  cycle time would be too long. (Also collisional losses would likely be prohibitive). Main atom number limitations are (i) inelastic collisions and (ii) density limits from rescatter – see 10.1103/PhysRevA.59.1216
  Narrow-line cooling and evaporative cooling numbers are as reported in Schreck group 10.1103/PhysRevA.87.013611. Similar numbers are achieved in the JILA group – see e.g. 10.1126/science.aam5538. Both sequences are ~ 30 seconds.
  Jason Hogan mentioned he wanted to skip out evaporative cooling altogether, instead exploiting a dark SPOT MOT induced by a transparency beam as partially demonstrated in 10.1103/PhysRevLett.110.263003. This will probably help (I was thinking to try the same thing), but its temperature/density limits are unclear.
  Few uK heating is quoted in the moving tweezers (focus-tuneable lens) in 10.1088/1367-2630/16/9/093028. A moving lattice combined with Bessel beam waveguide sounds more promising – see 10.1088/1367-2630/8/8/159 for 20 cm transport with < 30 nK axial heating (but note that transverse heating is not reported)
Notes added by RH 26/02/19: Citations for “state of the art”

## Slide 3
High-flux 87Sr source: 1011 slow atoms/second
  State of the art: 109 atoms/second – Realistic 3 year deliverable: 5 x 109 atoms/second
Big 87Sr “blue” MOT: 1011 atoms
  State of the art: 5 x 108 atoms – Realistic 3 year deliverable: 5 x 109 atoms
Narrow-line cooling of 1010 atoms to 1 uK in dipole trap (+ optical pumping)
  State of the art: 107 atoms – Realistic 3 year deliverable: 3 x 107 atoms to 1.5 uK
Evaporative cooling of 109 atoms to < 100nK
  State of the art: 2 x 105 atoms – Realistic 3 year deliverable: 1 x 107 atoms to < 500 nK
Horizontal transport over 50 cm with heating < 100 nK
  State of the art: few uK heating – Realistic 3 year deliverable: Nothing!
  (We should make a best effort to demonstrate transport, but progress on other stages is more important in years 1-3)
Notes added by RH 26/03/19: I have added realistically achievable deliverables within 3 year AI-Upgrade programme. These will hopefully be refined more in coming weeks. The stretch goals listed in the main bullets are guided by strain sensitivity goals of AI-100, not by achievability in 3 year timescale.
I would hope we could do better than the “realistic deliverables” even within 3 year timescale, in some cases hopefully by an order of magnitude, but I wouldn’t be comfortable guaranteeing it. The stretch goals will need longer - they need beyond state of the art in both atom density and trap volume. Plausible methods are available – Jason has some ideas and so do we – but each step is risky and the stretch goals are definitely at the limit of what seems possible. I think we can promise larger improvements in the earlier stages of cooling (i.e. high flux source; blue MOT) simply because we will do these stages first.

## Slide 4: Upgrade task 2b: Spin squeezing
Apply 20 dB spin squeezing on “clock” transition – State of the art: 0 dB (i.e. not yet done!)
  Option 1: Cavity – either weak measurement or one axis twisting (“cavity feedback”)
  Option 2: Interactions – e.g. through Rydberg dressing
Squeezing must be metrologically useful
  Low dephasing and decoherence
Squeezing must not induce too much heating (< 100 nK)
  Cavity: Challenging due to dipole forces from cavity spatial mode; Rydberg: untested
Squeezing must be compatible with 109 atoms
  Cavity: large cavity mode volume; Rydberg: must avoid inelastic collisions
Squeezing must be compatible with transport, lattice launch and delta-kick lens
  Preserve squeezing in magnetic sublevels, then transfer to clock states in AI tube?
Detection noise < 10-6 to measure squeezed population distribution
Realistic 3 year deliverable: Cavity weak measurement at a signal to noise compatible with 20 dB squeezing of 109 atoms (note: this is beyond state of the art). I don’t think we can guarantee metrological usefulness in years 1-3; we should wait until years 4-6 before promising to characterise dephasing & heating to the required level. Ultimately to get metrological usefulness in years 4-6 may involve upgrading the cavity or detection scheme based on lessons learned in years 1-3
Vuletic (MIT) cavity feedback squeezing between ground states of Yb: arXiv:1901.10499
Kasevich (Stanford) 20 dB cavity feedback and weak measurement squeezing between ground states of Rb: 10.1038/nature16176
Jones (Durham, UK) Proposal for Rydberg dressed squeezing (possible alternative to cavities): 10.1103/PhysRevLett.112.103601
Citations for state of the art squeezing:

## Slide 5: Upgrade task 2: Budget estimate
Labour: £600k
£600k = 2 PDRA staff at £100k/yr each
+ in kind contributions (e.g. students)
Capital: £1.0M
See table below
Laser systems for cooling | £605,000
Laser stabilisation ("clock" laser + stability transfer) | £580,000
Experimental control and electronics | £125,000
Vacuum system, camera and squeezing cavity | £140,000
Test and measurement | £100,000
Estimated in-kind contributions from hosts | -£550,000
Total capital budget | £1,000,000
87Sr
But this is only 107 atoms…
I recognise that there are finite resources but 2 PDRA is probably not enough to deliver this task unless there is a lot of synergy with other WPs