## Slide 1: Simulations
Marco Barbone
m.barbone19@imperial.ac.uk
Simulations
14/04/2021

## Slide 2: About me
M.Sc. in Computer Science and Networking Scuola superiore Sant’Anna & Università di Pisa
CERN OpenLab Summer student
Research Software Engineer, Maxeler Technologies
Ph.D. Student, Custom Computing research group, Imperial College London, Supervisor Prof. Wayne Luk
Member of Imperial College CMS group
Associate Ph.D. Student, The Institute of Cancer Research, London

## Slide 3: MR-Linac
Source: https://www.icr.ac.uk/news-features/mr-linac
combines an MRI scanner and a linear particle accelerator

## Slide 4: Real Time Adaptive Radiotherapy
Monte Carlo
New computing challenges

## Slide 5: Workflow
Clinicians
Physicists
Engineers
Requirements
Modelling
Implementation
Monte Carlo
Simulator

## Slide 6: Expensive
particles needs to be simulated to achieve statistical significance
The stochastic behaviour breaks the pipeline of modern CPUs
Not suitable for GPU due to the lack of branch-predictors
Random memory accesses due to many lookup tables
Modern CPU and GPU implementations take more than 1 minute (Ziegenhein2015)
Other cloud-based approaches have reliability concerns (Ziegenhein2017)
Source: https://iopscience.iop.org/article/10.1088/0031-9155/60/15/6097/meta https://iopscience.iop.org/article/10.1088/1361-6560/aa5d4e/meta

## Slide 7: Worst-case for branch predictors
Assuming rng uniformly distributed:
if(rng.getRandom() < 0.5) then f(x) else g(y)
In the GPU case branches can significantly affect the instruction throughput by causing threads of the same warp to diverge.
The diverging branches are de-scheduled!

## Slide 8
Rejection sampling
Inversion method
F(u) {
  do { generate (U) }
  while ( U > threshold);
  Return U;
}
At compile time invert F
F(u) {
  u = generate (U);
  Return
}
No while loop!

## Slide 9
Rejection sampling
Inversion method
RNG
Sample
Stall
Stall
RNG
Value
Inverse
Source: https://www.doc.ic.ac.uk/~wl/papers/iee07dt.pdf
Inversion method is the most efficient on FPGA (Thomas2006)

## Slide 10: Breathing
courtesy of Andreas Wetscherek

## Slide 11: Radiotherapy
Source: https://doi.org/10.1016/j.semradonc.2019.02.005
Planning
Desired outcome
Outcome

## Slide 12: Adaptive Radiotherapy
Seconds
Minutes
Source: https://pubmed.ncbi.nlm.nih.gov/30201276/