## Slide 1: Accelerating MC simulations
Marco Barbone
m.barbone19@imperial.ac.uk

## Slide 2: Project status
Develop a reliable MC simulator that:
Supports electrons, photons and positrons
Supports different materials
It is readable and extendable
Accelerator agnostic optimizations only
It is validated against experimental data

## Slide 3: Optimization: Not uniform distributions
Rejection sampling
Inversion method
F(u) {
  do { generate (U) }
  while ( U > threshold);
  Return U;
}
At compile time invert F
F(u) {
  u = generate (U);
  Return
}
No while loop!
Inversion method is the most efficient on FPGA (Thomas2006)
Since removing a while loop is equivalent to removing a branch, it is more efficient on GPU as well
Source: https://www.doc.ic.ac.uk/~wl/papers/iee07dt.pdf

## Slide 4: Optimization: Ray-plane intersection
There are three main ways to compute the point where the particle (ray) enters the phantom:
  Creating an air phantom (slowest)
  Using trigonometry to compute the distance (slow)
  Using the dot-product (fastest)
Faster methods are less accurate but compered to the measurement accuracy dot-product is accuracy is sufficient.

## Slide 5: Validation against Dose Planning Method (DPM)
https://pubmed.ncbi.nlm.nih.gov/10958194/
6 Mev Electrons
6 Mev Photons

## Slide 6: Validation against experimental data
6 Mev Electrons
6 Mev Photons

## Slide 7: Future step: GPU vs FPGA

## Slide 8: GPU CUDA cores vs FPGA CLBs
CLB and CUDA cores have similar impact on the throughput
GPU clock frequency tripled over the same period while FPGA frequency stayed constant

## Slide 9
 | CPU | GPU | FPGA
Engineering time | short | medium | very long
Compilation time | short | short | very long
Debugging | easy | medium | hard
Maintainability | easy | medium | hard
Development effort
Changes to the simulation do not require
to re-develop the entire architecture

## Slide 10: Execution time break-down

## Slide 11: Possible Partitioning
Partition | Data Transfer Time (s) (PCIe3x16)
Beam on CPU | From 0.30s to 6.05s
Beam and Photon simulation on CPU | From 11.51s to 115.10s
Accelerating Electron tracking only | From 20.39s to 203.92s
Splitting the simulation will not allow to meet time requirements

## Slide 12
(Voss 2019)
implemented features
https://pure.tudelft.nl/ws/portalfiles/portal/82584147/Voss2020_Article_TowardsRealTimeRadiotherapySim.pdf

## Slide 13: FPGA performance assumptions
simulation size
clock frequency 250 MHz (pessimistic)
not accelerated portions complete instantaneously (optimistic)
data transfer time = 0
One iteration per clock cycle (deeply pipelined)

## Slide 14: FPGA performance predictions
https://pure.tudelft.nl/ws/portalfiles/portal/82584147/Voss2020_Article_TowardsRealTimeRadiotherapySim.pdf
Implementation | Parallelism | Simulation Time
Voss2019 (imprecise) | 8 | 2,989 s
Beam on CPU | 2 | 522,15 s
Beam and Photon simulation on CPU | 4 | 261,08 s
Accelerating Electron tracking only | 8 | 130,54 s

## Slide 15: GPU performance assumptions
simulation size
NVIDIA GeForce RTX 3080 Ti
10240 CUDA cores
Stock clock frequency

## Slide 16: GPU performance predictions
# instructions (SPMD) | Efficiency | Compute Time
100000 | 1 | 0,59s
100000 | 0,5 | 1,17s
100000 | 0,1 | 5,87s
1000000 | 1 | 5,87s
1000000 | 0,5 | 11,73s
1000000 | 0,1 | 58,65s
500000 | 0,25 | 11,73s

## Slide 17: Price
FPGAs cost 5.80 times more than GPUs

## Slide 18: Conclusions
GPU acceleration allows further improvements to the simulation
FPGAs do not allow to meet the time requirements
GPUs potentially meet time requirements, or they will likely meet it in the near future