## Slide 1: Trigger Happy Or How & why we analyse a really, very large amount of data really, very fast
Andy Rose, Imperial College, London
awr01@imperial.ac.uk
www.hep.ph.ic.ac.uk/~awr01

## Slide 2: Science: The basics
Science is the art of knowing what to record, and when

## Slide 3: Science: The basics
Science is the art of knowing what to record, and when
Or being cynical, it's being in the right place at the right time

## Slide 4: Science: The basics
Science is the art of knowing what to record, and when
With CMS & ATLAS in “discovery mode”, we care about the Higgs Boson or rarer
  Higgs Boson production is ten orders of magnitude below the total interaction rate
Ten orders of magnitude

## Slide 5: Science: The basics
Science is the art of knowing what to record, and when
With CMS & ATLAS in “discovery mode”, we care about the Higgs Boson or rarer
  Higgs Boson production is ten orders of magnitude below the total interaction rate
  That is a needle in a haystack the same mass as the Empire State Building

## Slide 6: Science: The basics
Science is the art of knowing what to record, and when
With CMS & ATLAS in “discovery mode”, we care about the Higgs Boson or rarer
  Higgs Boson production is ten orders of magnitude below the total interaction rate
  That is a needle in a haystack the same mass as the Empire State Building
  Or if you collided protons once per second, that is one event every 316 years, 324 days (5 hours, 6 minutes and 17 seconds give or take)

## Slide 7: Science: The basics
Science is the art of knowing what to record, and when
With CMS & ATLAS in “discovery mode”, we care about the Higgs Boson or rarer
  Higgs Boson production is ten orders of magnitude below the total interaction rate
  That is a needle in a haystack the same mass as the Empire State Building
  Or if you collided protons once per second, that is one event every 316 years, 324 days (5 hours, 6 minutes and 17 seconds give or take)
And one Higgs boson is pretty much USELESS We need loads of them to be able to study them…

## Slide 8: This is why the LHC collides…
̴50 protons at a time × 40 million times a second

## Slide 9: This is why the LHC collides…
̴50 protons at a time × 40 million times a second
1 Higgs boson every ̴5 seconds

## Slide 10: This is why the LHC collides…
̴50 protons at a time × 40 million times a second
1 Higgs boson every ̴5 seconds
But this causes problems

## Slide 11: One proton-proton collision

## Slide 12: Many proton-proton collisions
25 proton-proton collisions

## Slide 13: Many proton-proton collisions
25 proton-proton collisions
Even if you get a Higgs boson, the RUBBISH makes it hard to find

## Slide 14: This is why the LHC collides…
̴50 protons at a time × 40 million times a second
1 Higgs boson every ̴5 seconds
But this causes problems
This causes problems too

## Slide 15: The CMS detector
~65M Silicon Pixels
~10M Silicon Strips
~80k PbWO4 Ecal Crystals
~15k channel Brass/Plastic sampling HCAL
~568k RPC/DT/CSC Muon channels
~3500 physicists/engineers

## Slide 16: The CMS detector
~65M Silicon Pixels
~10M Silicon Strips
~15k channel Brass/Plastic sampling HCAL
~568k RPC/DT/CSC Muon channels
~3500 physicists/engineers
~80k PbWO4 Ecal Crystals
× 40 million measurements per second

## Slide 17: The CMS detector
~65M Silicon Pixels
≡ 21 PBit per second
~10M Silicon Strips
≡ 4 PBit per second
~15k channel Brass/Plastic sampling HCAL
≡ 10 TBit per second
~568k RPC/DT/CSC Muon channels
≡ 23 TBit per second
~3500 physicists/engineers
~80k PbWO4 Ecal Crystals ≡ 40 TBit per second
× 40 million measurements per second

## Slide 18: The CMS detector
~65M Silicon Pixels
≡ 21 PBit per second
~10M Silicon Strips
≡ 4 PBit per second
~15k channel Brass/Plastic sampling HCAL
≡ 10 TBit per second
~568k RPC/DT/CSC Muon channels
≡ 23 TBit per second
~3500 physicists/engineers
~80k PbWO4 Ecal Crystals ≡ 40 TBit per second
What does that even mean?

## Slide 19: How much data?

## Slide 20: How much data?
1 Gb/s
1 Tb/s
1 Pb/s
1 Mb/s
4 PB/yr
4 EB/yr
4 ZB/yr
4 TB/yr
CMS Raw

## Slide 21: How much data?
1 Gb/s
1 Tb/s
1 Pb/s
1 Mb/s
4 PB/yr
4 EB/yr
4 ZB/yr
4 TB/yr
1× Home broadband
1,000,000× Home broadband
1,000× Home broadband
CMS Raw
CMS tape-store

## Slide 22: How much data?
1 Gb/s
1 Tb/s
1 Pb/s
1 Mb/s
4 PB/yr
4 EB/yr
4 ZB/yr
4 TB/yr
1× Home broadband
1,000,000× Home broadband
1,000× Home broadband
CMS Raw
CMS tape-store
But do we need to store it all?
The Higgs is rare, after all

## Slide 23: So what do we do?
We keep the data safe on the detector for several microseconds
We quickly analyse some fraction of the data and select the interesting crossings to keep

## Slide 24: So what do we do?
We keep the data safe on the detector for several microseconds
We quickly analyse some fraction of the data and select the interesting crossings to keep
Called Triggering

## Slide 25: So what do we do?
We keep the data safe on the detector for several microseconds
We quickly analyse some fraction of the data and select the interesting crossings to keep
Called Triggering
uninteresting crossings to discard
The LHC is a discovery machine, after all

## Slide 26: But!
If you get it wrong
If your system fails you throw away your valuable physics
If you take too long

## Slide 27: But!
If you get it wrong
If your system fails you throw away your valuable physics
If you take too long
And that is a *really, really* expensive mistake

## Slide 28: This is why the LHC collides…
̴50 protons at a time × 40 million times a second
1 Higgs boson every ̴5 seconds
But this causes problems
This causes other problems too

## Slide 29: A note on timescales
At 40MHz BX rate, a 4GHz CPU could perform 100 CPU operations before the next data arrives
  Not enough to be useful
Compare that to the O(10M) detector channels

## Slide 30: Sequential processing
6pm | 7pm | 8pm | 9pm | 10pm | 11pm | 12pm | 01am | 02am | 03am

## Slide 31: Sequential processing
6pm | 7pm | 8pm | 9pm | 10pm | 11pm | 12pm | 01am | 02am | 03am

## Slide 32: Sequential processing
6pm | 7pm | 8pm | 9pm | 10pm | 11pm | 12pm | 01am | 02am | 03am
That would just be stupid

## Slide 33: Sequential processing
6pm | 7pm | 8pm | 9pm | 10pm | 11pm | 12pm | 01am | 02am | 03am
That would just be stupid
But this is exactly what a PC does

## Slide 34: Pipelined processing
6pm | 7pm | 8pm | 9pm | 10pm | 11pm | 12pm | 01am | 02am | 03am

## Slide 35: Pipelined processing
6pm | 7pm | 8pm | 9pm | 10pm | 11pm | 12pm | 01am | 02am | 03am
So why doesn’t my PC do this?

## Slide 36: Pipelined processing
6pm | 7pm | 8pm | 9pm | 10pm | 11pm | 12pm | 01am | 02am | 03am
Because writing code like this is *really, really* hard
So why doesn’t my PC do this?

## Slide 37: Field-Programmable Gate Arrays
Programmable circuit-on-chip
Upwards of 8.9 million logic cells & up to 12,000 “math” cells
  All clocked at ̴500MHz
Over O(1015) operations/second
  That is PetaBOps
Fully parallel and fully pipelineable

## Slide 38: Field-Programmable Gate Arrays
Programmable circuit-on-chip
Upwards of 8.9 million logic cells & up to 12,000 “math” cells
  All clocked at ̴500MHz
Over O(1015) operations/second
  That is PetaBOps
Fully parallel and fully pipelineable
and *really, really* hard to program efficiently

## Slide 39: Field-Programmable Gate Arrays
A chip needs to be attached to something!
Imperial’s latest platform: Serenity
  208 optical transmit links & 208 optical receive links @ 28.5Gbps =
  Skewable to
5.9 + 5.9 Tbps
7.0 + 4.8 Tbps

## Slide 40: The future: High-luminosity LHC
Up to 250 proton-proton collisions per event
Really, really hard to find the interesting event under all that rubbish
Need to sift through 300Tbps to find the interesting events
150 proton-proton collisions

## Slide 41: But this is the 21st century…
How do you deal with hard problems and big data?

## Slide 42: But this is the 21st century…
How do you deal with hard problems and big data?

## Slide 43: But this is the 21st century…
How do you deal with hard problems and big data?
Ummm… It's not quite that simple

## Slide 44: Why can't you just use Machine Learning at HL-LHC?
The data is still only safe on the detector for ~10 microseconds
  Not much time
The trigger is receiving ~100Tbps from the tracker, ~100Tbps from the barrel calorimeter and ~100Tbps from the endcap calorimeter
  AKA 1 hellavalotta data
Recall, that you can't see the data the trigger throws away…
  You need to be *REALLY* sure you know what your algorithm is doing.
The detector environment is always changing, inference may not look anything like your training data

## Slide 45: That said… if it works, why wouldn't you use it?
For certain, well-defined sections of the trigger chain, machine-learning is a useful and powerful tool
  Tools developed for translating Neural Networks for use in high-throughput and low-latency systems
Work being done in the area of understandable AI
Work being done in the area of continual learning

## Slide 46: Conclusion
The hardware triggers at the LHC are some of the most computationally challenging problems on the planet
They are a great deal of responsibility

## Slide 47: Conclusion
The hardware triggers at the LHC are some of the most computationally challenging problems on the planet
They are a great deal of responsibility
And, if you like puzzles, a great deal of fun 