## Slide 1: ATLAS inner detector decommissioning
Tolerance study of robotic components for use in high radiation environment
Alice Cryer, University of Sheffield

## Slide 2: Birmingham Irradiation facility
Revised radiation estimates less than previous simulations
Future high luminosity colliders will have high radiation -> need remote tooling
Also has Industry applications
Cyclotron beam of 23MeV protons focussed to 1cm2

## Slide 3: ImagingSource GigE camera
First irradiation was an ImagingSource GigE camera
The camera was irradiated by scanning the beam over its profile
Moved by a "Cartesian Robot" scanning system
23MeV proton beam @10nA
Irradiation Facility
Source: ImagingSource

## Slide 4
ImagingSource GigE camera
Glycol chiller set to 10°C
Camera mounted on the lid of the box
Camera uses Ethernet for both power and data
Camera is monochrome
Camera was live during irradiation, sending 1 picture/second
Experimental Setup

## Slide 5: ImagingSource GigE camera
Minor pixel degradation before failing
It recovered after a period of inactivity
Ethernet used as both power and data: design is a significant radiation weakness
First picture
During the irradiation showing hot pixels
Ultimate cause of failure inconclusive
Results

## Slide 6
Shadow Robot manipulator
The robotic manipulator was one of the three fingers from Shadow Robot company’s Smart Grasping System
It was programmed to perform a set of repetitive tasks, moving itself in and out of the beam
It was irradiated with a static beam
Experimental Setup
Source: Shadow Robot
Source: Shadow Robot
Source: Shadow Robot

## Slide 7
Shadow Robot manipulator
The Robotic manipulator
3 driver chips, 3 motors and a sensor on the finger tip
Source: Shadow Robot

## Slide 8
Shadow Robot manipulator
The finger in the first orientation was significantly resistant to radiation
23MeV proton beam @10nA
Second orientation placed the beam directly above a driver chip
23MeV proton beam @5nA (beam drift)
Second orientation
First orientation
The Irradiation

## Slide 9
Shadow Robot manipulator
Data readout from the finger show where and when it failed
Program movement incomplete: driver failure
2 other drivers still working
Program fail conditions creates weakness to radiation
Results

## Slide 10
Shadow Robot manipulator
The manipulator proved to be significantly resistant to radiation:
  Would be suitable for use in radioactive environments
A second irradiation experiment within the cyclotron vault has been proposed
Inside the vault there is much broader range of radiation:
  More comparable with industrial nuclear decommissioning
Analysis

## Slide 11: Thank you for listening
Any questions?