## Slide 1: A history and development of the LHCb Scintillating Fibre Tracker
by Dr. Blake Leverington

## Slide 2
aimed at young scientists regarding the development of a novel tracker for the LHC .
  no fixed process, but I think it is a similar experience among all detectors.
    There’s some fixed LHCC milestones I will describe that a subdetector must pass
  heavily weighted by my own perspective.
  Some technical details, but I’d like to keep the focus on the process

## Slide 3: Evolution of Detectors
LHCb in the Technical Proposal (1998), very similar to HERA-B
LHCb re-optimized (2003) to be lighter
CERN-LHCC-2001-024
CERN-LHCC-98-004
CERN-LHCC 2003-030
Notes: Hera-b 5–10 MHz by moving a target wire into the halo of the circulating proton beam at DESY. The vertex locater was also moved very close to the beam, about 1cm

## Slide 4
February 2005
LHCb Dector Installation starts
June 2006
Installation of the Outer Tracker bridge
October
2006
Installation of the Outer and Inner Tracker begins
August 2008
LHCb Assembly is Complete
LHC Start Planned in April 2007
April 2007
Start delayed due to magnet supports
10 Sept. 2008
LHC circulates first beam
19 Sept. 2008
Magnet Quench
Notes: YouTube: In May 2005, the first video
June 2007, Apple released the iPhone

## Slide 5
January 2007
1st LHCb Collaboration Upgrade Workshop
Prediction, by Franz Muheim
Expression of Interest (EoI) for a detector upgrade submitted in April 2008

## Slide 6: Upgrade of the LHCb Detector (as planned in 2007-2008)
Motivation
No data or published papers yet, but lots of MC
Smaller uncertainties to find SM deviations
  10 fb-1  100 fb-1
  Physics case should be robust
  stat.uncertainties of O(few %)  O(1%) in many channels
Detector Requirements
40 MHz detector readout electronics (25 ns bunch crossing)
Remove the L0 Hardware trigger  flexible software
Instantaneuous luminosity x 10 (above design) 2  20 x 1032 cm-2s-1
High tracking efficiency (99%)
Reasonable detector occupancy for pattern recognition
Try to reduce material where possible
  Secondaries were a large problem for HERA-B
  Secondaries produce more hits than primaries in T-stations

## Slide 7
Main tracking System of LHCb
5 m
6 m

## Slide 8: Outer Tracker
Marcel Merk at
, 2007
Notes: You can’t just change the electronics to a faster readout. There’s some fundamental geometry and signal timing problems. The detector has a good performance (they think, at this point) though they’re worried about some aging aspects. The material budget of this detector is quite good. Straw tube gas detector. But you just start to have that more than one track crosses a single straw tube in the same bunch crossing, and you can’t count more than one per tube.

## Slide 10: IT+OT Material for 1 T-Station
LHCb-2008-054

## Slide 11
January 2007
1st LHCb Collaboration Upgrade Workshop
April 2008
Expression of Interest letter Submitted
UPGRADE
Nov. 20 2009
LHC circulates beam again
March 2010
3.5 TeV Beams
LHCb starts taking data
Keep old OT/IT but new electronics
GEMs?
upgrade in 2013 or in 2017?
commissioning
First published paper
August 2010
Radiation damage? (OT/IT aging)
Shorter straw tubes / more silicon
Partial scintillating fibre + Straw + Silicon?
Partial staged upgrade?
Letter of Intent Submitted
March 2011
CERN-LHCC-2011-001
CERN-LHCC-2008-007

## Slide 12
LoI: Letter of Intent
An initial document submitted to the LHCC of CERN describing interest in performing a new experiment or major upgrade, outlining the physics case and detector required in broad terms. The LHCC reviews the document and determines if the collaboration should proceed to the next stage of approval, typically a Technical Proposal or Framework TDR.
For the original LHCb experiment this is CERN/LHCC-95-5. For the LHCb Upgrade I there was initially a shorter Expression of Interest document CERN/LHCC-2008-007. This was followed by a Letter of Intent document CERN/LHCC-2011-001.
Similar documents are often required in the LHCb member countries for their scientific review and funding agencies, focusing for the detector on the elements that will be constructed in that country, as part of their approval process.
From https://lhcb.github.io/glossary/

## Slide 13: LoI Proposals
40 MHz Bigger Silicon IT
Thick fibre OT option
Thin-fibre IT option
40 MHz straw-drift tube OT
1.
2a.
2b.

## Slide 14: Previous SciFi Trackers
UA2 & CHORUS (Early ’90s)
image intensifier and CCD
  High voltage (20-35kV)
  doesn’t work in magnetic fields
1mm and 0.5mm diameter fibres
single hit spatial resolution of 0.35mm (for 1mm diam.)
The sensor (fibre) also transports the signal outside of the acceptance!
  No RF noise problems, few metre attenuation
Nuclear Instruments and Methods in Physics Research A 387 (1997) 278-281
UA2
Chorus
microchannel plate (MCP)

## Slide 15: Previous SciFi Trackers
D0 scintillating fibre tracker at Tevatron (early 2000’s)
  DO: 72,000 double clad 3HF 0.8mm diameter fibres 1.7m – 2.7m long
  Each scintillating fibre is mated to a clear fibre waveguide. The length of waveguides ranges from 8.2 to 11.4...
Visible Light Photon Counter (VLPC)
  a solid-state device capable of high-rate single photon counting with excellent quantum efficiency
  Cryogenic cooling (5 - 7 Kelvin)
  Also used at MICE
20,000 to 60,000 electrons per detected photon. QE ~80% .
hit efficiency of 99.5% and a doublet hit resolution of 100 micron.
Nucl.Instrum.Meth.A 387 (1997), 278-281
Notes: ~150 km of fibre

## Slide 16: Previous SciFi Trackers
The PEBS balloon experiment(s) (2006-2012)
Possible with the advent of the SiPM and SiPM array
  Insensitive to magnetic fields.
  (near) Room temperature operation
  Operation at 10s of Volts
  1E6 gain
0.25 mm fibres
  55 micron hit resolution (14 bit ADC)
  SPIROC readout chip (designed for calorimeters)
SCSF-78MJ scintillating fibres
Hamamatsu MPPC 5883
https://doi.org/10.1016/j.nima.2010.07.011
60-80 cm

## Slide 17: Let the workshops begin!
“A fiber TT could be a shorter version of the “Long fibers” version” – Ueli Straumann
but silicon was the main focus.
Notes: Still idea proposals with some bits of tech here and there as early proof-of-concept taken from other research.

## Slide 18: Tracking and the upgrade
High(er) granularity in VELO and Trackers important for pattern recognition.
  Ghosts: Time consumption in trigger and offline
Momentum resolution (dp/p) determined by:
  Multiple scattering term (constant versus p)
  Hit resolution term (rises versus p).
Hit resolution contribution
  determined mainly by OT (IT)resolution.
Current LHCb: We lose 10-15% of our tracks due to material interaction, thus
  little material (not only dead material) is important for high efficiencies
Inner segmentation would be nice (an IT)
Jeroen van Tilburg

## Slide 19: Critical R & D Points
Detector signals to have >99% hit efficiency
  Light yield from the scintillating fibres
  Photon detection efficiency (PDE) of the photodetector
  Noise, dead-time, and spillover effects
  Radiation effects on the fibre and photodetector
Electronics for 40 MHz readout
  Digitise the signal from each 25ns bunch crossing, zero dead time
Minimise the material (<1%X0 per layer for 12 layers)
Fibre mat production (non-commercial)
  Tooling. How could you build a fibre tracker?
Given the incrememental nature of most technology development, it is not clear if everything performs well when put all together.
Prototype all the things!

## Slide 20: Things are getting serious now
First test beams August 2011
Regular SciFi Tracker Meetings
Photoelectron signal

## Slide 21: First 2.5 m long fibre mats
~3cm wide
More difficult than the PEBS 80cm mats. We need semi-automation winding machines. Too big for standard turning machines.
LHCb Upgrade requires hundreds of mats without defects.
Dec 2011
Notes: Idea Similar to winding wire chambers: fixed tension; needs to be glue. (does it?)

## Slide 22
vs.
CERN/RUSSIA

## Slide 23: First electronics concepts appear
Developing specifications for electronics (April 2012)
5 or 6 bits  max 32 photon signals
separate signal and noise (1 - 2 p.e.)
SiPM parameters needed as input
Back-end DAQ

## Slide 24: Towards a TDR
.... a framework TDR (May 2012)
(something to go to the funding agencies with, and start to divide tasks among institutes officially)

## Slide 25: A growing collaboration
Yours truly, since 2012

## Slide 26: Radiation Damage in Fibres
How to simulate 10 years of radiation damage at 5x available intensity on a 2.5m long fibre with varying integrated dose???
  When the magnitude of the effect is rate dependant
  Annealing effects are unknown (at this stage)
  Oxygen effects?? (conflicting literature)
Beam scan at Karlsruhe in 2012
Fixed Beam at CERN PS
Garching tandem accelerator
LHCb in-situ (VELO wall)

## Slide 27: A team effort
Studies for the LHCb SciFi Tracker - Development of Modules from Scintillating Fibres and Tests of their Radiation Hardness
Robert Ekelhof (Doctorarbeit, TU Dordmund, 2016)
We base the performance of the Tracker after 50fb-1 on this data.
Attenuation coefficient from radiation
Attenuation coefficient from radiation per kGy
Natural attentation of the fibre

## Slide 28: Viability Assessment (Feb 2013)
To be honest, it wasn’t clear in the previous years if a SciFi tracker could work at the LHCb Upgrade
Held an LHCb-internal review:
  find that the light yield from current(2013) fibers, and PDE from current(2013) SiPMs are at the limit of the requirements for the LHCb upgrade
  the needed performance will be reached with the expected improvements
  More fibre layers (5->6), better SiPMs with higher PDE in the pipeline
Fluka

## Slide 29: The PACIFIC is born
June 2013
288,000 channels
3 analog channels, Submitted in May 2013
PACIFICr1
PACIFICr1 channels are used to test different blocks implemented; Fast Shaper, Slow Shaper and Dual Interleaved Integrator.
(IBM) 130 micron technology through CERN.
(low-Power ASIC for the sCIntillating FIbres traCker)
Notes: Details on Voltages appear, control, signal formts, etc

## Slide 30: First 3m long fiber mat!
Dortmund: winds first 3m SciFi mat, width approx 1cm!!
Scintillating fibre wound on a threaded wheel. Titanium dioxide loaded glue is used to bond the fibre together.
The prototype Dortmund winding machines.

## Slide 31: First Idea Conflict! (But not the last)
Bi-layer assembly of the fibre module panels
-> (80cm construction proven) maybe extends to 250cm??
Mono-layer: strip out all unneccesary materials. Lightest option. Protects the fibres.
Workshops for resolving idea conflicts with internal LHCB reviewers to resolve the issue.
  Need to maintain a friendly collaboration
  Specifications become well defined.
  Competing ideas allowed for them to be tested
  Sometimes you need to pick a single path, and go, and deal with the consequences.
Fibre mat mounted on top of foam and carbon fibre sandwich

## Slide 32: The first 2m dummy SciFi Module
July 2013
Testing assembly concepts. Would be ~1% of a radiation length in material thickness.

## Slide 33: Decision day...

## Slide 34: The light Silicon IT
Silicon strips
  320 micron thick sensor
  200 micron wide strips
  Carbon fibre ladder support
High-flow chilled air(+15C) for cooling
  Reduced material in the acceptance
  Still requires signal and power cables
A viable option for an inner tracker
LHCb-PUB-2014-009

## Slide 35: State of the SciFi
7cm mats without defects!!
Only 1 detector technology proposed to cover the entire acceptance! 10,000km of fibre (0.5m3 of plastic)
1% X0/layer

## Slide 36: The best laid plans.
Plans should not be confused with schedules.
The estimated time is always wrong by a factor of 2 in R&D (at least).

## Slide 37: Project Management
Divided into Work Packages:
  Project Leader and Deputy
  Package Coordinators (like a WG convener)
  Lead by institutes (staff, postdocs, phd) with primary interests in topics
  Multiple Interfaces between packages.
From LoI to EDR
From PRR to Installation
(i.e. things we haven’t be educated for)
I would estimate that the majority of delays and errors were due to poor communication in the team.
Find the (multiple) communication channels that work best for your team.
Email and Twikis are the worst.
In person, Video/Telephone, Mattermost chat are the best.

## Slide 38
TDR: Technical Design Report
A document submitted to the LHCC of CERN describing the design of a subdetector or other subsystem (e.g. online, trigger, computing). This document also describes the cost of the detector and which institutes will be responsible for which elements of the construction. The TDRs of LHCb and the upgrades are collected here. The document is reviewed by the LHCC, with involvement from the RRB for financial aspects.
A clear understanding of the requirements, the environment, and the constraints
real “proof-of-concept” prototypes and Monte Carlo simulation to estimate the performance and a good idea how to build this detector
Conceptual Designs and estimated Performances of your sensors, electronics, tooling, etc.

## Slide 39: Fibres in the TDR (March 2014)
the “Bump Problem”
  Causes defects in the fibre winding
  Time consuming to fix defects.
Present the radiation damage studies
  40% signal loss expected
  Need a 6th layer of fibre
one scintillating fibre manufacturer, Kuraray
  sole sourcing your central component is risky
  Kuraray willing to improve
  Bicron/Saint Gobain had poorer quality and wasn’t interested in development.

## Slide 40: SiPMs in the TDR
Working with two SiPM manufactureres Hamamatsu (good) and KETEK (packaging issues)
PDE improving regularly (peak at 28%  40% now)
  40% improvement in 2 years!
SiPMs needs cooling to -40 degC due to radiation damage
Signal and hit efficiency is understood
SiPM irradiation  -40C cooling will be required
KETEK Sipm Array
Hamamatsu SiPM array

## Slide 41: Conceptual Integration (2014)
Mostly detector physicists’ conceptual designs, and not engineering.

## Slide 42
January 2007
1st LHCb Collaboration Upgrade Workshop
April 2008
Expression of Interest (EoI) Submitted
UPGRADE
Letter of Intent Submitted
March 2011
CERN-LHCC-2011-001
Framework
TDR
May 2012
Viability
Assessment
February 2013
November 2013
Tech choice.
Tracking TDR
March 2014

## Slide 43: Prototypes
The first 5m (mostly) dummy module hung on the wall in Heidelberg.
Fibre modules for test beam.

## Slide 44: Test beams (2015-2016)
Single fibre mat modules at the SPS H8 beamline
Spiroc electronics connected to an SiPM arrray

## Slide 45: Production numbers
We need to produce 128 scintillating fibre modules
  10,000 km of fibre to process
Mats & Modules:
  1024 mats + mats
  128 modules+ spares
Sipms:
  4096 arrays + spares
Electronics:
  8192 PACIFIC asic + spares , 2048 boards
  2048 FPGA boards
  512 Master boards
Assemble all of this as 12 C-Frames

## Slide 46
EDR: Engineering Design Review
A milestone during the construction of a subdetector. The EDR is a meeting with accompanying documentation that describes the detailed design of a component system of the detector (e.g. sensors, an ASIC, high voltage system) based on drawings and prototypes that have been produced. Reviewers with relevant expertise from other subdetectors in LHCb and from other experiments are usually appointed to conduct the review and make recommendations.
The next major milestone is the PRR.

## Slide 47: Fibre Mats in the EDR
The fibre mat production reaches an advanced stage
Step by step production process is defined
4 custom winding machines are to be ordered for mat production

## Slide 48: 8 EDR fibre mats (Summer 2015)
Notes: 8km of fibre per mat. About 1/3rd of D0 in terms of number of KM of scintillating fibre, just for a prototype

## Slide 49: Modules
First prototype module is made with the EDR fibre mats
Alignment tooling developed
  Creating the tooling is almost as much work as the objects themselves
Not the final version but the collaboration gives the go ahead to prepare everything for serial production
  Design of beam pipe modules
  Fire safety burn tests
  Light leaks

## Slide 50: SiPM EDR in 2016
H2011: First version of 128 channel, 230μm x 1.32mm (WxH), 84 pixels,y,ΔV=1.3V.
  Low PDE (~30% peak)
  High cross-talk (~20%)
  Very temperature sensitive due to low ΔV
H2014: First version with trenches, 230μm x 1.5mm (WxH), 96 pixels , ΔV=3.5V
  Medium PDE (~40% peak)
  Medium cross-talk (~12%)
  Large stable operation range
H2015: new trench LCT5, smaller dead zones, 230μm x 1.625mm (WxH), 104 pixels, typical ΔV=3.5V
  High PDE (~50% peak)
  Low direct cross-talk but medium AP and delayed cross-talk (9% correlated)
Ketek arrays were very nice, with similar or better performance but there were too many production problems with the silicon and packaging at this time
KETEK Sipm Array
Hamamatsu SiPM array
1 year later than TDR plan

## Slide 51: The Cold-Box (2016)
Rob Walet, engineer and designer for SciFi

## Slide 52: Electronics EDR (Summer 2016)
Prototype Front-end

## Slide 53: PACIFIC ASIC Development
TDR
EDR

## Slide 54: Electronics EDR
Full processing chain is understood.
All components are designed and prototyped.
All the specifications and requirements are met.
128-channel SiPM
524,288 channels  4096 data links, 1024 control fibres

## Slide 55: More prototypes and testbeam
64-channel PACIFICr5 board at DESY test beam
Scintillating fibre telecope, and two SciFi DUT mats

## Slide 56
PRR: Production Readiness Review
A milestone during the construction of a sub-detector. The PRR occurs after the EDR.
The PRR is a meeting with accompanying documentation that describes the detailed design of a component system of the detector (e.g. sensors, an ASIC, high voltage system). Reviewers with relevant expertise from other sub-detectors in LHCb and from other experiments are usually appointed to conduct the review and make recommendations.
The PRR makes recommendations for revisions or approves that the final production of this element of the sub-detector can start.

## Slide 57: PRR
Reviewed by internal LHCb collaboration referees (experts)
Typically a lot of time and expense involved in building a detector
Improvements in processes since EDR
  Step-by step-description of the process, documented
Materials are in hand to start full production
Designs are fully tested. Tooling is ready. QA is ready.
  This was the most time consuming part between EDR and PRR.
Fibre mat Glue-casting
Foil-lamination

## Slide 58: SciFi Module Production Model

## Slide 59: Testbeam with final electronics and production modules (July 2018)
99% hit eff., 70 micron hit resolution

## Slide 60: Production C-Frame model

## Slide 61: Be ready on time...
mats and modules
electronics
SiPM
Cold-box
C-Frame Assembly
COVID Lockdown
COVID Lockdown
Production
1 – 2 years longer to start and finish production than guessed at in the TDR
   The end date always matched the end of LS2 (which shifted)
15 years from conception to the end of installation.
Old TDR schedule

## Slide 62
First module assembly (June 2016)
Module storage at Point8 (July 2020)

## Slide 63: First SiPMs on a cold-bar

## Slide 64
First 7cm fibre mat with SiPM
(August 2014)
First finished C-Frame (Feb. 2020)

## Slide 65: First 4 Frames Installed (May 2021)
6 of 12 C-Frames installed (July)

## Slide 66: This looks familiar...
What if we had 300 fb-1 of data instead of just 50?....
First workshop in April 2016.
The LHCb Upgrade II EoI was submitted to the LHCC in February 2017.
Expression of Interest is CERN-LHCC-2018-003, Physics Case CERN/LHCC-2018-027.

## Slide 67: The End(?)

## Slide 68
backup

## Slide 69: References
Advances in Tracking Detectors Frank Hartmann and Jochen Kaminski Annual Review of Nuclear and Particle Science 2011 61:1, 197-221 https://doi.org/10.1146/annurev-nucl-102010-130052
THE USE OF SCINTILLATING FIBERS FOR CHARGED-PARTICLE TRACKING R. C. Ruchti Annual Review of Nuclear and Particle Science 1996 46:1, 281-319 https://doi.org/10.1146/annurev.nucl.46.1.281

## Slide 70: Thoughts for Upgrade 2
Higher granularity means more channels:
  Lots of power to dissapate
  Lots of optical fibres to clean and inspect
Silicon means cooling when there’s radiation damage
  Cooling and cables in the acceptance are bad for LHCb
Don’t underestimate the infractructure requirements...
  Density of services, cables and fibres

## Slide 74: The LHCb Upgrade
Letter of Intent for LHCb “While LHCb will be able to measure a host of interesting channels in heavy flavour decays in the upcoming few years, a limit of about 1 fb−1 of data per year cannot be overcome without upgrading the detector. The LHC machine does not face such a limitation. With the upgraded detector, read out at 40MHz, a much more flexible software-based triggering strategy will allow a large increase not only in data rate, as the detector would collect 5 fb−1 per year, but also the ability to increase trigger efficiencies especially in decays to hadronic final states. In addition, it will be possible to change triggers to explore different physics as LHC discoveries point us to the most interesting channels.”

## Slide 75
Technical Proposal
A document submitted to the LHCC of CERN describing the design of a new experiment or major upgrade, outlining the physics case and detector design. This document contains more detail than the LoI, for example reporting on R&D that shows the feasibility of the project and possibly estimating the cost. The LHCC reviews the document and determines if the collaboration should proceed to the next stage of approval, typically TDRs for the individual subdetectors and systems of the experiment. If costs are involved the RRB of CERN is involved in the approval.
For the original LHCb experiment this is CERN-98-004 followed by an LHCb reoptimized detector design and performance TDR that is CERN/LHCC 2003-030. For the LHCb Upgrade I the equivalent document is known as a Framework TDR, and is CERN/LHCC-2012-007. For the LHCb Upgrade II the equivalent document is due to be submitted around late 2020.