## Slide 1: at the A. E. Lalonde Accelerator Mass Spectrometry Lab
Liam Kieser
André E. Lalonde AMS Laboratory and
Dept of Physics
University of Ottawa
The New Reserch Injector Line
W1-6 Instrumentation for the Detection of Low-Level Radioactiivity
CAP 2016 Congress June 15

## Slide 2: Overview
The New Research Line
a) Principal components
b) Example: the isobars in 90Sr analysis
a) General operating principles
c) The ion optics of deceleration
d) The new pre-commercial system
b) Some general ion optics
The Isobar Separator for Anions (ISA)
Accelerator Mass Spectrometry (AMS) – some basic information
a) Advantages over conventional Mass Spectrometry
b) New applications made possible – (research using AMS)
Physics Research into AMS Itself
a) The generation of ions from the sample – materials, quantity & efficiency
b) Dealing with Isobars – especially atomic, but also molecular
c) Elimination of ME/q2 and E/q ambiguities
Summary

## Slide 3
Mass Spectrometry – basic functions:
Liberate atoms from the sample and give them an electrical charge
Use electric and magnetic fields to manipulate and sort the ions
Count the ions as an electrical current or by measuring other effects on matter
Ion Source
Filter or Analyzer
Sample
Detector
Ions
Heavier Ions
Lighter Ions
Challenges:
Atoms (or molecules) that have the same charge and mass as the analyte isotope – Isobars – are always much more abundant
Useful isotopes occur at very low concentrations (10-12 to 10-16) in nature – need large ion currents, highly selective analyzers and very sensitive detectors
Solution:
The accelerator provides the energy to destroy molecular isobars, to discriminate against some atomic isobars and for noise-free single atom counting.
Notes: 3

## Slide 4
The Accelerator Mass Spectrometer – an overview
Negative ions produced from samples loaded in the Ion Source
Ions selected by mass and energy in the Low Energy Mass Spectrometer
Ions accelerated to high voltage (3 MV) electrode in accelerator
Ion charge changed to positive and molecules destroyed in argon filled canal
Positive ions and molecular fragments accelerated to higher energies
Analyte Ions sorted from fragments in the High Energy Mass Spectrometer
Analyte Ions counted and identified in the Faraday Cups and Gas Ionization Detector

## Slide 5
New Applications – Tracing examples:
a) Iodine-129 as a tracer of circulation patterns in the world’s oceans – using only 200 ml of sea water.
b) Tracking new pharmaceuticals through human metabolic processes – label compound with 14C, administer at extremely low dose levels (Microdosing).
c) Monitoring the flow and recharge rate of groundwater in aquifers with 36Cl
d) Monitoring calcium metabolism in human bone using 41Ca (t1/2=102 ka, EC decay)
Dating and timing examples:
a) Compound-specific 14C dating – more precise association with process to be dated
b) Forensic use of weapons test produced 14C – “bomb-pulse” dating
c) Use of 129I (t1/2=15.8 Ma) to time subduction processes on continental margins
Nuclear Industry examples:
a) Monitoring of Pu uptake by nuclear workers
b) Tracking the movement of illicit nuclear material: 235,236 U, 230-243Pu, 90Sr, 135,137Cs
c) Monitoring the industrial use of T using organically bound tritium (OBT)
Notes: 5

## Slide 6
Development of the negative ion caesium sputter source for nuclear physics work in the1970s made AMS possible
a) Ion Source Development – need to :
Generate large ion currents (at least 10s of μA, 100s good if possible)
to obtain sufficient counting statistics for low concentration of rare species with a large ratio to abundant species
Produce negative ions from a wide range of elements
Maintain stable operation for a variety of sample matrices
Operate with a relatively low memory of previously analysed samples
SIMS Design
High Current Design
2. Research into AMS Technology:
Notes: 6

## Slide 7
Caesium reservoir
Extraction Anode
Sample
(Target, Cathode)
Spherical Ionizer ~1200°C
~ -28 kV
~ -35 kV
Ion Source Schematic – in cross section
Caesium reservoir neater
Cooling Channel
Analyte
Ions
0
10
20 mm
Notes: 7

## Slide 8: AMS Research – b) Isobaric Interferences:
Atomic Isobars:
Several isobars can be eliminated just by using negatitve ions:
e.g. 12CH2, 13CH, 7Li2 for 14 C analysis – broken up in the accelerator HV terminal
14N for 14C analysis, 26Mg for 26Al analysis, 129Xe for 129I analysis
Others can be attenuated using higher energy and interacting with gases or foils:
e.g. 10B for 10Be analysis – requires higher energy for heavier masses
Molecular Isobars:
New Approaches for Atomic (and Molecular) Isobars:
1. Retard ions from ion source energy (E > 35 keV) to eV scale energies
2(a) Either use gas-ion collisions to “chemically” remove the isobar (as in ICP-QQQ-MS) or
2(b) Use photon-ion interactions to selectively de-ionize the isobar
Process in 2(a) developed as the Isobar Separator for Anions (ISA)
Notes: 8

## Slide 9
3. Second Injection Line – overall layout
Injector 1
(Supplied by HVE)
Injector 2
“Innovation Line”
Pre-commercial Isobar Separator
ρ = 35.6 cm Injector Magnet
45° Rotatable Electric Analyser
54° Rotatable Electric Analyser
SO-110 / 200 Ion Source
SO-110 / 200 Ion Source
GIC 834
SIMS type
Ion Source
120° High Resolution Injector Magnet
45° Magnet for off-line analysis
Notes: 9

## Slide 10
Second Injection Line – basic ion optics
Einzel lens
Ion Source Target
Electric Analyzer – spherical plates
Electric Analyzer Image, Magnet Object Slits
Ion Source to Electric Analyzer Image,
Notes: 10

## Slide 11
Second Injection Line – basic ion optics
Magnet Image, Isobar Separator Object Slits
From Electric Analyzer Image to Isobar Separator Entrance
Electric Analyzer Image, Magnet Object Slits
Isobar Separator Deceleration Region
Isobar Separator Image Slits
Notes: 11

## Slide 12
Second Injection Line – basic ion optics
Isobar Separator Image Slits
From Isobar Separator Exit to HVE Magnet Image
Isobar Separator Acceleration Region
Einzel lens
HVE 120° Magnet Image Slits
Notes: 12

## Slide 13
1. Standard AMS ion source, with mass selection in injection magnet
2. Deceleration of rare mass beam to appropriate energy (≈ the ion source voltage)
4. Cooling of the ions using a light gas (He) if required
5. Interaction of the ions with the gas in the reaction cell
6. Re-acceleration to ion source energy for injection into AMS system
7. Standard AMS analysis and detection of interaction products
System schematic
High Voltage Deck
4. The Isobar Separator for Anions (ISA) – basic principles
3. Radio-frequency Quadrupoles (RFQs) used to contain the slow ions

## Slide 14
Began testing using a single cell for both cooling and reactions
Lab Ground
Deceleration Lenses
Deceleration Quads
Cooling / Reaction Cell
Acceleration Quad, Lenses
Lab Ground
To Accelerator
Notes: 14

## Slide 15
Isobar Suppression Demonstration: Sr – Y – Zr system:
Simulate 90Sr with 88Sr

## Slide 16
Simulate 90Sr with 88Sr, 90Zr as itself
ZrF3– / SrF3– = 4 x 10-6
Isobar Suppression Demonstration: Sr – Y – Zr system:

## Slide 17
Simulate 90Sr with 88Sr, 90Zr as itself and 90Y with 89 Y
Isobar Suppression Demonstration: Sr – Y – Zr system:

## Slide 18
3D view of a deceleration geometry as entered into and displayed by Simion 8.1
Magnet
Image
Slits
Einzel Lens
Deceleration Gap
Lab Ground
“”Deck” Voltage
Pre-commercial ISA Deceleration Calculations::
Isobarex
Company formed to develop and market the ISA as a commercial product:

## Slide 19
0 V(L)
Lab Ground
-35 kV(L) = 0 V (D) – Deck Ground
26.5kV(L)
0 V(L)
RO 10 V(D)
1,500 V(D) =
-33,500 V (L)
Beam at Magnet Image
3 mm Ǿ, ± 17 mr
Calculated Transmission
100%
5 mm Ǿ, ± 17 mr
95%
Deceleration Calculations::
Calculated by X-L Zhao using SIMION 8.1

## Slide 20
To avoid duplication of ion sources an magnets, the system is designed to easily be change from normal AMS operation to Isobar Separation operation
Plan View
Removable Section
Isobarex
Pre-commercial ISA – Mechanical Design
Split Flow Turbopump
Split Flow TurbopumpU

## Slide 21
Replaceable RFQ column – supports and frame removed
Deceleration Electrode
Re-aceleration Electrode
RFQ Modules
Isobarex
Pre-commercial ISA – Mechanical Design

## Slide 22
Deceleration end of column being assembled
Isobarex
Column in vacuum housing with turbopumps, lenses and beamline insulators
Pre-commercial ISA – Mechanical Design

## Slide 23
The energy provided by the accelerator enables the destruction of molecular isobars and noise-free, single atom counting capability
Summary
The new injection line will support research in AMS technologies such as ion source development, the elimination of atomic isobars and applications using new elements and isotopes for tracing and dating.
The collaboration agreement between Isobarex Corp. and uOttawa will lead to new ISA applications and the further development and expansion of ISA technology.
Wide-ranging abundance sensitivity and small sample sizes make AMS the method of choice for many isotope applications in Earth, Environmental, Materials, Cultural and Bio-medical Sciences
Thank you

## Slide 24
Notes: 24

## Slide 25
Notes: 25

## Slide 26: Radio-frequency Quadrupoles:
Stability parameters set limits on the geometrical design and electrical operation of the cell
where:
e is the elementary charge
Vrf is the peak-to-peak RF voltage
Vdc is the DC voltage between the pole pairs
m is the ion mass
ω is the angular RF frequency, and
r0 is the radius of a circle tangential to the inner surface of the rods.
q | = | 2 | e Vrf
 |  |  | mω2r02
a | = | 4 | e Vdc
 |  |  | mω2r02
r0
For quadrupoles:
For confinement only, a = 0
i.e., no mass resolution
For stability (adiabicity), q ≤ 0.3
i.e., more power doesn’t always help

## Slide 27
Close-up of deceleration end
Isobarex
Pre-commercial ISA – Mechanical Design

## Slide 28
Close-up of deceleration end – one quad support module removed
Isobarex
Pre-commercial ISA – Mechanical Design

## Slide 29
Close-up of deceleration end – support module and one pole removed
Isobarex
Pre-commercial ISA – Mechanical Design