## Slide 1: Ba-ion extraction and identification from high pressure Xenon gas for nEXO
Yang Lan for the nEXO collaboration
CAP2016-June 13th, 2016
TRIUMF/
Department of Physics & Astronomy
University of British Columbia
136Ba

## Slide 2: EXO 0νββ sensitivity
nEXO:
5 tons of liquid xenon
Enriched to 90%
of Xe-136
Without Ba-tagging:
With 100% Ba-tagging:
Sensitivity X 2
No ba-tagging
50% ba-tagging
100% ba-tagging
=80 ton xenon!
or, 160 years 

## Slide 3: Ba-tagging
Ba-tagging concept in xenon gas
1. Locate the event in TPC
2. Get the Ba-ion
      Ion extraction
3. Identification (tagging)
      Laser spectroscopy
      TOF Mass spectrometry
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
e-
Ionization
Scintillation
Ba?
Cathode
Gaseous TPC

## Slide 4: Ba-tagging
Stanford’s prototype
Goal: 10-6 mbar
Ba-tagging for a gaseous Xenon
  Extract Ba-ions from high pressure xenon gas (RF funnel)
  Ba-ions identification
    Linear Paul trap (TRIUMF) – laser spectroscopy (Carleton)
    MR-TOF-MS (McGill) – mass spectrometry

## Slide 5: Ion-extraction
Stanford’s prototype developed by T. Brunner and D. Fudenberg (moving to McGill)
International Journal of Mass Spectrometry 379, 110 (2015)
      Extract ions from up to 10 bar to vacuum
      Close to 100% extraction efficiency
Challenges:

## Slide 6: Ba-tagging in gas Xenon
Ion extraction from high pressure
T. Brunner et al.,IJMS 379, 110 (2015)

## Slide 7: RF-funnel
T. Brunner et al.,IJMS 379, 110 (2015)
Ion transmission efficiency
Gas dynamic calculations

## Slide 8: Linear Paul trap
Purpose
  Cool and store Ba-ions from RF-funnel
  Laser spectroscopy for Ba-ion identification
  Bunch the ions for an MR-TOF mass spectrometer
Challenges:
  Close 100% ion transmission efficiency
  Open geometry for florescence light collection

## Slide 9: Linear Paul trap design at TRIUMF
Segmented design: 3D trapping region
Filled with Helium gas (~6 Pa)
  A 90° deflector to prevent He gas back flow
SIMION simulation: ion trapping, cooling
Trapping region
RF voltage: 166 V (1.1 MHz)

## Slide 10: Laser fluorescence spectroscopy
R. Killick, MSc thesis (2015)
Initial study at Stanford (~2007), now at Carleton University
B. Flatt, et. al., Nucl. Instr. and Meth. A 578 , 399 (2007)
Light scattered from electrodes

## Slide 11
Open geometry for laser spectroscopy
25.5°
59.5°
Minimum quadrupole potential distortion:
re/r0=1.14511
re/r0=0.357

## Slide 12: Summary and outlook
Ba-tagging in gaseous xenon
  RF-funnel successfully extract ions from 10 bar xenon (Stanford, McGill)
  Linear Paul trap (TRIUMF) & MR-TOF-MS (McGill) under development
  Laser fluorescence spectroscopy successfully developed for Ba-ion identification (Stanford, Carleton)
  Combine the RF-funnel, linear Paul trap, laser spectroscopy, MR-TOF-MS
Linear Paul Trap
  Simulation of ion deflection, capture, cooling
  More simulations, optimizations
  Build the linear Paul trap, Experiments!

## Slide 13
University of Alabama, Tuscaloosa AL, USA — T Didberidze, M Hughes, A Piepke, R Tsang
University of Bern, Switzerland — J-L Vuilleumier
Brookhaven National Laboratory, Upton NY, USA — M Chiu, G De Geronimo, S Li, V Radeka, T Rao, G Smith, T Tsang, B Yu
California Institute of Technology, Pasadena CA, USA — P Vogel
Carleton University, Ottawa ON, Canada — I Badhrees, Y Baribeau, M Bowcock, M Dunford, M Facina,
R Gornea, K Graham, P Gravelle, R Killick, T Koffas, C Licciardi, K McFarlane, R Schnarr, D Sinclair
Colorado State University, Fort Collins CO, USA — C Chambers, A Craycraft, W Fairbank Jr, T Walton
Drexel University, Philadelphia PA, USA — E Callaghan, MJ Dolinski, YH Lin, E Smith, Y-R Yen
Duke University, Durham NC, USA — PS Barbeau, G Swift
University of Erlangen-Nuremberg, Erlangen, Germany — G Anton, R Bayerlein, J Hoessl, P Hufschmidt, A Jamil, T Michel, T Ziegler
IBS Center for Underground Physics, Daejeon, South Korea — DS Leonard
IHEP Beijing, People’s Republic of China — G Cao, W Cen, X Jiang, H Li, Z Ning, X Sun, T Tolba, W Wei, L Wen, W Wu, J Zhao
ITEP Moscow, Russia — V Belov, A Burenkov, A Karelin, A Kobyakin, A Kuchenkov, V Stekhanov, O Zeldovich
University of Illinois, Urbana-Champaign IL, USA — D Beck, M Coon, S Li, L Yang
Indiana University, Bloomington IN, USA — JB Albert, S Daugherty, TN Johnson, LJ Kaufman, G Visser, J Zettlemoyer
University of California, Irvine, Irvine CA, USA — M Moe
Laurentian University, Sudbury ON, Canada — B Cleveland, A Der Mesrobian-Kabakian, J Farine, U Wichoski
Lawrence Livermore National Laboratory, Livermore CA, USA — O Alford, J Brodsky,
M Heffner, G Holtmeier, A House, M Johnson, S Sangiorgio
University of Massachusetts, Amherst MA, USA —S Feyzbakhsh, S Johnston, M Negus, A Pocar
McGill University, Montreal QC, Canada — T Brunner , K Murray
Oak Ridge National Laboratory, Oak Ridge TN, USA — L Fabris, D Hornback, RJ Newby, K Ziock
Pacific Northwest National Laboratory, Richland, WA, USA — EW Hoppe, JL Orrell
Rensselaer Polytechnic Institute, Troy NY, USA — E Brown, K Odgers
Université de Sherbrooke — S Charlebois, D Danovitch, R Fontaine, JF Pratte, J Sylvestre, F Bourque, T Rossignol, S Parent, M Côté, F Vachon, F Nolet, H Dautet
SLAC National Accelerator Laboratory, Menlo Park CA, USA — J Dalmasson, T Daniels, S Delaquis,
G Haller, R Herbst, M Kwiatkowski, A Odian, M Oriunno, B Mong, PC Rowson, K Skarpaas
University of South Dakota, Vermillion SD, USA — J Daughhetee, R MacLellan
Stanford University, Stanford CA, USA — R DeVoe, D Fudenberg, G Gratta, M Jewell, S Kravitz,
D Moore, I Ostrovskiy, A Schubert, M Weber
Stony Brook University, SUNY, Stony Brook, NY, USA — K Kumar, O Njoya, M Tarka
Technical University of Munich, Garching, Germany — P Fierlinger, M Marino
TRIUMF, Vancouver BC, Canada — J Dilling, P Gumplinger, R Krücken, Y Lan, F Retière, V Strickland
The nEXO Collaboration

## Slide 14
Backup slides

## Slide 15: EXO-200
EXO-200 progresses
  2011 May: Started collecting data
  2011 August: first measurement of 2νββ in 136Xe:
    Phys. Rev. Lett. 109, 032505 (2011)
    Agrees with KamLAND-Zen soon after:
  Phys. Rev. C 85, 045504 (2012)
  2014 set lower limit on 0νββ in 136Xe:
  T1/2 2νββ =2.11 ± 0.04(stat) ± 0.21(syst) ×1021 yr
  T1/2 2νββ =2.38±0.02(stat)±0.14(syst) ×1021 yr
  T1/2 0νββ > 1.1×1025 yr @ 90% confidence level
Nature 510, 229 (2014)

## Slide 16: Enriched Xenon Observatory (EXO)
EXO-200 Status
  Started collecting data in 2011
  Still running
Single-site events
Multi-site events
Q=2457.83±0.37 keV
Nature 510, 229 (2014)

## Slide 17: Ba-tagging
Ba-tagging for liquid Xenon
  Colorado State U.:
    Cold probe
    Freeze Ba-ion to the probe
    Laser induced florescence
      Move the probe out of TPC
      Florescence detection in situ
  Stanford U.:
    Transport Ba-ion out of TPC
    Resonance Ionization Spectroscopy
      Selectively ionize Ba
      Identification by ion’s time-of-filght (TOF)
nEXO, P.R.A 91, 022505 (2015)
nEXO, Rev. Sci. Instrum 85, 095114 (2014)

## Slide 18
Ion extraction from SPIG: a ∅2-mm aperture
-5 V
-30 V
-100 V
Transmission efficiency: ~98% in SIMION simulation
Focusing electric potential

## Slide 19
90° deflector between SPIG and linear Paul trap
  Purpose:
    Prevent He gas back flow
    Additional ions sources & ion counts measurements
  SIMION simulations:
    4-way quadruple deflector Cylindrical mirror analyzer
Second ion source
Second ion source

## Slide 20
90° deflector : SIMION simulations
Ion detector
Ion detector
Ion loss

## Slide 21: Linear Paul trap
Ion stability region in pure quadrupole potentials
  Equation of motion
  Mathieu equation
Todd, John F. J. Quadrupole storage mass spectrometry.

## Slide 22: Quadrupole electrodes
Hyperbolic
Circular
Blade
Modified blade
K. Deng et al., J. Appl. Phys. 118, 113106 (2015)

## Slide 23: Optimized blade-like electrodes
J. Appl. Phys. 118, 113106 (2015)