## Slide 1
SuperCDMS and CUTE at SNOLAB
Wolfgang Rau
Queen’s University
for the
SuperCDMS Collaboration

## Slide 2
SuperCDMS Collaboration
California Institute of Technology CNRS/LPN Durham University
Fermi National Accelerator Laboratory NISER NIST Northwestern University
PNNL Queen’s University Santa Clara University SLAC/KIPA
South Dakota School of Mines & Technology Southern Methodist University
Stanford University Texas A&M University of British Columbia
University of California, Berkeley University of Colorado Denver
University of Evansville University of Florida
University of Minnesota University of South Dakota University of Toronto

## Slide 3
Overview
SuperCDMS Detectors Readout and DAQ Experimental Setup Goals
CUTE Motivation Design Status
Project Status Funding Review Process Schedule Development
Conclusions

## Slide 4
SuperCDMS
Ge / Si
100 mm  x 33 mm
Operated at 30 mK
iZIP
HV
Phonon Readout:
Tungsten TES
R vs T
Add: charge readout (few V)
Background discrimination
Threshold < 1 keV
Add: high voltage (~100 V)
Phonons from drifting charges
Threshold < 0.1 keV (phonon)
+
0
–
0
+ 50 V
– 50 V
remove surface
background
–
+
large phonon signal from
charges
Phonon signal
Charge signal
Nuclear recoils:
signal
Electron recoils: background
< 1 background event for whole exposure
effective threshold: one (or few) electron-hole pairs
Detectors

## Slide 5
SuperCDMS
DAQ
Lead institution: UBC, with assistance from Toronto, the TRIUMF DAQ group, and several US institutions
Goal: design a deadtime-free DAQ system for new SuperCDMS electronics, including:
Optimal filtering of noise in trigger
Integrated data quality system
Integrated environmental monitoring
Fully usable and tested at SuperCDMS test facilities (Queen’s, CUTE, SLAC, UMN, Berkeley)
Built on MIDAS DAQ system
New prototype SNOLAB readout card, and noise measurements from prototype DAQ (May 2016)

## Slide 6
SuperCDMS
6 detectors  1 tower
Inner neutron shield (PE)
Fridge to provide <15 mK at the detector
Mounted on spring- loaded platform (earthquake)
Gamma shield (Pb)
Signal vacuum feedthroughs
1 HV tower (4 Ge/2Si)
3 Ge iZIP towers
1 Si iZIP tower
Outer
neutron shield
(PE and water)
Setup
(space for up to 31 towers)

## Slide 7
SuperCDMS
DAQ
Radon filter
Clean room
Cryo
Cryogenics and radon filter plant
Experimental area
Access drift
CUTE
SNOLAB

## Slide 8
SuperCDMS
DAMA
DAMA
CDMS Si
LUX 2013
DEAP
CDMS II 2015
DAMIC 2012
SuperCDMS LT 2014
CRESST
2015
CDMSlite
2015
Solar Neutrinos
Atmospheric Neutrinos
Si HV
Si iZIP
Ge HV
Ge iZIP
LZ
Goal

## Slide 9
Project Status
Funding approved (CFI: 2012, DOE/NSF: 2014)
DOE/NSF review process: First step passed (CD 1: conceptual design review) Next step in spring 2017: technical design review (CD 2)
Reviews at SNOLAB: passed Gateway 1 (space allocation) in fall 2015; GW2 (begin of construction) in December 2016
Total project costs ~$30M
2013
2014
2015
2016
2017
2018
2019
CFI application
GW 1
GW 2
CFI approved
US G2 decision
DOE/NSF proposals
CD 1
CAP 16 Ottawa
CD 2
CD 3
CD 4
Start of operation
Main construction phase
Schedule and Funding

## Slide 10
Project Status
Detectors: larger crystals; iZIP: design ready, prototypes exist and have been tested; HV detectors: close to final design, first test anticipated later this year
Detector tower (mechanical structure, wiring): design ready, mechanical prototype exists; some delay for wiring prototype; first thermal tests later this year
Readout electronics: Preamp: thermal readout design ready; charge readout: circuits are being tested “Warm electronics” (outside cryostat): prototype exists, tests underway
DAQ: MIDAS based, being developed at UBC with help from TRIUMF (version for detector test facilities already in use)
Cryogenics and shielding: design advanced, but not ready yet Procurement of dilution refrigerator under way
Backgrounds: devised extensive material screening program; tracking and monitoring program being developed; radon filter to be installed for detector assembly cleanroom at SNOLAB.
Development

## Slide 11
CUTE
Cryogenic Underground TEst facility (CUTE)
 Xiaohe Zhang, PPD Poster #88 (19:02)
Motivation
Detector performance: Detector integrity after transportation Background discrimination Noise performance (impact of background)
Background studies Confirm that screening program and handling procedures are appropriate Study cosmogenic backgrounds (3H, 32Si)
Test EURECA detectors in a SuperCDMS environment (possibly join forces)
Schedule
Cryostat design ready; order imminent
Infrastructure (water tank, cleanroom, services): in 2016
Feb 2017: test at Queen’s; late spring installation underground
Commissioning: early summer 2017 (~2-3 years ahead of SuperCDMS)
Water Shield
Fridge: <10 mK
Vibration damping
Cleanroom
Pb

## Slide 12
Conclusions
SuperCDMS SNOLAB aims at detecting dark matter WIMPs
Main focus are low-mass WIMPs (< 10 GeV/c2)
Project planning well under way
Main R&D is done, full technical design expected for spring 2017
Start of operation expected in 2020
Upgrades (improved HV detectors, EURECA detectors, …) will allow us to reach the neutrino floor at low mass and/or check discovery claims at high mass
CUTE: Queen’s initiative for an underground test facility, operational in about a year  See poster: Xiaohe Zhang, 1307 (19:02).