## Slide 1
The Ultra-Cold Neutron Facility
at TRIUMF
Overview and Construction Status
L.Lee (Jun.15, 2016)
2016 CAP Annual Congress
T. Adachi1, E. Altiere2, T. Andalib3,4, C. Bidinosti3, J. Birchall4, C. Davis5,
M. Gericke4, S. Hansen-Romu3,4, K. Hatanaka6, B. Jamieson3, S. Jeong1, D. Jones2,
K. Katsika5, S. Kawasaki1, T Kikawa5,6,1, A. Konaka5,8, E. Korkmaz7 , M. Lang3, T. Lindner5,
L. Lee4,5, K. Madison2, J. Mammei4, R. Mammei3, J.W. Martin3, R. Matsumiya6, E. Miller2,
T. Momose2, S. Page4, R. Picker5, E. Pierre6,5, W.D. Ramsay5, L. Rebenitsch3,4, J. Sonier9,
I. Tanihata6, W.T.H. van Oers4,5, Y. Watanabe1, and J. Weinands2
1KEK, Tsukuba, Ibaraki, Japan
2The University of British Columbia, Vancouver, BC, Canada
3The University of Winnipeg, Winnipeg, MB, Canada
4The University of Manitoba, Winnipeg, MB, Canada
5TRIUMF, Vancouver, BC, Canada
6RCNP, Osaka, Japan (Osaka University, Osaka, Japan)
7The University of Northern BC, Prince George, BC, Canada
8Osaka University, Osaka, Japan
9Simon Fraser University, Burnaby, BC, Canada

## Slide 2
UCN ENERGY MANIPULATION
UCN TRANSPORT
2
Properties of UltraCold Neutrons
2
Can be stored & manipulated using:
UCN constrained to h < 3 m
3m
g
UCN POLARIZATION
polarizing magnet
source
 experiment
UCN guide
Strong interaction
(Fermi potential, total reflection from walls)
Gravitation
(100 neV 1 m)
Material
wall
low-field seeker
high-field seeker
Magnetic interaction
(force on magnetic moment)
Localize & Use in Experiments

## Slide 3
3
UCNs for Fundamental Physics
3
Fundmental Symmetries
Neutron oscillations (
  DB=2 Baryon Number Violation, BAU
Neutron EM properties
  High precision test of SM, Search for BSM physics
Neutron Electric Dipole Moment
  New sources of CP violation
  Baryon asymmetry (BAU)
  Many BSM formulations have new sources of CP violation  measured bound on nEDM seriously constrain these models
  nEDM efforts at: PSI, Munich, RCNP/TRIUMF, SNS (precession of spin-polarized neutrons in )
Experimental limit today:
Goals for next experiments:
[ Baker, et al. Phys Rev Lett 97 (13), 2006 ]
See talk by J.W.Martin, Thur @ 13:15, R2-3

## Slide 4
Spallation-driven Superfluid He-II UCN Source
10 K D2O or D2
He-II
300 K D2O
Graphite
W-Target
Spallation – Liberate neutrons from W target
Moderation – Thermalize, cool neutrons in D20 ice
Conversion – Convert cold neutrons to UCN in He-II
44 cm
30 cm
Moderators
Thermal: Graphite, 300K D2O
Cold: 10K D2O ice
d
75 cm
400 MeV protons
MeV neutrons
Thermal, Cold &
Ultra-Cold neutrons
General Layout of UCN Source at RCNP Osaka
Cold neutron energy transferred to He-II via phonon emission
UCN production recipe:
10K D2O Ice Cryostat (Cold Neutrons)
0.7K He-II Cryostat (Ultra-Cold Neutrons)
UCN Source
Cryostats
D2O Cryostat
He-II
Cryostat

## Slide 5
Japan-Canada UCN Project
at TRIUMF
Proton-driven Spallation Superthermal UCN Source
CFI $4.2 M awarded in 2009 (Total $12 M)
MOU (KEK, RCNP, TRIUMF, U.Winnipeg) in 2011
Construction of 1st beamline component in 2012 (KEK)
First installation period in 2014 (Meson Hall)
May ’16: UCN Beamline & Source Front-end installed

## Slide 6
UCN’s at TRIUMF
6
Meson Hall

## Slide 7
BL1U: UCN Beamline
BL1U
Floorspace
for nEDM
Experiment
BL1A
BL1V: 500 MeV, 120 mA Beam
Beam Microstructure
Cyclotron
Kicker Magnet
kicks every 3rd beam bunch
Lambertson Septum
bends kicked beam 9 into 1U
unkicked beam to BL1A

## Slide 8
BL1U: UCN Beamline
BL1U
Floorspace
for nEDM
Experiment
BL1A
BL1V: 500 MeV, 120 mA Beam
Beam Microstructure
BL1U: 500 MeV, 40 mA protons, Tungsten target
1 min 3 min
BL1A
BL1U
Cyclotron
Kicker Magnet
kicks every 3rd beam bunch
Lambertson Septum
bends kicked beam 9 into 1U
unkicked beam to BL1A

## Slide 9
BL1U: UCN Beamline
BL1U
BL1A
BL1U: 500 MeV, 40 mA protons, Tungsten target
Dipole Magnet
Bends beam 7 onto target
Quad Doublet
Set beam size at target
Tungsten Spallation Target
12 cm, Ta-cladded, water cooled, power: 20 kW (peak), 5 kW (avg)
D2O Cryostat
10K D2O ice
Cold Neutrons
3He/He-II Cryostat
0.7K 3He, 0.8K He-II
Ultra-Cold Neutrons
SC Polarizer
UCN guide to experiments
Shielding Pyramid

## Slide 10
UCN Facility Installation Timeframes
Kicker
Septum
Dipole
Quads
Target
UCN
Source
Floorspace
for nEDM
Experiment
BL1U
BL1A
2014
Septum
Dipole & Girder
Shielding Plug
U/S section
Vault section
2015
Vault Components
M13 Decommission
Quads & D/S section
Shield Pyramid Base
UCN Source in 2016-17
D2O cryostat (cold moderator)
He-II cryostat
Kicker in 2016
Pyramid base
Target in 2016
D/S section

## Slide 11
UCN Facility 2016 Installation
Kicker
Septum
Dipole
Quads
Target
UCN
Source
Floorspace
for nEDM
Experiment
BL1U
BL1A
Water-cooled Target
& R/H Rail System
2016
Kicker Magnet
Target Crypt
Target & Rail System
UCN Source Front-end (CN)
Shield Pyramid
Target Crypt
Kicker Magnet
D2O Cryostat
(UCN Source
Front-end)

## Slide 12
BL1U Downstream & UCN Source Front-End
12
D2O Cryostat
BL1U
Downstream
Target R/H system
May 12/2016
After closing up
UCN Beamline Installed (Kicker Target)
Source Front-End Installed (D2O Moderator)

## Slide 13
1 2 3 4
1 2 3 4
1 2 3 4
1 2 3 4
1
2015
2016
2017
2018
UCN
EDM
@RCNP
@TRIUMF
@RCNP
@TRIUMF
Calendar year
quarter
UCN development
move D2O
to TRIUMF
Source install/commission
Beamline,target,shielding install
EDM
install
EDM development
LD2 upgrade
move to TRIUMF
EDM Phase 2
EDM R&D for Phase 2
EDM Phase 1
move He-II
to TRIUMF
Safety upgrades
UCN and nEDM Timeline
13
Milestones: Proton Beamline (BL1U) & CN Source installed

## Slide 14
nEDM Phase 2 Strategy
Room temperature experiment
  Enables more rapid development
Planned improvements
  higher UCN density with LD2 moderator
  2 cells, probably “horizontal” loading
  dual Xe/Hg comagnetometer
  improved magnetic environment
  simultaneous counting of both polarizations
Ongoing extensive R&D program
  magnetics
  UCN detector
  comagnetometer
  HV/EDM cell
  Simulations
Keep layout as flexible as possible
  to take advantage of R & D outcomes
protons
moderator
cryostat
He-II volume
SC polarizer
4 UCN detectors
spin flipper/
analyzer
UCN switch
inner passive shielding
EDM cell(s)
A possible topology
2.5 m
magnetically shielded room
spallation target
HV feed
Sensitivity goal: dn < 10-27 e·cm

## Slide 15
Summary
UCN Facility
Proton beamline, Target, & CN Source installed on schedule
He-II Superfluid Cryostat to arrive at TRIUMF in Summer 2016
Control Hardware & Software in progress
Commission BL1U, CN and UCN source in 2016-17
  CN Source Commissioning Tests  T.Kikawa talk (next talk)
nEDM Experiment (Phase-I and Phase-II)
  Talk by J.W.Martin, Thursday at 13:15, R2-3 (Fundamental Sym. II)

## Slide 16
UCN Facility, nEDM & 2nd Experiment Port
N
UCN source
Spallation target
& moderators
UCN Beamline
2nd port
3m x 3m
Second experiment port
Short term:
detector and guide development
Long term:
real user facility
Gravity: Q-Bounce
Lifetime: PENeLOPE
Neutron decay: UCNA
Neutron charge
(TRIGA Mainz)
EDM space
6m x 9m
EDM cell & magnetic shielding
laser lab
4.5m x 5m
Laser lab for nEDM

## Slide 17
FINIS

## Slide 18
2011
2015
2014
2013
2012
2016
2017
ACTIVITY
J A J O
J A J O
J A J O
J A J O
J A J O
J A J O
J A
Schedule( 2010-2016 )
2012
2016
2015
2014
2013
2017
2018
Cleanup M11,1A/1B roof-beam
Dismantle PIENU & M13-DS
MESON HALL (& Vault):
Core M13 I-block
UCN APPARATUS:
Spallation Target & R/H
UCN Source (D2O Cryostat)
BEAMLINE 1U:
Kicker
Septum
Dipole
Beamline (incl Quads, PS,…)
Design & Review
Assy
Fab/Assy
Procure
Design & Review
Design & Review
Fabricate
Inst.
Fabricate
Specify/Conceptual design
COMMISSION @ TRIUMF
BL1U & Source Commissioning
HELIUM LIQUEFIER:
Upgrade He Liquefier System
He Liquefier System
Install/Test/Run @ RCNP
Procure/Install
Kicker Stand & Beamtube
Design/Order
Fabr
MILESTONES
Shutdown Activities
Activities Elsewhere
(KEK, RCNP, CERN, Acsion)
Non-Shutdown Activities
Mod. 1VQ5; Mod. Shield-Plug
Inst.
Dismantle M13-US, Mod.Shld
Design/Order/Fabricate
Inst.
Inst.
Design/Fabr
Shielding
Design/Procure
Design & Review
Procure
Inst.
Inst.
Inst.
- He-II Cryostat to TRIUMF
UCN Schedule Overview & He-II Cryostat
Install/Test/Run @ RCNP
Prep
Procure/Install
p/CN/UCN
UCN
Inst.
Procure
Mod/Test/Move
Order/Fabricate/Deliver
Schedule: Source Installation
 Regular Shutdown (4 m)
Install D2O cryo during S/D
 Post-Shutdown (4 m)
Commission beamline, CN
 Mini-Shutdown (Sep’16)
Vacuum D2O to He-II
Install He-II cryo (not S/D)
Delivery of
He-II cryostat


## Slide 19
19
Definition of Ultra Cold Neutrons
19
Neutron Classification
Neutron Kinetic Energy Temperature Velocity Wavelength
Relativistic > 1 GeV 1013 K 0.875 c 1 fm
Fast > 1 MeV 1010 K 0.046 c 30 fm
Thermal  25 meV 300 K 2 km/s 0.2 nm
Cold < 3 meV < 35 K 760 m/s 0.5 nm
Very Cold (VCN) 0.01 – 0.8 meV 1.5 K 150 m/s 1 – 10 nm
Ultra Cold (UCN) < 300 neV < 3 mK < 8 m/s > 50 nm
UCNs:

## Slide 20
20
Strong Interaction and UCNs
20
Long Wavelengths l UCN >> Rnuclear
(only S-wave scattering from nuclei)
Characterized by scattering length,
Fermi eff. Potential:
gives correct scatt. amplitude at large
Fermi Potential for materials
Material V acoh floss=W/V
[neV] [x10-13 cm] [x10-5 ]
--------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------------
Ni58 335 14.4 8.6
BeO 261 13.6 1.35
Ni 252 10.6 12.5
Be 252 7.75 0.5(300K)
0.08(100K)
DLC 220-270
NiMo(85-15) 227
Fe 210 9.7 8.5
S.S. 183
C 180 6.6 0.6
Cu 170 7.6 15.5
Teflon 123 17.6
Al 54 3.45 2.25
PE (CH2)n -8.7 -0.84
H2O -14.7 -1.68
Coherent scattering from a collection of nuclei
Step-function pseudo (Fermi) potential
x
V
En < V will be reflected
(Reflection Losses from: absorption, inelastic upscattering  )
Coated materials (pipes, bottles) to transport & store UCNs
Effective Int.n
with any
given material

## Slide 21
21
UCNs for Fundamental Physics
21
UCN key features: (a)“Readily” stored with interaction times  tn ; (b) Can be spin-polarized.
Lifetime: PENeLOPE
Neutron decay: UCNA
Neutron b decay
Studies:
  CKM unitarity (Vud)
  Weak Couplings: l(gA/gV), gS, gT
  BSM, right-handed couplings (V-A vs V+A)
  He/H ratios in early universe, BBN uncertainties (in tn)
Neutron Lifetime tn
  New initiatives: Makes use of magnetic, magneto-gravitational traps (PENeLOPE, UCNt)
Neutron b decay angular corr.n
  A coeff. (UCNA)
)

## Slide 22
22
UCNs for Fundamental Physics
22
UCN as quantum bouncing balls
Gravity Tests with UCNs
Studies of:
  Gravitational quantum levels
  Extra dimensions (mm scale)
  Neutron constraints on new forces (strength, range) & dark matter candidates, axion models
  Neutron mass
Q-Bounce, GRANIT
  UCN mirror below and absorber (or scatterer) above
  Quantized gravitational levels observed
  Transitions induced (vibrating mirrors, magnetic fields)
Count rate s-1
Absorber height (mm)
Classical
expectation
data +
quantum fit
Strength & Range of new Forces
Dubbers and Schmidt, arXiv:1105.3694 (2011)
Gravity: Q-Bounce
Limits on axion-like
particles