## Slide 1: DEAP-3600 Dark Matter Search at SNOLAB
Mark Boulay
Carleton University
Queen’s University
@

## Slide 2
DEAP-3600 Dark Matter Search
Liquid Argon for DM (Single-phase)
Scattered nucleus detected via scintillation in LAr
Good Pulse-shape discrimination between
b/g and nuclear recoils with scintillation
Argon is easy to purify
Very large target masses possible, no
absorption of UV scintillation photons
in argon, no pileup until beyond tonne-scale
Position reconstruction allows surface background removal, based on photon detection (~5 cm resolution allows removal
of radon daughter events from analysis)
DM Sensitivity
1 tonne fiducial mass (3.6 tonnes total) designed for < 0.2 background events/year with 60 keVr
threshold
c
40Ar
40Ar
c

## Slide 3
3600 kg argon
in sealed ultraclean
Acrylic Vessel (1.7 m ID)
Vessel is “resurfaced”
in-situ to remove
deposited Rn daughters
after construction
255 Hamamatsu
R5912 HQE PMTs 8-inch
(32% QE)
50 cm light guides +
PE shielding provide neutron moderation
Steel Shell immersed in 8 m water shield at SNOLAB
DEAP-3600 Detector
3.5 meters
v. high coverage of
light-sensors, 80%
strict radiopurity
control

## Slide 4
DEAP Collaboration: 65 researchers in Canada, UK, and Mexico

## Slide 5: Fabrication and Assay of DEAP Acrylic
Fabrication from pure MMA monomer at RPTAsia (Thailand), strict control of radon exposure for all steps, to < 10-20 g/g 210Pb (RPT was fabricator of the SNO Acrylic Vessel)
Assay of production acrylic < 2.2x10-19 g/g 210Pb
(Corina Nantais M.Sc. Thesis 2014, <0.2 bkg events/3 years)
Thermoformed Panel at RPT Colorado
Monomer cast at RPT Asia, 2010

## Slide 6
DEAP Acrylic Vessel, Panel Sections at Reynolds Polymer, Colorado

## Slide 7
DEAP Acrylic Vessel with Light Guide “Stubs” July 2012, U Alberta

## Slide 10
AV neck bonding underground (December 2012-January 2013)

## Slide 11
Bonding light guides to the DEAP AV, underground at SNOLAB

## Slide 12
DEAP Acrylic Vessel (2013)

## Slide 13
Moving the AV into assembly room

## Slide 14: DEAP-3600 Detector Assembly
Acrylic Light Guide
PE neutron
shielding “blocks”
PMT with
silicone oil
coupling
Copper sleeve over PMT
Specular reflector + opaque wrap
2,500 person-weeks of assembly
(students, faculty, PDFs, technicians,
engineers)

## Slide 16
Acrylic Vessel Resurfacer
Mechanical sander to clean inner surface
Components selected for low radon emanation
Remove 0.5-mm surface in situ with N2 purge
Cleans surface to bulk-level impurities
(order 100,000 cleaner than SNO vessel)

## Slide 17
Completed Detector and Shield Tank
Completed Detector: Steel Shell, calibration tubes, muon veto in Shield Tank (fall 2015)
Shield Tank and emergency vent lines,
tank was filled with water Oct 2015

## Slide 18
Detector event rate during shield tank water fill
2 feet
7 feet
16 feet
Tank Full
(Filled October 2015)

## Slide 19
Electronics and trigger system operational
for over a year (CAEN v1720s)
Commissioning, electronics calibration
Optical calibration with internal fibers
(AARFs) and deployed diffusing laserball
source

## Slide 20
In-situ calibration of relative PMT efficiencies
(Diffusing laserball source at center)
Internal fiber system (20 fibers into light guides)
~2% relative efficiency calibration

## Slide 21: A high energy event (Commissioning running, Spring 2015)
Run: 9406 Subrun: 3 Event: 300460
High-E event rate: ~1 event/day
Expected muon rate: 1.6 muons/day
preliminary

## Slide 22
Identify alpha events from scintillation in TPB

## Slide 23
PRELIMINARY – NOT FOR DISTRIBUTION!

## Slide 24
DEAP-3600 Cryogenic Systems

## Slide 25
DEAP-3600 Cryocooler System Installed May 2012
3500 L LN2 dewar allows 4-day “buffer”
in cooling system
3 x 1.2 kW @ 77 K
to DEAP

## Slide 26
Bulk LAr storage on surface
2x240L
(transfer)
LN2-cooled storage dewar
underground
Liquid Argon Target Transfer and Storage
Transferring underground started March 3, 2015
From RGA scans (before purification in the DEAP system):
CH4 < 10 ppb, H2O < 10 ppb, N2 < 4 ppb, O2 < 6 ppb
(<100 ppt after purification)

## Slide 27
Argon Purification
Target stored as liquid,
boiled and purified
in gas phase,
then (re-)liquefied into AV
(Gettering, radon
and
particulate filtration)
AV cooldown started
Feb 2016

## Slide 30
DEAP-3600 Analysis Groups
Working group leader | Institution | Group
Marcin Kuzniak | Carleton | Analysis Coordinator
James Bueno | Alberta | Gamma/other backgrounds
Berta Beltran | Alberta | Position reconstruction
Chris Ouellet | Carleton | Global backgrounds, Run Selection
Chris Jillings | Laurentian | PMTs
Rashid Medyev | Carleton | Efficiency/optical calibration
Tina Pollmann | Laurentian | PSD
Ben Smith | TRIUMF | Low-level calibration (electronics)
Joe Walding | RHUL | Neutron calibration
Nasim Fatemighomi | RHUL | Energy response
Eric Vazquez Jauregui | UNAM | Neutron backgrounds
Working group structure, additional students/scientists contribute to various
working groups, require additional effort on reconstruction, mu-veto calibration,
surface backgrounds, optical calibration

## Slide 31: Summary
DEAP-3600: 3.6 tonnes of liquid argon (1 tonne fiducial)
>20X improvement in experimental sensitivity, excellent high WIMP mass sensitivity
(similar sensitivity to XENON-1T for high WIMP mass)
Collecting data in commissioning phase since early 2015, detector calibration and analysis well advanced
Start of detector cooldown Feb 2016, start of liquid filling June 11, 2016
Expecting first physics data summer 2016

## Slide 32: END