## Slide 1: Detection of radiation induced changes in human lens epithelial cells using Raman spectroscopy
Harry Allen

## Slide 2: Acknowledgements
Dr. Sangeeta Murugkar
Dr. Vinita Chauhan
Dr. Balazs Nyiri
Achint Kumar
Abrar Ahmad
Hamid Moradi
Chris Dedek
Thank you!
Carleton Biophotonics Research Group

## Slide 3: Outline
Rationale
Objectives
Raman Scattering
Raman Spectroscopy
Procedure
Analysis Techniques
Results
Conclusions

## Slide 4: Rationale
Lens is radiosensitive
IR induces cataracts
Threshold dose was thought to be 2 Gy for detectable opacities
Recent epidemiological studies suggest 1 Gy threshold for low LET IR.
ICRP currently suggests a nominal threshold of 0.5 Gy
Increase in reported injuries due to new diagnostic procedures such as fluoroscopy
Need for sensitive assays capable of detecting minute biological changes due to low dose IR exposure
http://www.aao.org

## Slide 5: Human Lens Epithelial Cells
HLE Cells maintain homeostasis of the lens
Differentiate into lens fiber cells
http://www.abc.net.au/science/drkarl/img/4253961/lens.jpg

## Slide 6: Objectives
Determine whether IR induced changes in Raman spectra of HLE cells are detectable over a range of doses
Analyse those differences, if present, to determine which biomolecules are changing in concentration
Determine whether we can discriminate between Raman spectra by dose using multivariate statistical techniques
Doses investigated:
0.01 Gy
0.05 Gy
0.25 Gy
0.5 Gy
2 Gy
5 Gy
Low dose range

## Slide 7: Raman Scattering
Inelastic scattering of light
Photon either loses (Stokes) or gains (anti-Stokes) energy
Molecule reciprocally gains or loses the same amount in vibrational energy
The difference in energy gives a “Raman Shift” wavenumber
http://www.hamamatsu.com
The probability of a spontaneous Stokes Raman scatter is ~10-7

## Slide 8: Raman Scattering
Quantum nature of a molecule limits its allowed vibrational frequencies to a discrete set characteristic of that molecule
Raman shift wavenumbers are thus characteristic of the scattering molecule
Raman scattering thus generates a “fingerprint” spectrum which can be analysed
https://en.wikipedia.org/wiki/Raman_spectroscopy

## Slide 9: Raman Scattering
Quantum nature of a molecule limits its allowed vibrational frequencies to a discrete set characteristic of that molecule
Raman shift wavenumbers are thus characteristic of the scattering molecule
Raman scattering thus generates a “fingerprint” spectrum which can be analysed

## Slide 10: Confocal Raman Microspectroscopy
http://microscopy.duke.edu/learn/introtomicroscopy/confocals.html
8 Pinhole lens Pinhole
3
Long-pass Dichroic
Sample
Raman scattered light transmitted
Rayleigh scattered light reflected

## Slide 11: Procedure
How the data was acquired

## Slide 12: Procedure
HLE cells grown
Irradiated
X-Rays
24 hour
Incubation
period
7 Quartz coverslips
Cells Fixed
Raman Spectra Collected
Averaging + BG subtraction

## Slide 13: Procedure
Raman spectra recorded using the CRM, with a 785 nm laser and a 60x immersion objective
Sample coverslips with adhered cells immersed in Phosphate-buffered saline (PBS) solution
20 nucleus and 20 cytoplasm measurements taken per slip
Each measurement is the average of 9 one minute spot measurements over a 3x3 grid

## Slide 14: Processing Spectra
After spectrum-based method for iterative removal of fluorescence (SMIRF)

## Slide 15: Data Analysis Techniques
Once we have our data, we need to analyze it
Spectral differences can be seen visually by simply plotting the mean spectra of different doses together
We also take the ratio of the area under a peak for a dose to that of the control to see how peak sizes change with respect to dose
For our classification objectives, we need to test how well we can separate measurements from the 6 doses plus control (0 Gy)
We are currently using Principal Component Analysis and Linear Discriminant Analysis to do this

## Slide 16: Principal Component Analysis
Spectra have 1024 wavenumbers with a lot of correlation
PCA gives uncorrelated variables by finding the eigenvectors of the covariance matrix
Choose first N PCs, accounting for most (>95%) of the variance
Data dimensionality reduced from 1024 to less than number of measurements per dose
PC1
PC2

## Slide 17: Linear Discriminant Analysis
Wish to discriminate between N classes (doses) in data
Multiclass LDA projects data onto an N-1 hyperplane, maximizing between class variance and minimizing within class variance
A distance metric is then used to determine which class mean a data point being tested is closest to in the transformed space

## Slide 18: Results
Comparing mean spectra for different doses

## Slide 19: Results: Nucleus Spectra

## Slide 20: Results: Nucleus Spectra

## Slide 21: Results: Nucleus Spectra

## Slide 22: Results: Nucleus Spectra

## Slide 23: Results: Nucleus Spectra

## Slide 24: Results: Nucleus Spectra

## Slide 25: Results: Nucleus Spectra

## Slide 26: Results: Cytoplasm Spectra

## Slide 27: Results: Cytoplasm Spectra

## Slide 28: Results: Cytoplasm Spectra

## Slide 29: Results: Cytoplasm Spectra

## Slide 30: Results: Cytoplasm Spectra

## Slide 31: Results: Cytoplasm Spectra

## Slide 32: Results
Dose discrimination using PCA-LDA

## Slide 33: Results: PCA-LDA
Data for nucleus, cytoplasm analyzed separately as well as combined
For each analysis, data is randomly partitioned into ~25% test set and ~75% training set
Training set is used to find linear discriminants for classification
100 different partitions tested and an average accuracy with error is found

## Slide 34: Results: PCA-LDA of Nucleus Spectra
Average test set accuracy: (92 ± 3)%
469 nuclei measurements
50 PCs
 | 0 Gy | .01 Gy | .05 Gy | .25 Gy | .5 Gy | 2 Gy | 5 Gy
0 Gy | 16 | 0 | 0 | 0 | 0 | 0 | 0
.01 Gy | 0 | 16 | 0 | 0 | 0 | 0 | 0
.05 Gy | 1 | 0 | 14 | 0 | 0 | 1 | 0
.25 Gy | 0 | 0 | 0 | 14 | 0 | 1 | 1
.50 Gy | 0 | 0 | 0 | 0 | 12 | 1 | 3
2 Gy | 0 | 0 | 0 | 1 | 0 | 15 | 0
5 Gy | 0 | 0 | 0 | 0 | 0 | 0 | 16
Actual Dose
Predicted Dose
Table 1: Nucleus Test Data Confusion Matrix

## Slide 35: Results: PCA-LDA of Cytoplasm Spectra
259 cytoplasm measurements
30 PCs
Average test set accuracy: (90 ± 2)%
 | 0 Gy | .01 Gy | .05 Gy | .25 Gy | .5 Gy | 2 Gy | 5 Gy
0 Gy | 8 | 0 | 0 | 1 | 0 | 0 | 0
.01 Gy | 0 | 8 | 1 | 0 | 0 | 0 | 0
.05 Gy | 0 | 0 | 7 | 0 | 0 | 1 | 1
.25 Gy | 0 | 0 | 0 | 9 | 0 | 0 | 0
.50 Gy | 0 | 0 | 0 | 0 | 8 | 0 | 1
2 Gy | 0 | 0 | 0 | 0 | 0 | 9 | 0
5 Gy | 0 | 0 | 0 | 0 | 0 | 1 | 8
Actual Dose
Predicted Dose
Table 2: Cytoplasm Test Data Confusion Matrix

## Slide 36: Results: PCA-LDA of all Spectra
742 combined measurements
70 PCs
Average test set accuracy: (94 ± 2)%
 | 0 Gy | .01 Gy | .05 Gy | .25 Gy | .5 Gy | 2 Gy | 5 Gy
0 Gy | 26 | 0 | 0 | 0 | 0 | 0 | 0
.01 Gy | 0 | 25 | 0 | 0 | 0 | 0 | 1
.05 Gy | 0 | 0 | 25 | 0 | 0 | 0 | 1
.25 Gy | 0 | 0 | 0 | 22 | 0 | 3 | 1
.50 Gy | 0 | 0 | 0 | 0 | 22 | 2 | 2
2 Gy | 0 | 0 | 0 | 0 | 0 | 26 | 0
5 Gy | 1 | 0 | 0 | 0 | 0 | 0 | 25
Actual Dose
Predicted Dose
Table 3: Combined Test Data Confusion Matrix

## Slide 37: Summary
Spectral Differences in Raman spectra of HLE cells are visible
We can identify bands that show the largest changes, such as proteins, lipids, DNA and glutathione
Greater than 90% accuracy can be obtained using a 25% test, 75% train model of our data
Combining nucleus and cytoplasm data increases classification accuracy
Thank you for your time!