## Slide 1: Precision antihydrogen gravity Magnetic trap design in ALPHA-g
CAP 2018, 6-11-2018
Dr. Chukman So / TRIUMF

## Slide 2: Antimatter gravity
Test of fundamental physics
  Weak equivalence principle
  Never before attempted
Antihydrogen
  Pure antimatter system
  Electrically neutral, not susceptible to electrostatic field
ALPHA’s antihydrogen production and trapping technology
  CERN’s AD + positron accumulator
  Penning trap manipulates antiprotons and positrons
  Magnetic trap confines antiatoms
  > 100 antiatoms trapped per experiment cycle
  Compatible with in-situ gravity measurement
How? Challenges?

## Slide 3: Magnetic minimum trap
radial
|B|
axial
octupole
mirror
mirror
Anti-atoms confined via dipole moment in a region of minimum
Radial confinement: octupole
Axial confinement: mirror coils
Additional force from gravity

## Slide 4: Measurement method
radial
|B|
axial
octupole
mirror
mirror
During gravity measurement:
  Anti-atom trapped
  Octupole stays on
  Mirror coils slowly turned off
  Observe antiatom escape, through outside annihilation detector

## Slide 5: Measurement method
Simplified picture
  Up-down z motion in 1D
  x,y motion ignored
Equal coil currents
  Gravity favour downward escape
  Up-down measurement, sign of gravity
Slightly stronger bottom coil
  Equal escape infers gravity
  1% precision measurement

## Slide 6: Measurement method
Simulation:
  How escape swings from bottom to top when bottom coil is boosted
  Curve shifts in with
Experimentally:
  One current setting is used
  Observed balance determines compatible curve
Function’s sharpness
  Push intersects further apart
  Improves precision
  Cooled Hbar increase sharpness
  Adiabatic cooling
  Future: laser cooling

## Slide 7: Challenges
Trapping antihydrogen
  O(1011) decrease in energy
  Method developed and refined in ALPHA and ALPHA-2
Gravity measurement
  O(105) further reduction in energy scale
  10 ppm magnetic control, to < 0.1 G level

## Slide 8: Overall magnet design
Number and position of elements carefully tailored to achieve 10 ppm B control
Centre: minimal magnet
  Precision measurement
Bottom: Strong magnets
  Initial trap & up-down measurement
Top: reflected copy
Factors that influenced the design:
  Persistent field
  Wire placement error
  Quasi-trapped antiatoms
  etc...

## Slide 9: 1. Persistent field
Induced field in superconductor
  Current loops induced in response to field changes
  Analogous to eddy current in normal conductors
  Indefinite memory, no direct control
ALPHA-2
  O(10 G) persistent field >> 0.1 G
Mitigation:
  Weak magnets, minimal NbTi around precision region
  Thin, numerous NbTi filaments in magnet wire, effect similar to lamination in iron transformer core
  Symmetrise magnetic history
  Expected to reach < 0.1 G

## Slide 10: 2. Wire placement
Two types of winding
Octupole winding
  CNC wire laying
  Impact of octupole error most severe near end turns
  Measurement regions avoid these zones
  Instead of 3 separate octupoles, full length + boost octupole minimises number of end turns in the middle

## Slide 11: 2. Wire placement
Coil winding
  Each layer is macro-photographed and precisely analysed
  Turns located to within ± 0.025 mm (1/1000”)
  Each coil trimmed by adaptive turn removal on outermost layer
Fitting ruler markings
Fitting wires
Macro photograph
(24 M pixel)
Turn position / mm
Turn #
Turn deviation
from linearity / mm

## Slide 12: 3. Quasi-trapped anti-atoms
Energetic escape very unlikely
  Requires hitting pin hole with all energy allocated to z
  Slow (x,y) and z energies mixing
  Anti-atoms mostly escape off-axis, at much later time
Tailor potential for all radii
  Balance escape under gravity
  Two extra correction coils to manipulate off-axis field
bottom coil
top coil

## Slide 13: Summary
ALPHA-g magnet system
  Vertical geometry
  Compensate gravity with offset coil currents
  Equal escape infers
Assembly in Aug
Commissioning in Sept
Physics shortly after
Currently being manufactured
  BNL, US: magnet windings
  Babcock, Germany: solenoid magnet
  RAL, UK: cryostat, beamline and support
  AMI, US: high current leads
  Triumf & York, Canada: annihilation detector, cosmic veto
  UBC & SFU, Canada: magnetometry

## Slide 14: End

## Slide 15: Environmental field
Gradient in external fields → spurious force
  Earth
  Nearby ferromagnetic material
  Beamlines
  Other experiments
Copper coils outside the experiment compensating environmental fields
  Generating , and proportional to , , ,
coils
coils

## Slide 16: Quasi-trapped anti-atoms
Octupole – mirror coil interaction
  Fields add as vector, but anti-atom feels only |B|
  Quadrature stiffening
  Mirror coil less capable of increasing field at higher radii
Increase |B| by a short corrector octupole at each coil
Mirror coil – mirror coil interaction
  Off-axis field from coil is stronger than on-axis field
  Correctly compensating gravity for all radii requires coils of different widths
  Equivalent: two coils of different widths sharing current
Each barrier made of three bodies in total