## Slide 1: Laser-Induced Breakdown Spectroscopy as a Rapid Diagnostic Tool for Bacterial Detection and Discrimination
Alexandra Paulick, Steven Rehse, Dylan Malenfant, Kevin Beaugrand, Mark Armstrong

## Slide 2: Motivation
Current methods of bacterial identification in a clinical setting
  require expertise in microbiology
  labor-intensive
  slow
  For example: standard culturing techniques for bacterial identification take 1-3 days
Patients are treated with broad-spectrum drugs that have given rise to the crisis of antibiotic resistant bacteria
Rapid and accurate diagnosis of bacterial infection are required so that more targeted treatment can begin as soon as possible

## Slide 3
  GOAL:
  Rapidly identify bacteria based on their elemental composition using laser-induced breakdown spectroscopy (LIBS)
  This includes developing a quick bacterial preparation method prior to testing that utilizes equipment and methods that are common in a clinical setting

## Slide 4: Laser-Induced Breakdown Spectroscopy (LIBS)
LIBS is an elemental analysis technique
Target material is vaporized, generating a cloud of atoms above the target surface
Cloud of atoms absorbs the remaining laser energy, forming a plasma
As the plasma cools, photons are emitted and collected for elemental analysis
Pulsed laser is focused on target surface which absorbs laser energy

## Slide 5: LIBS Advantages
Can be done on solids, liquids, gases and bacteria
Little to no sample preparation
Requires only g of sample
Fast: elemental composition can be determined in under 1 second
Simultaneously detects all elements in periodic table
The use of the laser allows for point sampling & elemental mapping

## Slide 6: Overview of Methodology
Bacteria is cultured on TSA plates
Bacterial cells are removed and suspended in 1.5 mL deionized water
Bacterial suspension is vortexed and deposited on nitrocellulose filter paper
Filter paper is mounted on a steel piece and ablated with laser
1
2
3
4

## Slide 7
After laser ablation, light from the plasma is dispersed, revealing the sample’s elemental composition
P
C
Mg
Ca
Na
CN
Black – blank filter paper
Red – filter with bacteria
Wavelength (nm)
LIBS Intensity (A.U)
Ar
5

## Slide 8
Bacteria are discriminated based on elemental composition
Bacterial classification based on elemental composition measured by LIBS
C, P, Mg, Ca, and Na can be used to identify a bacterium’s species Bacterial spectra are classified using discriminant function analysis (DFA)
Unknown spectra are classified against a precompiled library of known spectra
Sensitivity 98  2%
Specificity 99  1%
6
Bacterial library:
164 independent variables (intensities of elemental lines and ratios of these lines to each other)
~ 1500 spectra acquired over 3 months from 4 species of bacteria (E. coli, S. epidermidis, M. smegmatis, P. aeruginosa)

## Slide 9: Preparation Method to Separate a Contaminant from a Bacterial Suspension
Cell sizes:
Bacteria ~ 1 m
Red blood cell ~ 6-8 m
Eukaryotic cells ~ 10-100 m
Biological samples (blood sample, swab sample, etc.) will likely contain unwanted cells that would need to be separated from the bacteria before testing with LIBS
centrifuge tube insert
centrifuge tube
5 m filter
0.45 m filter
filter papers are placed here
Isolate the bacteria using filter papers with different pore sizes (5 m and 0.45 m)

## Slide 10
5 m filter
0.45 m filter
Tungsten powder (12 m average particle size) added to E. coli suspension to simulate unwanted cells in a biological sample
Wavelength (nm)
LIBS Intensity (A.U)
Black – 5 m filter
Red – 0.45 m filter
5 m filter
0.45 m filter
W
C
Mg
Ca
Na
W powder

## Slide 11: Previous Bacterial Deposition Procedures
1) Well-plate 2) Centrifuge tube insert
Bacterial LOD ~ 50 000 CFU per laser ablation event
Bacterial LOD ~ 90 000 CFU per laser ablation event
Bacterial lawn
filter paper
Number of bacterial cells present in clinical samples:
< 100 CFU/mL in blood
0-200 CFU in typical nasal swab
These LOD’s are not clinically relevant.
Bacterial LOD with LIBS MUST be lowered.

## Slide 12: New Deposition Procedure: Metal Cone
bacteria
Metal cone to force deposition of bacteria onto smaller region at center of filter paper Why do this? Increases the number of bacterial cells per unit area, leading to more bacterial cells ablated in a laser shot compared to previous deposition procedures
cap of centrifuge tube presses metal cone into filter paper
filter paper sits here
Method:
metal cone
centrifuge tube insert
Bacteria is concentrated at center of filter paper

## Slide 13: Metal Cone: Bacterial Concentration
E. coli deposited on filter paper with metal cone
569 LIBS spectra acquired across filter
Colour indicates bacterial LIBS intensity  purple: no bacterial signal
red: strong bacterial signal
Approximate location of where metal cone presses into filter paper
Intensity map depicting bacterial deposition on filter paper for bacteria deposited with metal cone
Image of filter paper after data acquisition
Discolouration due to presence of bacteria

## Slide 14
Recall:
Well-plate  LOD ~ 50 000 CFU per laser ablation event
Insert  LOD ~ 90 000 CFU per laser ablation event
LOD  5 500 CFU per laser ablation event
Comparison of LIBS Signal to Previous Deposition Methods
Metal Cone Limit of Detection
well-plate
insert
metal cone
blank filter
Suggestive of a lower LOD for bacteria deposited with metal cone

## Slide 15: Conclusions
Preparation method to separate unwanted material from bacterial suspension was effective Future work: test this method using a contaminant that more closely simulates biological cells
Metal cone:
  effective at concentrating bacterial cells to a small region of the filter paper
  significantly lowered bacterial LOD with LIBS compared to previous methods of bacterial deposition
Future work: LIBS analysis on bacteria collected with swabs that are used in hospitals

## Slide 16
Flocked swab
Foam swab
flocked
foam
Cannot shoot right on the swab
Surface is too irregular
Bacterial cells are not concentrated

## Slide 17
~ 80% of the bacterial cells were released from the flocked swab
Wavelength (nm)
LIBS Intensity (AU)
C
Mg
Ca
P
Na

## Slide 18: Acknowledgments
NSERC
University of Windsor Student Life Enhancement Fund
University of Windsor Faculty of Science

## Slide 19
New students welcome!
If interested, contact Dr. Steven Rehse rehse@uwindsor.ca

## Slide 20: Bacterial Collection with Swabs
Some clinical specimens are collected with swabs
time consuming & require microbiology expertise
Swab is streaked on culture plate containing growth media for bacterial cells
Can we use LIBS instead?
If bacteria is present on the swab, it will grow on the plate