## Slide 1: Simultaneous Positron Emission Tomography/Magnetic Resonance (PET/MR) Imaging
Presented on behalf of The University of Winnipeg Brain Imaging and Metabolic Research Lab with:
Sidney Leggett (University of Winnipeg); Vanessa Palmer (Cubresa, Inc); Sheryl Herrera (University of Winnipeg, Cubresa, Inc.); Katrina Armstrong (University of Manitoba); Katinka Stecina (University of Manitoba); Melissa Anderson (University of Winnipeg); Henri Sanness Salmon(University of Winnipeg); Huixin Zhang (Winnipeg Regional Health Authority); Michael Zhang (University of Winnipeg); Liping Huang (Chinese PLA General Hospital, Beijing, China)
Melanie Martin
University of Winnipeg

## Slide 2: Outline
MR (magnetic resonance) and PET (positron emission tomography) imaging
Simultaneous PET-MR (our latest development)
  What it is
  How it works
  Preliminary results

## Slide 3: What is PET imaging?

## Slide 4: An Anatomical Image of the Earth
Slides courtesy of Andrew Goertzen, University of Manitoba

## Slide 5: What is PET, and how is it different from MRI and CT?
PET
PET stands for Positron Emission Tomography
Is a functional imaging modality
Involves the injection of a positron emitting radio-nuclide to act as a tracer
Image is of the distribution of the radio-nuclide in the object being imaged
Slides courtesy of Andrew Goertzen, University of Manitoba

## Slide 6: Physics of Positron Emission p  n + n + b+ + energy
188O10
189F9
b+ (KE=E)
n
+
-
Unstable proton-rich 18F*
e and b+ form positronium
short lived (0.1 ns)
+
-
511 keV
511 keV
+
-
180
electron-positron
annihilation
Conservation of energy and momentum
b+ slows down through collisions with electrons
* 18F is an isotope of the stable, natural fluorine 199F10
Notes: A diagram of p emission process

## Slide 7: PET System
The back-to-back photons produced in e+-e- annihilation are detected using rings of detectors
The origin of the photons lies
on the line connecting the two detectors, called Line of Response (LOR)
An event is called coincidence when two photons are detected within a set time window (6-24 ns)
The recorded coincidence events make the image data
coincidence ?
yes
The event is recorded
An annihilation process

## Slide 8: Synthesis of a PET Tracer (Radiochemistry at Work)
PET radioisotope is attached to a biologically useful molecule
18F-FDG (fluorodeoxyglucose)
  an analog of glucose
  is a marker of glucose metabolism
  preferentially taken up in metabolically active cells
Figure from Mankoff DA et al. Sem in Rad Onc 2001;11(1):16-27
FDG is the most widely used PET radiopharmaceutical

## Slide 9: A Functional Image of the Earth
Slides courtesy of Andrew Goertzen, University of Manitoba

## Slide 10: Functional Imaging of a Defect
Slides courtesy of Andrew Goertzen, University of Manitoba

## Slide 11: Simultaneous vs Sequential Multimodality Imaging
Traditionally images are collected from one modality, then the subject moved, and then images are collected from another modality. (Sequential)
If the subject moves between images or the anatomy and/or function changes with time, it is difficult to correlate the images.

## Slide 12: Simultaneous vs Sequential Multimodality Imaging
Collecting both images simultaneously can overcome many of these problems
We use the NuPET system from Cubresa, Inc.
The PET scanner fits inside the bore of the MRI and images can be acquired simultaneously.

## Slide 13: Simultaneous PET/MR images of rats
2 rats were imaged
PET tracer used was 18FDG
3D FISP MRI
Aims were to
  Register PET and MR images
  Segment out the brain
  Quantify SUV of FDG in the brain
  Describe the time course of the SUV
Aims 1 and 2 have been completed

## Slide 14: Images
brain
eyes
harderian glands

## Slide 15: Images

## Slide 16: 3D images – coronal view

## Slide 17: 3D images – axial view

## Slide 18: Segmented brain

## Slide 19: Segmented brain

## Slide 20: Discussion and Conclusion
Simultaneous PET/MR allowed for
  The visualization of 18FDG uptake in the rat head
  Straight forward registration of the PET and MR images
  Straight forward segmentation of the brain
Next steps
  Quantify the FDG uptake
  Examine the time course

## Slide 21: Acknowledgments