## Slide 1: A linear quadrupole ion trap for barium tagging in nEXO
Yang Lan
for the nEXO collaboration
TRIUMF/UBC

## Slide 2: nEXO: a search for neutrinoless double beta decay (0νββ)
2νββ:
0νββ:
  If 0νββ detected,
    Validate neutrinos to be their own anti-particles (Majorana)
    Derive neutrinos’ absolute mass
    …
  Challenge: 0νββ half-life > 1026 yrs
    Requires low background
      Underground detector
      Radiation shielding
      Barium tagging
        A 5-year upgrade to nEXO

## Slide 3: Barium tagging: the ultimate method for background rejection
Multiple approaches to barium tagging in nEXO:
  Stanford U: laser resonance ionization, mass spectrometry
  Colorado State U: cold probe, laser spectroscopy
  McGill, Carleton, TRIUMF: RF funnel, ion trap, laser spectroscopy, mass spectrometry
nEXO TPC
“An apparatus to manipulate and identify individual Ba ions from bulk liquid Xe”
K. Twelker et al., Rev. Sci. Instrum. 85, 095114 (2014)
“Imaging individual Ba atoms in solid xenon for barium tagging in nEXO”
C. Chambers, et al., Nature 569, 203-207 (2019)
“An RF-only ion-funnel for extraction from high-pressure gases” T. Brunner, et al., Int. J. Mass Spec. 379, 110 (2015)
RF funnel
Mass spectrometry

## Slide 4: Linear quadrupole ion trap (LQIT): radial dimension
Radio frequency (RF) quadrupoles for ion confinement
Pseudopotential
Vary at radio frequency
VRF
VRF
- VRF
- VRF
Figure credit: Green (2010)
Radial confinement
Figure credit: Molhave (2000)

## Slide 5: Linear quadrupole ion trap (LQIT): longitudinal dimension
Components:
  Quadrupole mass filter (QMF): ion purification according to ion mass-to-charge ratio
  Cooler: cool ions with helium buffer gas
  Ion storage: identify barium with laser spectroscopy
  Buncher: Ion ejection for a Multi-Reflection Time-of-Flight (MR-TOF) mass spectrometer
QMF
Cooler
Ion storage
Buncher
Ions from RF funnel
Ions to MR-TOF
Longitudinal confinement

## Slide 6: Simulations
High temperature ions are bad
  Doppler broadening in laser spectroscopy
  Worse time spread and energy spread of ions in MR-TOF
RF heating
AxialDepth: 4 V

## Slide 7: Simulations
Dependent on the axial trap depth and q value
  For a required axial trap depth of 30 V: lowest ion temperature at q = 0.55
AxialDepth: 30 V
Insufficient
trapping
RF heating
Laplace equation
quadrupole solution

## Slide 8: Vacuum requirements and design
Differential
Pumping scheme:
Turbo molecular pump (TMP)
TMP
Backing pump
Pre-cooler:
Cooler:
Laser Spec. region:
Ion buncher:
QMF:
  QMF requires as good vacuum as possible; cooler requires higher buffer gas pressure

## Slide 9: Vacuum simulation
6×10⁻² mbar
5×10⁻⁴ mbar
6×10⁻⁴ mbar
1×10⁻⁵ mbar
5 cm
Helium gas in
Pump
Pump
Avoid gas buildup
Tool: Molflow+ (https://molflow.web.cern.ch)
  Molecular flow simulation using ray-tracing

## Slide 10: Mechanical design
QMF
RF Cooler
Diff. pumping
Laser spec.
Ions in
Ions out
to MR-TOF
Design and 3D drawings in Solidworks
  Completed in Nov 2018

## Slide 11: Experimental preparation
Electronics and data acquisition
Vacuum
Ion source
ion detector

## Slide 12: Prototypes
100+ happy hours in machine shop

## Slide 13: Quadrupole Mass Filter (QMF) prototypes
  Mechanical tolerance ~ 0.2 mm
  Tested as an ion guide
    Saw optimum ion transmission at 20 Vpp, 530 kHz
    Things are working: electronics, DAQ, ion source, ion detector …
Acrylic QMF (V1.0)
  Novel design
0.02 mm (20 μm) tolerance needed

## Slide 14: QMF V2.1
Mechanical tolerance ~ 50 μm (0.002'')
  RF amplitude: 20 Vp-p, frequency 0.3 to 0.9 MHz
Figure credit: Niessen (2017)
23Na
39K
85Rb
133Cs

## Slide 15: QMF V2.2
Mechanical tolerance <10 μm (0.0005'')
  RF amplitude: 200 Vp-p,
  frequency 0.7 to 1.8 MHz
Achievable mass resolving power: M/MFWHM>100 ✓
Good enough to separate 136Ba+ from its isotopes & contaminant ions

## Slide 16: RF cooler prototype
More complicated geometries
Less tolerance requirement: 0.3 mm
Try 3D printing for rapid prototyping
  Tolerance ~ 0.1 mm ✓
  Tested vacuum compatibility
    Below 10-6 Torr within 10 hours of pumping ✓
Ongoing experiment with ion cooler:
  Ion trapping and ion ejection

## Slide 17: Summary and outlook
Barium tagging is the unambiguous way for the ultimate background rejection of nEXO
A linear quadrupole ion trap (LQIT) is needed
  Simulated and designed
  Experimental setup
    A QMF prototype already meets requirements
    Tests with an RF cooler prototype are ongoing
MR-TOF under development at McGill
  The LQIT is to be tested together with RF funnel and
  MR-TOF next year

## Slide 18
University of Alabama, Tuscaloosa AL, USA
M Hughes, O Nusair, I Ostrovskiy, A Piepke, AK Soma, V Veeraraghavan
University of Bern, Switzerland — J-L Vuilleumier
Brookhaven National Laboratory, Upton NY, USA
M Chiu, G Giacomini, V Radeka, E Raguzin, S Rescia, T Tsang
University of California, Irvine, Irvine CA, USA — M Moe
California Institute of Technology, Pasadena CA, USA — P Vogel
Carleton University, Ottawa ON, Canada
I Badhrees, R Gornea, C Jessiman, T Koffas, D Sinclair, B. Veenstra, J Watkins
Colorado State University, Fort Collins CO, USA
C Chambers, A Craycraft, D Fairbank, W Fairbank Jr, A Iverson, J Todd
Drexel University, Philadelphia PA, USA
MJ Dolinski, P Gautam, E Hansen, YH Lin, E Smith, Y-R Yen
Duke University, Durham NC, USA — PS Barbeau
Friedrich-Alexander-University Erlangen, Nuremberg, Germany
G Anton, J Hoessl, T Michel, M Wagenpfeil, T Ziegler
IBS Center for Underground Physics, Daejeon, South Korea — DS Leonard
IHEP Beijing, People’s Republic of China
G Cao, W Cen, Y Ding, X Jiang, Z Ning, X Sun, T Tolba, W Wei, L Wen, W Wu, X Zhang, J Zhao
IME Beijing, People’s Republic of China — L Cao, X Jing, Q Wang
ITEP Moscow, Russia
V Belov, A Burenkov, A Karelin, A Kobyakin, A Kuchenkov, V Stekhanov, O Zeldovich
University of Illinois, Urbana-Champaign IL, USA — D Beck, M Coon, J Echevers, S Li, L Yang
Indiana University, Bloomington IN, USA — JB Albert, SJ Daugherty, G Visser
Laurentian University, Sudbury ON, Canada
B Cleveland, A Der Mesrobian-Kabakian, J Farine, C Licciardi, A Robinson, U Wichoski
Lawrence Livermore National Laboratory, Livermore CA, USA
J Brodsky, M Heffner, A House, S Sangiorgio, T. Stiegler
University of Massachusetts, Amherst MA, USA S Feyzbakhsh, D Kodroff, A Pocar, M Tarka
McGill University, Montreal QC, Canada
T Brunner, K Murray, T Totev, L Darroch, S Al Kharusi, T McElroy
University of North Carolina, Wilmington, USA — T Daniels
Oak Ridge National Laboratory, Oak Ridge TN, USA — L Fabris, RJ Newby
Pacific Northwest National Laboratory, Richland, WA, USA
I Arnquist, EW Hoppe, JL Orrell, G Ortega, C Overman, R Saldanha, R Tsang
Rensselaer Polytechnic Institute, Troy NY, USA — E Brown, K Odgers
Université de Sherbrooke — F Bourque, S Charlebois , M Côté, D Danovitch, H Dautet,
R Fontaine, F Nolet, S Parent, JF Pratte, T Rossignol, J Sylvestre, F Vachon
SLAC National Accelerator Laboratory, Menlo Park CA, USA
S Delaquis, A Dragone, G Haller, LJ Kaufman, B Mong, A Odian, M Oriunno, PC Rowson, K Skarpaas
University of South Dakota, Vermillion SD, USA — T Bhatta, A Larson, R MacLellan
Stanford University, Stanford CA, USA — J Dalmasson, R DeVoe, D Fudenberg,
G Gratta, M Jewell, S Kravitz, G Li, M Patel, A Schubert, M Weber, S Wu
Stony Brook University, SUNY, Stony Brook NY, USA — K Kumar, O Njoya
Technical University of Munich, Garching, Germany — P Fierlinger, M Marino
TRIUMF, Vancouver BC, Canada — J Dilling, P Gumplinger, R Krücken, Y Lan, F Retière, V Strickland
Yale University, New Haven CT, USA — A Jamil, Z Li, D Moore, Q Xia
Also thanks to the TITAN group at TRIUMF for discussions and equipment!

## Slide 19: Vacuum simulation
Tool: Molflow+ (https://molflow.web.cern.ch)
  Molecular flow simulation using ray-tracing
Simplified geometry

## Slide 20: QMF performance
Transmission efficiency vs mass resolving power
G:\LinearPaulTrap\Experiment\Data\AcetalQMS_20190218\20190404\KPeaks_DC16.2Step0.5percent

## Slide 21: QMS performance simulation
Transmission efficiency
  – acceptance
Mass resolving power
Validate mechanical tolerance

## Slide 22: Measure QMS electrode tolerance
Use the digital readout on a lathe

## Slide 23: RF ion cooler
Novel rectangular electrode for cooler
  Optimum configuration: width/r0=0.7
    Thickness doesn’t matter much
For reference, circular quadrupole electrodes:
  re/r0=1.145

## Slide 24: Novel rectangular electrode for cooler
Housed in a floated metal tube (~ -100 V)
  Change electrode width to create DC drag field

## Slide 25: Novel rectangular electrode for cooler
Width: 4 mm
Width: 2mm

## Slide 26: Laser spectroscopy
Initial study at Stanford (~2005)
now at Carleton University