## Slide 1
Accelerated Diffusion-Weighted Hyperpolarized 129Xe Gas Lung MRI
Physics & Astronomy
Fumin Guo1, Matthew Fox2,3, Grace Parraga4,5, and Alexei Ouriadov3,2
1Sunnybrook Research Institute, University of Toronto, Toronto, Canada,
2Lawson Health Research Institute, London, Canada,
3Department of Physics and Astronomy, 4Robarts Research Institute,
5Department of Medical Biophysics, Western University, London, Canada
June 4, 2019

## Slide 2
Declaration of Relevant
Financial Interests and/or Relationships
A. Ouriadov and all co-authors:
We have no relevant financial interests or relationships to disclose with regard to the subject matter of this presentation.

## Slide 3
Thermal Polarization
Nuclei with spin = ½ are placed in an externally applied magnetic field
Polarization (P) arises from a population difference in energy levels of spin = ½ nuclei

## Slide 4
Spin-Exchange Optical Pumping
Rubidium electrons are optically pumped into an excited state using circularly polarized laser light
The electronic polarization of Rb is transferred to the noble gas nuclei via collisions

## Slide 5
Spin-Exchange Optical Pumping
  Polarization: 30%
  Cryogens required for operation
  Production Rate:
  ~800ml/hour
  129Xe Polarizer, Polarean, USA

## Slide 6
1H MRI vs Hyperpolarized Gas MRI

## Slide 7
Hyperpolarized Gas MRI
Helium-3 Xenon-129
Kirby M. et al. Radiology 265, 600-610, (2012)

## Slide 8
129Xe MRI Hardware

## Slide 9
Single Breath-hold Isotropic 129Xe MRI
Barker A, et all, ISMRM 2019

## Slide 10
Emphysema: Pathology
Evaluating Emphysema
  Spirometry and Plethysmography
  Computed Tomography
  Diffusion-Weighted (DW) Hyperpolarized Gas MRI
Normal
Emphysema

## Slide 11
DW Hyperpolarized Gas MRI
r
r
ADC
ADC
ADC = apparent diffusion coefficient
r = distance the helium atoms diffuse
t =diffusion time
Emphysema
Healthy

## Slide 12
DW Hyperpolarized Gas MRI
=
=
=
1Ouriadov A, et all, Magn Reson Med 2018; 79: 439-448.

## Slide 13
Limitations to DW Hyperpolarized Gas MRI
2Ouriadov A. et al. Magn Reson Med (2012)
3Chan H. F. et al. Magn Reson Med, (2016).
4Abascal J. F. A. et al. ArXiv, (2017)
Hyperpolarized Gas MRI-based emphysema biomarkers may help to evaluate and phenotype patients with COPD, Bronchopulmonary Dysplasia and Alpha-1 Antitrypsin Deficiency but these cannot be obtained in a single breath-hold (<16 sec)
This means that multi-breath methods2 (which may lead to lung volume variability, patient distress or fatigue) will require longer duration scans (>90 sec for 129Xe with several breaths), reduction in number of b-values and a reduction in 3D image resolution to help reduce total scan time.
A stretched exponential method3 (SEM) combined with under-sampling (compressed sensing) in the imaging and diffusion directions4 was proposed for the evaluation of hyperpolarized gas multiple b-value diffusion-weighted MRI.
The major advantage of this method is the possibility to significantly speed up the data acquisition using acceleration factors (AF) between 7 and 10.4

## Slide 14
Research Objective
Research Hypothesis
Accelerated (7 folds faster) methods can be developed to provide whole lung hyperpolarized gas MRI-based emphysema biomarkers including static-ventilation, T2*, ADC and morphometry maps in a single 16 sec breath-hold.
To develop the accelerated SEM-based 129Xe MRI approach and generate hyperpolarized gas MRI-based emphysema biomarkers in a small group of young healthy volunteers and Alpha-1 Antitrypsin Deficiency subjects.

## Slide 15
 | Hyperpolarized 129Xe MRI
Pulse Sequence Parameters | Accelerated 2D Gradient Echo DW Short-TE/TE/TR/FA/BW = 2ms/10ms/5ms/4°/31.25kHz Matrix Size = 128x20, Acceleration Factor = 7 Diffusion time (Δ) = 5.2ms b-values =0, 0, 12, 20, 30, 45.5 s/cm2 FOV =40x40cm2, 8 slices, 30 mm slice thickness
Dose | 
Coil | CMRS flexible transmit/receive chest coil
3.0 T Discovery MR750 (GEHC)
Methods: MRI Protocol
129Xe
4He

## Slide 16
Methods: Image Analysis
= ,
DDC= diffusivity, = heterogeneity index;
and mean diffusion length (LmD)=(2 Δ <DDC>)1/2
Diffusion Attenuated MR Signal in SEM:
4Ouriadov A. et al. Magn Reson Med (2017)
5COuriadov. et al. ISMRM, (2016).
6Yablonskiy D. A. et al. J Appl Physiol 107, 1258-1265, (2009).
7Kirby M. et al. Radiology 265, 600-610, (2012)

## Slide 17
Methods: Pulse Sequence

## Slide 18
Results: Accelerated 129Xe MRI
Ouriadov A, et all, Submitted to Magn Reson Med

## Slide 19
Results: Accelerated 129Xe MRI
Ouriadov A, et all, Submitted to Magn Reson Med

## Slide 20
Conclusions
Accelerated 129Xe MRI provides a way to generate alveolar morphometry estimates to regionally characterize emphysema and airspace enlargement in patients with AATD in a single 16 sec breath-hold scan
The Signal-to-Noise Ratio (35-40) of the short-TE image was more than adequate for the calculation of the Ventilation Defect Percentage which may be simultaneously generated with T2*, ADC and Lm values in a single rapid breath hold
This is the first in patient demonstration of this acceleration (7x) method for 129Xe and it suggests that the acceleration factors of 10 fold are possible. It will help retain resolution, maintain high number of b-values
Ouriadov A, et all, ISMRM 2019

## Slide 21
London ON:
Robarts Research Institute
Toronto ON:
The Hospital for Sick Children
Hamilton ON:
Firestone Institute for Respiratory Health
St. Joseph’s Healthcare
Thunder Bay ON:
Thunder Bay Regional Research Institute
Montreal QC:
CHU Sainte-Justine
Université de Montreal
Vancouver BC:
The Institute of Heart and Lung Health
St. Paul’s Hospital
Translating 129Xe MRI Across Canada

## Slide 22
Physics & Astronomy
London Lung Imaging Research Team