## Slide 1
CUTE: An Overview and Applications to SuperCDMS
Aditi Pradeep
CAP Congress
June 6, 2022

## Slide 2: Cold, colder.... dark matter
SuperCDMS looks for DM interactions in cryogenic, semiconductor crystals producing phonons and e-h pairs.
Phonon energy is collected using Transition Edge Sensors
Charges drifted with a bias voltage:
  Maximum background discrimination: Small voltage (< 10 V); measure both phonons and charges
  Lowest threshold: Large voltage (10 – 100 V); electric potential energy converted to phonons (NTL effect) giving signal amplification

## Slide 3
iZIP |  |  | HV |  | 
Interleaved Z-sensitive Ionization and Phonon detectors (12 phonon + 4 charge channels) |  |  | High Voltage detectors (12 phonon channels), plan to apply up to 100V |  | 
Excellent discrimination between electron and nuclear recoils using phonon and charge signals |  |  | Low threshold from high Luke amplification. For a bias voltage Vb, amplification factor, , where Y: Ionization yield, e: electric charge, ε: energy required to produce a single (e-h) pair |  | 
Resolution* | Ge | Si | Resolution* | Ge | Si
σphonon | 33 eV | 19 eV | σphonon | 34 eV | 13 eV
σcharge | 160 eV | 180 eV | σcharge | N/A | N/A
Phonon threshold | 350 eV | 175 eV | Phonon threshold | 70 eV | 35 eV
Charge threshold | ~1 keV | ~1 keV | Charge threshold | N/A | N/A
iZIP |  |  | HV |  | 
Interleaved Z-sensitive Ionization and Phonon detectors (12 phonon + 4 charge channels) |  |  | High Voltage detectors (12 phonon channels), plan to apply up to 100V |  | 
Excellent discrimination between electron and nuclear recoils using phonon and charge signals |  |  |  |  | 
Resolution* | Ge | Si | Resolution* | Ge | Si
σphonon | 33 eV | 19 eV | σphonon | 34 eV | 13 eV
σcharge | 160 eV | 180 eV | σcharge | N/A | N/A
Phonon threshold | 350 eV | 175 eV | Phonon threshold | 70 eV | 35 eV
Charge threshold | ~1 keV | ~1 keV | Charge threshold | N/A | N/A
SuperCDMS detectors
iZIP prototype
* https://arxiv.org/pdf/2203.08463.pdf

## Slide 4: CUTE facility

## Slide 5: Motivation
Cosmogenic activation, high background rate at ground level: need a low background test site
CUTE : 2 km underground at SNOLAB in Sudbury, ON. Background: ~7 events/ keV/ kg/ day (10-100 keV range)
Located next to SuperCDMS in SNOLAB. Ongoing SuperCDMS detector characterization, hardware/software testing and optimization of readout configuration.
Possibility of early science results from CUTE before the main experiment is commissioned.
CUTE is open to new players post SuperCDMS!

## Slide 6: Shield design
1.5 m water shield: neutron & gamma shield
10.7 cm inner and outer Pb cylinders: gamma shield
Mu metal: magnetic shield
20 cm HDPE top cover: shields neutrons from the top
15 cm Internal Pb: shields gamma from the top

## Slide 7: Calibration
  133Ba gamma source deployable into the shielding with a stepper motor
  252Cf neutron source is being installed: Ge activation for low energy calibration, iZIP neutron/gamma discrimination
  55Fe source (Kα 5.9 keV, Kβ 6.5 keV) with Al foil (~μm thick, 1.5 keV fluorescence) for low energy calibration.
Cf source inside first layer of Cu encapsulation
55Fe source

## Slide 8: Vibration mitigation
Pulse Tube is a major source of vibrations in our setup
Vibrational noise is decoupled by mounting the cryostat on a suspension system
CUTE slow control system automatically adjusts the suspension system in response to lab pressure changes
CUTE: an underground test facility for cryogenic detectors R. Germond| CAP Congress 2021
Average noise in our detector as a function of frequency when the cryostat is coupled to vs decoupled from the pulse tube
Frequency (Hz)
Coupled to PulseTube
Vibrationally decoupled

## Slide 9: SuperCDMS @CUTE

## Slide 10: Detector testing : Cryogenic Photon Detector
CPD: 10.6 g, 3.8 cm radius, 1 phonon channel
Originally designed to detect light from cryogenic scintillators; low threshold
Assessed noise performance
Calibrated with 55Fe Kα, Kβ lines and Al fluorescence peak accounting for local saturation effects
Resolution from least noisy series: ~12 eV
Empirical calibration model with local saturation correction
Calibrated energy spectrum for CPD

## Slide 11: Detector testing : Cryogenic Photon Detector
Empirical calibration model with local saturation correction
Calibrated energy spectrum for CPD
CPD: 10.6 g, 3.8 cm radius, 1 phonon channel
Originally designed to detect light from cryogenic scintillators; low threshold
Assessed noise performance
Calibrated with 55Fe Kα, Kβ lines and Al fluorescence peak accounting for local saturation effects
Resolution from least noisy series: ~12 eV

## Slide 12: Detector testing: iZIPs
Jonathan Corbett| MASc thesis
Event distribution as a function of Z estimator at various source positions
Calibrated 133Ba spectrum at various source positions
Soudan iZip (8 phonon + 4 charge channels) – Ge, 0.6 kg
Currently, only reading out phonon channels at CUTE
Calibrated with 356 keV Ba gamma peak
Performed background simulations with GEANT4 - M. Baiocchi| CAP Congress 2021
Performed directionality studies to understand position sensitivity
--- 356 keV line

## Slide 13: Detector testing: HV
E. Fascione | TRIUMF Science week 2021
G124 spectrum at different bias voltages
S101 spectrum at different bias voltages
SNOLAB HVs (partial readout): G124 (Ge,1.4 kg), S101 (Si,0.6 kg)
Assessed noise performance and pulse shapes
Studied NTL amplification
Currently focusing on calibrating S101 with Compton steps- Gamma’s can be used to strip e-s from Si atomic shells producing steps for each shell

## Slide 14: Outlook
SuperCDMS SNOLAB is expected to begin operation in 2024
CUTE can house 1 SuperCDMS tower (6 detectors) at a time
The first detector tower (6 Ge iZIPs) has been tested successfully at SLAC
This tower will be shipped to CUTE this summer for testing, and towers 2,3 and 4 will follow.id
First SCDMS tower assembly at SLAC

## Slide 15: Outlook
SuperCDMS SNOLAB is expected to begin operation in 2024
CUTE can house 1 SuperCDMS tower (6 detectors) at a time
The first detector tower (6 Ge iZIPs) has been tested successfully at SLAC
This tower will be shipped to CUTE this summer for testing, and towers 2,3 and 4 will follow.id
First SCDMS tower assembled at SLAC

## Slide 16: Summary
CUTE is an underground test facility for low background experiments.
Various types of SuperCDMS detectors and other operation hardware & software have been successfully tested at CUTE.
The first SuperCDMS tower consisting of 6 Ge iZIP detectors will arrive for testing at CUTE this summer.
Keep an eye out for dark matter results from CUTE in the near future!

## Slide 17: Backup slides

## Slide 18: CUTE Calibration
Cf source enclosed in PE box, placed in the water tank

## Slide 19: Energy estimator: Optimal Filter
Credit: Jorge Morales| Texas A&M

## Slide 20: Saturated pulse
Unsaturated pulse
Time
Current
Current
Time

## Slide 21: Soudan iZIP channel map and source position (measured from top) for directionality study