## Slide 1: Measuring Light Distribution of LED Sources for HyperK
NICHOLAS BOOTH CAP Congress 2022
TRIUMF: Mark Hartz, Michael Sekatchev University of Victoria: Dean Karlen

## Slide 2: Neutrinos and Hyper-Kamiokande
Neutrinos only interact through the weak force
There are multiple potential flavour and mass states, and a neutrino particle can oscillate between the various states.
The Hyper-Kamiokande (HyperK) experiment employs water-Cherenkov detectors to study this phenomenon.

## Slide 3: HyperK’s Intermediate Detector
The Intermediate Water-Cherenkov Detector (IWCD) is a close-to-source detector of much smaller volume than the main HyperK tank.
Will be lined with mPMTs that will reconstruct the interaction vertex and other properties of events
Due to small size, high timing precision and photogrammetry are necessary for vertex reconstruction
Notes: IWCD much smaller detector (10m vs 70m radius); smaller detector needs high timing precision for vertex reconstruction (the point where the incident happens) to confirm vertex is within fiducial area; also need high spatial precision (photogrammetry) to reconstruct vertex.

## Slide 4: Purpose - LEDs for Calibration
M. Pavin, R. Gaur
13 calibration LEDs beneath sealed dome; powered and controlled by interior electronics
12 directional LEDs for photogrammetry
1 pulsed LED for timing calibration
Notes: Pulsed led for the time delay to synchronize clocks

## Slide 5: Purpose - LEDs for Calibration
Light transported from LEDs below PMTs to surface of dome by light guides and emitted through attached lens
Must fully quantify the affect of lens and light guide on calibration light
M. Sekatchev
Bivar Inc. SMFLP36.0 Light Guide
Lens Attachment

## Slide 6: Theory – Brightness from 2D image
P = (x, y, d)
y
Source
θ
ϕ
r
d
x
O
x
y
z
Camera
Relate pixel brightness to incoming polar angle θ
  Each pixel has corresponding (x, y) coordinates
  Convert from Cartesian to Spherical to determine θ
Plot brightness vs polar angle to determine distribution
Camera, source, and origin of target plane are all on-axis
d = the distance from the source to the origin of the target plane

## Slide 7: Experimental Set-up
Power & LED
Light Guide
Target Plane
Camera
Lens
Light Distribution

## Slide 8: Data Collection
Calibration Screen
d = 1 in
d = 5 in
d = 3 in
The LED source is moved further away from target plane for each trial. Angular distribution should be constant as the physical source is not changing.
Each set of trials requires a calibration photograph with known cartesian coordinates to convert to and from pixel coordinates.

## Slide 9: Calibration Technique
Step 1 – Locate all circles
  Uses Hough Circles
Step 2 – Define Corners
  Rough pixel location found via Paint
Step 3 – Define Known Circles
Step 4 – Interpolate between Knowns
  Uses LinearNDInterpolater
Step 5 – Convert Pixel to True Coordinates

## Slide 10: Calibration Technique
Step 1 – Locate all circles
  Uses Hough Circles
Step 2 – Define Corners
  Rough pixel location found via Paint
Step 3 – Define Known Circles
Step 4 – Interpolate between Knowns
  Uses LinearNDInterpolater
Step 5 – Convert Pixel to True Coordinates

## Slide 11: Calibration Technique
Step 1 – Locate all circles
  Uses Hough Circles
Step 2 – Define Corners
  Rough pixel location found via Paint
Step 3 – Define Known Circles
Step 4 – Interpolate between Knowns
  Uses LinearNDInterpolater
Step 5 – Convert Pixel to True Coordinates

## Slide 12: Analysis Technique
Determine centre of maximum possible circle
cos(theta) limit
Point Source –
Uniform distribution in both cos(theta) and phi
Notes: Draw maximum circle on simulation

## Slide 13
Isolate Full Width at Half Maximum
Approximate isolated data as Gaussian
Fit Gaussians to each data set
Extract centres of Gaussian as the pixel coordinates of the centre of the light distribution

## Slide 14: Simulation Results
Uniform distributions in both cos(theta) and phi
Notes: Vertical offset due to potential background light contribution

## Slide 15: Example Test Results : d = 5 in
d = 5 in
Notes: Vertical offset due to potential background light contribution

## Slide 16: Looking Forward
Create more stable lens stand
Remove background light contribution
Model angular distribution in both cos(theta) and phi
Pass information to full simulation of IWCD tank

## Slide 17: Questions?
Thank you!
Merci!