## Slide 1: Aim of the workshop
Learn about each other’s work
Identify synergies:
  design/simulation (e.g. TCAD, Silvaco, ANSYS, …)
  Fabrication (TSMC, DALSA, FBK, Hamamatsu,…)
  Characterization
Discuss implementation strategies
  How to avoid being sub-critical? Aka great idea but fail to implement
  How to start and get funding at low “technology readiness level”?
  How to foster emergence of “Canadian technology”?
Working together?

## Slide 2: 3D integrated digital technology
Aim: measure charged particle and photon position & time within a single package
Solution: 3D integration
Technology available at Teledyne-DALSA + Sherbrooke
Sensor layer
Particle/photon to detectable quanta
Electronics layer
Quanta to bits
Molecular bonding
Switching to my personal interest

## Slide 3: 4Dimension Digital Detector, 4D3 concept
Single Photon Avalanche Diode
  1 photon → 1e- * 106 (Gain) → 106 e-
Low Gain Avalanche Diode
  1 MIP → 1,000e- (15um ionization) * 100 (Gain) → 105 e-
CMOS
Aka. electronics
Molecular bonding
Ultra-thin contact 1-5nm
Thin passivation ~100nm
e-
Drift field region
Avalanche region
photons
CMOS
Aka. electronics
e-
Charged particle
e-
e-
e-
e-
e-
e-
e-
30um
~106 gain
~100 gain
Signal close enough to be handled by similar electronics
Made in Canada technology: Sensor layer and 3D integration could be done at Teledyne-DALSA (Bromont, QC)

## Slide 4: Other configurations
~5keV electron detection for hybrid photo-detector (JP Yanez, Alberta)
Thick (300-500um) for direct dark matter detection with Geiger-mode and linear gain (with P. Agnes and J. Monroe, from RHUL, UK)
?Heavy ionizing particle for nuclear physics?

## Slide 5: Electronics + information management
“Analog” side
  1 comparator per diode (pixel)
  Possibly 2 for time over threshold
Digital. Tailor to needs. Possible configurations:
  Blue single photon sensor + high speed TDC (10ps) + coarse position (1-5mm) [PET, plastic scintillator,..]
  VUV/blue single photon sensor + low speed TDC (1ns) + coarse position (1-5mm) [ARGO, nEXO]
  Charged partice sensor + high speed TDC (10ps) + fine position (<100um) + rad hard [collider]

## Slide 6: Making this happen… challenges
Sensor development
  Currently only front side configuration exists. Need to move to Back side
  <350nm wavelength detection require very shallow doping
  Radiation hardness
Molecular bonding development
  Available at DALSA but not used yet
CMOS
  Sherbrooke has produced 2 flavors both with coarse position information: high speed/high power, and low speed/low power
  Radiation hardness
Need $$$ and possibly/probably a collaboration structure