## Slide 1: The liquid deuterium moderator for TUCAN
TRIUMF Ultra-Cold Advanced Neutron collaboration
Jeff Martin
The University of Winnipeg
Land acknowledgement
We acknowledge that we are gathered on ancestral lands, on Treaty One Territory. These lands are the heartland of the Métis people. We acknowledge that our water is sourced from Shoal Lake 40 First Nation.
See also:
M. McCrea, T2-6
S. Vanbergen, T4-6

## Slide 2: TRIUMF Ultracold Advanced Neutron (TUCAN) Source
Concept:
  Use superfluid helium (He-II) to convert cold neutrons into ultracold neutrons.
  Couple the He-II directly to a spallation source of neutrons and cold moderators that can be optimized fully.
  Transport UCN to a room-temperature neutron EDM experiment located farther away from the neutron source and cryogenic systems.
We have been operating this system first at RCNP Osaka, then at TRIUMF. We are now completing a new upgrade, scaling up the previous system with several key improvements to reach world-record UCN performance.
A major part of this upgrade is a new liquid D2 cold neutron moderator.

## Slide 3: What is deuterium?
Hydrogen atom (H)= nucleus of one proton, which is orbited by an electron.
Hydrogen molecule (H2) = two hydrogen atoms in a covalent bond.
Deuteron (d) = one proton and one neutron bound together in a stable nucleus.
Deuterium atom (D) = deuteron, which is orbited by an electron.
Deuterium molecule (D2) = two deuterium atoms in a covalent bond
Hydrogen/deuterium gas = think of the Hindenburg
At about 20 K or so, both hydrogen and deuterium become a liquid (LH2, LD2).
At about 4 K, helium becomes a liquid (He-I); below 2.7 K it becomes a superfluid (He-II).
Slow moving, free neutrons (n) are what we want to make, ultracold neutrons or UCN. Kinetic energy < 300 neV.

## Slide 4: UCN production and losses in superfluid 4He
Production:
  Incident CN @ 1 meV excites one phonon Golub and Pendlebury, 1975, 1977
  Multiphonon excitation give additional production.
Losses:
  Loss rate dominated by 2-phonon upscattering ~ T7
  T = 1.1 K gives τUCN = 64 s
  We must keep the superfluid much colder than Tλ
Courtesy O. Zimmer
Korobkina et al., PLA 301 (2002) 462
Leung et al., PRC 93, 025501 (2016)
Maximize 1 meV neutrons;
Minimize losses, heat.

## Slide 5: How to cool neutrons from 1 MeV to 1 meV?
It is easy to cool neutrons from 1 MeV to 1/40 eV = 25 meV. Let them bounce off nuclei at room temperature T = 300 K.
e.g. a neutron moderator based on hydrogen
  Neutrons scatter off protons elastically with const. Their mfp is
  After N collisions , so in order to reach 25 meV, you need about 25 collisions.
  Assuming random walk ; D is roughly the thickness of material needed to thermalize.
If you want colder neutrons, just use a colder material, like liquid hydrogen! Then T = 20 K or <E>N = 2 meV.
In general, light materials that don’t absorb neutrons are best thermal moderators.
Deuterium captures fewer neutrons, and as a result there is less gamma heating.

## Slide 6: Why LD2?
Relative to LH2:
  The scattering cross-section is smaller (bad)
  The absorption cross-section is MUCH smaller (great!) leading to fewer losses and less gamma heating of the nearby superfluid.
Relative to D2O:
  No problem with the oxygen in D2O.
  Crystal structure makes D2O vibrate, even at low temperatures. In previous experiments, we deduced that T = 80 K for neutrons in much colder D2O.
  Burping is a problem for D2O. Progressive radiation damage to the crystal stores energy eventually leading to a catastrophic warm up.
Issues for LD2:
  Cryogenics, safety: engineering!
Maxwell-Boltzmann energy distribution (neutrons in thermal equilibrium with a material at temperature T)

## Slide 7: Neutron production and heat load requirements
Heat load to LD2 is 60 W instantaneously.
W. Schreyer, et al., NIM A 959 (2020) 163525.

## Slide 8: How to keep it cold? LD2 thermosyphon (natural circulation system)
Features: single-phase, no moving parts
Cold
Hot
Cryocooler + HEX
~ 60W for 40μA current (inst.)
To Ballast
T(s,t) (K)
Distance along thermosyphon loop (m)
HEX
Heat
for
  Time-dependent thermodynamic model by Kiera Augusto and Shawn Stargardter

## Slide 9: Construction Status
2219 Aluminum Domes
“Wall 1” in kapton super-insulation, all sensors installed
Innermost vessel “Wall 1” completed (it has even been tested with ultracold neutrons!)
Now preparing and assembling the layers of the other vessels; the next layer to be assembled is the LD2 layer.
Thermal shock tests with LN2

## Slide 10: LD2 Cryostat – C. Marshall, et al. (TRIUMF)
Expert review of the LD2 system - Completed Oct 2022.
Detailed drawings are now complete.
Many parts starting to come together.
LD2 Heat exchanger section
D2 storage tank installed October 2022
LD2 cryostat assembly
Gas handling design
LD2 purifier design

## Slide 11: Summary and final thoughts
The TUCAN source needs a large flux of 1 meV neutrons, so that they can downscatter in superfluid helium and become ultracold.
An LD2 moderator at 20 K has been optimized to provide the 1 meV neutrons.
The system relies on a thermosyphon design to cool the LD2.
The technical design of the LD2 moderator is nearing completion, with the component pieces (cryostat, heat exchanger, purifier, …) being prepared for construction.
The LD2 system will be completed in 2024.

## Slide 12: Thank you!
Collaboration meeting January 2023

## Slide 14: TUCAN source and EDM Experiment
Enable search for neutron EDM with 1 x 10-27 ecm precision.
EDM experiment
UCN source
View of future facility at TRIUMF
3.4 m

## Slide 15: Horizontal source upgrade
Tail section (constr.)
To nEDM
Shielding
He-II cryostat (tested in Japan, at TRIUMF)
LD2 cryostat (designed)
Cryo-connection box (with vendor, Canada)
3He-4He heat exchanger (prototype, Japan)
Superconducting polarizer
(previous project, Japan)
Target

## Slide 16: Horizontal source upgrade
Tail section (constr.)
To nEDM
Shielding
He-II cryostat (tested in Japan, at TRIUMF)
LD2 cryostat (designed)
Cryo-connection box (with vendor, Canada)
3He-4He heat exchanger (prototype, Japan)
Superconducting polarizer
(previous project, Japan)
Target

## Slide 17: TUCAN Source Upgrade Concept and Goals
proton beam (20 kW)
3He pumping
liquid 3He
300 K
20 K
LD2 moderator
  increase cold neutron flux at 1 meV (×2.5)
Helium Cryostat with high cooling power
  production volume (×3)
  proton beam power (×50)
    0.5 kW -> 20 kW
    heat load on superfluid : 8.1 W
      include heat deposit on vessel
  superfluid helium temperature (×1/3)
    THe-II = 1.2 K (0.8 K@RCNP)
    Storage lifetime : ～ 30 sec
Estimated source performance
  production rate: 1.4 x 107 UCN/s
  UCN density
    6×103 UCN/cm3 @ production
    ～220 UCN/cm3 @ measurement

## Slide 19: TUCAN Sensitivity Estimate
UCN production rate | 1.4×107 UCN/sec | 
UCN loaded into EDM cell | 220 pol. UCN/cm3 | 14M UCN
UCN detected at end of cycle | 23 pol. UCN/cm3 | 1.4M UCN
E = 12.5 kV/cm
tc = 188 s
α = 0.6 (visibility)
To reach statistical sensitivity of σd = 1×10-27 ecm
400 days of running required
Compare to typ 15,000 UCN detected at previous best expt. (ILL/PSI), and 121,000 UCN projected for n2EDM
N. Ayres, et al. arXiv:2101.08730
S. Sidhu, et al. arXiv:2212.04958
σd = 2 x 10-25 ecm/cycle