## Slide 1: Measurement of SiPM External Crosstalk in a LXe Detector
David Gallacher
PhD Candidate – Brunner Neutrino Lab
McGill University
2024 CAP Congress - May 27th
Notes: Notes from local group practice:
Finished in 11, spend more time on slides 8,9 and 10 explaining figures
Update plot on slide 4 to only show relevant curves for the plot, make sure line styles are bold to emphasize

## Slide 2: LXe detectors & SiPMs
Liquid Xenon (LXe) is a scintillating material that produces ultraviolet light from radiation interactions
Silicon photomultipliers (SiPMs) are solid-state single-photon counting sensors
We use SiPMs to count photons from radiation in LXe to perform a proportional energy measurement
Fig: Hamamatsu VUV4 Packages in LoLX detector during installation

## Slide 3
Light only Liquid Xenon (LoLX) is a modular small-scale LXe experiment
  📍 McGill University
Two experimental phases to date:
  Phase-1 – This Talk
  Phase-2 (See Alex Li’s Talk [M2-1-3:00])
Phase-1 employed 96 Hamamatsu SiPMs in an octagonal prism geometry
  Equipped with a 90Sr beta source needle
Fig: Cross-section of LoLX Phase-1 Detector
~4 cm
Sr90/Y90 Decay

## Slide 4
SiPMs are grouped in packages of 4
23/24 packages are covered by optical filters
  22x >220 nm longpass filters
  1x 175 nm bandpass filter
Filters separate LXe scintillation from SiPM External Crosstalk
Fig: Overview of wavelength-dependent optical properties in LoLX

## Slide 5: SiPM External Crosstalk
During the SiPM detection process near-infrared (NIR) photons are produced
These photons may escape the SiPM and be detected elsewhere
  Known as SiPM External Crosstalk or ExCT
This is a source of correlated avalanches (CA)
Our goals:
  Characterize SiPM ExCT in a LXe detector
  Create a simulation model of ExCT to predict impact on future LXe detectors
Legend
90Sr Needle
Longpass Filter
Bandpass Filter
Unfiltered
Initial Photon
eXT Photon
*Not to scale

## Slide 6: What’s the impact?
Next generation rare event search experiments will use large quantities of SiPMs
  Neutrino-less double beta decay (nEXO)
  Dark Matter (ARGO/DS20K)
Cylindrical geometries enhance ExCT impact
Need to evaluate the impact of SiPM ExCT on energy resolution, threshold and position reconstruction
Fig: Rendering of nEXO TPC design, SiPM barrel faces inward with ~50k devices

## Slide 7: Measuring SiPM ExCT with LoLX
To measure SiPM ExCT we look at time
Signature of ExCT is two pulses in time coincidence from two different channels
We look late in the event window for correlated delayed pulses
Time
Intensity
Source Channel
Search Window
Target
Channel
eXT Source
Candidate
Coincidence Window

## Slide 8: Measuring SiPM ExCT with LoLX
To measure SiPM ExCT we look at time
Signature of ExCT is two pulses in time coincidence from two different channels
We look late in the event window for correlated delayed pulses
PRELIMINARY
Fig: Occupancy for all channels in LoLX, search window is [800,1500 ns] post trigger

## Slide 9: How do we see ExCT?
By collecting pairs of pulses in the low-occupancy region we build a distribution in
  Pairs are between unfiltered “source” and longpass filtered “targets”
Excess at over combinatorial background is attributed to SiPM ExCT
Repeat for each run and voltage (4 + 5V OV)
PRELIMINARY
Fig: Fit to summed delta-time distribution for all 5V data summed

## Slide 10: ExCT simulation model
Simulations of SiPM ExCT carried out using custom GEANT4 physics extensions
Similar implementation to fluorescence in GEANT4
  For each “detected” photon, we trigger ExCT process and produce photons to track through detector
Photons are produced “at source” (Within Silicon) with a “Mean emission intensity”
  ~97% of photons produced in Si do not escape the SiPM
  Using input from TRIUMF measurements of ExCT and detailed SPAD simulations†
  Randomly sample each photon property and determine if it escapes
Distribution of escaping ExCT photons shown to the right
PRELIMINARY
Fig: Distribution of simulated emitted ExCT photons, normalized to proportion of emitted photons in the outgoing hemisphere (2π)
† K. Raymond et. al. 2024 (2402.09634)

## Slide 11: What do we see?
First sweep over simulated ExCT intensities
  Mean # of Photons/Avalanche (#ph/av.)
Compare the measured ExCT yield with simulation results
  Interpolate simulation curve for #ph/av. produced at each voltage
Determine #ph/av. emitted from simulations
PRELIMINARY

## Slide 12: What do we see?
Probabilities are for detecting ExCT from any unfiltered to any longpass filtered channel in LoLX
Emission reported as internal (before escaping) and external (transmitted into LXe)
Systematic uncertainties dominate over statistical at ~10% from data and ~20% from simulations
Ex-situ measurements reported values 39.2 +/- 9.3 ph/av. and 1.23 +/- 0.43 in LXe†
PRELIMINARY
† K. Raymond et. al. 2024 (2402.09634)

## Slide 13: Outlook and next steps
SiPM ExCT measured directly in a LXe detector
Developed a GEANT4 simulation method for characterizing ExCT
Good agreement between simulation and data with nominal inputs
Measurement of ExCT emission intensity are within uncertainty of ex-situ measurements†
† K. Raymond et. al. 2024 (2402.09634)
Manuscript for this work is nearing completion, keep an eye out soon!
Building on the simulation method here, we will evaluate the impact of SiPM ExCT for nEXO
Follow up measurements with faster timing and angular dependence planned in LoLX Phase-2

## Slide 14: Thank you for your attention from the LoLX Collaboration!

## Slide 15: Questions?
Please reach out to get in touch!
DavidGallacherPhysics.com
How to find me:
David.Gallacher@mail.mcgill.ca

## Slide 16: Backup slides

## Slide 17: Backup – Event and Pulse Selection
Excerpts from paper draft (in Review, preliminary)

## Slide 18: Backup – SPE Selection
Maximize our signal/background by using the Unfiltered SiPMs as the “Source” and 220 nm cutoff filtered channels as “Targets”
To ensure nominal ExCT intensity, we select SPE pulses for source candidates
SPE selection is done by gaussian fits to each channel with 90% acceptance region
No after-pulsing permitted

## Slide 19: Backup – Simulation Details
Surface normal

## Slide 20: Backup – LoLX outline
Legend
Longpass Filter
Bandpass Filter
No Filter
Top
Bottom
Side

## Slide 21: Backup – Systematic Budget

## Slide 22: lolxsim: VUV4Volume
*not to scale
15 mm
Ceramic
Quartz Window (h= 0.5mm)
LXe
Silicon_SD (h= 0.05 mm)
SiO2 (h= 110 nm)
LXeBuffer (h= 0.05 mm)
2.5 mm
eXT photons generated in the gap to avoid doubling optics at boundaries(shift 0.2mm along surface normal)
Photons detected at Si boundary
5.9 mm

## Slide 23: Backup

## Slide 24: Backup- Simulation Details
In our data measurements we measure “total correlation probability”
This includes “Direct” correlation
  Source->Target
Also includes “Backwards” correlation
  Target->Source
For simulations, we measure both independently
Source->Target
  Enable ExCT Simulation ONLY for source
Target->Source
  Enable ExCT Simulation for all EXCEPT source
Sum of two contributions is the “Total Correlation Probability”
From simulations we see roughly ~16% contribution of backwards correlation to total
  Stable across many simulation configurations, driven by solid-angles and transport efficiency + emission angular distribution
1
2
Source
Target
In simulation, we use the MC truth information, so estimates have no background