## Slide 1
SuperCDMS
at SNOLAB
Wolfgang Rau
Queen’s University
for the
SuperCDMS Collaboration

## Slide 2
SuperCDMS Collaboration
Southern Methodist University Stanford University
Texas A&M University of British Columbia/TRIUMF
University of California, Berkeley
University of Colorado Denver University of Evansville
University of Florida University of Minnesota
University of South Dakota University of Toronto
California Institute of Technology
CNRS/LPN Durham University
Fermi National Accelerator Laboratory
NISER NIST Northwestern University
PNNL Queen’s University
Santa Clara University SLAC/KIPA
South Dakota School of Mines & Technology
SNOLAB/Laurentian University

## Slide 3
SuperCDMS Technology
Implementation at SNOLAB
Status of the Project
Expected Sensitivity
CUTE (time permitting)

## Slide 4
Semiconductor operated at few 10s of mK
ZIP
HV
Phonon Readout:
Tungsten TES
R vs T
Add: charge readout (few V)
Background discrimination
Threshold < 10 keV
Add: high voltage (~70 V)
Phonons from drifting charges
Threshold < 0.1 keV (phonon)
+
0
–
0
0 V
– 70 V
remove surface
background
–
+
large phonon signal from
charges
Phonon signal
Charge signal
Nuclear recoils:
signal
Electron recoils: background
< 1 background event for whole exposure
effective threshold: few hundred eV (NR)
Detectors
i
Neganov-Luke Effect
+
-
-
In Vacuum
-
+
-
In Matter
Electron gains kinetic energy
(E = q · V  1 eV for 1 V potential)
Deposited energy in crystal lattice:
Neganov-Luke phonons
 V, # charges
Luke phonons mix charge and phonon signal  reduced discrimination
Apply high voltage  large final phonon signal, measures charge!!
ER much more amplified than NR  gain in threshold; dilute background from ER
Technology

## Slide 5
Ge / Si
100 mm  x 33 mm
Operated at 30 mK
iZIP
HV
Phonon Readout:
Tungsten TES
R vs T
Add: charge readout (few V)
Background discrimination
Threshold < 1 keV
Add: high voltage (~100 V)
Phonons from drifting charges
Threshold < 0.1 keV (phonon)
+
0
–
0
+ 50 V
– 50 V
remove surface
background
–
+
large phonon signal from
charges
Phonon signal
Charge signal
Nuclear recoils:
signal
Electron recoils: background
< 1 background event for whole exposure
effective threshold: few (or one) electron-hole pairs
Detectors
SuperCDMS
SNOLAB
Technology

## Slide 6
6 detectors  1 tower
Implementation (SNOLAB setup)
iZIP
Implementation

## Slide 7
Fridge to provide <15 mK at the detector
Mounted on spring-loaded platform (seismic isolation)
Initial Payload:
1 Ge iZIP tower (6 Ge)
1 Ge/Si iZIP tower
(4 Ge/2 Si)
2 HV towers
(4 Ge/2 Si each)
Implementation (SNOLAB setup)
Detector volume
(space for up to 31 “towers”)
Cold finger
6 detectors  1 tower
30 cm HDPE
20 cm Pb
60 cm HDPE base / water
Signal vacuum feedthroughs
Additional cooling (70 K/4 K)
Implementation

## Slide 8
SNOLAB
Radon filter
Cryogenics and radon filter plant
Experimental area
Access drift
CUTE
Backup cooling (ice)
Clean room
Cryo
Implementation

## Slide 9
Funding approved (CFI: 2012, DOE/NSF: 2014)
DOE/NSF review process: First step passed (CD 1: conceptual design review) Next step end of 2017: technical design review/ construction readiness (CD 2/3)
Reviews at SNOLAB: passed Gateway 1 (space allocation) in fall 2015 / GW2a (early construction) in December 2016; upcoming: GW2 (construction) fall 2017
Total project costs ~$30M
2013
2014
2015
2016
2017
2018
2019
CFI application
GW 1
GW 2a
CFI approved
US G2 decision
DOE/NSF proposals
CD 1
CAP 17 Queen’s
GW 2
CD 2/3
CD 4
Start of operation
Main construction phase
Schedule and Funding
Status

## Slide 10
Detectors: larger crystals; sensor layout optimized individually for iZIP and HV
prototypes for both types been tested (using old electronics): performance meets or exceeds expectation
Detector tower (mechanical structure, wiring): design ready, mechanical prototype exists; wiring prototype exists – final version expected soon
Developments (selection of activities)
HV
Status
iZIP
iZIP
HV

## Slide 11
Detectors: larger crystals; sensor layout optimized individually for iZIP and HV
prototypes for both types been tested (using old electronics): performance meets or exceeds expectation
Detector tower (mechanical structure, wiring): design ready, mechanical prototype exists; wiring prototype exists – final version expected soon.
Readout electronics: Preamp: thermal readout design ready; charge readout: circuits are being tested “Warm electronics” (outside cryostat): prototype exists, tests underway
Developments (selection of activities)
Status

## Slide 12
Status
Detectors: larger crystals; sensor layout optimized individually for iZIP and HV
prototypes for both types been tested (using old electronics): performance meets or exceeds expectation
Detector tower (mechanical structure, wiring): design ready, mechanical prototype exists; wiring prototype exists – final version expected soon.
Readout electronics: Preamp: thermal readout design ready; charge readout: circuits are being tested “Warm electronics” (outside cryostat): prototype exists, tests underway
DAQ: MIDAS based, being developed at UBC with help from TRIUMF, UofT and others
Cryogenics design completed; Dilution refrigerator is procured; shielding: design close to complete
Backgrounds: extensive material screening; tracking and monitoring; minimizing cosmogenic exposure; radon filter to be installed for detector assembly cleanroom at SNOLAB
Developments (selection of activities)
Shielded transport container
Radon Filter

## Slide 13
DAMA
DAMA
CDMS Si
LUX 2013
DEAP
CDMS II 2015
DAMIC 2016
SuperCDMS LT 2014
CRESST
2015
CDMSlite
2015
Solar Neutrinos
Atmospheric Neutrinos
Si HV
Si iZIP
Ge HV
Ge iZIP
LZ
Sensitivity
XENON1T 2017
Goal
Longterm goal

## Slide 14
Cryogenic Underground TEst facility (CUTE) – a Queen’s Project
Motivation
Detector performance: Detector integrity after transportation Background discrimination Noise performance (impact of background)
Background studies Confirm that screening program and handling procedures are appropriate Study cosmogenic backgrounds (3H, 32Si)
Available for testing of other cryogenic detectors for rare event searches (e.g. EURECA detectors for integration with SuperCDMS)
Opportunity for early science! (BG O (few evt/keV/kg/d below 10 keV))
Schedule
Cryostat ordered, to arrive at Queen’s this summer
Infrastructure (water tank, platform, crane): ordered, installation starts in July
Sept/Oct: test cryostat at Queen’s; installation underground end of 2017/early 2018
Commissioning: winter/spring 2018 (~2-3 years ahead of SuperCDMS)
Water Shield
Fridge: <10 mK
Vibration damping
Pb
CUTE

## Slide 15
Conclusions
SuperCDMS SNOLAB aims at detecting dark matter WIMPs
Main focus are low-mass WIMPs (< 10 GeV/c2)
Project planning well under way
R&D is completed, full technical design close to completion
Start of operation expected in 2020
Initial payload: ~30 kg, significant push in threshold and sensitivity
Upgrades (e.g. improved HV detectors, EURECA detectors, …) will allow us to reach the neutrino floor at low mass and/or check discovery claims at high mass
CUTE: Queen’s initiative for an underground test facility, operational in early 2018 (detector performance studies, background checks, early dark matter science)