## Slide 1: SoLAr V2 Track Reconstruction
Guilherme Ruiz - 22/11/2023

## Slide 2: Charge - Track reconstruction
Apply DBSCAN clustering
  Cluster hits in the -plane
  Determine the intervals in between clusters
  Generate fake data filling dead areas withing the intervals
  Cluster hits + fake data in the -plane
  Cluster hit labels from first stage with hit -coordinates
  Remove fake data
Fit line to clusters with RANSAC regression
  Use hit charge as weight for fit
  Optionally re-cluster and fit outliers to find secondary tracks
Define same sized stacked cylinders centered around fitted line
  Two parameters are needed: the radius and height of the cylinders
  Apply buffer regions at the extremities of the tracks
  Discard points already accounted for in previous cylinders when iterating over all cylinders

## Slide 3: per cylinder translates into !
With dead area
Interpolating dead area with mean

## Slide 4: statistics
P-value: Probability of RANSAC fit being “random”

## Slide 5: Light – Correlating events
~68% of the charge events have external trigger and survive pre-processing
~97% of the surviving charge events find a matching light event
~65% of the charge events survive  1+ light events per charge event

## Slide 6: Correlated charge and light event display
“Ooh!” - Stefan

## Slide 7: Light and Charge – Event level correlation
Non-zero gaussian peak plus exponential decay in ratio plot
Two populations in 2D histogram
All events

## Slide 8: Light and Charge – Event level correlation
Fit peak farther from 0
Single populations in 2D histogram
Only single tracks larger than 30cm

## Slide 9: Light track – Fit method
Select top 5 SiPMs with largest light signal
  Must be non-zero
  Minimum of 3 SiPMs
  and are determined by SiPM coordinates
is calculated by averaging the -coordinate of the charge hits within that SiPM’s quadrant weighted by their charge
  If there is no charge data (i.e. dead chip), is the -coordinate of the closest point in the fitted charge track to the SiPM in , provided that the track crosses the SiPM’s quadrant
  If no track crosses the SiPM’s quadrant, is the average z from all hits in the event
Apply RANSAC fit to resulting points

## Slide 10: Light track versus Charge track

## Slide 11: Analysis code overview
Load charge file
Filter events
seconds
~ 30 seconds
Load light file
Filter SiPMs
Minutes
~ 7 Minutes
Match events
Seconds
~ 30 Seconds
Fit tracks
Minutes
~ 4 Minutes
Load charge file
Filter events
Load light file
Filter SiPMs
Match events
Fit tracks
Run time
Event #
Track #
Track labels mask
Fit line
(point & vector)
Fit length
Fit p-value
SiPM #
dQ list
dx
Etc…
Total charge
Total light
Angle
Distance
Light
SiPM data
SiPM #
Light fit line
Fit threshold
Average z
Charge
Light
Etc...
Output file structure
Light and Charge data frames are saved to bz2 files (compressed CSV)
Dictionary of light to charge matches is saved to JSON file
Analysis output file is saved to pickle file to preserve non-JSON-serializable objects
Saved data can be loaded instead of reloading root files to speed up processing

## Slide 12: Summary
Reconstructing events required refined methods due to the large areas without charge pixel coverage
Track reconstruction is performing remarkably well by combining DBSCAN with RANSAC algorithms
Most charge events find a matching light counterparts
There is a visible correlation between track position and the light detected, but still not fully understood
Light “tracks” are in reasonable agreement with their respective charge counterparts
The analysis is being coded with scalability and ease of usage in mind

## Slide 13: Thank you!

## Slide 14: Backup slides

## Slide 15: Dead area map

## Slide 16: FAQ
DBSCAN parameters:
  xy_epsilon = 8 mm (2 pixels)
  Z_epsilon = 8 mm
RANSAC parameters:
  Residual_threshold = 6
  Max_trials = 1000
RANSAC has random component and may not always return the same fit
Cylinder parameters are determined dynamically but bound by DBSCAN parameters

## Slide 17: Cylinder parameters - estimation
z_epsilon
xy_epsilon

## Slide 18: Cylinder parameters - estimation
z_epsilon
xy_epsilon
Minimum is bound to