## Slide 1: Energy reconstruction with Q-Pix readout
Guilherme Ruiz
University of Manchester
Notes: Far Detector 2 on Wednesday

## Slide 2: Solar neutrinos
Solar neutrinos are very low energy processes which hopefully will be within the Module of Opportunity’s physics range
With SoLAr, we aim to have sufficient efficiency to probe the the HEP and B8 region (from 5MeV)
Our biggest challenge ahead is dealing with the background in such low energies
  Below 5MeV the background completely dominates the signal
The combination light and charge on a pixel readout is our technology of choice for this task

## Slide 3: Solar neutrinos vs. Radiogenic background
Left: incoming energy from solar neutrinos
Right: deposited energy from solar neutrinos and radiogenic background in the detector
10000 events per process
10000 events per process

## Slide 4: Background discrimination
Scintillation light (L) and ionization charge (Q) yield are anticorrelated and thus complimentary in Lar (see graph).
Both come with properties we can use for background discrimination.
Our group is currently working on discrimination methods using
Pulse shape discrimination from L (Nicholas Lane)
Track directionality reconstruction from Q (Shion Kubota)
Particle identification from Q (Me)
https://journals-aps-org.manchester.idm.oclc.org/prb/pdf/10.1103/PhysRevB.20.3486

## Slide 5: Particle identification (PID) - method
Each particle has a particular energy deposit curve in LAr
We can associate a track to its primary particle by looking at its profile
We can associate a track to its primary particle by looking at its 𝑑𝐸/𝑑𝑥 profile
Protons, muons and pions are particularly easy to identify via
Protons, muons and pions are particularly easy to identify via 𝑑𝐸/𝑑𝑥
Each particle has a particular energy deposit curve in LAr

## Slide 6: Energy reconstruction from Q-Pix resets
Each reset corresponds to 0.1475MeV of deposited energy
Each reset corresponds to 1fC of deposited charge
Each electron corresponds to 23.6eV of deposited energy
(LAr function for ionization)
Each electron corresponds to 23.6eV of deposited energy
(LAr 𝑾 function for ionization)
Each reset corresponds to 0.1475MeV of deposited energy
Each reset corresponds to 1fC of deposited charge

## Slide 7: reconstruction from Q-Pix resets
Generate single proton, muon and pion Geant4 simulations* with energies 200, 300, 400 and 500 MeV along the y coordinate
Compute the energy deposited per pixel by summing resets.
Average the reset times in each pixel to get the mean z coordinate
Sort pixels by x, y and t respectively to obtain tracks
Compute and by taking the difference of deposited energy and coordinates of the sorted pixels
Compute 𝑑𝐸 and 𝑑𝑟=√(𝑑𝑥^2+𝑑𝑦^2+𝑑𝑧^2 ) by taking the difference of deposited energy and 𝑥, 𝑦, 𝑧 coordinates of the sorted pixels
Generate single proton, muon and pion Geant4 simulations* with energies 200, 300, 400 and 500 MeV along the y coordinate
Compute the energy deposited per pixel by summing resets.
Average the reset times in each pixel to get the mean z coordinate
Sort pixels by x, y and t respectively to obtain tracks
“I’ve got to start somewhere”
Every result presented here is for 200MeV protons only
*No diffusion or recombination

## Slide 8: reconstruction - Finding tracks
Event 0
Good track
Event 1
Bad track
Event 4074
No track

## Slide 9: reconstruction - Finding tracks
Good track
No Recombination
No Diffusion
200MeV single proton events

## Slide 10: reconstruction - Finding tracks
Bad track
No Recombination
No Diffusion
200MeV single proton events
The reconstruction obviously fails

## Slide 11: reconstruction - Finding tracks
Original event
Processed event
Processing ”bad tracks”
DBSCAN
DBSCAN parameters:
Min samples = 3
Epsilon = 1.5 x pixel size
Use DBSCAN to exclude resets that do not form a track and small clusters off-track

## Slide 12: reconstruction - Finding tracks
Processed event
Cluster #0
Cluster #2
One track or two tracks?
What is the Geant4 truth?
Particle index
Track #0
Track #2
Geant4 truth

## Slide 13: reconstruction - Finding tracks
Processed event
Cluster #0
Cluster #2
One track or two tracks?
What is the Geant4 truth?
Particle index
Track #0
Track #2
Geant4 truth
Luck or consistent with other events?

## Slide 14: reconstruction – Filtering “bad tracks”
Filtering bad events
Experimental method:
Use pixel size – no G4 truth
Exclude events with a maximum reconstructed value larger than a certain ratio of the pixel size
Exclude events with a maximum reconstructed 𝑑𝑟 value larger than a certain ratio of the pixel size
Experimental method:
Use pixel size – no G4 truth
Above , the number of events excluded becomes “approximately constant” at
This corresponds to maximum (the pixel diagonal pitch )

## Slide 15: reconstruction – “good tracks” after DBSCAN
Processed events
200MeV single proton events
Bad events filtered
Maximum reconstructed residual range is 34 cm

## Slide 16: 200MeV single proton events
Event 0
Good track
Event 1
Bad track
Event 4074
No track
No Recombination
No Diffusion
reconstruction – “good tracks” after DBSCAN
How many of the originally “bad tracks” are “now good” tracks?

## Slide 17: Summary
The 𝑑𝐸/𝑑𝑟 reconstruction works remarkably well for “Good tracks”
“Bad tracks” can be usable after some processing with clustering algorithms but still produce “noise”
Using a value slightly above the pixel pitch as maximum 𝑑𝑟 to filter events is the simplest way to optimize the reconstruction
It is expected that at higher energies we will see less “good tracks”. Lower energy events may be easier to reconstruct
This method only works for tracks. Neutrinos and electrons will be considerably more challenging
Some events are impossible (?) to be used for this study regardless of clustering algorithms

## Slide 18: Thank you!

## Slide 19: Backup slides

## Slide 20: Radiogenic background

## Slide 21: reconstruction – Originally “good tracks”
Only “good” events
200MeV single proton events
Bad events filtered
Max reconstructed residual range is 44.3 cm

## Slide 22: 200MeV single proton events
Event 0
Good track
Event 1
Bad track
Event 4074
No track
No Recombination
No Diffusion

## Slide 23: reconstruction – Impossible tracks
”Worse tracks”
Geant4 truth
Processed RTDs
Impossible to use (?)

## Slide 24: Diffusion study
Generate 10 MeV single electron Geant4 simulations with drift distances 1mm, 5mm, 1cm, 2cm, 5cm, 10cm, 20cm, 50cm, 1.0m, 1.5m, 2.0m, 2.5m, 3.0m and 3.5m
Compute the energy reconstruction efficiency from RTDs with and without recombination
Plot the mean of the distribution for each drift distance with binomial error as error bars

## Slide 25: 10 MeV single electrons – No recombination
No Recombination

## Slide 26: 10MeV single electron events
No Recombination
10 MeV single electrons – No recombination

## Slide 27: 10MeV single electron events
With Recombination
10 MeV single electrons – With recombination

## Slide 28: 10MeV single electron events
With Recombination
10 MeV single electrons – With recombination

## Slide 29: 10MeV single electron events
With Recombination
X
No Recombination
10 MeV single electrons – Recombination ratio