## Slide 1: Neutrino CP Violation with the European Spallation Source neutrino Super Beam Marcos Dracos IPHC-Strasbourg
Lake Louise Winter Institute 2022
Design Study financed by EU

## Slide 2: European Spallation Source
under construction phase
(~2 B€ facility)
Neutron facility
(equivalent to SNS in the USA)

## Slide 3: ESS proton linac
The ESS will be a copious source of spallation neutrons.
5 MW average beam power.
125 MW peak power.
14 Hz repetition rate (2.86 ms pulse duration, 1015 protons).
Duty cycle 4%.
2.0 GeV protons
  up to 3.5 GeV with linac upgrades
>2.7x1023 p.o.t/year.
Linac ready by 2025 (full power)
4
8
time (ms)
Brightness (n/cm2/s/sr/Å)
7
5
x1014
UK TS1
128 kW
UK TS2
32 kW
SNS
1-2 MW
JPARC
0.3-1 MW
ILL 57 MW
ESS 5 MW
2015 design
0
1
2
3
3
4
1
2
6
λ = 1.5 Å
ESS 5 MW
2012 design (TDR)
empty space for energy upgrades

## Slide 4: European Spallation Source
Oct. 2020
July 2021
European Research Infrastructure Consortium (ERIC) since 2015
target
instruments
utility buildings
linac
Beam commissioning end 2022, construction complete by 2025

## Slide 5: European Spallation Source as Neutrino Facility for CP violation observation (2nd Oscillation maximum)
νμ→νe
or, what else can we do with 5 MW proton beam?

## Slide 6: Oscillation probability (neutrino beams)
"solar"
"atmospheric"
"interference"
matter effect
δCP dependence,
sizable matter effect for long baselines and high energy
for antimatter: δCP →-δCP and a→-a
fake matter/antimatter asymetry due to matter effect
Matter-antimatter asymmetry

## Slide 7: δCP and matter-antimatter asymmetry magnitude
(Jarlskog invariant)
Theoretical models predict that if |sinδCP|≳0.7 (45°<δCP<135° or 225°<δCP<315°), this could be enough, under assumptions, to explain the observed asymmetry.
(from the already observed CP violation in the hadronic sector)
(Nucl.Phys.B774:1-52,2007, arXiv:hep-ph/0611338)

## Slide 8: Use all this ESS linac power to go to the second oscillation maximum
but why?

## Slide 9: Neutrino Oscillations with "large" θ13
solar
more sensitivity at 2nd oscillation max.
P(νμ→νe)
L/E
1st oscillation maximum
2nd oscillation maximum
θ13=1º
("small" θ13)
θ13=8.8º
("large" θ13)
dCP=-90
dCP=0
dCP=+90
L/E
for small θ13 1st oscillation maximum is better
for "large" θ13 1st oscillation maximum is dominated by atmospheric term
CP interference
CP interference
solar
atmospheric
atmospheric
θ13=1º
θ13=8.8º
(arXiv:1110.4583)
L/E
L/E
solar
1st oscillation max.: A=0.3sinδCP
2nd oscillation max.: A=0.75sinδCP
(see arXiv:1310.5992 and arXiv:0710.0554)
(before 2012)
(after 2012)

## Slide 10: Having access to a powerful proton beam…
What can we do with:
5 MW power
2 GeV energy
14 Hz repetition rate
1015 protons/pulse
>2.7x1023 protons/year
p
π
ν
decay tunnel
proton beam
target
hadrons
hadronic collector
(focusing)
Detector
physics
⨂B
conventional neutrino (super) beam
at 100 km from the target, per year (in absence of oscillations)
almost pure νμ beam
small νe contamination which could be used to measure νe cross-sections in a near detector

## Slide 11: Can we go to the 2nd oscillation maximum using our proton beam?
Yes, if we place our far detector at around 500 km from the neutrino source.
Water Cherenkov detector
Neutrino Oscillations
Proton decay
Astroparticles
Understand the gravitational collapsing: galactic SN ν
  Supernovae "relics"
Solar Neutrinos
Atmospheric Neutrinos
500 kt fiducial volume (~20xSuperK)
Readout: ~20” PMTs
30% optical coverage
78 m
78 m

## Slide 12: Neutrinos in the far detector
540 km (2.5 GeV), 10 years
Below ντ production, almost only QE events, not suffering too much by π0 background.
neutrinos
anti-neutrinos
5 years
5 years
δCP=0

## Slide 13: 2nd Oscillation max. coverage
2nd oscillation max.
well covered by the ESS neutrino spectrum
1st oscillation max.
full coverage of the 2nd oscillation max.

## Slide 14: ESS Linac modifications to produce a neutrino Super Beam
European Spallation Source Linac

## Slide 15: How to add a neutrino facility?
The neutron program must not be affected and if possible synergetic modifications.
Linac modifications: double the rate (14 Hz → 28 Hz), from 4% duty cycle to 8%.
Accumulator (C~400 m) needed to compress to few μs the 2.86 ms proton pulses, affordable by the magnetic horn (350 kA, power consumption, Joule effect)
  H- source (instead of protons),
  space charge problems to be solved.
~300 MeV neutrinos.
Target station.
Underground detector.
Short pulses (~μs) will also allow DAR experiments (as those proposed for SNS) using the neutron target.

## Slide 16: Which baseline?
~60% δCP coverage at 5 σ C.L.
>75% δCP coverage at 3 σ C.L.
systematic errors: 5%/10% (signal/backg.)
CPV (Nucl. Phys. B 885 (2014) 127)
Zinkgruvan
Garpenberg
Candidate active mines
pre-project studies

## Slide 17: ESS modifications and operation
H- source
time operation option
injection
RF
extraction
collimation
accumulator latice
Split Proton Beam
Neutrino Beam Direction
Collimators
Horns and Targets
Decay Volume
(He, 4x4x25 m3)
Beam Dump
8 m concrete
Switchyard

## Slide 18: Latest Improvements
New Magriation Matrices for the far detector
Genetic Algorithm for Target Station optimisation
WC detector
Phys. Rev. ST Accel. Beams 16, 061001 (2013)
new far detector reconstruction algorithm
(publication is coming)
horn optimisation

## Slide 19: Improvements and Optimisations
360 km
540 km
ESSnuSB
θ12 = 33.44°
θ13 = 8.57°
θ23 = 49.2°
Δm221 = 7.42e-5
Δm231 = +2.517e-3
2nd osc. max.
507 ktons far detector
very preliminary
(to be confirmed)
very preliminary
(to be confirmed)
https://arxiv.org/abs/2107.07585

## Slide 20: Improvements and optimisations
360 km
540 km
>72% after 10 years
very preliminary
360 km
540 km
Precision measurements
ΔδCP<8° for all values

## Slide 21: Muons at the level of the beam dump
<Eμ>~0.5 GeV
<Lμ>~3 km
() | ( ) | ( ) | ( ) | ()
decay tunnel length

## Slide 22: ESSνSB and (R&D) synergies
Super Beam
Neutrino Factory
Muon Collider
+Decay At Rest and Coherent scat.
(with short pulses)
nuSTORM
nm or nm
nm + ne
ne + nm
2.7x1023 p.o.t/year
ESSμSB
ESSνSB

## Slide 23: Supporting institutions of ESSνSB
COST Action EuroNuNet (CA15139): ended March 2020
  https://euronunet.in2p3.fr
  video for scientists: https://www.youtube.com/watch?v=PwzNzLQh-Dw
EU-H2020 Design Study ESSνSB: on going up to March 2021 (3 months extension due to COVID19)
  https://essnusb.eu
  video for general public: https://www.youtube.com/watch?v=qAnvft0nAlg

## Slide 24: Conclusion
The ESS proton linac will be soon the most powerful linac in the world.
ESS can also become a neutrino facility (ESSνSB ) with enough protons to go to the 2nd oscillation maximum and increase significantly the CPV sensitivity and precise measurement of δCP.
The European Spallation Source will be ready by 2025, upgrade decisions by this moment.
Rich muon program for future ESS upgrades
  Low energy nuSTORM
  Muon Collider R&D
Conceptual Design Report by end of March 2022
New applications under preparation

## Slide 25: Backup

## Slide 26: Possible ESSνSB schedule (2nd generation neutrino Super Beam)
2021: End of ESSνSB Design Study, CDR and preliminary costing
2012: inception of the project
2016-2019: beginning of COST Action EuroNuNet
2018: beginning of ESSνSB Design Study (EU-H2020)
2022-2024: Preparatory Phase, TDR
2025-2026: Preconstruction Phase, International Agreement
2027-2035: Construction of the facility and detectors, including commissioning
2036-: Data taking
Nucl. Phys. B 885 (2014) 127
CDR

## Slide 27: ESSνSB at the European level
11 countries
Starting date: 01/01/2018
Ending date: 31/12/2021 → 31/03/2022,
Duration: 48+3 Months,
3 months extension due to COVID19
Kick-off meeting: 15 January 2018, Lund (ESS),
90% of the budget already received,
All deliverables and milestones ready on time (some rescheduling due to COVID19 has been arranged with the EU Project Officer)

## Slide 28: ESSνSB at the European level
A H2020 EU Design Study (Call INFRADEV-01-2017)
Title of Proposal: Discovery and measurement of leptonic CP violation using an intensive neutrino Super Beam generated with the exceptionally powerful ESS linear accelerator
Duration: 4 years
Total cost: 4.7 M€
Requested budget: 3 M€
15 participating institutes from 11 European countries including CERN and ESS
6 Work Packages
Approved end of August 2017
ESSνSB
BENE (2004-2008)
ISS (2005-2007)
EUROν (2008-2012)
LAGUNA (2008-2010)
LAGUNA-LBNO (2010-2014)
COST Action CA15139 (2015-2019)

## Slide 29: Muon Collider as Higgs Factory
Carlo Rubbia
arXiv:1908.05664
HIFI Uppsala Workshop 2-3 March 2020

## Slide 30: Muons at ESS (ESSμSB)

## Slide 31: Decay At Rest at ESS
Possible if short pulses (~μs)
A
+
-
~99%
+
e+
p


e
  26 ns
  2.2 μs
Fragments
DAR
capture
Well known neutrino spectra (DAR).
Very high neutrino intensities ~ 5x1015 n/s.
Separate neutrinos of different flavors by time cut.
Role that neutrino-nucleus interactions play in the supernova explosion process and subsequent nucleosynthesis.
Accurate knowledge of neutrino-nucleus cross sections is important (almost no data exist).
This lack of knowledge significantly limits our understanding of supernovae and of terrestrial observations of cosmic neutrinos to probe the deepest layer of these powerful explosions.

## Slide 32: Coherent Scattering at ESS
JHEP 02 (2020) 123
ESS can generate the largest pulsed neutrino flux suitable for the detection of Coherent Elastic Neutrino-Nucleus Scattering (CEνNS ).
Innovative detector technologies able to profit from the order-of-magnitude increase in neutrino flux provided by the ESS, along with their sensitivity to a rich particle physics phenomenology accessible through high-statistics, precision CEνNS measurements, are under study.

## Slide 33: Possible scenario for new near future applications
Possible WPs:
Civil engineering (onsite and offsite) abd safety.
Linac accumulator and race-track.
Target Station, hadron/muon production and muon extraction.
Low Energy nuSTORM.
Detectors and physics performance (synergy between ESSnuSB and LEnuSTORM).
Muons for future. applications, including 6D cooling tests (several locations are possible).

## Slide 34: Low Energy nuSTORM at ESS
Proposed at FERMILAB and CERN (~3.8 GeV muons)
Sterile Neutrino searches
Neutrino cross sections measurements with unprecedented precision
LBL performance improvement by systematic error mitigation
To be adapted for lower muon energies (~0.5 GeV)
preliminar studies for ESS
sterile neutrino searches