## Slide 1
William Shields
(william.shields@rhul.ac.uk)
on behalf of BDSIM group:
A. Abramov, S. Boogert, S. Gibson, H. Garcia-Morales, H. Pikhartova, L. Nevay, J. Snuverink, S. Walker
BDSIM:
https://arxiv.org/abs/1808.10745
http://www.pp.rhul.ac.uk/bdsim
7th December 2018, JAI Fest – RHUL.
BDSIM Applications for Proton Therapy

## Slide 2: Outline
Introduction.
Building a BDSIM model.
Proton therapy gantry example.
Collaboration.
Summary & outlook.
07th December 2018

## Slide 3
Radiotherapy technique using high energy protons.
Dose deposited at a precise depth.
Vary beam energy to build up Spread Out Bragg Peak.
Correct dose is crucial – energy, size, shape, etc.
Gantry nozzle simulations – no prior accelerator.
Proton Therapy Simulations
07th December 2018
http://www.shi.co.jp/
Example TOPAS Simulation: https://gray.mgh.harvard.edu
Notes: Constant desire to improve proton therapy machines:
  Treatment quality, efficiency, safety & reduced costs.
Monte Carlo modelling used in machine design.
Simulation challenges still exist:
  Tight beam profile constraints at isocentre – high precision.
  Significant losses – many particles required for accurate statistics.
  Computationally expensive.
  Separate simulations.

## Slide 4
Standard Approach
07th December 2018
Inspect machine optics and identify regions of interest.
  Develop Monte Carlo simulations as required.
Degrader and collimation
Wall aperture.
Nozzle and isocentre.
Simulation challenges - high precision, many particles:
  Computationally expensive.
  Separate simulations.
Notes: Constant desire to improve proton therapy machines:
  Treatment quality, efficiency, safety & reduced costs.
Monte Carlo modelling used in machine design.
Simulation challenges still exist:
  Tight beam profile constraints at isocentre – high precision.
  Significant losses – many particles required for accurate statistics.
  Computationally expensive.
  Separate simulations.

## Slide 5: Simulating a Beam Line
Regions of a proton therapy beamline:
  Particle source / acceleration.
  Beam transport to gantries.
  Gantry beam transport.
  Gantry nozzle.
  Isocentre.
  Shielding & Environment
07th December 2018
Our aim: To demonstrate a start-to-end model of a proton therapy gantry in a single simulation.
1
2
3
4
5
6

## Slide 6
Python utilities for automatic conversion:
  Pybdsim, pymadx, pymad8, pytransport
Optimise model with options.
Building a BDSIM Model
Components
Sequence
Beam
Options
User geometry placement
07th December 2018

## Slide 7
Custom external geometry can be placed and field maps overlaid.
Geometry e.g. GDML can be placed in the beam line.
Python package pyg4ometry to create Geant4 geometry
  https://bitbucket.org/jairhul/pyg4ometry/
  STL/STEP meshes.
BDSIM Geometry
07th December 2018
Example concrete shielding
Custom GDML collimator.
R. Bodenstein & A. Abramov.
STL conversion to GDML.

## Slide 8
Interleaved wedge degrader based on design from Center for Proton Therapy at PSI .
Significant impact on beam phase space distribution and spectrum.
Energy Degrader
Before
After
07th December 2018

## Slide 9
Degrader for energy selection
Beam transport
Suggested shielding
Isocentre
Treatment Room
Support block
Shielding wall with aperture
Gantry 2 from Paul Scherrer Institute in Switzerland.
  Lattice publicly available: http://aea.web.psi.ch/Urs_Rohrer/MyFtp
  Conceptual design – different from real machine.
Example Proton Therapy Gantry
07th December 2018
Degrader and collimators added.
Example shielding and element support block geometry generated.

## Slide 10
Particle properties recorded after every element (position, momentum, energy etc).
Twiss functions calculated with full statistical uncertainties.
Excellent agreement with PTC tracking routines.
Lattice Optics
07th December 2018

## Slide 11
Energy deposition per 10 cm along curvilinear axis for full machine length.
Loss Map and Energy Deposition
07th December 2018

## Slide 12
Profiles prior to nozzle section.
  Primary protons and secondary particles.
Spectra of all particle species.
Spectra and Lateral Beam Profiles
07th December 2018

## Slide 13
Collaboration with IBA (Ion Beam Applications), Belgium.
Simulation of two beam lines.
Improve beam profile with optimised nozzle and optics.
Enhanced dose rate from degrader efficiency studies.
Loss maps for shielding activation.
Publish next year.
Collaboration with IBA
Nozzle (enclosed)
Water Phantom
Degrader
To second room
Proscan Eyeline Beam Line
Isocentre
Degrader (enclosed)
Gantry rotation point
Proteus One Compact Gantry
07th December 2018

## Slide 14
Excellent agreement with BDSIM and other tracking codes.
IBA Compact Gantry Optics
07th December 2018

## Slide 15
IBA Compact Gantry Loss Map
07th December 2018
Loss map for 70 MeV beam.

## Slide 16
Calculate shielding activation rate.
Presented in Robin Tesse PhD thesis (ULB).
ICAP 18 (20-24th Oct, Key West, Florida).
IBA Shielding Activation Studies
Proton interactions
Protons & Neutron interactions
Shielding only
07th December 2018

## Slide 17
First start-to-end simulations of proton therapy beam lines.
Verified optics, generated loss maps, shown spectra and lateral profiles, and demonstrated potential for shielding & dosimetry.
BDSIM development:
  Dosimetry, further fringe fields, nozzle components.
Expanded analyses.
More detailed model.
Watch this space!
Summary & Outlook
07th December 2018

## Slide 18
Thank you
William Shields
william.shields@rhul.ac.uk
http://www.pp.rhul.ac.uk/bdsim/