## Slide 1: A beam position monitor for the AWAKE experiment based on Cherenkov diffraction radiation
Collette Pakuza
JAI Fest
Friday 10th December 2021

## Slide 2: Contents
The AWAKE experiment
Motivation for the Cherenkov diffraction radiation (ChDR) beam position monitor (BPM)
Design considerations
Status and future tests

## Slide 3: The AWAKE experiment
AWAKE: Advanced Proton Driven Plasma Wakefield Acceleration Experiment

## Slide 4: The AWAKE experiment
Run 1 (2016-18)
ChDR BPMs
Protons 48 nC, 250 ps sigma
Electrons 150 pC, 2.5 ps sigma
Laser 120 fs, 450 mJ
Rb vapour

## Slide 5: Motivation for ChDR BPM
Proton signal dominates below 2 GHz
Current system cannot measure electrons in presence of protons
Exploit the different bunch lengths
Operate at high frequency
Very mechanically challenging for traditional electrostatic monitors

## Slide 6: Motivation for ChDR BPM
New technique based on Cherenkov diffraction radiation
Polarization radiation produced when charged particle travels in close proximity to the surface of a dielectric target
  Non-invasive measurement
  Large emitted photon flux
  Well-defined angular emission

## Slide 7: Design for AWAKE
Limited space available
ChDR buttons designed to be compatible with existing p-BPM body
Plan:
Convert one p-BPM to c-BPM
Split signal of e-BPM to measure protons
Install additional c-BPM in drift space

## Slide 8: Design for AWAKE
Proton bunch not gaussian, spectrum extends to frequencies higher than expected
Operating frequency in the range of 10s GHz means electron signal dominates
30 GHz chosen due to availability of waveguide (WG) components in house
WR28 WG used with cutoff 21 GHz acting as high-pass filter
Collaboration with TRIUMF for the front-end electronics
Schematic of entire ChDR BPM setup

## Slide 9: Design for AWAKE
Alumina rod ⌀6 mm
Flange
Button
Beam
Transition can be attached here
Mechanical design:
⌀6 mm alumina dielectric radiator oriented at Cherenkov angle (, )
In metallic flanged button
Cut flush on beampipe side and extended at the exit for attachment of a matched-impedance transition to an industry standard WR28 rectangular waveguide

## Slide 10: WG transitions
Transition designed to maximize power transfer at 30 GHz between dominant modes of the waveguides
Based on quarter-wave impedance transformer
Section introduced with intermediate value of dielectric constant
Alumina
Fused quartz
WR28 (Ka-band)
9.88 mm
TE11 mode
TE10 mode

## Slide 11: WG transitions
Numerical analysis shows forward transmission coefficient for all modes below 40 GHz
Length of intermediate section optimized to produce largest contribution of power from the fundamental mode of circular dielectric (TE11)
S21^2 = 99% power transmission @ 30 GHz
Contributions from all other modes in circular dielectric are suppressed
Mode number in brackets

## Slide 12: Numerical simulations
Full simulation with beam to investigate system behavior
Parameter | Value
Bunch sigma | 2.5 ps
Bunch charge | 150 pC
Radiator angle | 71˚
Radiator length | 86.27 mm
Radiator dielectric constant (alumina 99.5% purity) | 9.9
Mesh | 10 mesh cells per wavelength
Total number of mesh cells | 252 million
Average simulation time | Approx. 15 h
Beampipe diameter (AWAKE) | 60 mm
R281A WR28 to 50 Ω coaxial adapter
Circular to rectangular waveguide transition

## Slide 13: Numerical simulations
ChDR
Electron beam field
E-field
30 GHz, 300 MHz BW Butterworth filter
Provides the expected signal output for different beam offsets
Promising signal level out

## Slide 14: Numerical simulations
Parameter | Value
Position sensitivity | 5.86 %/mm
Signal-to-noise ratio | Approx. 60/70 dB
Resolution | 34.6 µm (300 MHz BW BPF)
Summary of BPM specifications for 150 pC, 2.5 ps σ electron bunch
By taking the signal level at a given time for different beam offsets, provides position response curve
Useful system requirements for development of front-end electronics by TRIUMF

## Slide 15: Status of BPM and future tests
Alumina rods and fused quartz pieces should arrive in following weeks
Allows for completion of manufacturing process of buttons and transitions
Buttons to be tested in-vacuum at CLEAR once accelerator restarts in March 2022
Installation of c-BPMs at AWAKE with TRIUMF electronics in Summer 2022
ChDR buttons in existing pBPM body
Radiator (alumina)
Collar
Flanged button compatible with pBPM body
WG transition

## Slide 16: Thank you for your attention! Wish you all a Merry Christmas!