## Slide 1: Synchrotron Radiation Interferometry for Beam Size Measurement at the LHC
Daniele BUTTI

## Slide 2: Introduction

## Slide 3: Why measure transverse beam size?
P4
BI & RF
Large Hadron Collider
Luminosity:
→ quantifies collider performance
→ depends on transverse beam size
event rate
Machine optimization ⇒ beam size measurement

## Slide 4: Transverse diagnostics at the LHC
Synchrotron radiation telescope
no absolute measurement, calibration required
non-invasive
→ continuous monitoring
Wire-scanners
absolute measurement
invasive
→ limited use
Current status: telescope calibrated against wire-scanners in dedicated fills and used in nominal operation
Beam
Carbon wire
Shower of
secondaries
Scintillator
Wire position
Shower intensity
Beam profile
2σy
x
y
Beam image
2σx
Beam profile
2σy
Beam
Synchrotron radiation (SR)
Telescope
Camera

## Slide 5
Synchrotron radiation interferometer
absolute measurement
non-invasive
not suitable for continuous monitoring (intensifier ageing)
Goal: use interferometer to complement SR telescope and wire-scanners.
periodically check calibration stability
redundant and independent measurement
Need for synchrotron radiation interferometry
Synchrotron radiation telescope
no absolute measurement, calibration required
non-invasive
→ continuous monitoring
Wire-scanners
absolute measurement
invasive
→ limited use
Present…
… future?

## Slide 6: Synchrotron radiation interferometry at the LHC

## Slide 7: Interferometry for source size measurement
light source
lens
interferogram
slits
In classical optics, Van Cittert-Zernike theorem:
If source is Gaussian:
Assumptions about the source:
(apparently) small
incoherent
isotropic
Typical application field
→ astronomy (stellar interferometer)

## Slide 8: LHC Synchrotron Radiation source
U
D3R
extraction
mirror
~100m straight section
D3L
LHC ring
Point 4
mirror
acceptance
Undulator and dipole at the right side of LHC Point 4
In-vacuum mirror to intercept and extract SR

## Slide 9: Injection energy
U
D3R
extraction
mirror
D3L
LHC ring
Point 4
Injection energy → undulator main source of light
quite smooth and broad light distribution
well localized source at undulator centre
marginal mirror effect
SR intensity at the extraction mirror plane simulated at
~100m straight section
mirror acceptance
beam
⇒ VCZ should work as it is
≈

## Slide 10: LHC Synchrotron Radiation source
U
D3R
extraction
mirror
D3L
LHC ring
Point 4
Flat-top energy → dipoles main source of light
asymmetric and narrow light emission
two interfering sources ~100m afar
relevant diffraction effects from mirror edge
SR intensity at the extraction mirror plane simulated at
~100m straight section
mirror acceptance
beam
⇒ dedicated simulations needed
≠

## Slide 11: Simulations
Package based on Synchrotron Radiation Workshop written
computation of radiated SR field
Physical Optics Propagation through interferometer system
Goal: test interferometer performance aiming at relative error (requested by operation)
Ok VCZ ( )
Ok VCZ ( )
Ok VCZ ( )
with mitigation*
Ok VCZ ( )
with mitigation*
Vertical
Horizontal
Inj
FT
*specific slit configurations are needed to compensate for dipole interference effects, mirror diffraction…
Output: interferometry expected to meet operational requirements
Critical situation for horizontal beam size at flat-top (due to symmetry of dipole radiation)

## Slide 12: Interferometer for LHC Run 3

## Slide 13: Experimental setup
camera
polarizer
filters
eyepiece
lens
from
SR source
collimator
slits

## Slide 14: First measurements during beam test
Preparation test for Run 3 performed in Oct. 2021:
very tight schedule
only few nominal bunches injected
stable beams at injection energy only!
A few interferometer measurements taken in parallel with SR telescope operation
Example of 2D interferogram (horizontal beam size)
Extracted profile fitted to assess fringe visibility
First circulating beam captured by SR telescope

## Slide 15: First measurements during 2021 beam test
Dump and refill
Dump and refill
Interferometer
Telescope (not calibrated!)
Outcome:
good interferometer sensitivity to bunches of different size
precise measurement
qualitative agreement with telescope. Quantitative not available as telescope not calibrated (no time allocated in beam test)

## Slide 16: Conclusion

## Slide 17
Thank you for your attention!
Summary:
in principle, synchrotron radiation interferometry is a powerful technique to complement current LHC transverse diagnostics
synchrotron radiation source is rather complex. Dedicated simulations confirm the applicability to the LHC case.
setup to benchmark the simulation is now operational. Good qualitative results from beam test at injection energy
Plans for upcoming Run 3:
systematic and quantitative benchmark of simulations at injection
performance assessment during energy ramp and at flat-top

## Slide 18: Spares

## Slide 19: LHC SR source in the visible domain
B1
B2
extraction
mirror
UR
D3R
RF section
UL
D3L
mirror acceptance
Undulator radiation
Core radiation
Edge radiation
to P5
from P3

## Slide 20: Flat-top vertical
Scan the incoming light, expect a uniform visibility but…
assessed from fluctuates ~20%
SR source are the D3 dipoles
longitudinally extended
narrow emission
D3 interference oscillations
x center
y center
D
B1
extraction
mirror
UR
D3R
RF section
D3L
source
to slits
source
→ strictly, VCZ not satisfied

## Slide 21: Flat-top horizontal
x center
y center
D
B1
extraction
mirror
UR
D3R
RF section
D3L
source
to slits
source
Visibility cross-cut
oscillation
decay
Mitigation:
decay → adjust
oscillation → wider slits
D3R

## Slide 22: Flat-top horizontal
Source are two D3 → source not well-defined
slit configuration
x center
y center
is the nominal sigma ()
Is the measured visibility constant over the wavefront?
Take-home
VCZ validity around
visibility oscillations not compensated by a particular slit configuration
D
No significanlty better working region