## Slide 1: LhARA to serve the ITRF
Laser-hybrid Accelerator for Radiobiological Applications to serve the Ion Therapy Research Facility

## Slide 2
Our mission is to:
Deliver a systematic and definitive radiation biology programme
Prove the feasibility of laser-driven hybrid acceleration
Lay the technological foundations for the transformation of PBT
  automated, patient-specific proton and ion beam therapy
ITRF
/

## Slide 3: What is LhARA?
A novel, hybrid, approach:
Laser-driven, high-flux proton/ion source
  Overcome instantaneous dose-rate limitation
    Capture at >10 MeV
  Delivers protons or ions in very short pulses
    Bunches as short as 10—40 ns
  Triggerable; arbitrary pulse structure
Novel “electron-plasma-lens” capture & focusing
  Strong focusing (short focal length) without the use of high-field solenoid
Fast, flexible, fixed-field post acceleration
  Variable energy
    Protons: 15—127 MeV
    Ions: 5—34 MeV/u
Front. Phys., 29 September 2020; DOI: 10.3389/fphy.2020.567738

## Slide 4: Radiobiology in new regimens
T. Schneider, C. Fernandez-Palomo, Annaïg Bertho et al.
Dose escalation in the tumour possible – larger tumor control prob.
> 40 Gy/s

## Slide 5: Proton FLASH data review
Study impact of beam parameters in vitro & in vivo
Overall picture somewhat unclear
Continuing analysis of impact on LhARA specification
J. McGarrigle
To appear in

## Slide 6: SFTR data review
Study impact of beam parameters on effect in vivo
Seeking now to pursue experimental programme
J. McGarrigle
Publication in preparation

## Slide 7: Impact on specification of LhARA?
Initiative to build-up evidence base leading to prioritised parameter set underway:
  Measurements:
    At Birmingham MC-40 cyclotron
    Later at SCAPA (see later)
  Simulation/study:
    TOPAZ-nBio
Develop programme to build:
  Evidence base and understanding
  Collaborations with biologists
  Provide basis for prioritised beam/instrumentation specification
Parsons/McGarrigle
Puerta/Prezado

## Slide 8: Radiobiology in new regimens
The ideally flexible beam facility can deliver it all!
 substantial opportunity for a step-change in understanding!
Time
domain
Space
domain
Energy
Ion
species
In combination and with chemo/immuno Therapies

## Slide 9: Status: resources
To serve ITRF: 2 + 3-year project in 6 work packages:
  Project Management
  Laser-driven proton and ion source
  Proton and ion capture
  Real-time dose-deposition profiling
  Novel, automated, end-station development
  Facility design and integration
First two years of “Five-year plan”
CCAP-TN-10
2-year Preliminary Activity – Project start 01Oct22

## Slide 10: Progress: design & integration: Stage 1
Activation study:
Ongoing contract with TUVSUD; seek to determine:
  Required shielding thickness and building constraints
  Guidance on operation method
  Guidance on material use & activation
T.J. Kuo
K. Long
J. Pasternak
R. Razak
W. Shields
N. Bliss, A. Goulden, C. Hill, H. Owen, C. Whyte

## Slide 11: Progress: source
R&D objectives:
“Full-scale” tests in conditions approaching LhARA specification
LhARA-focused diagnostic and targetry development
High-repetition rate, automation and longevity studies
Accurate numerical modelling 3D simulation codes
PhysRevLett.90.185002
Realistic, 2-stage simulation on ARCHER2 using accurate “pre-plasma” profile
Study proton production as a function of angle of incidence, spot size, proton-layer thickness
Seek to benchmark against data
N. Dover
T.S. Dascalu

## Slide 12: Experiments at SCAPA
R. Gray
Laser energy
N. Dover, G. Casati

## Slide 13: Progress source: diagnostics & high rep-rate
Diagnostics
High-rep rate / longevity …
Scintillators: key for high rep rate operation
Dedicated calibration effort led by N. Dover (ICL):
  Birmingham MC40 cyclotron
N. Dover, O. Ettlinger, N. Xu, Z. Najmudin

## Slide 14: Progress: design & integration: Stage 1
Standardised TNSA source
Impact: look at entrance to arc:
Revised Stage 1 baseline
7 Gabor lens adopted
Greater flexibility
Drifts longer:
  Diagnostics
  Shielding
Gabor lens/solenoid focusing equivalence
M. Maxouti, N. Dover, K. Long
Important for (e.g.) activation calculation
Momentum selection in arc
Gabor lenses
Solenoids
W. Shields, J. Pasternak, K. Long

## Slide 15: Progress: capture
Key issues:
  Electron density, plasma stability
Measurements on Penning-Malmberg trap at Swansea University
  “Moving potential well” capture
  “Rotating wall” to “spin-up” plasma to gain stability
Ongoing campaign:
  Already significant increase in hold time and plasma density
  Next steps:
    Improved diagnostics
    Numerical analysis to interpret and optimise experiments
P. Ruksasakchia, A. Isaac, S. Eriksson
Future plan: K. Long, C. Dyson (PhD from Oct24)

## Slide 16: Progress: real-time dose measurment
M. Maxouti,
C. Bird,
O. Jeremy,
K. Ladhams,
K. Long,
D. Nardini
B. Cox, J. Bamber

## Slide 17: Progress: real-time dose measurment
M. Maxouti,
C. Bird,
O. Jeremy,
K. Ladhams,
K. Long,
D. Nardini
P. Hobson,
B. Cox, J. Bamber

## Slide 18: Progress: Stage 2: injection & FFA magnet
Injection-line update
FFA magnet
Resign revision encorporates:
Shielding, collimation & diagnostics
Continued design effort:
  Match to FFA cell requirements
  Study & mitigate space charge
BDSIM model now synced with accommodates:
  Vacuum valves, diagnostics, shielding shutters, correctors …
T.J. Kuo
K. Long
J. Pasternak
R. Razak
W. Shields
N. Bliss, A. Goulden, C. Hill, J.B. Lagrange, H. Owen, C. Whyte
Emerging collaboration with ISIS u/g team
T.J. Kuo
T.J. Kuo
J. Pasternak, W. Shields

## Slide 19: Progress: consultation & end-station
Peer-group consultation:
  Stage 1 in vitro & 2 in vivo
  Focus on Stage 1 in vitro
  Focus on Stage 2 in vivo
Beam-line diagnostics:
  Gas-jet (Liverpool): tested at DCF
Seek increasing engagement with more novel techniques:
  Initiated “ART” meeting series
Conclusions and recommendations documented at:
https://ccap.hep.ph.ic.ac.uk/trac/browser/LhARA/Governance/ProjectManagementBoard/LhARA-Gov-PMB-2023-04
to be updated!
N. Kumar, R. McLauchlan, T. Price

## Slide 21: Feedback on PA2 proposal to STFC Visions Team
Broad support
  High impact potential
  Could deliver step change
  Potential for broad reach
  Ambitious
But not selected
  Fit with international landscape unclear
  Potential for target community unclear
  Progress of first preliminary activity unclear (but only 9 months into 2 year project when written)
Now seeking access to bridging funds

## Slide 22: Structuring the bridging activity
Define bridging programme to optimise delivery of:
Biology/proof-of-principle programme
R&D programme to address key project risks
Strategic partnerships

## Slide 23
Development of radiation biology programme:
  At existing facilities:
    Novel (e.g. laser driven)
    Conventional
LhARA proof-of-principle experiment:
  CW: “… include as many of key LhARA elements as possible …”
“WP7”, led by J. Parsons
Increasingly import aspect of the programme going forward

## Slide 24: Conclusions
Significant progress in ITRF/LhARA:
  Beamline design and optimisation
  Engineering, initial studies of FFA magnet
  Initial characterisation of laser-driven source
  Progress on understanding and stablisation of plasma for Gabor lens
  Design of ion-acoustic proof-of-principle experiment
  Peer-group consultation leading to specification of end-station
Looking forward:
  Recognition of importance of development of biological programme:
    First steps in design and specification of proof-of-principle experiment as part of broader radiation-biology programme
  Project programme for Bridging Period now being developed
Exciting programme, but, clear need to make the case!

## Slide 25: Backup

## Slide 26
 compact, uniquely flexible facility
N. Bliss (DL)
Draft
Front. Phys., 29 September 2020; DOI: 10.3389/fphy.2020.567738

## Slide 27: The case for fundamental radiobiology
Relative biological effectiveness:
  Defined relative to reference X-ray beam
  Known to depend on:
    Energy, ion species
    Dose & dose rate
    Tissue type
    Biological endpoint
Yet:
  p-treatment planning uses 1.1
  Effective values are used for C6+
Maximise the efficacy of PBT now & in the future:
  Require systematic programme to develop full understanding of radiobiology
Paganetti, van Luijk (2013)
SemRadOncol

## Slide 28: Progress: selected engineering highlights

## Slide 29: Progress capture

## Slide 30: Progress: capture

## Slide 31: Progress capture

## Slide 32
Outreach & engagement (WP8); progress to date
Communication Strategy
  Public: LhARA Website – strategy devised for web development, management/domains/social media/LinkedIn for public and patient engagement
  Public engagement events: Planning for Great Exhibition and Royal Society Exhibition 2025
  Media: Mentioned as future innovation in cancer care on Radio4 Today podcast Feb 2024
  Parliamentary: Mentioned in UK Radiotherapy ten year Vision documents launched at HOC Feb 2024. Meetings being planned with Scottish SNP science spokesman Carol Monaghan and Shadow science minister Chi Onwurah. Planned to be included in future Westminster MedTech commission .
Stakeholder engagement
  Discission with MRC, the Radiotherapy UK charity and NGO-Global Coalition for Radiotherapy on engaging national and international clinical colleagues and radiobiology community, patients and the radiotherapy industry in parallel.
  International workshop of clinical/biologists planed for Q3 2024
Professional Bodies Engagement
  Links with IPO via Richard Amos and arranging engagement with other professional bodies
MRC Engagement
  Work started to engage MCR in biological/translational clinical areas
International Engagement
LMU, HZDR, CNRS/Institute Curie
CERN
ELI/ELIMED

## Slide 33
Multiple ion source & capture
Dosimetry, instrumentation image processing, fast feedback, control
Fundamental
radiobiology