## Slide 1
1
.
Green (gas) Cherenkov Radiators
(Partly based on previous presentations:
see reference slides)
(See also yesterday’s ALICE talk by Nicola Nicassio)
G. Hallewell
Aix Marseille Université,
CNRS/IN2P3, CPPM, Marseille, France
Gas optical properties are vital
for particle identification:
fluorocarbons have been ideal
May 12-15 2025 Online
Notes: 1

## Slide 2
RICH 1: C4F10 radiator
n = 1.00145 (4 m3):
lower momentum PID
RICH 2: CF4 (+CO2) radiator:
n = 1.00049 (100 m3):
higher momentum PID
COMBINED RICH PEFORMANCE & PARTICLE SPECIES IDENTIFCATION RANGE
Qc = cos-1 (1/bn)
G. Hallewell: Green Cherenkov radiators Sustainable HEP 4th Edition, CERN 12-15 May 2025
2

## Slide 3
“Green” fluorocarbons for Cherenkov radiators?
Saturated fluorocarbons (PFCs, SFCs: CnF(2n+2)) chosen for optical properties as Cherenkov radiators: C4F10 & CF4 in COMPASS & LHCb RICH1&2.
Non-conductivity, non-flammability, non-toxicity & radiation resistance
 ideal coolants
- C6F14 (liquid) used in all LHC experiments,
- C3F8 evaporatively cools ATLAS silicon tracker, TOTEM;
These fluids however have high GWPs (GWP20 > 5000*CO2);
Fluoro-ketones (CnF2nO), while not industrialised over a wide CnF2nO range,
can offer similar performance at very low, or 0 GWP;
Radiation tolerance & thermal performance of 3M NOVEC 649® (lin-C6F12O) sufficiently promising to be considered by CERN to replace C6F14 for cooling,
but acid production (in humidity) and materials compatibility issues to resolve.
G. Hallewell: Green Cherenkov radiators Sustainable HEP 4th Edition, CERN 12-15 May 2025

## Slide 4: Molecular shapes, GWP & toxicity
Cherenkov
Radiator
(hist.) + Cooling (Liq.)
Si cooling
(Evap.)
Ih.T H331,
reactive
Ih.T H330, reactive
Ih.T H331,
reactive
CAS# 756-13-8
Ih.T. H335
CAS# 756-12-7
Ih.T. H335
CAS# 337-20-2
Ih.T. H335
Cherenkov
Radiator
Cherenkov
Radiator
Cherenkov
Radiator
(hist.)
Cherenkov
Radiator
(hist.)
Upper: molecular shapes of SFCs, including common gaseous Cherenkov radiators.
Lower: shapes of some non-cyclic CnF2nO analogues (20-year GWPs & GHS inhalation toxicities (source www.synquest.com
C2F4O
Ih.T. H335
Ih.T. H335
Ih.T. H335
Ih.T. H335
Ih.T. H335
Ih.T. H335
G. Hallewell: Green Cherenkov radiators Sustainable HEP 4th Edition, CERN 12-15 May 2025

## Slide 5
C4F8O Linear with Oxygen atom as
internal link and double carbon
bonded link
C4F8O
CAS# 773-14-8
Cyclic
Perfluorotetrahydrofuran,
Octofluorotetrahydrofuran
(GWP20 = 8975) [ref EPJP]
[H335]
C4F8O Linear & iso, with
Oxygen atom on external spur
CAS# 67641-44-5
Octafloro-1-methoxyprop-1-ene
(GWP20 = ?) [H332, 335, 336]
CAS# 337-20-2
Octafluoro-2-butanone
(GWP20 = ?) [H335]
CAS# 335-42-2
Heptafluorobutyryl fluoride
(GWP20 = ?) [H331]
CAS# 677-84-9
Heptafluoroisobutyryl fluoride
(GWP20 = ?) [H335]
CAS# 10493-43-3
Pentafyoroethyltrifluorovinyl ether
(GWP20 = ?) [H332, 335]
Molecular shape is important for GWP and toxicity!!
Cyclic, non-cyclic & non-cyclic double c-bonded C4F8O isomers
Optical performance similar
to C4F10: (BTeV & ALICE VHMPID)
High GWP!!
GWP ?

GWP ?
GWP ?
G. Hallewell: Green Cherenkov radiators Sustainable HEP 4th Edition, CERN 12-15 May 2025

## Slide 6
But no mention at all of the ATLAS ultrasonic fluorocarbon leak monitor system !
https://doi.org/10.25325/CERN-Environment-2023-003
G. Hallewell: Green Cherenkov radiators Sustainable HEP 4th Edition, CERN 12-15 May 2025

## Slide 7: Ultrasonic detection of fluorocabon gas leaks: ATLAS silicon tracker: SFC leak monitoring
https://www.mdpi.com/2410-390X/5/1/6
Gas aspirated through
150m tubes from
silicon tracker
N2 environmental
volumes to
‘sonar’ devices
for C3F8
leak monitoring
(~ 10-5 C3F8 in N2 )
Chart: CO2 concentration (ppm)
G. Hallewell: Green Cherenkov radiators Sustainable HEP 4th Edition, CERN 12-15 May 2025
92 m

## Slide 8
This latest CERN environmental report https://doi.org/10.25325/CERN-Environment-2023-003
R449: (CFH blend) GWP=1397
R1234 (HFO): GWP = 7
NOVEC 649 (C6F12O): GWP=0
Collective loss of SFCs only around 10 tonnes (whole of LHC + expts)
(compare that to yearly mass-loss at a ‘grande surface’ supermarket!)
G. Hallewell: Green Cherenkov radiators Sustainable HEP 4th Edition, CERN 12-15 May 2025
SF6 GWP = 23000
NF3 GWP = 17000

## Slide 9
Some perspective (2): Auchan Aubagne (13) “Grande Surface” near Marseille
(Hectaires of A/C, tonnes of loss per year: R134a? (GWP=1430)  R32? (GWP=675?)
G. Hallewell: Green Cherenkov radiators Sustainable HEP 4th Edition, CERN 12-15 May 2025

## Slide 10
Refractive index & GWP ’load’ in a Cherenkov Gas Radiator
A Cherenkov radiator vessel of volume V(m3) filled with
a blend of gases of densities ri (kgm-3),
fractional concentrations wi and individual GWPi (tonnes CO2 eq.)
has a GWP environmental “load” (& release potential) L given by:
) (tonnes CO2 eq.) [Eq. (1)]
G. Hallewell: Green Cherenkov radiators Sustainable HEP 4th Edition, CERN 12-15 May 2025
LHCb RICH 1
(4m3 C4F10: GWP20 = 4880
GWP eqv. CO2: 274 tonnes
LHCb RICH 2
(100 m3: CF4 GWP20 = 6870
+ ≤ 5% CO2)
GWP eqv. CO2: 1737 tonnes
COMPASS RICH
(100 m3 C4F10: GWP20 = 4880)
GWP eqv. CO2: 6849 tonnes

## Slide 11: The big SFC-using Ring Imaging CHerenkov Detectors at CERN
LHCb RICH 1
(4m3 C4F10)
GWP eqv CO2: 274 tonnes
LHCb RICH 2
(100 m3: CF4 + ~5% CO2)
GWP eqv. CO2: 1737 t
COMPASS RICH
(100 m3 C4F10)
GWP eqv CO2: 6849 tonnes
Ideally… replace SFCs with
same-order GWP0 FKs
with good UV transparency, refractivity…
LHCb RICH 1
(4m3 lin-C4F8O)
GWP eqv. CO2: 0 tonnes
LHCb RICH 2
(100 m3: CF2O + ?)
GWP eqv. CO2: 0 t
COMPASS RICH
(100 m3 lin- C4F8O)
GWP eqv. CO2: 0 tonnes
CF2O Toxicity 
G. Hallewell: Green Cherenkov radiators Sustainable HEP 4th Edition, CERN 12-15 May 2025

## Slide 12
But if direct 1 for 1 substitution is not possible…
A Cherenkov radiator vessel of volume V(m3) filled with
a blend of gases of densities ri (kgm-3), fractional
concentrations wi and individual GWPi (t CO2 eq.)
has a GWP environmental “load” (& release potential)
L given by:
) (tonnes CO2 eq.) [Eq. (1)]
The corresponding radiator gas mixture refractivity for a gas blend is given by :
[Eq. (2)]
For just two gases we can blend small conc. wx of (heavier) SFC or Fluoro-Ketone
vapour of high refractivity (n-1)x with wy of light transparent gas, refractivity (n-1)y
to replicate refractivity (n-1)z of a lighter SFC at high conc. – for a lower GWP load.
wx = [Eq. (3)]
V,r
G. Hallewell: Green Cherenkov radiators Sustainable HEP 4th Edition, CERN 12-15 May 2025

## Slide 13: Targeting the refractivity of CF4 & C4F10 (100 m3: examples) at 1 barabs with gases of differing molecular weight in varying fractional concentrations with N2 (conc. > 100% indicate need for overpressure): includes hypothetical light fluoro-ketones
CF4
C4F10
G. Hallewell: Green Cherenkov radiators Sustainable HEP 4th Edition, CERN 12-15 May 2025

## Slide 14: CERN F-gas policy document on EDMS (July 2024)
https://edms.cern.ch/ui/file/3120169/1/
CERN_F-gas_policy_docx_cpdf.pdf
Page 1 of 4
G. Hallewell: Green Cherenkov radiators Sustainable HEP 4th Edition, CERN 12-15 May 2025
In the possible absence of suitable F-K alternatives (compatibility issues),
some options for better husbandry of heritage SFCs/PFCs follow:

## Slide 15
G. Hallewell: Green Cherenkov radiators Sustainable HEP 4th Edition, CERN 12-15 May 2025

## Slide 16
(1 of 2): Perspective from a recent e-mail exchange [Apr. 2025] with a chemical company producing Saturated Fluoro-Carbons (SFCs),
a.k.a Per-Fluoro-Carbons (PFCs)
“C5F12O et seq.: “NOVEC” Fluoro-ketones are undeniably good fluids: for the majority of applications:
they work well as a substitute for fully fluorinated alkanes but have compatibility issues to overcome.
“About 10 years ago I discovered a 3M report posted on the internet that detailed across 27 pages
the performance differences between NOVECs and fully fluorinated alkanes:
NOVEC’s unpredictable lack of compatibility with the many and varied materials of constructions
being a major reported issue along with poorer thermal stability and dielectric strength.
“We tell our customers that if fluid performance is absolutely critical to an application (e.g. aerospace)
prioritizing reducing leaks and / or capture and recycling is worth the effort ahead of a fluid swap.
Unfortunately it’s not a very glamorous or exciting solution.”
G. Hallewell: Green Cherenkov radiators Sustainable HEP 4th Edition, CERN 12-15 May 2025

## Slide 17
“[…] So far we have not seen any serious diminishing of business due to
PFAS or F-gas restrictions.
“[…] F-gas and PFAS are a constant topic of conversation with customers,
but the same conclusions seem to be happening over and over again.
“Simply there is no alternative that works as well, and compromising safety
or efficacy is not in anyone’s interest, in particular space and military are not
inclined to change for inferior performance.
In fact we are working with customers on new projects that use our PFC’s.
“Basically there was a initial wobble, but it doesn’t seem to have spooked
everyone - there are still brave souls out there.”
(2 of 2): Perspective from a recent e-mail exchange [Apr 2025] with
a chemical company producing Saturated Fluoro-Carbons (SFCs),
a.k.a Per-Fluoro-Carbons (PFCs)
G. Hallewell: Green Cherenkov radiators Sustainable HEP 4th Edition, CERN 12-15 May 2025

## Slide 18: Improved leak capture: Surrounding a FC RICH radiator with a thin (for example: N2) - purged leak sniffing plenum equipped with ultrasonic monitoring of FC molar mass
Continuous real-time monitoring;
Sensitivity better than 10-5 FC molar conc w;
Alarm raising;
Cumulative loss calculation (compliments tankage mass loss measurements)

Can also condense the FC leaking into the sampling volume to reduce losses!
Internal placement of ultrasonic transducers?
Aspiration to analyser: membrane pumps & tubes?
Aspiration from the bottom best: hydrostatics of heavier FC
Care with volume calculation if jacket walls are flexible:
(Hydrostatic bowing with heavy FCs)
SensComp
(ex-Polaroid) 50 kHz
Ultrasonic transducer
https://senscomp.com
G. Hallewell: Green Cherenkov radiators Sustainable HEP 4th Edition, CERN 12-15 May 2025
Sonar
Aspiration
pump
Cold trap to
liquify & recapture
fluorocarbon
https://www.mdpi.com/2410-390X/5/1/6

## Slide 19: Improved ‘Optigeneric’ FC blend RICH radiator gas recirculator suppression of moving parts like gas blowers & compressors (often major points of failure & leaks)
Atmospheric
reference pressure
safety bubbler
Radiator
vessel
Fluorocarbon
Evaporator
Fluorocarbon
Condenser
-80 °C
Light carrier
Gas escape
(eg N2)
Gas mixture
Monitor & control
FC liquid phase purifier
(O2, H2O removal etc.)
Keep cold coil
Mass Flow Controller
N2 in
Low mass flow
FC liquid
pump
Cooling fluid
to coils
(probably boil-off
from LN2, LAr
Liquid FC
rgh > Pevap evap sufficient to drive circulation
h
Condenser
Coil
IN
OUT
G. Hallewell: Green Cherenkov radiators Sustainable HEP 4th Edition, CERN 12-15 May 2025
Liq FC
Pevap

## Slide 20
Low temperature (-80°C)
N2 gas-induced condensation (B):
of C5F12 fromC5F12/N2 radiator gas (flow~1m3/hr, negligible C5F12 loss)
followed by (C) electric re-evaporation
(1-1.5m below condenser liq. level)
Cold N2 gas (‘conditioned’ by
counter-flow with boil-off LN2
from liquid argon calorimeter: (A))
Ultrasonic (speed of sound) – aided
“on-the fly” mixing of typical
17%N2 /83%C5F12 (molar) radiator gas mixture (D)
Example of such a thermosiphon recirculator: SLD CRID C5F12/N2 gas radiator:
A
B
C
D
G. Hallewell: Green Cherenkov radiators Sustainable HEP 4th Edition, CERN 12-15 May 2025

## Slide 21
So where are we (May 2025)..?
(Interim conclusion: as you have seen, PFAS are a moving target)
G. Hallewell: Green Cherenkov radiators Sustainable HEP 4th Edition, CERN 12-15 May 2025
Despite high GWP SFCs/PFCs (form CnF(2n+2)) currently indispensable as benign Cherenkov radiators (refractivity, good UV & near-UV transparency) ;
C4F10 & CF4 in COMPASS & LHCb RICH 1 & 2, possibly soon C2F6 (again).
3M Corp leaving PFAS market place by end of 2025: affects 3M SFC/PFC & NOVEC® Fluoro-Ketone PFAS fluids, but other manufacturers collectively filling gaps.
Examples: France: Dehon Co. (subsidiary Climalife): https://climalife.com
UK: F2 Chemicals: https://f2chemicals.com
USA: Synquest (FL): https://synquestlabs.com
China: Sanming Hexafluo Chemicals Co. : http://www.hexafluo.com
So how threatened will future PFAS availability really be?
(needs of electronics, semiconductor industry)..?
While not industrialised over a wide CnF2nO range fluoro-ketones might offer similar optical performance at very low, or 0 GWP Studies starting in DRD4;
Material compatibility issues, low order CnF2nO reactivity & toxicity an issue?
Lin (or iso?) -C4F8O could replace C4F10 while C4F8O or C5F10O blended with N2
& controlled in real time by sound velocity gas analysis - could replace CF4
Better usage of existing stocks of SFCs the best way to go?: ‘compressor-less’ (thermosiphon) circulation & leak capture plenums round large SFC volumes..?

## Slide 22: Previous related presentations & references
G. Hallewell: Green Cherenkov radiators Sustainable HEP 4th Edition, CERN 12-15 May 2025

## Slide 23
23
.
This is a follow-on from previous presentations in this vein:
(too much for here): for more information see:
“Green radiators”: Controlling refractive index & reducing Cherenkov gas radiator GWP: a challenge in an era of diminishing fluorocarbon availability
Related paper: https://link.springer.com/article/10.1140/epjp/s13360-023-04703-w
Also DRD4 meeting, May 2023 https://indico.cern.ch/event/1263731/contributions/5398511
ATLAS sustainability forum CERN, Jan 26 2024
https://indico.cern.ch/event/1371158/contributions/5773321/attachments/2788215/4861759/G_Hallewell_ATLAS_sustainability_forum_Jan_26_2024_v2.pptx
Sustainable HEP 2024 https://indico.global/event/4744/contributions/39611/
ICHEP2024 (July 2024): https://indico.cern.ch/event/1291157/contributions/5900402
DRD4 meeting Oct. 2024: https://indico.cern.ch/event/1456663/sessions/566400/#20241024
DRD4 meeting April 2025: https://indico.cern.ch/event/1473071/contributions/6430251/
G. Hallewell: Green Cherenkov radiators Sustainable HEP 4th Edition, CERN 12-15 May 2025
Notes: 23

## Slide 24
G. Hallewell: Green Cherenkov radiators Sustainable HEP 4th Edition, CERN 12-15 May 2025

## Slide 25: GHS Classification Criteria for Inhalation & skin Toxicity
H330 | Fatal if inhaled
H331 | Toxic if inhaled
H332 | Harmful if inhaled
H333 | May be harmful if inhaled
H334 | May cause allergy or asthma symptoms or breathing difficulties if inhaled
H335 | May cause respiratory irritation
H336 | May cause drowsiness or dizziness
H310 | Fatal in contact with skin
H311 | Toxic in contact with skin
H312 | Harmful in contact with skin
H313 | May be harmful in contact with skin
H314 | Causes severe skin burns and eye damage
H315 | Causes skin irritation
Global Harmonized System of Classification and Labelling of Chemicals (GHS). 10th revision, United Nations (2023}
About the GHS | UNECE https://unece.org/about-ghs
G. Hallewell: Green Cherenkov radiators Sustainable HEP 4th Edition, CERN 12-15 May 2025

## Slide 26
(from Guida talk)
Watch this (CEPS) space
- and GET SB MEMBERSHIP
- to represent the
Cherenkov detector
community and its needs!
CERN and the Environment (what?)Town Hall meeting 8 November 2024
G. Hallewell: Green Cherenkov radiators Sustainable HEP 4th Edition, CERN 12-15 May 2025

## Slide 27
Cherenkov radiator and related general references (1 of 2) from
https://link.springer.com/article/10.1140/epjp/s13360-023-04703-w
[1] CERN Environment Report 2017–2018 https://doi.org/10.25325/CERN-Environment-2020-001
[2] B. Mandelli; Eco-gas mixtures and mitigation procedures for Green-house Gases (GHGs);
ECFA Detector R&D Road-map Symposium: T.F. 1 Gaseous Detectors, 29/4/2021
https://indico.cern.ch/event/999799/contributions/4204191/attachments/2236047/3789965/BMandelli_ECFA.pdf,
[3] B. Mandelli; R&D for the optimization of the use of greenhouse gases in particle detector systems;
Mini workshop on gas transport parameters for present and future generation of experiments: CERN April 22, 2021
https://indico.cern.ch/event/1022051/contributions/4325947/
[4] G. Rigoletti; Studies to reduce greenhouse gas emissions from detectors at the LHC; EP-DT Seminar May 4, 2022.pdf (cern.ch)
[5] S. Dalla Torre et al; Long term experience with C4F10 in COMPASS RICH-1; Presentation 11th Intl. Workshop on Ring Imaging Cherenkov detectors, Edinburgh, Scotland, Sept 12-16 2022. https://indico.cern.ch/event/1094055/contributions/4932286/attachments/2508724/4311387/RICH2022_C4F10_dallatorre.pdf
[6] 3M PFG-3480: c-octofluorotetrahydrofuran (C4F8O). Note: fluid out of production : product reference now used for a non-fluidic product. For historic product data sheet mentioning its high GWP see (for example): http://static6.arrow.com/aropdfconversion/a7116f41dfdd5b79d2eb7b40afd687f8af23d8ef/mediawebserver(563).pdf
[7] M. Artuso et al; Nucl. Instr & Meth. A Volume 558, (2006), 373-387
[8] Product #2H07-2-08 Synonyms: 2,2,3,3,4,4,5,5-octafluorotetrahydrofuran, Perfluorotetrahydrofuran; CAS No: 773-14-8, MDL No. MFCD00465561: SynQuest Labs Inc., 13201 Rachael Boulevard, Alachua, FL 32615, USA https://www.synquestlabs.com/Home/ProductDetail?SearchText=Octafluorotetrahydrofuran
[9] T. Acconcia et al ; Nucl. Instr & Meth A 767 (2014) 50–60
[10] M. Vollmer et al; Abundances, emissions, and loss processes of the long-lived and potent greenhouse gas octafluorooxolane (octafluorotetrahydrofuran, c-C4F8O) in the atmosphere; Atmos. Chem. Phys., 19, 3481–3492, 2019
[11] 3M Novec® range of fluorinated fluids; https://www.3m.com/3M/en_US/p/c/b/novec/?Ntt=novec
[12] 3M Novec 649/1230 fluid (C6F12O); https://multimedia.3m.com/mws/media/569865O/3m-novec-engineered-fluid-649.pdf,
https://multimedia.3m.com/mws/media/124688O/3m-novec-1230-fire-protection-fluid.pdf]
[13] 3M Novec 5110 fluid (C5F10O); https://multimedia.3m.com/mws/media/1132123O/3m-novec-5110-insulating-gas.pdf
[14] CERN report EN-CV 22/12/2017, EDMS 1751219 2017-334 rev 1.0: Technical Note NOVEC Fluids Qualification Report: Report on the study executed for the qualification of the NOVEC Fluid for Detector Cooling applications.
[15] J. Owens, Understanding the stability and environmental characteristics of a sustainable Halon alternative.
3M Performance Materials 3M Center, St. Paul, MN 55144
G. Hallewell: Green Cherenkov radiators Sustainable HEP 4th Edition, CERN 12-15 May 2025

## Slide 28
Cherenkov radiator and related general references (2 of 2) from
https://link.springer.com/article/10.1140/epjp/s13360-023-04703-w
[16] CERN Mini-workshop on gas transport parameters for present and future generation of experiments 20/04/2021;
S. Easo; LHCb-RICH detectors and their gas radiators
https://indico.cern.ch/event/1022051/contributions/4333562/attachments/2231064/3780374/LHCb-RICH-Current-GasRadiators-April-2021.pdf,
Options for alternate radiators in LHCb-RICH system (including calculations by O. Ullaland); S. Easo,
https://indico.cern.ch/event/1022051/contributions/4319538/attachments/2231436/3781060/LHCb-RICH-Future-Radiators.pdf
[17] S.Easo; Nucl.Inst.& Meth. A 876 (2017) 168-173
[18] E. Lemmon, M. Huber, & M. McLinden; REFPROP Standard reference database 23, version 9.0 (2010)
U.S. National Institute of Standards & Technology.
[19] E. Nappi and J. Seguinot Rivista del Nuovo Cimento Vol. 28, N. 8-9 2005 DOI 10.1393/ncr/i2006-10004-6
[20] K. Abe et al. ; IEEE Trans. Nucl. Sci. 45 (1998) 648 SLAC-PUB-7705 DOI: 10.1109/23.6826 [21] G. Hallewell et al; Nucl. Instr. & Meth A264 (1988) 219-234
[22] G. Hallewell; Nucl. Instr & Meth A 876, (2017) 50-53
[23] G. Hallewell et al; MDPI Instruments (2021) 5(1), 6;
[24] P. Stassi et al; Ultrasonic Gas mixture analysis system in the Forward RICH of DELPHI,
DELPHI Internal Note 95-124 RICH73, 25 July 1995
[25] M.Sannino; Nucl. Instr. and Methods in Physics Research A 595 (2008) 208–211
[26] C. D'Ambrosio et al; Monitoring, Alignment and Control of the RICH Detectors; LHCb-Memo-2000-80 RICH 6 September 2000.
[27] P. Fauland, PhD thesis; (COMPASS experiment) University of Bielefeld March 2004.
[28] Now marketed as SensComp model 600 transducer, http://www.senscomp.com/ultrasonic-sensors/
[29] T. Blake et al; Nucl. Instr. Meth A791 (2015) 27-31
[30] A. Papanestis; Nucl. Instr. Meth. A766 (2014) 14–18
[31] R. Calabrese et al; 2022 JINST 17 P07013
[32] J. Vavra (SLAC National Laboratory); private communication.
G. Hallewell: Green Cherenkov radiators Sustainable HEP 4th Edition, CERN 12-15 May 2025

## Slide 29
[33] P. Tropea; The CMS tracker fluorocarbon cooling system,
Engineering Forum: experiences from cooling systems for LHC detectors Oct 30 2008
[34] G. Aglieri Rinella et al, 2019 JINST 14 P07010
[35] G. Anelli et al ; 2008 JINST 3 S08007
[36] D. Attree et al, 2008 JINST 3 P07003
[37] W. Adam et al ; 2021JINST16P02027 CMS Technical Design Report; Pixel Detector Upgrade CMS-TDR-011, CERN-LHCC-2012-016 07/09/2012
[38] ATLAS Insertable B-Layer Technical Design Report; CERN-LHCC-2010-013 ATLAS TDR 19 15/09/2010
[39] O. de Aguiar Francisco et al; Nucl. Instr. Meth A. 1039 (2022) 166874
https://www.sciencedirect.com/science/article/pii/S0168900222003394
[40] Fluoroketone C2F5C(O)CF(CF3)2 as a Heat Transfer Fluid for Passive and Pumped 2-Phase Applications; P. Tuma, 3M Co., 3M Center, 236-2B-01St. Paul, MN 55144, USA, Proc. 2008 IEEE 24th IEEE Semiconductor Thermal
Measurement and Management Symposium, San Jose CA, March 16-20 DOI: 10.1109/STHERM.2008.4509386
also accessible via: https://twiki.cern.ch/twiki/pub/LHCb/SciFiDemoCooling/F.Tuma_c6K_as.....pdf
[41] L. Gruber et al; Nucl. Instr. & Meth. 958 (2020) 162025 https://www.sciencedirect.com/science/article/abs/pii/S016890021930422X?via%3Dihub
[42] ”Building the future of LHCb”; C. Frei, S. Gambetta, B. Leverington; CERN Courier, September 2021 (2 September 2021)
https://cerncourier.com/a/building-the-future-of-lhcb
[43] M. Battistin et al; Int. J. Chemical Reactor Engineering 2015; 13(4): 511–521
[44] R. Bates et al; 2015 JINST 10 P03027
[45] https://lhc-commissioning.web.cern.ch/schedule/LHC-long-term.htm
[46] L. Contiero et al; Cold Krypton system for the Phase III Upgrade of the LHC,
Forum on Tracking Detector Mechanics 2023, Tuebingen Germany May 31-June 2 2023
[47] L. Contiero et al; Krypton, applied as refrigerant for cooling of silicon detector trackers;
GL 2022: 15th IIR-Gustav Lorentzen Conference on Natural Refrigerants, Trondheim, Norway, June 13-15 2023
[48] D. Alvarez et al: Thermo-Mechanical Performance of the Local Supports for the ATLAS ITk Pixel Outer Barrel:
Experimental and FEA Studies; Forum on Tracking Detector Mechanics 2023, Tuebingen Germany May 31-June 2 2023
[49] B. Verlaat; CO2 cooling experiences in the LHCb Velo Thermal Control System
Engineering Forum: experiences from cooling systems for LHC detectors Oct 30 2008
[50] R. Bates et al; 2013 JINST 8 P02006
[51] ECHA/NR/23/04; https://echa.europa.eu/-/echa-publishes-pfas-restriction-proposal]
[52] ECHA Candidate List of substances of very high concern for Authorisation; https://echa.europa.eu/candidate-list-table
[53] Annex to the Annex XV restriction report proposal for restriction: Per- & polyfluoroalkyl substances (PFASs);
ECHA; 22/03/2023 https://echa.europa.eu/documents/10162/d2f7fce1-b089-c4fd-1101-2601f53a07d1
[54] Per- and polyfluoroalkyl substances (PFAS); ECHA https://echa.europa.eu/hot-topics/perfluoroalkyl-chemicals-pfas
Silicon tracker cooling and related general references FROM
https://link.springer.com/article/10.1140/epjp/s13360-023-04703-w
G. Hallewell: Green Cherenkov radiators Sustainable HEP 4th Edition, CERN 12-15 May 2025

## Slide 30: Back up matl.
G. Hallewell: Green Cherenkov radiators Sustainable HEP 4th Edition, CERN 12-15 May 2025

## Slide 31: What gives NOVEC 649/1230 (lin C6F12O: FK-5-1-12) its low GWP?
A: Structure!: a double-bonded oxygen atom on a peripheral spur of the molecule
This fluoro-ketone configuration is:
CF3CF2C(O)CF(CF3)2
31
G. Hallewell: Green FCs for Cherenkov detectors & Si tracker cooling Sustainability session: ICHEP2024 Prague 18-24 July 2024

## Slide 32: What gives NOVEC 649/1230 (lin C6F12O: FK-5-1-12) its low GWP?
Scission by UV photons of l ~300 nm in upper atmosphere (low P, high UV): fragments do not re-associate* into CnF(2n+2) SFCs
*The Environmental Impact of CFC Replacements HFCs and HCFCs
T. WALLINGTON et al Environ.Sci.Technol.1994(28)7 320A https://doi.org/10.1021/es00056a714
https://www.nist.gov/system/files/documents/el/fire_research/R0301570.pdf
32
[15]
G. Hallewell: Green FCs for Cherenkov detectors & Si tracker cooling Sustainability session: ICHEP2024 Prague 18-24 July 2024

## Slide 33: Q: What gives NOVEC 649/1230 its low GWP?
Scission by UV photons of l around 300 nm
In the atmosphere (low pressure, high UV): the fragments do not reassociate* into saturated fluorocarbons of the type CnF(2n+2) (which would have high GWP)
*The Environmental Impact of CFC Replacements HFCs and HCFCs
T. WALLINGTON et al Environ.Sci.Technol.1994(28)7 320A https://doi.org/10.1021/es00056a714
https://www.nist.gov/system/files/documents/el/fire_research/R0301570.pdf
33
[15]
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025
Problematic UV absorbance
band for Cherenkov
light detection?

## Slide 34
Refractive index & GWP ’load’ in a Cherenkov Gas Radiator
3 large RICH detectors currently in operation at CERN:
using saturated fluorocarbon gas volumes:
C4F10 (COMPASS: 100m3, LHCb RICH 1: 4m3): GWP20 = 4880,
CF4 (LHCb RICH 2: 100m3): GWP20 = 6870
A Cherenkov radiator vessel of volume V(m3) filled with
a blend of gases of densities ri (kgm-3),
fractional concentrations wi and individual GWPi (tonnes CO2 eq.)
has a GWP environmental “load” (& release potential) L given by:
) (tonnes CO2 eq.) [Eq. (1)]
The corresponding radiator gas mixture refractivity is given by :
) [Eq. (2)]
For just two gases we can blend small conc. wx of (heavier) SFC or Fluoro-Ketone
vapour of high refractivity (n-1)x with wy of light transparent gas, refractivity (n-1)y
to replicate refractivity (n-1)z of a lighter SFC at high conc. – for a lower GWP load.
wx = [Eq. (3)]
V,r
With j contaminant gases of known molar concentrations wj present we can still
add a small concentration wx of (heavier) SFC or Lin-FK vapour of high refractivity
(n-1)x with wy of light transparent gas to substitute the refractivity (n-1)z(target)
of a lighter SFC at high concentration – to achieve a lower overall GWP load.
+
[Eq. (2) Eq. (2b)]
wx = [Eq. (3)  Eq. (3b)]
G. Hallewell: Green Cherenkov radiators Sustainable HEP 4th Edition, CERN 12-15 May 2025

## Slide 35
EU strategy to reduce Fluronated (PFAS) compound production and use
(includes also fluorinated plastics not shown here: see back-up material)
From: ICHEP2024
Projected Usage
Dynamic price hiking :
like Trimposing demand-dependent tariffs…?
G. Hallewell: Green Cherenkov gas radiators DRD4 WG-2 session: 11/04/2025

## Slide 36
Chart: 
| 361.57150866452997 | 256.66370132773199 | 207.76041110631601 | 177.74100163378299 | 156.771959339836 | 140.96541864529999 | 128.432486611158 | 118.12923971441801 | 109.42497216462201 | 101.912772216321 | 95.316482075286103
e thresh | 0.20021 | 0.16566 | 0.14445 | 0.12974 | 0.11878 | 0.11019 | 0.10324 | 0.09746 | 0.092555 | 0.088324 | 0.084626
mu thresh | 4.2043 | 3.4788 | 3.0335 | 2.7246 | 2.4943 | 2.3141 | 2.1681 | 2.0467 | 1.9436 | 1.8548 | 1.7772
pi thresh | 5.4857 | 4.5391 | 3.9579 | 3.555 | 3.2545 | 3.0193 | 2.8288 | 2.6704 | 2.536 | 2.4201 | 2.3188
kthresh | 19.9006 | 16.4666 | 14.3584 | 12.8965 | 11.8065 | 10.9534 | 10.2622 | 9.6876 | 9.1999 | 8.7794 | 8.4119
pthresh | 37.4788 | 31.0115 | 27.0412 | 24.288 | 22.2351 | 20.6285 | 19.3269 | 18.2446 | 17.3262 | 16.5342 | 15.842
% C5F12 | 0 | 10 | 20 | 30 | 40 | 50 | 60 | 70 | 80 | 90 | 100
C5F12 concentration (%)
LHCb RICH 2 with C5F10O/N2
GWP load = (0.13 molar*1*V.r)
LHCb RICH 2: CF4 thresholds
GWP load = (0.95 molar*4880*V.r)
Cherenkov threshold: lin-C5F10O (eg: 3M NOVEC 5110)/N2
& (heritage) C5F12/N2 blend and GWP load comparison with LHCb RICH2 (CF4: 100m3)
N2-NOVEC5110 (C5F10O) will be very similar (MW 266 vs. 288)
~ 14% molar Novec 5110 gives a GWP load reduction of 1737 tonnes
(everything in the 100m3 radiator vessel):
Even substituting CF4 with ~ 13% molar heritage stock C5F12 SFC (!) reduces GWP load by ~800 tonnes
36
G. Hallewell: Green FCs for Cherenkov detectors & Si tracker cooling Sustainability session: ICHEP2024 Prague 18-24 July 2024

## Slide 37
Base fluid | Base fluid density (1bar,25˚C) kgm-3 | Base fluid GWP (20-yr) | Component (n-1) (*106) (@ nm) | % Blend with N2 to match (n-1) CF4 | GWP load (t.CO2) | % Blend with N2 to match (n-1) C4F10 | GWP load (t.CO2)
CF4 LHCb RICH2 (100m3) | 3.56 [18] | 4880 [16] | 488 (180-310 nm) [19] | 100 | 1737 | not applicable | n/a
CF2O | - |  |  | ~100 | 1 | n/a | n/a
C2F6 | 5.63 [18] | 8210 [16] | 793 (180-310 nm) [19] | 38.1 | 1762 | not applicable | n/a
Lin-C2F4O | - |  |  | - |  | n/a | n/a
C3F8 | 7.75 [18] | 6640 [16] | 1180 (250 nm) [16] | 21.4 | 1099 | not applicable | n/a
Lin-C3F6O | - |  |  | - |  | n/a | n/a
C4F10 LHCb RICH1 (4m3): COMPASS (100m3) | 9.97 [18] | 6870 [16] | 1450 (250 nm) [16] | 16.3 | 1119 | 100 | 6849
Lin-C4F8O (Non-cyclic C4F8O)* | 9.5 (est.) | Probably < 1 (NOVEC 5110 Analogy) | 1380 @ 400nm (based on 3M PFG-3480 c-C4F8O [7]: linear C4F8O not yet measured but assumed similar) | 18.4 | 0.18 | 112.7* (>100% would imply necessity of operating C4F8O at slight overpressure) | 1.07
C5F12 | 11.63 [18] (BP 30 ˚C at 1 bar) | 6350 [16] | 1750 (180-310nm)[19] (40 ˚C, undiluted) | 13.0 | 957 | 79.3 | 5857
NOVEC 5110 C5F10O | 10.7 [13] (BP 27 ˚C at 1 bar) | <1 [13] | Not yet measured: probably around 1650 by analogy with C4F10 and C4F8O ratio | 13.9 | 0.149 | 85.2 | 0.91
Table 1: GWP loads of various SFCs and NOVEC 5110 blended with N2 ((n-1) = 310.10-6) to match refractivity of CF4 and C4F10
assumed radiator volume: 100 m3
Positions of presently unavailable-in-bulk CnF2nO fluids are shown in italics. Refractivities to match (CF4 and C4F10) shown in bold.
GWP loads and refractivities calculated using eqs. (1)-(3): assumed radiator volume: 100 m3
*Made in research quantities by Synquest Inc. as isomers Heptafluorobutyryl fluoride PN: 2116-2-07 CAS: 335-42-2
Octafluoro-2-butanone PN: 2117-2-10 CAS: 337-20-2 & Heptafluoroisobutyryl fluoride PN: 2116-2-0A CAS: 677-84-9
https://link.springer.com/article/10.1140/epjp/s13360-023-04703-w
GWP load reduction through CF4 index matching (LHCb RICH2)
G. Hallewell: Green FCs for Cherenkov detectors & Si tracker cooling Sustainability session: ICHEP2024 Prague 18-24 July 2024

## Slide 38
Base fluid | Base fluid density (1bar,25˚C) kgm-3 | Base fluid GWP (20-yr) | Component (n-1) (*106) (@ nm) | % Blend with N2 to match (n-1) CF4 | GWP load (t.CO2) | % Blend with N2 to match (n-1) C4F10 | GWP load (t.CO2)
CF4 LHCb RICH2 (100m3) | 3.56 [18] | 4880 [16] | 488 (180-310 nm) [19] | 100 | 1737 | not applicable | n/a
CF2O | - |  |  | ~100 | 0 | n/a | n/a
C2F6 | 5.63 [18] | 8210 [16] | 793 (180-310 nm) [19] | 38.1 | 1762 | not applicable | n/a
Lin-C2F4O | - |  |  | - |  | n/a | n/a
C3F8 | 7.75 [18] | 6640 [16] | 1180 (250 nm) [16] | 21.4 | 1099 | not applicable | n/a
Lin-C3F6O | - |  |  | - |  | n/a | n/a
C4F10 LHCb RICH1 (4m3): COMPASS (100m3) | 9.97 [18] | 6870 [16] | 1450 (250 nm) [16] | 16.3 | 1119 | 100 | 6849
Lin-C4F8O (Non-cyclic C4F8O)* | 9.5 (est.) | Probably < 1 (NOVEC 5110 Analogy) | 1380 @ 400nm (based on 3M PFG-3480 c-C4F8O [7]: linear C4F8O not yet measured but assumed similar) | 18.4 | 0.18 | 112.7* (>100% would imply necessity of operating C4F8O at slight overpressure) | 1.07
C5F12 | 11.63 [18] (BP 30 ˚C at 1 bar) | 6350 [16] | 1750 (180-310nm)[19] (40 ˚C, undiluted) | 13.0 | 957 | 79.3 | 5857
NOVEC 5110 C5F10O | 10.7 [13] (BP 27 ˚C at 1 bar) | <1 [13] | Not yet measured: probably around 1650 by analogy with C4F10 and C4F8O ratio | 13.9 | 0.149 | 85.2 | 0.91
Table 1: GWP loads of various SFCs and NOVEC 5110 blended with N2 ((n-1) = 310.10-6) to match refractivity of CF4 and C4F10
assumed radiator volume: 100 m3
Even bigger GWP load reduction through C4F10 index matching
(eg here: COMPASS RICH)
G. Hallewell: DRD4 WG 2 Low GWP FC radiator gases: June 19 2024

## Slide 39: CnF2nO fluid selection search criteria
Start(ed)
Non-toxic
(MSDS)
?
N
Y
Non-
Flammable
(MSDS)
?
N
Y
Non-
Oxone-
depleting
?
N
Y
Next CnF2nO fluid
(order & isomer)
to evaluate
Materials/
purifier
Compatible
?
N
Y
N
Y
Rad.
Tolerant
(more for
cooling)
?
N
Y
Dielectric
?
Acid
formation
with H2O
?
N
Y
N
Y
N
Recirc.
Thermo-
dynamics
OK
?
Y
Y
Y
UV-Vis
transparency
OK
?
(n-1) &
Chrom. Disp.
OK
?
N
N
Accept
fluid
Optotests
Materials tests
Bibliographic
Low GWP!
?
N
Y
G. Hallewell: Green FCs for Cherenkov detectors & Si tracker cooling Sustainability session: ICHEP2024 Prague 18-24 July 2024

## Slide 40
G. Hallewell: Green FCs for Cherenkov detectors & Si tracker cooling Sustainability session: ICHEP2024 Prague 18-24 July 2024
UV transparency, refractivity, cmhemical stability & compatibility studies needed
for different CnF2nO molecular shapes. RICH detector community very competent & equipped for detailed UVT & (n-1) - much ex-DELPHI RICH diagnostic equipment at CERN for example
Minuteman Model 302 VM.
Most probable PC spectral range
in new build gas RICH detectors
A
ALICE VHMPID: transparancy
measurements in c-C4F8O
Octafluorotetrahydrofuran
CAS: 773-14-8
Synquest Inc. FL, USA

## Slide 41
Some perspective (1): Val Thoiry (01) “Grande Surface” shopping centre near CERN:
G. Hallewell: Green Cherenkov radiators Sustainable HEP 4th Edition, CERN 12-15 May 2025