## Slide 1: Measurement of the muon anomalous magnetic moment with the Fermilab g-2 experiment
Saskia Charity, University of Liverpool
Birmingham EPP Seminar, 06 December 2023

## Slide 2: Muons & magnetic moments
g determines spin precession frequency in a magnetic field
Magnetic Moment
Torque in B-field
B

## Slide 3: Muons & magnetic moments
g determines spin precession frequency in a magnetic field
Magnetic Moment
Torque in B-field
For a pure Dirac spin-½ charged fermion, g is exactly 2
Interactions between the muon and virtual particles alter the value: X & Y particles could be SM or new physics
B

## Slide 4: Standard Model components of gμ
Dirac
Charged,
spin ½

## Slide 5: Standard Model components of gμ
Dirac
Schwinger
1st Order QED
Charged,
spin ½

## Slide 6: Standard Model components of gμ
Dirac
Schwinger
Kinoshita
1st Order QED
+12671 diagrams
Charged,
spin ½
Up to 10th Order QED

## Slide 7: Standard Model components of gμ
Hadronic
Dirac
Schwinger
Kinoshita
1st Order QED
Charged,
spin ½
+12671 diagrams
Up to 10th Order QED

## Slide 8: Standard Model components of gμ
Hadronic
Dirac
Schwinger
Kinoshita
1st Order QED
Charged,
spin ½
+12671 diagrams
Up to 10th Order QED
Electroweak

## Slide 9: Standard Model components of gμ
Hadronic
Dirac
Schwinger
Kinoshita
1st Order QED
Charged,
spin ½
+12671 diagrams
Up to 10th Order QED
Electroweak
BSM?

## Slide 10: Muon g-2 Theory Initiative
Hadronic Light-by-Light
Dirac Equation
Electroweak
Hadronic Vacuum Polarization
QED
Consortium of 100+ theorists who compile the theoretical inputs and provide recommendations
Last compilation in 2020:
SM values taken from the Muon g-2 Theory Initiative
White Paper: Phys. Rept. 887 (2020) 1-166
https://doi.org/10.1016/j.physrep.2020.07.006
https://muon-gm2-theory.illinois.edu/
TI in Bern, September 2023

## Slide 11: The muon anomalous magnetic moment
Define the quantity aμ : muon anomalous magnetic moment
aμ arises due to higher-order interactions / loop contributions
All SM particles contribute
Calculate & sum all sectors of the SM
QED dominates the value
Hadronic terms dominate the uncertainty

## Slide 12: Hadronic Vacuum Polarisation (HVP): dispersion relation
Dispersion Relation
follows from causality
Optical Theorem
follows from unitarity of scattering matrix
Cross section data used in TI 2020 prediction
Davier et. al, Eur. Phys. J. C. 80 (2020)
1/s weight low energies most important
contributes 73% to LO
Need to know total hadronic cross-section σhad(s)

## Slide 13: Hadronic Vacuum Polarisation (HVP): lattice approach
First principle calculation to predict aµ
Numerical integration on finite space-time lattice very computationally expensive
Lattice results not included in TI 2020 white paper due to low precision
So far, no other high-precision aµ from different group
Ongoing cross-checks by many groups at different energies
Preliminary agreement in ‘intermediate energy window’
First prediction with <1% uncertainty by BMW
Dispersive (TI 2020)
Exp. (FNAL Run-1)

## Slide 14: FNAL Measurement: status in 2021
First announcement of the FNAL experiment using Run-1 (2018) data in April 2021
Using the TI(2020) value for the SM comparison (data-driven HVP only)

## Slide 15: FNAL Measurement: status in 2023
In August 2023, FNAL published updated result using Run-2 (2019) and Run-3 (2020) data
>4x higher statistics than the Run-1 result
Excellent agreement with Run-1 and BNL
BNL, Run-1 and Run-2/3 statistics dominated
Assume 100% correlated systematics
World Average dominated by FNAL

## Slide 16: Comparison with the Standard Model
Tension between dispersive and lattice approaches to HVP
Lattice result needs independent confirmation
Long-standing tension between experiment and dispersive result approaches 5σ
New cross-section results from CMD-3 makes the dispersive situation quite puzzling
Very dynamic situation: huge effort to reconcile differences and tensions

## Slide 17: The CMD-3 result
Plot by F. Ignatov
In WP2020
2 new HVP LO results since WP2020
SND2k and CMD-3 released 2 new results for since the theory combination in 2020
Detailed view of shows CMD-3 as outlier, but it agrees with lattice

## Slide 18
The Fermilab g-2 Experiment

## Slide 19: The FNAL Muon Campus
Recycler ring: 8 GeV protons
  1012 protons / bunch ; 10k stored muons / bunch
8 GeV protons  pion production target
Pions  delivery ring  decay to μ+ and momentum-selected
3.09 GeV μ+  g-2 storage ring magnet
Beam arrives in 120 ns wide bunches
Each bunch corresponds to a “fill”  1 ms

## Slide 20: The Storage Ring
B
Cross-section slice of magnet
1.45 T vertical B field in muon region

## Slide 21: Injecting and storing the beam
Beam injected through inflector magnet  cancel main magnetic field

## Slide 22: Injecting and storing the beam
Kicker magnet applies fast radial magnetic field on first turn
Beam injected through inflector magnet  cancel main magnetic field

## Slide 23: Injecting and storing the beam
Kicker magnet applies fast radial magnetic field on first turn
Quads pulse throughout muon fill  vertical focusing
Beam injected through inflector magnet  cancel main magnetic field

## Slide 24: Injecting and storing the beam
Kicker magnet applies fast radial magnetic field on first turn
Quads pulse throughout muon fill  vertical focusing
Beam injected through inflector magnet  cancel main magnetic field
Magnetic field map measured every 3 days, changes monitored continuously

## Slide 25: Injecting and storing the beam
Straw trackers measure beam profile at 180o and 270o
Kicker magnet applies fast radial magnetic field on first turn
Quads pulse throughout muon fill  vertical focusing
Beam injected through inflector magnet  cancel main magnetic field
Magnetic field map measured every 3 days, changes monitored continuously

## Slide 26: Calorimeter detectors
Positive muons, 3.09 GeV/c, injected into Storage Ring in 125 ns bunches
Muons orbit inside storage ring, spin precesses about vertical B field
Decay to positrons  lower momentum  spiral into centre of storage ring
Calorimeters
Each calo is a 6x9 array of PbF2 crystals
  2.5 cm x 2.5 cm x 14 cm (15X0)
Readout by SiPMs to 800 MHz WFDs (1296 channels in total)

## Slide 27: Spin Precession in the Storage Ring
Muons orbit the ring with cyclotron frequency ωc
Spin precesses with frequency ωs
Both spin and cyclotron frequencies are proportional to B
Spin rotates ahead of momentum as the muon orbits the ring
Difference frequency ωa is proportional to aμ and B
Measure
Extract
If g were exactly 2, ωs = ωc and ωa = 0
149 ns
138 ns

## Slide 28: Spin Precession in the Storage Ring
Measure
Extract
Muons orbit the ring with cyclotron frequency ωc
Spin precesses with frequency ωs
Both spin and cyclotron frequencies are proportional to B
Spin rotates ahead of momentum as the muon orbits the ring
Difference frequency ωa is proportional to aμ and B
If g were exactly 2, ωs = ωc and ωa = 0
149 ns
138 ns

## Slide 29: Measuring ωa
Highest energy e+ preferentially emitted in direction of muon spin
Oscillation in number of emitted decay e+ vs time directly proportional to decay asymmetry
Count N(t) = number of e+ above an energy threshold over time.
Higher fraction detected above threshold when e+ emitted parallel to muon spin
N(t) depends on anomalous precession frequency ωa
Frequency of oscillation = ωa

## Slide 30: Measuring muon spin precession
Number of high energy positrons oscillates as a function of time as muon spin points towards/away from detector
Count positrons above an energy threshold
Counts oscillate at frequency ωa  extract from time spectrum
Threshold Energy
Time Spectrum
Energy Spectrum
Real Data (Run-3a)

## Slide 31: Extracting ωa: 5-parameter fit function
Time-dilated muon lifetime
Asymmetry
Precession frequency
Average spin phase at injection
Number of e+ vs time
Five-parameter fit function

## Slide 32: Fitting the wiggle
Calorimeter Performance
32
Simplest 5-parameter fit function captures exponential decay and the g-2 oscillation only
Not sufficient  large spikes in residuals FFT
Need to measure and account for additional terms in the fit
/ndf = 51530/4150

## Slide 33: Tracking detectors: measuring the muon beam
Calorimeter Performance
Straw trackers: two stations located at 180⁰ and 270⁰
One station = 8 modules
One module = 128 Argon-Ethane gas-filled straws
Fit tracks and extrapolate to muon decay point
Tracker Module
10 cm

## Slide 34: Tracker measurement of the muon beam
Calorimeter Performance
34
The mean and width of the muon beam distribution varies as a function of time
Average radial and vertical position vary around the ring  measure at two locations
Frequency of beam oscillations must be measured  affects ωa measurement

## Slide 35: Fitting the wiggle
Calorimeter Performance
35
Accounting fully for all the beam oscillations shifts ωa by 1.6 ppm
Final fit function has 27 fit parameters
8 different analysis teams, 19 separate analyses
/ndf = 4086/4138
Run 3a
Simple Fit Function
Full Fit Function

## Slide 36
Extracting aμ

## Slide 37: Relativistic expression for ωa
Non-relativistic limit
Motion non-perpendicular to B-field
Cyclotron motion assumes motion perpendicular to B-field
Relativistic motional magnetic field
Proportional to electric field
Disappears for “magic” γ = 29.3  magic momentum 3.09 GeV / c
Not all muons are at the ‘magic’ momentum of 3.1 GeV
Vertical momentum component aligned with B field
E-field correction
Pitch correction

## Slide 38: “Never measure anything but frequency…”
Phys. Rev. A 83, 052122 (2011)
Metrologia 13, 179 (1977)
Rev. Mod. Phys. 88 035009 (2016)
Phys. Rev. Lett. 82, 711 (1999)
We measure the ratio of two frequencies: ωa and ωp
  ωa : anomalous spin precession frequency
  ωp : muon-weighted magnetic field expressed in terms of Larmor frequency of free proton

## Slide 39: “… and corrections”
Clock blinding frequency
Anomalous precession frequency
Beam dynamics corrections
Transient magnetic field corrections
Muon beam distribution
Magnetic field map
Absolute calibration frequency

## Slide 40: “… and corrections”
Transient magnetic field corrections
Muon beam distribution
Magnetic field map
Absolute calibration frequency

## Slide 41
Measuring the magnetic field

## Slide 42: The g–2 Storage Ring magnet
Dipole field has ppm-level uniformity (<20 ppm RMS across the full azimuth)
Shimming devices (active and passive) minimise gradients and keep field uniform
B
Field in muon storage region
Weight measured field by the muon beam distribution

## Slide 43: Measuring the magnetic field
Trolley containing 17 NMR probes maps full azimuth every few days (muons not present)
378 fixed probes monitor between trolley runs (during muon data collection)
Field map is interpolated between trolley runs using fixed probe information
Fold with muon beam distribution
Sequence 2D field slices as trolley moves
NMR probe

## Slide 44: Absolute Calibration
Trolley and fixed NMR probes use petroleum jelly as the proton sample – low volatility
Need to measure protons in H20 (measurement standard)  calibration
Trolley and cylindrical H20 calibration probe switch places to repeatedly measure the same field in the same place. Calibration performed ~once per year.
Cylindrical H20 probe
Trolley probes
Uncertainty
17 ppb
Calibration region
Spherical H20
Spherical 3He
Cross-check with spherical probes
Uncertainty: 9 ppb

## Slide 45: Transient fields from pulsed systems: Quads
Grey regions = muon storage times
Locations mapped in Run-1
Q1
Q2
Q4
Q3
Electrostatic quadrupoles pulse during muon storage
No pulsing during trolley runs
Quad plates vibrate  induces a field
Muons experience a field change which the fixed probes do not see (shielded by Al)
Must be measured using dedicated apparatus

## Slide 46: Transient fields from pulsed systems: Quads
Locations mapped in Run-1
Locations mapped in Run-2
Run-1: -17 (90) ppb Run-2/3: -21 (20) ppb
Electrostatic quadrupoles pulse during muon storage
No pulsing during trolley runs
Quad plates vibrate  induces a field
Muons experience a field change which the fixed probes do not see (shielded by Al)
Must be measured using dedicated apparatus
Q1
Q2
Q4
Q3
Grey regions = muon storage times

## Slide 47: Transient fields from pulsed systems: Kicker
Kicker pulse of 22 mT for 150 ns just after muon injection
Field change caused by residual field (eddy currents) after kicker pulse
Muons present from 30μs to 700μs after the kick (fit region)
Measure eddy current using Faraday magnetometer
Run-2/3: improved hardware setup reduced vibrations
Correction
Run-1: -27 (37) ppb Run-2/3: -21 (13) ppb

## Slide 48: Magnetic field systematics in Run-2/3
Main reduction in uncertainty comes from better understanding of transient field effects
Interpolation uncertainty has also reduced with number of trolley runs
Uncertainty already at TDR goal

## Slide 49
Improvements between Run-1 and Run-2/3

## Slide 50: Damaged resistors
In Run-1, 2 out of 32 resistors damaged in quad plates  unstable beam storage
Redesigned and replaced before Run-2
Reduces phase acceptance (Cpa) uncertainties 75ppb  13 ppb
Beam oscillation frequencies also become more stable
ωa phase change
Vertical beam width change

## Slide 51: Kicker strength upgrade
Fractional Momentum Shift: dp/p0 [%]
Run 1 beam
Late Run 3 beam
Upgraded kicker cables while Run-3 so kicker can run at nominal strength
Muon distribution more centered
  All systematics related to asymmetric beam shape reduced
Muon momentum distribution better centered on magic momentum
  E field correction reduced
Phase space matching improved
  Smaller beam oscillations

## Slide 52: Statistical improvement: Run-2/3 vs Run-1
Dataset | Statistical Error [ppb]
Run-1 | 434
Run-2/3 | 201
Run-1 + Run-2/3 | 185

## Slide 53: Total uncertainty
Total uncertainty: 462 ppb
434 ppb
Total uncertainty: 215 ppb
Run-2/3
201 ppb
Run-1
70 ppb
157 ppb
Radius: uncertainty Area: variance
Uncertainty reduced by factor >2
Statistic and systematic uncertainty reduced by similar amount
Systematic uncertainty below TDR goal
Still statistics dominated

## Slide 54: Unblinded result & cross-checks
aμ(Run-1) = 0.00 116 592 040(54) [463 ppb]
aμ(Run-2/3) = 0.00 116 592 057(25) [215 ppb]
aμ(FNAL) = 0.00 116 592 055(24) [203 ppb]
aμ(Exp) = 0.00 116 592 059(22) [190 ppb]
Different runs performed at different magnet set-points – a useful consistency check
Also divide datasets by other variables to check consistency (e.g. day/night, temperature, etc)

## Slide 55: Beyond Run-2/3 : Total statistics
MAY 2018
JULY 2023
x3 Run-1/2/3
statistics
Surpassed proposal goal!

## Slide 56: Conclusions
High precision measurements of Muon g-2 stringent test on SM theory
Run-2/3 data consistent with Run-1 and BNL
Factor >2 in statistical and systematic uncertainty
Surpassed TDR goals in statistics and systematics
First time a three-way comparison of aµ is possible (dispersive-approach, lattice approach, experiment)
Another reduction by factor of 2 in statistical uncertainty from Run-4/5/6
Expect final result in 2025

## Slide 57
Thank you!

## Slide 58: Acknowledgements
Department of Energy (USA)
National Science Foundation (USA)
Istituto Nazionale di Fisica Nucleare (Italy)
Science and Technology Facilities Council (UK)
Royal Society (UK)
Leverhulme Trust (UK)
European Union’s Horizon 2020
Strong 2020 (EU)
German Research Foundation (DFG)
National Natural Science Foundation of China
MSIP, NRF, and IBS-R017-D1 (Republic of Korea)