## Slide 1: Newest results from the NEWS-G dark matter experiment
Philippe Gros
On behalf of the NEWS-G collaboration
Lake Louise Winter Institute 2024

## Slide 2: Low mass WIMP search motivation
Given the absence of canonical WIMPs, there is motivation to look at the parameter space left at lower masses (~0.1-1 GeV) for WIMP-like dark matter candidates.
arXiv:2104.07634 [hep-ex]

## Slide 3: NEWS-G and SPCs
The NEWS-G experiment uses spherical proportional counters (SPC) to search for low mass dark matter.
SPCs are metallic spheres filled with gas, with a central anode producing a radial electric field.
The last dark matter limits are from the SEDINE detector (60 cm diameter) at the Laboratoire Souterrain de Modane (LSM) in 2017.
The latest detector, S140, is a 135 cm of diameter copper sphere currently at SNOLAB, after a short commissioning at the LSM in 2019.
The SEDINE detector
doi: 10.1016/j.astropartphys.2017.10.009
S-140 detector model

## Slide 4: How an SPC works:
doi: 10.1016/j.nima.2019.162390
Nuclear or electronic recoil causes ionization of the gas.
Primary electrons drift towards the central anode.
Townsend avalanche near the anode amplifies the signal.
Drifting secondary ions induce a current on the anode.

## Slide 5: Sensor: achinos
NEWS-G now uses a multi-anode sensor that can achieve high gain while keeping a strong electric field at a high radius.
The sensor is divided in two channels connecting the anodes of each hemisphere.
A signal on one channel induces a negative signal on the other one (Shockley-Ramo effect).
About 2/3 of the volume leads to the south anodes, due to the effect of the rod on the electric field.
doi:10.1088/1742-6596/2156/1/012059
arXiv:2301.05183
Only pure south events were kept as candidate events.

## Slide 6: Shielding and data taking with S140
The sphere is made of C10100 copper, with the inner 0.5 mm being electroformed ultra-pure copper.
Lead, archeological lead and polyethylene (PE) make the shielding, although a temporary water shield was used at the LSM.
10 days of physics data taken in 135 mbar of CH4 at the LSM before the detector was shipped to SNOLAB.
SNOLAB detector paper doi:10.1088/1748-0221/18/02/T02005

## Slide 7: Calibration
A UV laser is directed at the inner copper surface of the sphere and releases electrons through the photoelectric effect. The UV light also goes to a photodetector so the laser events can be tagged as a control.

## Slide 8: Calibration
270 eV peak
2.8 keV peak
doi:10.1088/1742-6596/2156/1/012059
A UV laser is directed at the inner copper surface of the sphere and releases electrons through the photoelectric effect. The UV light also goes to a photodetector so the laser events can be tagged as a control.
Some argon-37 is released inside the sphere, and the gas diffuses in the whole volume. This isotope is radioactive and has two peaks that enable energy calibration, as well as ionisation and attachment parametrization .

## Slide 9: Calibration
A UV laser is directed at the inner copper surface of the sphere and releases electrons through the photoelectric effect. The UV light also goes to a photodetector so the laser events can be tagged as a control.
Some argon-37 is released inside the sphere, and the gas diffuses in the whole volume. This isotope is radioactive and has two peaks that enable energy calibration, as well as ionisation and attachment parametrization .
The quenching factor was measured at COMIMAC as well as obtained from literature W-values.
270 eV peak
2.8 keV peak
doi:10.1088/1742-6596/2156/1/012059
doi:10.1140/epjc/s10052-022-11063-9

## Slide 10: Peak counting and time separation
The exponential decay of the preamplifier and the ion response are deconvolved from the raw signal.
It is possible to count individual primary electrons.
Surface events experience more diffusion than volume events, which causes the time separation between the first and last peak to be larger.
SURFACE (laser)
VOLUME (37Ar)
scipost_202210_00005v1
DOUBLE-DECONVOLUTION

## Slide 11: Alpha contamination
There is ~25 mHz of alphas from 210Po contamination in the copper surface.
Alphas ionize a lot of gas and create a space charge that disturbs the electric field, and changes the electron drift time.
A high rate of very low energy events keep happening for around 5s after each alpha. It is likely due to electronegative contaminants capturing electrons and becoming slow drifting ions
We remove most of the low-energy background due to alphas with a 5s cut after each one, keeping 88% of the total time.
Methane 135 mbar 1630 V
RATE
DRIFT TIME

## Slide 12: Physics data fits
30% of the full data was set aside as a test data before the rest is unblinded.
Profile likelihood fits of the test data were made for 2-3-4 peak data
Fits with contributions from surface background, coincidences and WIMP signal.
No significant WIMP signal was detected.
WIMP exclusions limits with ~0.12 kg·days of data
Strongest constraints for the proton spin-dependent interaction in the 0.2 - 1 GeV range.
Data unblinded, final checks
Final blind data results to come in a few weeks.
scipost_202210_00005v1

## Slide 13: News from SNOLAB
One physics data campaign taken, preparing the next one
Still countable electrons
Delays due to HV issues and alpha BG mitigation
Improvements from LSM:
  Trigger on three channels (North, South, laser)
  Reduced noise
  Better gas purity
  Neon+2%CH4, CH4, Ar+CH4, He+CH4 etc.
Single electron sensitivity
37Ar
13
Good gas quality
Reduced noise

## Slide 14: Future projects
ECuME (& miniECuME):
  Fully underground electroformed 140 cm of diameter copper sphere in SNOLAB. (30 cm prototype to be built in 2024 at PNNL)
DarkSPHERE:
  Fully electroformed 3m of diameter sphere in a water shield in Boulby. (under consideration)
NEWS-G³ (or G3):
  Shield at Queen’s University intended for CEνNS detection at nuclear reactors. (shield completed, ongoing testing and calibration)
General sensor R&D
  Smaller anodes for high pressure operation
  New structures with 3D printed resistive material
  Multi-channel acquisition
arXiv:2301.05183
G3

## Slide 15: Conclusion
NEWS-G and SPCs well suited for low mass dark matter search.
2019 data at LSM in pure methane will set new SD-p WIMP constraints with CH4.
  Coming soon!
Currently taking physics data at SNOLAB with many improvements.
  Data to be analysed. New target gases coming
Promising future projects in the works.

## Slide 16: Thank you!

## Slide 17: Thank you

## Slide 18: Extra slides

## Slide 19: Pulse shape discrimination
Wide
There are spurious pulses caused by electronic discharges in the data.
Those can be discriminated from physical events with two different methods:
  Spurious pulses are either measurably spikier or wider than physical events.
  Spurious pulses do not cause a negative induced pulse on the opposite channel.
Around 95% of the spurious pulses are removed with cuts usings theses discriminants, while still keeping 77% of the physical events.
19

## Slide 20: How an SPC works:
20
Animation by Philippe Gros
Nuclear or electronic recoil causes ionization of the gas.
Primary electrons drift towards the central anode.
Townsend avalanche near the anode amplifies the signal.
Drifting secondary ions induce a current on the anode.

## Slide 21: Copper electroforming
Even the C10100 copper bulk contains traces of 210Pb, which emits bremsstrahlung X-rays through their beta decay.
The electroforming of the 0.5mm inner copper surface was done in collaboration with the Pacific Northwest National Lab at the LSM.
This reduces the overall background by 98%, and the sub-keV background by 70%.

## Slide 22: Double deconvolution
Ionization equations:
Primary ionization follows a COM-Poisson distribution, and the avalanche follows a Polya distribution.
The exponential decay of the preamplifier and the ion response are deconvolved from the raw signal.
The integrated double-deconvolved amplitude is proportional to the energy, while the rise time is a measure of the diffusion which relates to the event radial position.
DOUBLE-DECONVOLUTION
22
INTEGRATION
There is work on using machine learning as an alternative

## Slide 23: Peak counting and time separation
With the large sphere of S140, it is possible to count individual primary electrons using ROOT TSpectrum.
The single-electron trigger efficiency is 60%, with a noise trigger proportion around 10-4.
Surface events experience more diffusion than volume events, which causes the time separation between the first and last peak to be larger.
Number of electrons is a measure of the energy.
SURFACE (laser)
VOLUME (37Ar)
scipost_202210_00005v1
23

## Slide 24: Laser calibration
A 213nm UV laser is directed at the inner copper surface of the sphere and releases electrons though the photoelectric effect.
The UV light also goes to a photodetector so the laser events can be tagged.
Low-intensity laser data enables measurements of the single electron detector response (gain, avalanche statistics, trigger efficiency, peak detection threshold).
High intensity laser data is used in all runs to enable constant monitoring of the detector.
Gas degradation inducing a decrease in gain can be seen through laser events.
24

## Slide 25: 37Ar Calibration
Some argon-37 is released inside the sphere, and the gas diffuses in the whole volume. 37Ar is produced at the Royal Military College in Kingston, in their SLOWPOKE-II reactor from CaO irradiation.
This isotope is radioactive and has two main X-ray peaks (270 eV and 2.8 keV). It decays with a half-life of 35 days through electron capture.
270 eV peak
2.8 keV peak
doi:10.1088/1742-6596/2156/1/012059
25
Argon-37 enables:
  Energy calibration
  Electron attachment parametrization
  W-value and Fano factor measurements
  South-channel anodes gain measurements

## Slide 26: Quenching factor
The quenching factor was measured at COMIMAC as well as obtained from literature W-values.
Lower energy quenching factor were extrapolated logarithmically (more conservative).
Future quenching factor measurements for lower energies and other gas mixtures in preparation.
doi:10.1140/epjc/s10052-022-11063-9
26

## Slide 27: Future DM projects
ECuME
Fully underground electroformed 140 cm of diameter copper sphere to be made inside SNOLAB.
Mini-ECUME prototype with 30 cm of diameter to be built during the second half of 2023 at PNNL.
Last tests before Mini-ECUME currenlty being completed.
DarkSPHERE
  Fully electroformed 3m of diameter sphere in a water shield for the Boulby Underground Laboratory, in England (under consideration).
27
arXiv:2301.05183

## Slide 28: Neutrino research
NEWS-G³ (or G3)
Shield at Queen’s University intended for CEνNS detection at nuclear reactors.
The shield is comprised of multiple layers of lead, polyethylene, scintillators (muon veto) and copper. It was completed last summer.
Tests, simulations and calibrations are currently being done at Queen’s.
28

## Slide 29: Double deconvolution
Integration
Double deconvolution
The ballistic deficit is the signal amplitude that gets underestimated due to the exponential decay of the preamplifier.
The full amplitude (energy) is retrieved by doing a double deconvolution of the raw signal, and then integrating the pulses.
29