## Slide 1: Measuring the Neutrino Mass with the Project 8 Experiment
Luiz de Viveiros - Penn State
Project 8 Collaboration
Axial (ωa)
Cyclotron (ωc)
Grad-B (ωg)
B-field
Frequency -24GHz (MHz)
Time (ms)

## Slide 2: Project 8: Measuring the Neutrino Mass with CRES
Neutrino flavor oscillations ⇒ neutrino masses > 0 eV/c2
Absolute mass scale and ordering are still unknown
Tritium β- spectroscopy is the leading technique for direct neutrino mass measurements
  Best limits from KATRIN:
  Beta decay endpoint should match the mass difference (~18.6 keV) for
  Determine the neutrino mass from the shape of the tritium β-decay spectrum endpoint
New spectroscopy technique: Cyclotron Radiation Emission Spectroscopy (CRES)
Electron on a magnetic field: cyclotron motion; emitted cyclotron radiation depends on electron kinetic energy
Frequency falls in the microwave K-band for ~1T fields
  Tritium endpoint at 18.6 keV ⟹ For B ~ 0.95 T, f ~ 25.6 GHz
  83mKr conversion electrons (e.g. 17.8 keV) can be used for calibration ➞ f ~ 25.0 - 26.5 GHz
Radiated Power P = ~ 1 fW for 18.6 keV electrons
  Surprisingly, this had never been observed for a single electron!
Project 8 proposes to use this technique to build a detector with sensitivity to 40 meV /c2 neutrino mass!
electron energy [keV]
decay rate [arb. units]
only 2×10-13 of decays in the last 1eV interval
B-field
Superconducting Magnet
Superconducting Magnet
n
n
p
p
n
p
𝜈e
e-
3H
3He
β-decay
electron
anti-neutrino
n
n
p
p
n
p
𝜈e
e-
3H
3He
β-decay
electron
anti-neutrino

## Slide 3: The Project 8 Scientific Programme: A Phased Approach
Phase I:
Demonstrate CRES technique on 83mKr mono-energetic electrons.
Phase II:
Measure Tritium spectrum endpoint. Study systematics and backgrounds.
Phase III:
(a) “Large Volume” CRES
(b) Atomic tritium production and trapping at high densities
Phase IV:
Large atomic tritium experiment. Inverted mass ordering reach (40 meV)
n
n
p
p
n
p
𝜈e
e-
3H
3He
β-decay
electron
anti-neutrino

## Slide 4: Phases I and II - The Detector
repurposed NMR
superconducting
magnet ~ 1 T,
52 mm warm bore
83mKr gas system
2x cryogenic low-noise
microwave amplifiers
(54 dB)
40 K cold head
Receiver
Insert:
Gas Cell, Magnetic Trap, and Waveguide
(inside)
signal
B-field
waveguide
pre
amp
Phase I setup
Assembled at the University of Washington in Seattle, WA
Phase I: 83mKr only (2016); Phase II: 83mKr and T2 (2024)
trap
coils
windows
Waveguide to amplifiers
130 mm
Bmin
10 mm
Axial (ωa)
Cyclotron (ωc)
Grad-B (ωg)
B-field
Phase II
Insert

## Slide 5: Measuring the Cyclotron Radiation and the Tritium Spectrum
time (ms)
Frequency of first track gives initial electron kinetic energy
linearly rising frequency: radiative energy loss, slope ~ 1fW
jumps: electrons scatters of gas molecule, losing energy and changing pitch angle
scale: 1 MHz ~ 20 eV
First detection of single-electron cyclotron radiation - Phys. Rev. Lett. 114, 162501 (2015) [arXiv:1408.5362]
First T2 endpoint neutrino mass measurement using CRES - Phys. Rev. Lett. 131, 102502 (2023) [arXiv:2212.05048]
  Frequentist: ; Bayesian:
Science run with 82 net days of data taking, 3770 events, 4 trap coils, 1 mm3 effective volume
No events past endpoint ⇒ sets limit on background rate:

## Slide 6: The Project 8 Scientific Programme: A Phased Approach
Phase I:
Demonstrate CRES technique on 83mKr mono-energetic electrons.
Status: Complete! Technique demonstrated.
Phase II:
Measure Tritium spectrum endpoint. Study systematics and backgrounds.
Status: Complete! First Tritium spectrum!
Phase III:
(a) “Large Volume” CRES
(b) Atomic tritium production and trapping at high densities
Phase IV:
Large atomic tritium experiment. Inverted mass ordering reach (40 meV)
n
n
p
p
n
p
𝜈e
e-
3H
3He
β-decay
electron
anti-neutrino

## Slide 7: Large Volume CRES
We need a new CRES technology to reach cubic meter volumes!
  Waveguide-centric design is no longer suitable
Project 8 has considered and investigated an antenna array design significantly in the last few years (arXiv:2504.15387). A number of challenges identified during R&D have focused development on resonant cavities
  Large volume efficiency, high SNR, and small channel count
Antenna Arrays
Cavities

## Slide 8: Desirable cavity characteristics
Compatibility with atomic tritium
  Current experiments use T2, switching to T will allow reduction of uncertainty on decay final states ⇒ Improved mass sensitivity
  Require minimizing exposed surfaces (metal) inside the cavity interior space, to prevent tritium recombination;
  Require magnetic atom trap (Ioffe coils), which constraining cavity volume, feedthroughs and connections on the sides
Open cavity for gas flow, pumping, atomic tritium beam injection
Cavity external coupling: Over-couple from to
Pinches & solenoid
Atomic trap coils
Cavity Termination
TE011 electric field
Loop antennas
Mid-section readout
Richard Mueller

## Slide 9: Cavity Development Program
Scaling up cavity design to 10-100 m3
Multiple detectors planned to demonstrate key technologies
  CCA: Cavity CRES Apparatus (L ~ 14 cm, 26 GHz)
  LFA: Low Frequency Apparatus (L ~ 5 m, 560 MHz)
~20 m
cavity length: 14 cm
26 GHz
Cavity CRES Apparatus (CCA)
Credit: J. Stachurska
560 MHz
Low Frequency Apparatus (LFA)
150 MHz Pilot
~150 MHz
Phase IV
Credit: M. Huehn, R. G. H. Robertson
5 m

## Slide 10: Cavity Development Program
Scaling up cavity design to 10-100 m3
Multiple detectors planned to demonstrate key technologies
  CCA: Cavity CRES Apparatus (L ~ 14 cm, 26 GHz)
  LFA: Low Frequency Apparatus (L ~ 5 m, 560 MHz)
6 GHz Prototype at Penn State: Cavity design and readout tests
~20 m
cavity length: 14 cm
26 GHz
Cavity CRES Apparatus (CCA)
Credit: J. Stachurska
560 MHz
Low Frequency Apparatus (LFA)
150 MHz Pilot
~150 MHz
Phase IV
Credit: M. Huehn, R. G. H. Robertson
6 GHz Open Cavity
@ Penn State
cavity length: 21.5 cm
radius:
3.2 cm
6 GHz
6 GHz Cavity
5 m

## Slide 11: Cavity CRES Apparatus (CCA):
CCA
electron gun
cavity
amplifiers
trapping coils
RF waveguide carrying cyclotron radiation
Demonstrate small scale cavity at high frequency (26 GHz) with large SNR
  L = 14 cm, R = 0.7 cm, V ~ 20 cm3
  Magnetic Field of 1 T
  Electron gun source
R&D goal: improve CRES precision
  Goal: <0.3 eV FWHM resolution
Built at the University of Washington in Seattle, WA

## Slide 12: Scaling up Cavity Size
Small 6 GHz Cavity Prototype tests high Q open cavity design, use of grooves for mode filtering, new readout techniques
  Room Temperature, open to air, in small anechoic chamber
cavity length: 21.5 cm
cavity radius: 3.2 cm
terminator length: 5.2 cm
Interior is grooved to limit inductive coupling
Credit: B. DiLella
Cavity built by ARL
S11 sweeps identify and measure resonant modes
  Top: Data vs Simulation | Bottom: Fitted S11 gives mode Q
~ 3700
TE011
~ 8800
TE011
Cut-ring readout with split barrel connector

## Slide 13: Low-Frequency Apparatus (LFA)
First test of CRES in a large volume at lower frequency => Prove compatibility of CRES with large volume atomic trap (Ioffe coils)
  highly stable, homogeneous magnetic fields at lower field
Frequency of ~560 MHz
  L ~ 5 m, V ~ 1.5 m3
  Magnetic Field of ~0.020 T
Collected power is O(1 aW = 10-18 W)
Sources: 83mKr and electron gun; upgrade to T for neutrino mass measurement
Sensitivity aim: eV (90 % CL) (one-year with atomic source)
Blueprint for Phase IV
Credit: M. Huehn, R. G. H. Robertson
5 m
TE011
E-fields
inside
cavity
Cavity
Pinch coil
Injection
line
T atom source
(not shown)
Magnetic guide
Solenoid

## Slide 14: Phase IV
Atomic tritium experiment with large (100s m3) instrumented volume ⇒ Target Mass Sensitivity: mβ ~ 40 meV
  Resolve the inverted ordering case (mβ ≳ 50 meV)
Collaboration is working to provide predictions for dependence of sensitivity against key systematics.
  Energy resolution: σE ~ 90 ± 2 meV
mass of lightest mass eigenstate (meV)
mβ (meV)
Inverted Ordering
Normal Ordering
Mainz, Troitsk
KATRIN (2024)
KATRIN (Goal)
Systematic Limit with T2
Project 8 with T (Goal)
(K. Kazkaz)
lifetime (years)
(T. Weiss)
Mass Limits vs Lifetime
Preliminary
Mass Limits for Different Experiments:

## Slide 15: Thank You!
This work is supported by the US DOE Office of Nuclear Physics, the US NSF, the PRISMA+ Cluster of Excellence at University of Mainz, and internal investments at all institutions.
Project 8 has demonstrated the potential of the CRES technique, and charts a promising path towards a direct neutrino mass measurement!
Lawrence Livermore National Laboratory
Massachusetts Institute of Technology
Johannes Gutenberg University, Mainz
Heidelberg
University
Karlsruhe Institute
of Technology
Lawrence Berkeley National Laboratory
University of Washington
Yale
University
University of Texas, Arlington
Interested in joining Project 8?
We are looking for a Postdoc at Penn State !
Please contact ldeviveiros@psu.edu !
Project 8 Collaboration Meeting October 2025 – MIT
Pacific Northwest National Laboratory
University of Illinois
University of Pittsburgh
Indiana
University
Ghent
University
Case Western Reserve University
Carnegie Mellon University
Colorado School of Mines
Penn State University
Notes: This material is based upon work supported by the following sources: the U.S. Department of Energy Office of Science, Office of Nuclear Physics, under Award No.~DE-SC0011091 to the Massachusetts Institute of Technology (MIT), under the Early Career Research Program to Pacific Northwest National Laboratory (PNNL), a multiprogram national laboratory operated by Battelle for the U.S. Department of Energy under Contract No.~DE-AC05-76RL01830, under Early Career Award No.~DE-SC0019088 to Pennsylvania State University, under Award No.~DE-FG02-97ER41020 to the University of Washington, and under Award No.~DE-SC0012654 to Yale University; the National Science Foundation under Award Nos.~1806251 to MIT; This work has been supported by the Cluster of Excellence “Precision Physics, Fundamental Interactions, and Structure of Matter” (PRISMA+ EXC 2118/1) funded by the German Research Foundation (DFG) within the German Excellence Strategy (Project ID 39083149); Laboratory Directed Research and Development (LDRD) 18-ERD-028 at Lawrence Livermore National Laboratory (LLNL), prepared by LLNL under Contract DE-AC52-07NA27344; the MIT Wade Fellowship; the LDRD Program at PNNL; the University of Washington Royalty Research Foundation. A portion of the research was performed using Research Computing at PNNL. The isotope(s) used in this research were supplied by the United States Department of Energy Office of Science by the Isotope Program in the Office of Nuclear Physics. We further acknowledge support from Yale University, the PRISMA+ Cluster of Excellence at the University of Mainz, and the Karlsruhe Institute of Technology (KIT) Center Elementary Particle and Astroparticle Physics (KCETA).

## Slide 16: Questions?