## Slide 1
Development of a
Lab Environmental Monitor
Felix Belair
Aug 23, 2021
CASST
Supervisors: Chris Chambers,
Thomas Brunner
and Soud Al Kharusi

## Slide 2: Intro About Myself
I am from Montreal
Finished CEGEP last May
Worked at the Brunner Neutrino Lab during the summer
I will start first year at McGill in physics next week!

## Slide 3: Purpose of the Lab Environmental Monitor
Goals:
Sensitive experiments require clean working space
Track temperature, pressure, humidity and dust levels
Verify if lab is positive pressure
Find out how dust enters the lab
The BνL at McGill

## Slide 4: Purpose of the Lab Environmental Monitor
Goals:
Sensitive experiments require clean working space
Track temperature, pressure, humidity and dust levels
Verify if lab is positive pressure
Find out how dust enters the lab
Design Requirements:
Low maintenance/ headless
Cost efficient ≈ 150$
Modular
Open source
The BνL at McGill

## Slide 5: Key Components and Sensors
Atmospheric Sensor (BME280)
Differential Pressure Sensor (SDP810)
Particulate Counter (SPS30)
Raspberry Pi 4
External Power

## Slide 6: Data Flow
Run Main
Program

## Slide 7: Data Flow
Readings stored
into a local .csv file
Run Main
Program
Obtain readings
from the sensors

## Slide 8: Data Flow
File deleted
locally
File uploaded
to a database
Readings stored
into a local .csv file
Run Main
Program
Obtain readings
from the sensors

## Slide 9: Data Flow
File deleted
locally
File uploaded
to a database
Readings stored
into a local .csv file
Run Main
Program
Obtain readings
from the sensors

## Slide 10: Software Framework
Determines the data
taking and uploading intervals
Sensor addresses
Config file

## Slide 11: Software Framework
Responsible for obtaining
readings from sensors
Formats the readings and a header for a .csv file
Sensor Functions
Determines the data
taking and uploading intervals
Sensor addresses
Config file

## Slide 12: Software Framework
Uploads the file to a database
MongoDB
Responsible for obtaining
readings from sensors
Formats the readings and a header for a .csv file
Sensor Functions
Main Program
Determines the data
taking and uploading intervals
Sensor addresses
Config file

## Slide 13: 3D-Printed Case Design
SDP810
Differential Pressure
Cooling
Fan
Raspberry Pi
SPS30 Particulate Sensor
Cooling
Slits
BME280
Temperature,
Pressure, Humidity
Port Openings

## Slide 14: Deployment of the Environmental Monitor
Current placement of the device
Ethernet
Power
Source
Exterior
lab air

## Slide 15
760 Torr = 1 atmosphere
Results
Instrumental resolution = ± 0.01 °C
Instrumental resolution = ± 0.1 Torr
Average Temperature = 21.6 °C - STD = 0.12 °C
Average Pressure = 760.4 Torr - STD = 0.6 Torr

## Slide 16
Instrumental resolution = ± 0.008 %H
Average % Humidity= 58.08 %H - STD = 0.63%

## Slide 17
Positive Pressure lab?
Verify measurements of the sensor
Instrumental resolution = ± 0.1 Pa

## Slide 18
Particulate Sensor results
SPS30
MET ONE

## Slide 19: Particle Counts Comparison
Location | Approximate Counts/L Particle size > 0.5μm
Ambient Air1 | 35000
BνL (SPS30) | 2600
BνL (MET ONE) | 860
SNO LAB2 | 70
* Log scale
2The deepest clean lab in the world - cerncourier.com/a/the-deepest-clean-lab-in-the-world/
1Cleanlab classification - clean-rooms.org/cleanroom-classifications/

## Slide 20: Concluding Remarks
Fully assembled and taking data
Will be uploaded later today onto https://github.com/Brunner-neutrino-lab/
Constructing a second Lab Environmental Monitor

## Slide 21: Acknowledgments
Thanks to:
Robert Turner,
Tsvetelin Totev,
Kevin Murray,
Chris Chambers,
Thomas Brunner,
Soud Al Kharusi