## Slide 1: Scintillating Bubble Chamber Silicon Photomultiplier Analysis
Queen’s University • Ciaran Byles-Ho • Aug. 12, 2022

## Slide 2: Scintillating Bubble Chamber: SBC-LAr10
Quasi-background-free Bubble Chamber
10 kg of liquid argon
Aims to hit lower thresholds (100 eV)
Snowmass 2021 Scintillating Bubble Chambers: Liquid-noble Bubble Chambers for Dark Matter and CEvNS Detection [https://doi.org/10.48550/arXiv.2207.12400]
2
Notes: Liquid argon:
Able to run much lower thresholds than freon bubble chambers while possibly remaining blind to electron recoils

## Slide 3: How does SBC work?
Relies on electron recoils to lose energy through scintillation
Bubbles nucleate after small energy depositions
SiPMs detect scintillation light to veto high energy single-bubble events
Snowmass 2021 Scintillating Bubble Chambers: Liquid-noble Bubble Chambers for Dark Matter and CEvNS Detection [https://doi.org/10.48550/arXiv.2207.12400]
3
Notes: Contains liquid argon in a metastable state to allow the nucleation of bubbles at low energys
Rapid compression allows for

## Slide 4: Silicon Photomultipliers (SiPMs)
Detect single photons near UV to near IR
SBC SiPMs detect LAr and LXe UV light
Consists of many single-photon avalanche photodiodes (microcells)
4
Notes: Recovery time after single photon detection

## Slide 5: Understanding SiPMs
A microcell drifts towards an avalanche region when a photon hits
The microcell then activates a self-sustaining avalanche
Dark Event: generation of pulse without light
  Crosstalk
  After Pulsing
5

## Slide 6: SiPMs Background Crosstalk
Occurs when primary avalanche in one microcell triggers another in an adjacent cell
Occurs in on top or near initial pulse
Causes increased initial pulse magnitude
May have inflection point
6

## Slide 7: SiPMs Background After-Pulsing
There is a probability that an adjacent cell may release a delayed pulse
Occurs in recover phase
Lesser magnitude than original if near original
7

## Slide 8: Motivation
To explore new methods of determining the dark noise rate and cross talk probability using machine learning methodologies and compare to algorithmic approaches.
8

## Slide 9: Pulse Counting with Computational Algorithms
VUV-sensitive Silicon Photomultipliers for Xenon Scintillation Light Detection in nEXO
Jamil et al. 2019
9

## Slide 10: Unsupervised Machine Learning K-means Clustering
50 Clusters • 10 000 Initial Pulses
Cluster 0
Normal 925 Pulses
Cluster 1
Delayed Crosstalk 160 Pulses
Cluster 12
After Pulsing 31 Pulses
10

## Slide 11: Resulting Algorithm
K-means Threshold Determinant
Data Input
Algorithm
Improved pulse parameter error from 20% to 1% on simulated data
11

## Slide 12: Supervised Machine Learning
~4000 hand-picked labels
Algorithm
Machine Learning
12

## Slide 13: Current Results
Traditional Algorithms
Accurately calculates t0
Calculates charge
Near 100% accuracy on simulated data
Machine Learning
Real Dataset
  Near-even distribution of labels
  ~80% accuracy
Trial run
  1000 unseen datapoints
  Uneven distribution of labels
  ~90% Accuracy
13

## Slide 14: Conclusion
Unsupervised ML effectively classifies background groups
Supervised ML can be used for pulse analysis
ML can effectively improve current algorithmic approaches
14

## Slide 15: Thank you
Ciaran Byles-Ho
ciaran.bylesho@queensu.ca
August 15, 2022
CAAST 2022